SUBPART B - STATION OPERATION STANDARDS



97.101  General standards.

     (a) In all respects not specifically covered by FCC Rules each
amateur station must be operated in accordance with good
engineering and good amateur practice.
     (b) Each station licensee and each control operator must
cooperate in selecting transmitting channels and in making the most
effective use of the amateur service frequencies.  No frequency
will be assigned for the exclusive use of any station.
     (c) At all times and on all frequencies, each control operator
must give priority to stations providing emergency communications,
except to stations transmitting communications for training drills
and tests in RACES.
     (d) No amateur operator shall willfully or maliciously
interfere with or cause interference to any radio communication or
signal.



97.103  Station licensee responsibilities.

     (a) The station licensee is responsible for the proper
operation of the station in accordance with the FCC rules.  When
the control operator is a different amateur operator than the
station licensee, both persons are equally responsible for proper
operation of the station.
     (b) The station licensee must designate the station control
operator.  The FCC will presume that the station licensee is also
the control operator, unless documentation to the contrary is in
the station records.
     (c) The station licensee must make the station and the station
records available for inspection upon request by an FCC
representative.  When deemed necessary by an EIC to assure
compliance with FCC Rules, the station licensee must maintain a
record of station operations containing such items of information
as the EIC may require in accord with Section 0.314(x) of the FCC
Rules.



97.105  Control operator duties.

     (a) The control operator must ensure the immediate proper
operation of the station, regardless of the type of control.
     (b) A station may only be operated in the manner and to the
extent permitted by the privileges authorized for the class of
operator license held by the control operator.



97.107  Alien control operator privileges.

     (a) The privileges available to a control operator holding an
amateur service license issued by the Government of Canada are:
          (1) The terms of the "Convention Between the United
States and Canada (TIAS No. 2508) Relating to the Operation by
Citizens of Either Country of Certain Radio Equipment or Stations
in the Other Country;"
          (2) The operating terms and conditions of the amateur
service license issued by the Government of Canada; and
          (3) The applicable provisions of the FCC rules, but not
to exceed the control operator privileges of an FCC-issued Amateur
Extra Class operator license.
     (b) The privileges available to a control operator holding an
FCC-issued reciprocal permit for alien amateur licensee are:
          (1) The terms of the agreement between the alien's
government and the United States;
          (2) The operating terms and conditions of the amateur
service license issued by the alien's government;
          (3) The applicable provisions of the FCC rules, but not
to exceed the control operator privileges of an FCC-issued Amateur
Extra Class operator license; and
          (4) None, if the holder of the reciprocal permit has
obtained an FCC-issued operator/primary station license.
     (c) At any time the FCC may, at its discretion, modify,
suspend, or cancel the amateur service privileges within or over
any area where radio services are regulated by the FCC of any
Canadian amateur service licensee or alien reciprocal permittee.



97.109  Station control.

     (a) Each amateur station must have at least one control point.
     (b) When a station is being locally controlled, the control
operator must be at the control point.  Any station may be locally
controlled.
     (c) When a station is being automatically controlled, the
control operator need not be at the control point.  Only stations
specifically designated elsewhere in this Part may be automatically
controlled.  Automatic control must cease upon notification by an
EIC that the station is transmitting improperly or causing harmful
interference to other stations.  Automatic control must not be
resumed without prior approval of the EIC.
     (d) No station may be automatically controlled while
transmitting third-party traffic, except a station retransmitting
digital packet radio communications on the 6 m and shorter
wavelength bands.  Such stations must be using the American Radio
Relay League, Inc. "AX.25 Amateur Packet-Radio Link-Layer Protocol,
Version 2.0," October 1984 (or compatible).  The retransmitted
messages must originate at a station that is being locally or
remotely controlled.



97.111  Authorized transmissions.

     (a) An amateur station may transmit the following types of
two-way communications:
          (1) Transmissions necessary to exchange messages with
other stations in the amateur service, except with those in any
country whose administration has given notice that it objects to
such communications.  The FCC will issue public notices of current
arrangements for international communications;
          (2) Transmissions necessary to exchange messages with a
station in another FCC-regulated service while providing emergency
communications;
          (3) Transmissions necessary to exchange messages with a
United States government station, necessary to providing
communications in RACES; and
          (4) Transmissions necessary to exchange messages with a
service not regulated by the FCC, but authorized by the FCC to
communicate with amateur stations.  An amateur station may exchange
messages with a participating United States military station during
an Armed Forces Day Communications Test.
     (b) In addition to one-way transmissions specifically
authorized elsewhere in this Part, an amateur station may transmit
the following types of one-way communications:
          (1) Brief transmissions necessary to make adjustments to
the station;
          (2) Brief transmissions necessary to establishing a
two-way intercommunication with other stations;
          (3) Transmissions necessary to remotely control a device
from a distant location;
          (4) Transmissions necessary to providing emergency
communications;
          (5) Transmissions necessary to assisting persons
learning, or improving proficiency in the international Morse code;
and
          (6) Transmissions necessary to disseminate information
bulletins.



97.113  Prohibited transmissions.

     (a) No amateur station shall transmit any communication the
purpose of which is to facilitate the business or commercial
affairs of any party.  No station shall transmit communications as
an alternative to other authorized radio services, except as
necessary to providing emergency communications.  A station may,
however, transmit communications to:
          (1) Facilitate the public's safe observation of, or safe
participation in, a parade, race, marathon or similar public
gathering.  No amateur station shall transmit communications
concerning moving, supplying and quartering observers and
participants for any sponsoring organization unless the principal
beneficiary of such communications is the public and any benefit
to the sponsoring organization is incidental.
          (2) Inform other amateur operators of the availability
of apparatus normally used in an amateur station, including such
apparatus for sale or trade.  This exception is not authorized to
any person seeking to derive a profit by buying or selling such
apparatus on a regular basis.
     (b) No amateur station shall transmit messages for hire, nor
for material compensation, direct or indirect, paid or promised.
The control operator of a club station, however, may accept
compensation for such periods of time during which the station is
transmitting telegraphy practice or information bulletins provided
that:
          (1) The station transmits the telegraphy practice and
information bulletins for at least 40 hours per week;
          (2) The station schedules operations on all amateur
service MF and HF bands using reasonable measures to maximize
coverage;
          (3) The schedule of normal operating times and
frequencies is published at least 30 days in advance of the actual
transmissions; and
          (4) The control operator does not accept any direct or
indirect compensation for periods during which the station is
transmitting any other material.
     (c) No station shall transmit communications in order to
engage in any form of broadcasting, nor to engage in any activity
related to program production or newsgathering for broadcasting
purposes. A station may, however, transmit communications to convey
news information about an event for dissemination to the public
when the following conditions are present:
          (1) The information involves immediate safety of life of
individuals or the immediate protection of property;
          (2) The information is directly related to event;
          (3) The information cannot be transmitted by any other
means because normal communications have been disrupted or because
there are no other communication systems available at the place
where the information is originated; and
          (4) Other means of communication could not be reasonably
provided before or at the time of the event.
     (d) No station shall transmit: music; radiocommunications or
messages for any purpose, or in connection with any activity, that
is contrary to federal, state, or local law; messages in codes or
ciphers where the intent is to obscure the meaning (except where
specifically excepted elsewhere in the Part); obscene, indecent,
or profane words, language, or meaning; and/or false or deceptive
messages or signals.
     (e) No amateur station shall retransmit programs or signals
emanating from any type of radio station other than an amateur
station, except communications originating on United States
Government frequencies between a space shuttle and its associated
Earth stations.  Prior approval for such retransmissions must be
obtained from the National Aeronautics and Space Administration.
Such retransmissions must be for the exclusive use of amateur
operators.
     (f) No amateur station, except an auxiliary, repeater or space
station, may automatically retransmit the radio signals of other
amateur stations.



97.115  Third party communications.

     (a) An amateur station may transmit messages for a third party
to:
          (1) Any station within the jurisdiction of the United
States.
          (2) Any station within the jurisdiction of any foreign
government whose administration has made arrangements with the
United States to allow amateur stations to be used for transmitting
international communications on behalf of third parties.  No
station shall transmit messages for a third party to any station
within the jurisdiction of any foreign government whose
administration has not made such an arrangement.  This prohibition
does not apply to a message for any third party who is eligible to
be a control operator of the station.
     (b) The third party may participate in stating the message
where:
          (1) The control operator is present at the control point
and is continuously monitoring and supervising the third party's
participation; and
          (2) The third party is not a prior amateur service
licensee whose license was revoked; suspended for less than the
balance of the license term and the suspension is still in effect;
suspended for the balance of the license term and relicensing has
not taken place; or surrendered for cancellation following notice
of revocation, suspension, or monetary forfeiture proceedings.  The
third party may not be the subject of a cease and desist order
which relates to amateur service operation and which is still in
effect.
     (c) At the end of an exchange of international third-party
communications, the station must also transmit in the station
identification procedure the call sign of the station with which
a third party message was exchanged.



97.117  International communications.

     Transmissions to a different country, when permitted, shall
be in plain language and shall be limited to messages of a
technical nature relating to tests, and, to remarks of a personal
character for which, by reason of their unimportance, recourse to
the public telecommunications service is not justified.   97.119
Station identification.
     (a) Each amateur station, except a space station or
telecommand station, must transmit its assigned call sign on its
transmitting channel at the end of each communication, and at least
every ten minutes during a communication, for the purpose of
clearly making the source of the transmissions from the station
known to those receiving the transmissions.  No station may
transmit unidentified communications or signals, or transmit as the
station call sign, any call sign not authorized to the station.
     (b) The call sign must be transmitted with an emission
authorized for the transmitting channel in one of the following
ways:
          (1) By a CW emission.  When keyed by an automatic device
used only for identification, the speed must not exceed 20 words
per minute;
          (2) By a phone emission in the English language.  Use of
a standard phonetic alphabet as an aid for correct station
identification is encouraged;
          (3) By a RTTY emission when all or part of the
communications are transmitted in the same digital code as the
station identification, or when the communications consist of a
data emission transmitted on the VHF 6 m or shorter wavelength
band;
          (4) By an image emission conforming to the applicable
transmission standards, either color or monochrome, of section
73.682(a) of the FCC Rules when all or part of the communications
are transmitted in the same image emission; or
          (5) By a CW or phone emission during SS emission
transmission on a narrow bandwidth frequency segment.
Alternatively, by the changing of one or more parameters of the
emission so that a conventional CW or phone emission receiver can
be used to determine the station call sign.
     (c) An indicator may be included with the call sign.  It must
be separated from the call sign by the slant mark or by any
suitable word that denotes the slant mark.
     (d) When the operator license class held by the control
operator exceeds that of the station licensee, an indicator
consisting of the call sign assigned to the control operator's
station must be included after the call sign.
(e) When the control operator is using privileges on the basis of
holding a CSCE, an indicator must be included after the call sign
as follows:
          (1) KT for Technician Class operator;
          (2) AG for General Class operator;
          (3) AA for Advanced Class operator; or
          (4) AE for Amateur Extra Class operator.
     (f) When the station is transmitting under the authority of
a reciprocal permit for alien amateur licensee, an indicator
consisting of the appropriate letter-numeral designating the
station location must be included before the call sign issued to
the station by the licensing country.  When the station is
transmitting under the authority of an amateur service license
issued by the Government of Canada, a station location indicator
must be included after the call sign.  At least once during each
intercommunication, the identification announcement must include
the geographical location as nearly as possible by city and state,
commonwealth or possession.
     (g) A self-assigned indicator may be included after the call
sign.  The identifier must not conflict with any other identifier
specified by the FCC Rules or by a prefix assigned to another
country.



97.121  Restricted operation.
          (a) If the operation of an amateur station causes general
interference to the reception of transmissions from stations
operating in the domestic broadcast service when receivers of good
engineering design, including adequate selectivity characteristics,
are used to receive such transmissions, and this fact is made known
to the amateur station licensee, the amateur station shall not be
operated during the hours from 8 p.m. to 10:30 p.m., local time,
and on Sunday for the additional period from 10:30 a.m. until 1
p.m., local time, upon the frequency or frequencies used when the
interference is created.
     (b) In general, such steps as may be necessary to minimize
interference to stations operating in other services may be
required after investigation by the FCC.