typ colour.txt
GETTING MORE COLOUR FOR YOUR ADAPTER!
-------------------------------------

By:  Andrew Tuline & Byron Sheppard


     Are you feeling limited with 4
colour graphics? Does the hi-res
mode look a little drab? Well, there
are ways to add excitement to your
monochrome and colour graphics. Among
them are artifacting and dithertizing,
two techniques used widely on other
colour computers. 
     Unfortunately for the RGB monitor
owner, those two methods have draw-
backs. In order to understand why, we
must first examine the differences
between the various types of colour
displays used.
     The colour television is the 
most widely used and also the poorest
quality display.  This is due to the
fact that all colour and synchro-
nization signals are combined to form
a single composite video signal. This
is then mixed with a higher frequency
signal, usually channels 2 or 3, and
applied to the  T.V.'s antenna
terminals. From here the T.V. converts
it back to its original form.  This
extra (and redundant) handling 
greatly reduces picture quality.
     The composite video monitor is
a step up from the T.V. The major
difference between the two is that
the composite signal described earlier
does not have to be converted to T.V.
frequencies. This then cuts down on
one of the conversion processes, ther-
eby reducing distortion.  Unfortunate-
ly, due to the complexities of the 
composite video signal, this type
of monitor still is not very good.
     The RGB monitor, recently intro-
duced to personal computing, is the
highest quality colour display
currently available. The reason for
this is that all of the signals are
sent to the monitor on separate wires.
Since this is the way that all the 
monitors actually USE the signals,
the whole series of combining,recom-
bining, and splitting done in the
previous two colour displays is
eliminated.  This simple and straight-
forward approach effectively results
in the RGB type of monitor having a
much higher picture quality.

            Artifacting
   
     The composite monitor and T.V., 
while having lower resolution than the
RGB, are capable of displaying more 
colours by taking advantage of faults
in the composite video signal. This
process is known as artifacting, and 
is the simplest method of increasing 
the number of colours for the display.
It involves drawing lines on alternate
even or odd columns.  Magenta, for
example, appears red if drawn on even
columns and blue if drawn on odd
columns. Unfortunately, this will not
work with RGB monitors.
(See last paragraph for exception.)

Below is a table of colours available
when using this technique.

Normal      Even         Odd
colours    columns      columns
      
Green       Red'         Green'
Red         Red''        Blue
Brown       Red'         Green''
Cyan        Black        Cyan
Magenta     Red          Blue
White       Brown        Cyan

The quotation marks beside the colours
represent a slightly different shade
of the original colour.

        Dithertizing

The next step in adding more colours
to your display is to use a technique
called dithertizing. It involves
setting points in a checkerboard
pattern of different colours. You
could, for instance, set all even
columns and rows to red, all odd rows
and columns to green, and the rest to
yellow, producing some alternate
colour.  Since this technique doesn't
depend on "faults" in the video
signal, it will work on RGB type
monitors.  The main drawback of this
technique is the increased time
necessary to draw a picture. However,
with the use of assembly language 
subroutines and/or preset shape
tables, you could speed up any
graphics action.

       Some Program Examples
   
     Using artifacting, the following
short program will show lots of 
colours in the medium resolution mode.

10 SCREEN 1,0
20 FOR I=0 TO 50
30 LINE (I,0)-(I,50),RND*4
40 NEXT
50 GOTO 20

It is even possible to turn the
"hi-res" monochrome mode into a multi
coloured spectacle with a change in
line 10.
 
10 SCREEN 2:OUT 984,&HA:OUT 985,&H32

OUT 984,&HA- Selects 320x200 colour
             graphics.
OUT 985,&H32- is binary 00110010
                          ^^  ^
     selects cyan palette-!!  !
     selects intensified---!  !
     select green backgnd.----!

The last addition will allow an RGB
monitor to use the standard 3 colour
palette. Otherwise, when using the
composite video input, there are many
colours available, even in this mode.

For more information, please refer
to pages 2-57 to 2-59 of the Technical
Reference Manual. More advanced 
programmers should also refer to the
BIOS video section starting on page
A-43.

     There is a device available for 
owners of RGB monitors which will
allow the use of the techniques
previously described. It is called an
N.T.S.C. demodulator, and converts the
composite video signal to RGB format.
The demodulator is manufactured by
Electrohome (model# I-1302) and is
available from the Byte shop for about
$100. Incidentally, the N.T.S.C. 
module enables you to attach your RGB
monitor to a video recorder or T.V.
tuner. In this case, it makes an 
excellent television monitor.


     
    MEDIUM RESOLUTION GRAPHICS MODE
    -------------------------------

          By: Andrew Tuline


     It   seems  someone  has  finally
found the 160 X 100 graphics mode I've
been having so much trouble with. It's
in the Dec.  82  issue  of  Dr.  Dobbs
Journal   by  John  Seal  of  Franklin
Indiana.

     Starting in  the  80  X  25  text
mode,  the  user  must  split a single
character    into    foreground    and
background  by  poking  character  222
into the display buffer. Then the 6845
CRT controller is set to  squeeze  the
four  video  pages  onto  one  screen,
effectively  giving  100   points   of
vertical   resolution.   To   set  the
points, the user must set  either  the
foreground,  or  background attributes
depending   on  the  location  of  the
character.   Below  is  a  copy of the
program submitted by the author.

100 '
110 'Set up low resolution 160 X 100
115 '    16-color graphics mode
120 '
130 SCREEN 0 : WIDTH 80          ' set up 80 X 25 alpha
140 KEY OFF : CLS                ' clear screen
150 OUT &H3D8,9                  'disable blink attribs
160 A%=&H3D4 : D%=&H3D5          ' crt controller ports
170 OUT A%,4 : OUT D%,&H7F       ' vertical total
180 OUT A%,6 : OUT D%,&H64       ' vertical displayed
190 OUT A%,7 : OUT D%,&H70       ' vert sync position
200 OUT A%,9 : OUT D%,1          ' max scan line addr
210 DEF SEG=&HB800               ' display buffer seg
220 FOR CC%=0 TO &H3FFE STEP 2   ' all character codes
230 POKE CC%,&HDE : NEXT         ' set to special char
240 FOR AT%=1 TO &H3FFF STEP 2   ' all attributes
250 POKE AT%,0 : NEXT            ' preset to black
260 '
270 ' Compute offset into display
275 '   buffer, based on X and Y
280 '
290 DEF FNOFFSET%(X%,Y%) =160 * Y% + (X% OR 1)
300 '
310 END

        Addenda
        -------

     An easy way to set the width to 40 while in 
screen 2 and then converting back without clearing
the screen or using get/put graphics is by typing:

def seg=&H40:poke &H49,4 'sets width 40
def seg=&H40:poke &H49,6 'sets width 80

     There is a video data area used by the BIOS
in Segment &H40 starting at address &H49 to 
address &H66. Again, refer to the technical manual
page A-3 for further information.

     An interesting mode of resolution I found
a long time ago while in screen 2 is as follows:

out 984,&H18

This is similar to the 160 X 100 mode shown above,
but unfortunately I have been unable to decode the
colour pattern.

     Also, the user could try to change the 
parameters of the 6845 Display Chip itself. There
are 19 registers in the 6845. 18 of them are 
addressed by the first one by the following. For
example, if we wanted to put a &H64 to register
6 we would type the following:

out &H3d4,6     ;set address register to point
                ;to register 6
out &H3d5,&H64  ;put &H64 into register 6 of 
                ;display chip.

Each of these registers controls different 
parameters for the display, such as the 
starting address of the display, the cursor
address, the total number of lines displayed
and so on. See page 2-56 of technical manual.

     Finally, to wrap it up, I'd like to say that
although I was initially dismayed at the resolution
of the colour graphics on the PC, I also found that
to do any reasonable animation that too many pixels
causes the speed to reduce drastically. While we may
not have 16 shades of each colour as on the Atari,
we do have enough to keep us busy. Maybe the next
version of the Flight Simulator will allow the
owners of RGB monitors to also enjoy the colour
of flight.


SIG/Access: