typ cpcpro

How to Print Screen from a Basic Program
(C) Copyright 1982, Peter Norton, author of The Norton Utilities for the IBM
PC)

When BASIC is operating on the IBM Personal Computer, the "print-screen" 
function doesn't work.  This article shows how your BASIC programs can perform
a print screen operation, and gives you an opportunity to learn more about how
the IBM PC works.

Before we explain it all, here is how to print-screen in BASIC.  First, you  
must set up a print-screen routine by executing these instructions, once:
        DEF SEG = 4095
        POKE 0, 205   :   POKE 1, 5   :   POKE 2, 203
        PRINT.SCREEN = 0
Then, your programs can print the screen contents at any time, by executing:
        CALL PRINT.SCREEN
As long as the "DEF SEG" hasn't been changed, then CALL statement will print
the current screen display.

This bit of BASIC program doesn't make the "PrtSc" key work-- it lets your
programs perform the print-screen function.  Your program must decide when to
print the screen, perhaps by acting on a special keystroke.

To understand how this works, we have to touch on some of the most fundamental
parts of the IBM PC.

Built into the IBM PC, in the read-only-memory, or ROM, are many service
routines that perform operations that are basic to the computer; among them is
the print-screen operation.  These services are activated by a mechanism known
as a "software interrupt," and print-screen is requested with interrupt number
5.

The programs that service the keyboard are also found in the ROM.  The ordinary
keyboard service program always checks for the "PrtSc" key: when this key is
pressed, the keyboard program performs an interrupt #5, and the screen is
printed.  The keyboard service routine uses interrupt #5, but doesn't own it
exclusively-- any program that knows how to request interrupts can use it.

When BASIC is running, BASIC takes charge of the keyboard, and so the regular
ROM keyboard program doesn't see the PrtSc key, and BASIC ignores this key.
This prevents us from using the PrtSc key to print the screen.

So, the print-screen operation is not available in BASIC, ordinarily.  But
BASIC has the ability to accept and perform machine language subroutines.  If
we set up a program that will request interrupt 5, then we can CALL it, and
print the screen.  That is what the BASIC program above does.  

Here's how it works.  Our machine language program consists of only two
instructions: one to request interrupt five, and the other to return to the
caller.  The "interrupt" instruction is two bytes long, and the "return" is
one, for a total of three bytes.  The three POKE statements above create those
three bytes.  The numeric values 205 and 5 are the interrupt #5 instruction,
and the value 203 is the return instruction.

There is one messy little problem that occurs whenever machine-language
programs are used in BASIC-- where to put them.  There is no one clean simple
way to deal with this problem; it has to be solved differently depending upon
the size of the computer's memory, and upon what else a BASIC program might do
with "DEF SEG" related statements.

The example above is set up for a computer with 64K of memory, and places the
print-screen program in the last 16 bytes of memory.  For another memory size,
"X" expressed in kilobytes, or "K," this formula will do the same 
        DEF SEG = X * 64 - 1
If X is 64K, then this formula works out to 4095, which is the number used in
the example above.
    
If your programs set the "DEF SEG" for any other reason, then it will have to
be coordinated with its use for the PRINT.SCREEN program, or any other such
machine language program.  When PRINT.SCREEN is called, DEF SEG must be set to
the same value used when the program was created with the POKE statements.



Printer Bit Image Graphics Demonstration 
by Dave Browning

This program demonstrates a portion of the Epson printer graphics capabilities
when the printer is connected to an IBM PC.

This program has been tested for an Epson MX-100 which comes with the
GraftraxPlus option standard.  Although not tested, the program should also 
run as is for an Epson MX-80 with the Graftrax option.  The program should 
also run as is for an Epson MX-70.  (The MX-70 has only normal density bit 
image graphics mode, as opposed to dual selectable modes on the MX-80 with 
Graftrax or the MX-100, but this program does not utilize the higher density 
mode.)

The reason for the WIDTH "LPT1:",255 statement in line 120 (use this statement
as is even if you have an 80 column printer), and for opening the printer
"LPT1:" as file #1 in line 130 is to suppress the line feed that Basic and
Basica automatically send after each carriage return (ASCII 13).  Since Basic
does not check context to distinguish between an actual carriage return and a
character with the value 13 used for other purposes, it adds a line feed (ASCII
10) after every character 13 output with a PRINT, PRINT #, PRINT USING, PRINT #
USING, or WRITE # statement.  The WIDTH #1,255 statement suppresses the
linefeed normally added to the end of lines also, so the program has to add it
where needed (the CHR$(10) at the end of line 3000).

This subject is addressed in part in several places in the IBM Basic manual. 
See the OPEN and WIDTH statements as well as the print and write statements
mentioned above.  You may test this by removing the OPEN and WIDTH statements
from the program and changing all PRINT #1 xxxxx statements to LPRINT xxxxx.

If this program still seems to be putting line feeds in strange places, you
might check your printer switches for proper setting.  Switch SW2-3 on the MX-
80 and MX-100 can be set to automatically add line feeds within the printer no
matter what the computer does.  See your printer manual for details of getting
at and setting the proper switch.

After running the program as is, you may want to experiment with different
settings of the parameters such as PRTLENGTH.  For MX-100s and MX-80s with 
GraftraxPlus, changing the 75 in line 2020 to 76 will set the printer to high 
resolution graphics (twice as many dots per inch).  Those with the MX-80 and 
MX-100 GraftraxPlus printer manual can now proceed with the excellent 
tutorials on bit graphics included in it.  Since the manual does not have a lot
of information on the IBM PC connection, this program was developed to show how
to overcome the "automatic linefeed" types of problems.

One additional note:  if you stop the program during execution with a control-
break, the printer may be in the middle of graphics mode and be waiting for
more graphics characters.  If you then try to RUN the program (with or without
changes) again, the printer may seem to do weird things until the buffer and
the program are back in synch.  Everything will be OK if the program runs to
completion, or if you turn the printer power off momentarily before reRUNning
the program.


100 '*** PRINTER BIT IMAGE GRAPHICS DEMONSTRATION ***
105 '***    PROVIDED BY DAVE BROWNING 1/10/83    ***
110 'set up BASIC to suppress automatic line feeds
120 WIDTH "LPT1:",255
130 OPEN "LPT1:" AS #1
140 GOTO 1000
200 'subroutine to output one character to printer
210 PRINT #1, CHR$(X);
220 RETURN
1000 ' ***  PRINTER TEST PROGRAM  *****
1010 DEFINT A-Z       'runs faster using integers
1020 CHRSTART = 0     'first graphics character to print
1030 CHREND = 255     'last graphics character to print
1040 PRTLENGTH = 50   'number of times to repeat the
         graphics char
1050 PRTLEN1 = PRTLENGTH MOD 256
        'printer expects two numbers-first remainder
1060 PRTLEN2 = PRTLENGTH \ 256
        'then number of "256's"
2000 FOR GRAFCHAR = CHRSTART TO CHREND 
        'repeats for graphics characters
2010 X = 27 : GOSUB 200   'sends <ESC> character
2020 X = 75 : GOSUB 200 
        'sends char K to shift printer to graphics
2040 X = PRTLEN1 : GOSUB 200 
        'sends n1 (# bit images modulo 256)
2060 X = PRTLEN2 : GOSUB 200
        'sends n2 (# bit images times 256)(n2 max is 7)
2070 FOR I = 1 TO PRTLENGTH 'send same character PRTLENGTH times
2080   X = GRAFCHAR : GOSUB 200 'send the character
2090 NEXT I
3000 PRINT #1, "   X = ";X;CHR$(10);
         'notes which graphics character was
3010 'printed, and sends line feed.
         This flushes the printer buffer and
3020 'returns the print head to the
         beginning of the next line.
3030 NEXT GRAFCHAR  'loop back for next character
3040 CLOSE #1 'resets the WIDTH statement to default
3050 END

PC Keyboarding for the Handicapped
by Mike Todd

A couple of months ago I received a letter from someone I greatly respect. 
Since he is handicapped, he is unable to press two keys on the keyboard
simultaneously. He asked if there was a way to create a CTRL, SHIFT, and/or ALT
lock through the keyboard so that he might be able to do a system reboot, use
Wordstar (or any other program that requires simultaneous pressing of multiple
keys), and whatever anyone else can do on a PC.  I mentioned the need at a
Capital PC general meeting and asked that someone with a little spare time just
take a look at how it might be done. John Black came to the rescue!  He didn't
just tell us how to do it but produced a sophisticated program and some really 
good documentation too! Thank you, John!

The program, called KEYLOC.EXE, along with the source code and documentation,
will be on the next Capital PC Software Exchange disk ($5 and stamped, self
addressed mailer to Capital PC Software Exchange, PO Box 6128, Silver Spring,
MD 20906).  The following is taken from the introduction to John's
documentation:

    Keyloc is a patch to the BIOS keyboard routine. It modifies the operation
    of the Alt, Ctrl, Left Shift and Right Shift keys. It allows one finger
    typing by locking those keys in their shifted state.

    Normally the Ctrl, Alt, Left Shift, and Right Shift keys have to be held
    down with one finger, while another finger is used to type another key. For
    example, if a program requires you to enter a ^P, you must hold down the
    Ctrl key with one finger, then depress the "P" key with another.

    When Keyloc is loaded into memory--this is done in DOS before executing the
    program--it changes the way these keys operate. To type in a ^P, you first
    type and release the Ctrl key. This locks the Ctrl key in its shifted
    state. Next the "P" key is depressed and released.  This enters a ^P.
    Depressing Ctrl again takes the key from its shifted to unshifted state.

    Keyloc gives an audio signal so the user can tell when he is shifting or
    unshifting a key. The first time the Ctrl key is depressed, a low tone
    followed by a high tone is sounded. This signals that the key has been put
    in the shifted state. The next time the Ctrl key is depressed, a low tone
    followed by a high tone is sounded. This signals that the key has been
    returned to the unshifted state.

I've tried John's program in DOS, from within Basic, with a Basic program,
right now with Volkswriter running, and with Wordstar. I haven't found a single
bug and the audible tones are separated enough to be useful, at first, but not
so much that they would become annoying after long hours at the keyboard. As a
matter of fact, some users who would just like to strike a single key at a time
may not find the new procedure too hard to accommodate.


Some Useful BASIC Function Definitions
by Harry Foxwell, SigSTAT chairman, Capital PC

Conspicuously missing from IBM Basic are predefined functions for computing the
maximum and the minimum of two numbers, and a function for converting a
character string from lowercase to uppercase.

Although it is fairly simple to code these functions with a few lines using IF
statements, using predefined functions makes the overall program more compact
and easily readable.

The maximum and minimum of two values can be computed using the following
functions:

    DEF FNMAX(X,Y) = X*ABS(X>=Y) + Y*ABS(X<Y)
    DEF FNMIN(X,Y) = X*ABS(X<=Y) + Y*ABS(X>Y)

A function that converts a lowercase letter to its uppercase equivalent is:

    DEF FNUCS$(A$) = CHR$(ASC(A$)+32*(A$>="a" AND A$<="z"))

Each of these function definitions depends upon the fact that the comparison
operators (<, >, and =) yield a value of 0 when the comparison is FALSE, and
yield -1 when the comparison is TRUE. These values, expressed simply as the  
original comparison, may be used in the same way as any other BASIC variable.



SIG/Access: