Patches for IBM's Personal Editor (PE):
   These were garnered from various BBS's & have been combined into one file.


===============================================================================

                 Written by James L.  Johnsen April 1st,1983

     This   write up is aimed at those people or persons who  have the   color
card  and a color monitor and the IBM Personal  Editor.  I'll  show you how to
change  some values in the .EXE file to give you colors while in the  Personal
Editor that you probably weren't of.

     Doing   this modification does not affect the performance  of your   per-
sonal editor in reguards to functions that it   performs.  It only causes  the
color(s)  of text either entered by you or text output by the Personal  Editor
to show up in colors of your choosing.

     This  mod  must be done (even if you do own DOS 2.00) from  or  with  DOS
1.10.    The  reason for this is that the first step in the mod  process is to
rename  PE.EXE to PE.COM.   The main reason  for renaming  the file  extension
from  .EXE to .COM is that the  DEBUG program will not allow you to write  the
changed  file back to disk if the file name had or has the extension of  .EXE.
There  would  be no  reason  NOT  to  use DOS 2.00 in this mod   except   that
I've  noticed  that if you rename a .EXE file to fname.COM and load   it  into
the  DEBUGger  then the DEBUG program recognizes that the file used to  be  of
extension .EXE because,   (in my best guess), of the header in all .EXE files.
There is a byte in the .EXE header that tells the command.  processor wheather
or not it is a valid  .EXE file.   I'm sure that the DOS 2.00 version of DEBUG
checks  that  or  the  command processor checks it and tells DEBUG  that  even
though the file had the extension of .COM that it's really a .EXE   file.  The
end   result is that DEBUG won't let you write the file  back off to the  disk
after you load it.

     DOS  1.10 version of the DEBUG program isn't that smart.   You can change
the extension from .EXE to .COM and the DEBUG  program will  go ahead and load
it  at  location 'X':0100.   That's why  the file is renamed and DOS  1.10  is
used.
------------------------------------------------------------------------------
                 What to do, how to do it and why it's done.

     First,   copy PE.EXE and PE.PRO and DEBUG.COM over to a WORK-DISK. Assume
that the work disk is in drive A>.

From Drive A>.

A>RENAME PE.EXE PE.COM <CR>
A>DEBUG <CR>
-N PE.COM <CR>
-L <CR>
-D A260 L10 <CR>

this is the output you should see;

'X':A260   07  70  17  71 71 07 04 00-BA 03 00 B0  50  00  28  00  [whatever]

location:      Value:    Function:
---------      ------    ---------

A260           07        Color  of text you see on the edit screen.  This  can
                         either  be  text  that you load into  the  editor  or
                         something that you type in yourself.

A261           70        Color  the text becomes when you mark it  for  either
                         moving or copying or what-have-you.

A262           17        Color  used  when you press the ESCAPE KEY  to  leave
                         entering text in the editor to the COMMAND LINE.  The
                         character  where  the cursor was is left 'MARKED'  on
                         the  edit screen.  This is the color value  for  that
                         'marker'.  Specifically, this is the color value used
                         when  leaving the edit screen if the cursor is on  an
                         unmarked (for block copy or move etc..) area of text.

A263           71        Color  used  when you press the ESCAPE KEY  to  leave
                         entering text in the editor to the COMMAND LINE.  The
                         character  where  the cursor was is left 'MARKED'  on
                         the edit screen. Unlike above (A262) this color value
                         is used if the cursor was resting on a marked area of
                         text (for block copy or move etc..).

A264           71        Color of text on the COMMAND LINE as you type it on
                         the command line. The '7' in the '71' is the color
                         used for the COMMAND LINE. On every monitor I've
                         seen, this color is low intensity white or grey.

A265           07        Color of text beneath the COMMAND LINE. This color is
                         used  for  the text 'Replace' and  'Insert'  and  the
                         numbers  that tell you what row and what column  your
                         currently type at.

A266           04        Color used for the error messages.

Things to keep in mind if you want to change the color values to get different
colors for the areas they affect.

First,  you must understand what the format is for the color values that we've
just  looked at.  The values were of cource in hex and of cource we're  two(2)
digit values, two numbers or letters, (in our case numbers).

Lets  look  at  two locations,  A260 and A261 to understand  the  color  value
format.

Location A260. The value there is 07. On the AMDEK COLOR II and NEC JC1202 RGB
monitors (and more than likely the new IBM Color Monitor), 07 is the attribute
for Low Intensity White, or Grey if you like. Lets take it apart.

The zero(0) of the '07' is the color used for the Background color.
The seven(7) of the '07' is the color used for the Forground color.

You  should understand that any number,  0 through 7 in the Background part of
the value does not cause the Forground characters to blink.  Number  eight(8),
number  nine(9)  and  characters 'A through F' in the Background part  of  the
value will cause the Forground characters to BLINK. So, unless you like blink-
ing Forground characters on your screen,  don't use number eight(8) or  number
nine(9)  or  characters 'A through F' in the Background part of the  attribute
value.

Also,  you  should be aware that numbers zero(0) through seven(7) in the  For-
ground part of the value (on every monitor I've ever seen color on), cause the
color  of the text displayed on the screen to be of low  intensity.  I'm  sure
that  the  hardware on these monitors are 'seeing' that if the 'I' bit is  OFF
(numbers  zero(0)  through seven(7)) that there is no  added  intensity.  That
seems  to make sence and in fact that is how it appears on the AMDEK COLOR  II
and the modified NEC JC1202 RGB's.

Numbers  eight(8)  and nine(9) and characters 'A through F' in  the  Forground
part of the attribute value cause the Forground characters to be of a brighter
intensity.

If  your  undecided about what colors you would like for what,  then  take  my
suggestion and enter the values into the locations outlined below.

example to try----after all, you can always change them if you don't like it.

From DEBUG


If  you arn't familiar with DEBUGS' E)nter command then please read that  sec-
tion in the DOS manual before attempting to ENTER the values for this  example
below.

-E A260 <cr>

L = Low Intensity
H = High Intensity

Preceeding character is first letter of color name except for 'Z' which is
Black.
                           Color                                   Color
location: Old Value: Forgnd     Bakgnd location:  New Value: Forgnd     Bakgnd
--------- ---------- ----------------- ---------  ---------- -----------------
A260         07      W L        Z L    A260          0F      W H        Z L
A261         70      Z L        W L    A261          1B      C H        B L
A262         17      W L        B L    A262          7C      R H        W L
A263         71      B L        W L    A263          1E      Y H        B L
A264         71      B L        W L    A264          1E      Y H        B L
A265         07      W L        Z L    A265          0A      G H        Z L
A266         04      R L        Z L    A266          0C      R H        Z L
------------------------------------------------------------------------------

                      TABLE OF COLOR VALUES TO CHOOSE FROM
______________________________________________________________________________
LOW INTENSITY NONBLINKING FORGROUND    | HIGH INTENSITY NONBLINKING FORGROUND
   COLORS WITH BLACK BACKGROUNDS       |    COLORS WITH BLACK BACKGROUNDS
------------------------------------------------------------------------------
BLACK           00                     |BLACK             08
BLUE            01                     |BLUE              09
GREEN           02                     |GREEN             0A
CYAN            03                     |CYAN              0B
RED             04                     |RED               0C
MAGENTA         05                     |MAGENTA           0D
YELLOW          06  looks brown        |YELLOW            0E
WHITE           07  looks grey         |WHITE             0F
______________________________________________________________________________
LOW INTENSITY BLINKING FORGROUND       | HIGH INTENSITY BLINKING FORGROUND
 COLORS WITH BLACK BACKGROUNDS         |   COLORS WITH BLACK BACKGROUNDS
------------------------------------------------------------------------------
BLACK           80                     |BLACK             88
BLUE            81                     |BLUE              89
GREEN           82                     |GREEN             8A
CYAN            83                     |CYAN              8B
RED             84                     |RED               8C
MAGENTA         85                     |MAGENTA           8D
YELLOW          86                     |YELLOW            8E
WHITE           87                     |WHITE             8F
______________________________________________________________________________
BACKGROUND COLORS WITH A BLACK FORGROUND COLOR [all are Low Intensity]
------------------------------------------------------------------------------
                                        Note:  You  can substitute any of  the
                                        columns  that either have an '8' or  a
                                        '0'  in  it with any  of  the  numbers
                                        listed  to  the left for a  background
                                        color  to go with the forground  color
                                        you choose. Remember any number in the
                                        left  column with a value  of  atleast
                                        '8'  but not greater than 'F' hex will
                                        cause   the  forground  character   to
                                        blink. The background values listed to
                                        the  left in the left column will  not
                                        cause   the  forground  character   to
                                        blink.
------------------------------------------------------------------------------

           ********************EXACT PROCEDURE********************

------------------------------------------------------------------------------
COPY B:DEBUG.COM
        1 File(s) copied
A>COPY B:PE.*
PE       EXE
PE       PRO
        2 File(s) copied
A>RENAME PE.EXE PE.COM

A>DEBUG
-F100 FFFF 00 <cr>
-N PE.COM <cr>
-L <cr>
-DA260 L10 <cr>
0C39:A260  07 70 17 71 71 07 04 00-BA 03 00 B0 50 00 28 00   .p.qq...:..0P.(.
-EA260 <cr>
0C39:A260  07.0F   70.     17.7C   71.1E   71.1E   07.0A   04.0C <cr>
-W <cr>
Writing B280 bytes
-Q <cr>

A>RENAME PE.COM PE.EXE

A>PE <cr>   and away you go!!!




===============================================================================




           *** Bypass the Professional Editor Logo ***

The Professional Editor, when invoked, displays a Logo and Copyright
Notice for approximately three (3) seconds before switching to the
initial options menu. The following patch bypasses this step, allowing
quicker initialization.

To do this, we replace the CALL to the routine that writes the Logo
and waits 3 seconds with NOP instructions. There is no real NOP
instruction for an 8088, so a XCH AX (&H90) is used.

Unfortunately, Debug can not handle the editor as a file, since it
can't 'unrelocate' an EXE file to write it back. Therefore, we have
to do the patch in sector mode.

We need to change the 102nd sector of the program. The easiest way to
find that sector (since DOS doesn't write a file in contiguous sectors)
is to format a new diskette, and copy the EDIT.EXE file to it. This
insures that contiguous sector allocation will be done. For double
sided drives, format with the /1 option to force single sided. For
DOS 2.0 users, use the /8 option as well.

Try the following after copying EDIT.EXE to the clean diskette:

  1. Put the target diskette in drive B:
  2. Invoke debug                        DEBUG
  3. Load the target sector              -L 100 1 6C 1
  4. Edit the CALL at +29 to a NOP       -E 129 E8.90 95.90 18.90
  5. Write the sector back to diskette   -W 100 1 6C 1
  6. Exit from Debug                     -Q

Now invoke this copy of EDIT.EXE to make sure it still works.
If it does, then you can copy it back over to your system diskette(s).

Brian Pierce
Rockville, MD




===============================================================================




Modification of the PERSONAL EDITOR to eliminate the IBM logo and
to change where he looks for pe.pro.

 1. ren pe.exe pe.zap  ( we must rename .exe for the debugger )

 2. debug pe.zap        ( use debug to make mods )

 3.a. To eliminate the IBM logo.

    -e d95 eb 2d ( should contain ff 36 before mod )
    -e dda d     ( should contain 78 before mod )

   b. To change where the PERSONAL EDITOR looks for pe.pro.

    -e b084 "c:pe.pro"  (This is the filespec for the pe.pro file.
                         It must not include a path name and must
                         not exceed 14 characters in length.  I
                         use drive 'c:' as an electronic drive which
                         has pe.pro copied to it by the autoexec.bat file.)
    -e e86 8 ( This is the length of the above filespec )

 4. -w ( to write modified pe.zap back to disk )

 5. rename pe.zap pex.exe ( make it executable again )

This works with either DOS 1.1 or DOS 2.0 and is especially nice for
DOS 2.0 since it allows you to keep only one copy of pe.pro.

Ted Reuss  Houston, Tx  August 1983


===============================================================================

End of PE patches file.