DESCRIPTION

		Copyright (c) 1983 by Bradley H. Hanson.

   Permission is granted for private, non-profit use.  This program
   may NOT be used for trade or sale.  Comments or corrections should
   be directed to:

          Brad Hanson,  3685 Eastwood Court, Bettendorf, IA  52722
                   319/332-4984, CompuServe 72115,22

  This contains a series of screen service routines for access
  from a BASIC program.  They can be loaded into a string array
  or unused file buffer in the program and then directly CALLed
  after defining entry variables to the routines.

  The following is a summary of the routines defined.  An expanded
  description can be found in the file SCRN.DOC.

  First the routine must be loaded into memory and a variable defined to
  point to the first byte of the code.  In this example the variable Z
  will point to the first byte and then the following entry variables 
  are then defined to enter the actual routines:

  SCRN=Z+2:  SCU=Z+4:  SCD=Z+6:  CEOL=Z+8:  CEOS=Z+10
  ATRB=Z+12: DEFW=Z+14

  The actual variables used in the program can named different than those
  listed above but the relative offset into the code must remain the same.

  Routine and location definitions using the variables defined above:

  SCRN  - POKE location to define the current window

          POKE SCRN,value  ' value is a number from 1 to 6 initial value=1

  SCU - Scroll the window up function

         I%=value:  CALL SCU(I%) ' Scroll <value> lines up.  Clear window if
                                    value=0.  Argument must be an integer.

  SCD - Scroll the window down function

          I%=value:  CALL SCD(I%) ' Scroll <value> lines down.  Clear window
                                 if value=0.  Argument must be an integer.

  CEOL - Clear from cursor to end of line with spaces

          CALL CEOL  ' No arguments allowed.  Cursor must be positioned within
                       the current window.

  CEOS - Clear from cursor to end of window with spaces

          CALL CEOS  ' No arguments allowed.  Cursor must be positioned within
                       the current window.

  ATRB - Change the default attribute in the window

          I%=value:  CALL ATRB(I%) ' Change space fill attribute to <value>

  DEFW - Define a window.  Up to six windows can be defined.  The current
         window will be changed to the window number defined.  Six arguments
         are required as follows:

         A1% - Screen number to define.  Value from 1 to 6.
         A2% - Upper left corner row position (1 to 24).
         A3% - Upper left corner column position (1 to 80).
         A4% - Lower right corner row position (1 to 24, >= A2).
         A5% - Lower right corner column position (1 to 80, >= A4).
         A6% - Attribute byte for space fill characters.
    Call:
         CALL DEFW(A1%,A2%,A3%,A4%,A5%,A6%)

    When initially loaded window 1 is defined with the following values:

         A1=1: A2=1: A3=1: A4=24: A5=80: A6=7