ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                      ³ On The Topic of 450 Baud! ³
                      ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

                           by Scott Loftesness
                              May  28, 1983

          Many users have asked about using 450 baud with this
RBBS system.  Typically, they are asking why such an option
exists (the N option on the main RBBS menu) when their modem and
IBM-PC BASIC don't appear to support such a speed.

          They are correct about IBM-PC BASIC not supporting 450
baud. In fact, the ROM BIOS routines in the PC don't support 450
baud as an option either.  It's not that IBM or Microsoft skipped
the speed when they developed the PC, but the fact that 450 baud
is not a standard communications speed for the RS-232-C
interface.  The next higher 'standard' speed above 300 baud is
600 baud, followed by 1200 baud, etc.  As a result, 450 baud is
not supported on most personal computer systems.

          As it turns out, however, most 300 baud modems will run
at somewhat higher speeds - up to, guess what!, 450 baud in most
cases. Although a somewhat higher error rate can be expected when
you "push" a 300 baud modem to 450 baud, the error rate is
typically still low enough to not be any kind of serious problem
to file transfer and message passing operations.  In fact, using
the XMODEM file transfer protocol, errors which do occur are
normally detected by the check sum error detection scheme used by
XMODEM and simply force a re-transmission of the block originally
received in error.

          Since the speed advantage of 450 over 300 baud can be
substantial, and since we are all interested in doing the most
work in the least amount of time with the equipment at hand, many
users have implemented 450 baud as an option which can used with
their "home-grown" communications programs.  (Note that standard
IBM-PC communications packages don't support 450 baud either -
such as PC-Talk III). I'll describe how 450 baud can be
implemented from a programming standpoint shortly. But first,
let's get rid of a few erroneous impressions about modem
operation.

          Your Hayes 300 baud SmartModem (or a Hayes 1200 running
in 300 baud mode) is capable of receiving modem commands and data
at up to 1200 baud.  What this means is that the microprocessor
in the Hayes is programmed to automatically look for the AT
command sequence - and performs automatic baud rate detection at
the speed you happen to be sending the command sequence to the
modem. This capability, for example, is used in the RBBS code to
send the various modem commands at 1200 baud - to minimize the
time spent sending them!

          Your Hayes 300 will even try to send data across the
line at 1200 baud - if you open your communications line at that
speed and attempt to go to data mode. However, the 300 is not
capable of handling data at that speed - in fact, it can only
transmit and receive data at up to slightly more than 450 baud -
with any reasonable error rate. Since the Hayes doesn't care at
what rate is receives data (anything from 1 to 1200 baud is
acceptable), it is possible to transmit data to the modem and have
the modem transmit it to the phone line at any of those speeds.
However, 450 baud is the reasonable upper limit for data
communications with the Hayes 300.

          Now that we understand the workings of the Hayes modem,
let's talk about how we can get the PC to send data from its
RS-232-C Asynchronous Communications Adapter at 450 baud. As
mentioned earlier, 450 is not an acceptable option to either the
BASIC OPEN statement or to the direct BIOS calls for asychronous
communications. However, as always, almost *anything* is possible
using software! The IBM ACA uses an 8250 chip which is capable of
running at speeds from 1 to 19,600 baud (officially, only up to
9600 baud, but that's another discussion!). The 8250 includes an
on-chip software programmable baud rate generator - which
actually determines the speed used to send and receive data
across the RS-232-C interface. This baud rate generator can be
programmed to run at *any* baud rate between 1 and 19,600 baud.
The IBM-PC ROM BIOS routines, however, were programmed to only
support the "standard" RS-232-C speeds. Since BASIC uses the BIOS
routines, BASIC only supports those same "standard" speeds.

          However, it is possible for you to program the 8250 to
run at any speed you like. In this case, we are only interested
in programming it to run at 450 baud. Programming the baud rate
generator in the 8250 consists of loading the baud rate generator
on the chip with a "baud rate divisor" - which takes the clock
frequency and divides it by the number you provide to come up
with the baud rate itself. (Those of you with Technical Reference
manuals for the PC can read all about this on pages 2-135 to
2-137). The divisor is a two byte value - which is stored into
two one byte registers within the 8250 chip. First, we need to
determine what the baud rate divisor should be for 450 baud
operation. Take it from me that the value is X'0100'.  Next, we
need to get this value from a BASIC program into the 8250 itself.
Fortunately, BASIC includes the OUT statement - which allows us
to send data to the various I/O ports on the system. The 8250
uses several of these ports - for the baud rate divisior, modem
control, and for actually sending and receiving the data across
the RS-232-C interface.

          The baud rate divisor ports are X'3F8' for the least
significant byte and X'3F9' for the most significant byte - when
using the COM1 port. (COM2 addresses are X'2F8' and X'2F9'
respectively. Before we can load these divisor ports, however, we
must load another value to another port to indicate that we are
setting the baud rate divisor. This third port is the Line
Control Register and is port X'3FB' (X'2FB' for COM2). The high
order bit (X'80') of the LCR controls access to the baud rate
divisor registers. When this bit is 1, we can load the baud rate
divisors. When it is 0, the 8250 resumes operation with the baud
rate loaded. The following sequence of BASIC statements will load
the baud rate divisor registers:

      OUT &H3FB, (INP(&H3FB) AND &H80) 'Enable divisor registers.
      OUT &H3F8,0 'Low order byte of X'0100'
      OUT &H3F9,1 'High order byte of X'0100'
      OUT &H3FB,(INP(&H3FB) OR &H80) 'Disable divisor registers.

          Adding this code to a BASIC program will cause the COM1
port to immediately switch to 450 baud operation.

          Switching to other speeds is just as easy. The only
thing you need to know is the baud rate divisor required for that
speed. Here are a few of the common divisors (see the full table
in the Tech. Ref.):

                300     X'0180'
                450     X'0100'
                1200    X'0060'

          I hope this discussion has helped to clarify the
subject of 450 baud operation. Perhaps with this help, you can
make some simple changes to whatever communications program
you're running which will allow you to use your Hayes 300 at a
speed which will allow up to 50 per cent faster communications!