RAMTEST                       Page 1


                                  WARNING
                                  -------

     Executing  this  program WILL destroy the contents of memory, in-
     cluding RAM disks!


     Now that you've been warned, I think you will find  this  program
     useful,  not  only  in identifying an existing fault, but also as
     part of a periodic maintainence program. This  program  has  been
     developed  as an exhaustive test of an IBM PC's system RAM. It is
     much more comprehensive than the PC Power On Self Test (POST) and
     delivers diagnostic messages which are much easier to understand.

     To start the test, just type RAMTEST at the DOS prompt. There are
     no additional parameters.

     This test is best run from a floppy disk which has been formatted
     using the /S option and contains no  other  RAM-based  utilities.
     Some of the commonly available memory-resident utilities (for ex-
     ample,  SIDEKICK  from  BORLAND) 'take command' of the system and
     will cause RAMTEST to crash.

     RAMTEST functions in several distinct phases.  After  signing-on,
     RAMTEST  starts  searching for the top of contiguous memory. This
     search is performed by examining RAM and not  by  consulting  the
     system  configuration  switches. Once the top of memory is found,
     the actual testing portion of the program is relocated and  test-
     ing begins.

     RAM  is  tested  beginning with address 0:500 and continues up to
     but not including the top 32k. These limits were chosen  for  the
     following  reasons. 1) BIOS uses RAM below 0:500 for scratch area
     and RAMTEST uses BIOS exclusively for screen I/O. 2) The  testing
     program needs a place to live undisturbed.

     RAM  is  tested  in 32k blocks. The pattern for the test is taken
     from the BIOS ROMs. Randomness is added by use of iteration count
     to modify the data. During PASS 1, each RAM location is  modified
     and  then  verified.  This  insures that each location can be ac-
     curately written to and read from. During PASS 2,  each  location
     is  re-read  and  compared  to it's reference byte in ROM and the
     parity bit is checked. This part of the  test  insures  that  the
     parity  generating  and  checking  circuitry  is functioning cor-
     rectly, that the address decoding is working  properly  and  that
     there are no locations in RAM shorted to other locations.

     Should  no  errors occur during the two passes, RAMTEST announces
     the successful completion of the test and prompts you to turn off
     the computer to stop the test. If not stopped,  however,  RAMTEST
     will  start  over,  using  a different set of patterns each time.
     Since some memory errors do not show  up  until  after  hours  of
     operating  time,  if you're trying to track down a failure, it is
     suggested that you let RAMTEST run awhile, perhaps overnight.




                Copyright (c) 1985  J & C Computer Services           




                                  RAMTEST                       Page 2


     Should an error occur, RAMTEST stops immediately, displays a mes-
     sage identifying the error, and halts. Note that the only way  to
     exit  this condition is to turn the computer off. A typical error
     message is:


          Memory contents failure.
          Address = 5000:0000
          Data is: 1B      Data should be: 1F

          Turn power off, wait 5 seconds, and turn power back on.


     The above example shows that the failure occured on an  expansion
     board  (System  memory extends to 0:FFFF on 64k motherboards, and
     to 3000:FFFF on 256k motherboards. The presence of 4116 RAM chips
     indicates a 64k motherboard.). It also shows that  bit  1  was  0
     when  it  should have been 1. In cases like this, the RAM chip in
     the bit 1 position is frequently at fault. The RAM chips are  the
     most delicate components in the memory system, and the easiest to
     test for defects. This is because the RAM chips are socketed (ex-
     cept  for the first 16k or 64k) and the rest of the chips such as
     address decoding and data buffers are rarely, if ever, socketed.

     The last two pages of this document diagram the location  of  the
     RAM  chips  on  the motherboard for both 64k systems and the 256k
     systems. Refer to the documentation that came  with  your  add-in
     memory board for instructions on locating and replacing RAM chips
     that  make up the memory above 1000:0 (64k motherboard) or 4000:0
     (256k motherboard).

     The failure codes which are analyzed at  the  top  of  each  page
     refer  to  the  code which the PC prints when an error is encoun-
     tered during POST. If this occurs, the code will be printed,  the
     speaker  will  beep,  the  screen will go blank, and the computer
     will have to be turned off. This will all happen in the  span  of
     about one second, so watch carefully to see the error code.



     RAMTEST  is provided at no charge to the user. Feel free to share
     it with your friends, but please do not give  away  altered  ver-
     sions  or  versions  which have had the copyright notice removed.
     The essence of 'user-supported' software is to  provide  personal
     computer users with quality software without high prices, and yet
     to  provide  incentive for programmers to continue to develop new
     products. If you find this program useful,  a  contribution  ($10
     suggested)  would be greatly appreciated. Any suggestions or com-
     ments you may have are also welcome.


                                 Jim Weisz
                          J & C Computer Services
                               P.O. Box 1356
                            Lombard, Il.  60148



                Copyright (c) 1985  J & C Computer Services           




                             RAMTEST                       Page 3












MEMORY FAILURE CODE ANALYSIS:  64k motherboard



SAMPLE FAILURE CODE:    4402 201
                        |||| |||
                        |||| +++---- SYSTEM CODE - INDICATES MEMORY FAILURE
                        ||++-------- FAILED BIT - 00 INDICATES PARITY
                        |+---------- FAILED 16K BLOCK - 0, 4, 8, OR C
                        +----------- FAILED 64K SEGMENT


SYSTEM BOARD  (Lower left corner when viewed from the front)

SEGMENT = 0000
                        BIT                             FIRST 2 DIGITS OF
ADDR            P       0   1   2   3   4   5   6   7   ERROR CODE

0000 - 3FFF     *       *   *   *   *   *   *   *   *   00  (This row is
                                                             soldered in.)
4000 - 7FFF     *       *   *   *   *   *   *   *   *   00

8000 - BFFF     *       *   *   *   *   *   *   *   *   00

C000 - FFFF     *       *   *   *   *   *   *   *   *   00

SECOND 2
DIGITS OF       00      01  02  04  08  10  20  40  80
ERROR CODE



















           Copyright (c) 1985  J & C Computer Services           




                             RAMTEST                       Page 4












MEMORY FAILURE CODE ANALYSIS:  256k motherboard



SAMPLE FAILURE CODE:    4402 201
                        |||| |||
                        |||| +++---- SYSTEM CODE - INDICATES MEMORY FAILURE
                        ||++-------- FAILED BIT - 00 INDICATES PARITY
                        |+---------- FAILED 16K BLOCK - 0, 4, 8, OR C
                        +----------- FAILED 64K SEGMENT


SYSTEM BOARD  (Lower left corner when viewed from the front)

                        BIT                             FIRST 2 DIGITS OF
SEGMENT         P       0   1   2   3   4   5   6   7   ERROR CODE

 0000           *       *   *   *   *   *   *   *   *   0x  (This row is
                                                             soldered in.)
 1000           *       *   *   *   *   *   *   *   *   1x

 2000           *       *   *   *   *   *   *   *   *   2x

 3000           *       *   *   *   *   *   *   *   *   3x

SECOND 2
DIGITS OF       00      01  02  04  08  10  20  40  80
ERROR CODE




















           Copyright (c) 1985  J & C Computer Services           

ROR CODE




















           Copyright (c) 1985  J & C Computer Services