FBLCC - THE FEDERAL BUILDING LIFE CYCLE COST PROGRAM

Note:  The National Bureau of Standards has changed its name (as of August
1988) to the National Institute of Standards and Technology.  

                    FBLCC Update: August 1, 1989

The FBLCC program on this disk is designated as version se2.3.  Several new
changes have been made since the release of version se2.1, which is described
on the following pages.  (Version se2.2 was a classroom version similar to
se2.3.)  These new changes include:

(1) The base date is now shown with the project input data as you enter
project data.  This date is taken directly from the clock in your computer
(i.e., it is the current year).  It cannot be changed except by changing your
clock.  It is important that your clock be set properly when you start up your
computer.

(2) You can no longer use the default energy prices on the disk.  You must
enter your local energy prices.  The energy price data on the disk are still
used to provide default energy price escalation rates.

(3) The Federal energy conservation credit (10%) is no longer used.  Therefore
the "initial conservation-related cost" data entry has been omitted from the
program.

(4) The discount rate defaults to 7% for energy conservation studies and 10%
for other Federal projects, as before.  However, these discount rates can now
be changed like any other variable (except the base date).  Remember that the
discount rate must be entered in real terms, i.e., net of general inflation.

(5) The main bar menu in LCCDATA (data entry subprogram) now highlights the
most logical next step after completion of a previous step.  (E.g., after
"getting" an existing file, the "EDIT FILE" choice will be highlighted.)

(6) Several small bugs have been cleaned up.  For example, all lower case
entries will now be converted to upper case to facilitate data entry.


Note: These changes are primarily related to data entry, and do not affect the
computational results, with the exception of omitting the Federal conservation
credit.


Be sure to read the section entitled "Additional Help" on page 5 of this DOC
file.


Additional Note (January, 1990): The latest Department of Energy energy price
forecast, released January 1990, is included on this disk in files
ENCOST90.SEQ and ENCOST90.RAN.




                              FBLCC.DOC  Page 1

      IMPORTANT NOTES FOR SCREEN-EDITOR VERSION se2.1 OF FBLCC

The FBLCC program is described in NBS Technical Note 1222 "A User's Guide to
the Federal Building Life Cycle Cost Program", May 1986.  For information on
how to obtain this publication, write to: 

          Applied Economics Group  
          Center for Computing and Applied Mathematics
          National Engineering Laboratory  
          National Institute of Standards and Technology
          Building 224, Room B120  
          Gaithersburg, MD 20899  

This disk contains a new version of that program, Version se-2.1.  While input
data and output results are (nearly) identical to the original version, the
program has been enhanced with full-screen data entry capabilities to
facilitate data entry and editing.  The Department of Energy's (DOE) energy
price projections included on the disk for direct access by the FBLCC program
were released in September, 1988.

This new version is also compatible with the DOE's ASEAM energy analysis
program for buildings.  If you are already using ASEAM with the FBLCC program,
you should discard the version of FBLCC supplied with ASEAM and use the new
version on these disks.


Files on FBLCC disk:


FBLCC   .EXE    FLCCDATA.EXE    FLCCMAIN.EXE    FCOMPARE.EXE    
FPRNTBCF.EXE    FPRNTLCC.EXE    DISCOUNT.EXE    BASRUN  .EXE    
ENCOST  .RAN    ENCOSTXX.SEQ    STATES
FIENECDT.FIS    FIENEEDT.FIS    FIOMCSDT.FIS    FLCCCAPC.FIS     
FLCCPROJ.FIS    FLCCREPL.FIS    
HDYESNO .DAT    
FED1.BCF        FED2.BCF        FED3.BCF        FED4.BCF
FED5.BCF        FED6.BCF        FED7.BCF
FED1.LCC        FED2.LCC        FED3.LCC        FED4.LCC
FED5.LCC        FED6.LCC        FED7.LCC
FBLCC.DOC

The first six files with the extension .EXE are FBLCC executable program
files.  BASRUN.EXE (copyright by IBM) is the runtime module needed to run
these six programs.  If you copy these programs to another disk you must copy
the runtime module as well or the FBLCC programs will not run.  The DISCOUNT
program is a stand-alone program discussed in the FBLCC User's Guide.  It is
now run simply by typing 'DISCOUNT' at the ready prompt.  (The previous
version required that you load the BASIC interpreter first.)  It does not need
the runtime module to be executed.






                              FBLCC.DOC  Page 2

The FBLCC User's Guide and the FBLCC program reference the subprograms
slightly differently than they are referenced above.  All of the FBLCC
subprograms on the disk are saved with the initial letter 'F' (to distinguish
them from similarly named NBSLCC programs).   The following list shows the 
correspondence between the actual program name and its reference in the
program:

         Actual program name           reference name
              FBLCC.EXE                    FBLCC
              FLCCDATA.EXE                 LCCDATA
              FPRNTBCF.EXE                 PRINTBCF
              FLCCMAIN.EXE                 LCCMAIN
              FPRNTLCC.EXE                 PRINTLCC
              FCOMPARE.EXE                 COMPARE

It is not essential that the user be familiar with this correspondence, since
the various subprograms are executed from a menu with functional choices. 
This list is included here primarily for sake of completeness.

The ENCOST.RAN file contains the 1988 DOE energy price forecast for the years
1985 through 2030, used to provide default energy prices and rates of energy
price escalation over those years.  It is in binary (random access) form to
conserve space on the disk and speed up disk access.  There are now only four
regions (northeast, southeast, midwest, and west) rather than ten regions as
in the earlier DOE projections.  The appropriate region for any location is
automatically selected by entering the two-character state code for the actual
location of the project rather than the DOE region itself.  The ENCOSTXX.SEQ
file is a shorter file which tells FBLCC how the larger energy price file is
arranged so that it can be read properly.  The STATES file is used to show the
appropriate code for all 50 states (plus the District of Columbia) in the help
mode.

All files with the extension .FIS provide the formatting needed to display the
data input screens.

HDYESNO.DAT is a small file used when calling ASEAM from FBLCC to determine
whether or not FBLCC and ASEAM are saved in the same subdirectory in a hard
disk.  The single upper case letter 'Y' or 'N' is contained in this file.


All files ending in .BCF are the building characteristics files used in the
examples in the FBLCC user's guide.

All files ending in .LCC are the life-cycle cost output files used in the
examples in the FBLCC user's guide.


STARTING FBLCC

To run the FBLCC program from the default drive, type 'FBLCC' at the ready
prompt.  IMPORTANT NOTE: YOU MUST HAVE A FORMATTED DISK IN YOUR B DRIVE FOR
SAVING AND RETRIEVING DATA FILES.  If you are running the program from a hard
disk and do not have a B drive, try putting the data disk in the A drive.  It
will usually act as though it were the B drive as well.  If you want to access

                              FBLCC.DOC  Page 3

the building characteristics files (extension = .BCF) and life-cycle cost
output files (extension = .LCC) that have been included on the master disk,
these must be copied to another disk that can be inserted into the B drive. 
(Alternatively, the FBLCC program can be run from the B drive; then these
files can be accessed directly from the master disk.  However, this is not a
recommended general procedure for running the program, since there is only
limited space available on the master disk.)

Refer to the FBLCC user's guide for general information about the FBLCC
program.  Information needed to run the screen-editor version of this program
is included below in this file.  Chapter 10 of the ASEAM user's manual
provides more complete documentation about the data input screens in this new
version of FBLCC.  


Change in DoE Energy Price Projections  

The DOE energy price projections contained in the ENCOST.RAN file on this
disk are current as of September 1988.  The energy cost analyses reported in
the examples in the FBLCC User's Guide are based on older (1985) projections. 
The building characteristics files on this disk which correspond to those
examples are based on the older DOE energy price projections and thus will
match the results reported if they are not edited.  However, if you load a
building characteristics file into the LCCDATA data entry module, the DOE
projections of energy price increases (if specified) will automatically be
updated.  Thus the resulting LCC analysis will no longer match the published
examples exactly.  Note that only the rates of energy price increase (i.e.,
the energy price escalation rates) over the study period are automatically
updated.  The unit energy price for each energy type is updated by pressing
<F8> when the cursor is at the energy price input line in order to retrieve
the appropriate price from the DOE energy price file.  


New Variables

Two new variables have been added to the FBLCC program: (1) a comment line (70
character maximum, no commas allowed)  which can be used to include general
reference information about a project in its building characteristics file for
future reference, and (2) a two-character state code for use in accessing the
DOE energy price projections.  The two-character state code must correspond to
the official Postal Service code (e.g., CA for California).  Use 'US' to
access DOE average U.S. energy price projections.  Use 'H' for help; then all
of the Postal Service codes can be scanned at the bottom of the screen using
the up and down cursor arrows.  (Once the appropriate code has been
determined, it must still be entered in the appropriate space.)










                              FBLCC.DOC  Page 4

Additional Help  

Do not confuse "Project Title" with "File Name".  The project title is used to
identify the project when printing out the LCC reports (LCC analysis and
comparative analysis).  It can have up to twelve characters.  The file name is
used to save and retrieve the data files to and from the disk, and must 
conform to the Disk Operating System (DOS) file-name conventions, i.e., no 
more than eight alpha-numeric characters.  Never include a file name 
extension with the file name; this is automatically added by the program to 
distinguish between file types.  Never insert a space in a file name; it will 
be saved but can't be retrieved.  

Note that a separate building characteristic file must be set up for each 
alternative project to be evaluated.  You cannot evaluate several projects  
simultaneously by specifying each as a separate component of a single  
project.  Separate components are specified to a single project to make it  
easier to compute replacements, depreciation, property taxes, and resale value
at the end of the study period.  (Operating, maintenance, and energy costs are
not specific to individual components but only to the entire building or
building system being evaluated.  Once you set up a building characteristics
file for a project and save it, it is often easier to edit that file with data
from the alternative project and then save it under a new name than to start
from scratch on a new file.  
 
 
Using LCC Menus

Menu choices are displayed in horizontal bars across the screen.  One of the
selections is highlighted by a reverse video box (the first selection when
entering a program).  Select the option you want by moving this box using the
right and left cursor control keys (the arrows on the 4 and 6 keys of the
numeric keypad) until it is over the option you desire and then pressing
<ENTER>.  This command will be executed or another menu will appear. 
Pressing any key other than the left or right arrow or <ENTER> will cause a
beep. 

Secondary menus may either appear as additional horizontal selections, or a
vertical "pull down" menu under the item first selected.  These vertical
pull-down menus work exactly like the horizontal menus, except that the up and
down arrows (instead of left and right) must be used to move the highlighted
selection.  Once again, pressing <ENTER> is required to "select" an option,
and pressing any key other than these three will cause the computer to beep.

Many times you will see "Exit" as a valid choice in a menu.  If you are in a
program's top level horizontal menu, "Exit" means to leave this program and to
go into another program.  On a secondary menu (either horizontal or vertical),
"Exit" means to return to a higher level menu - not to leave the LCC program.

When you begin running the LCC input program, the first menu appears on the
screen.  The fully expanded input menu is shown below.  Note that the second
bar menu appears if you select "Edit BCF Data" from the first menu bar. The
third menu bar and vertical menu appears if you select "Capital Components"
from the second menu bar.


                              FBLCC.DOC  Page 5

             FBLCC BUILDING CHARACTERISTICS INPUT PROGRAM
ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³ Get BCF File    Save BCF File    Edit BCF Data    Enter New Data    Exit ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³ All Data     Project     Capital Components     O&M     Energy     Exit  ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³ All Data     Component Data     Cost Phasing     Replacements     Exit   ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  
                             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ 
                             ³ All Components ³ 
                             ³ Component 1    ³ 
                             ³ Component 2    ³ 
                             ³ Component 3    ³ 
                             ³ Component 4    ³ 
                             ³ Component 5    ³ 
                             ³ Component 6    ³ 
                             ³ Exit           ³ 
                             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 


Get BCF File
The Get command retrieves an existing BCF data file from the data disk in
drive 'B' and loads it into memory.  You must use this command before you can
edit a file, since the editing program works within memory and not directly
from the disk.

When you choose "Get BCF File" the program will respond with a list of all BCF
input files stored on your data disk.  Move the highlighted bar with the
cursor control keys (up, down, right, left) until it is over the file you want
to get and press <ENTER>.  If the file which you want to edit is not on the
list, first mark "Exit" and press <ENTER> (to get out of "Get BCF File"), then
insert the correct data disk with the file to edit in drive 'B', and try "Get
BCF file" again.  Once you see the file you want, mark it with the reverse
video box and press <ENTER>.  A message will appear on the screen for a few
moments while the computer reads the file into memory.  When the Main Menu
reappears, you are ready to "Edit BCF File." 

If you use the "Get BCF File" command when data is currently in memory, a
warning will be issued.  Retrieving a file overwrites all data in memory with
the data from the file.


Save BCF File

The Save command saves a data file so that you can use the file again at a
later time.  This command copies the complete input data file from memory
(temporary storage) where you have been editing it, to disk (permanent
storage).  If you do not save a file, it will be gone forever once you exit
from the BCF Input program or get a different data file.  The Save command
should be used each time you are done editing a file.  The only exceptions are

                              FBLCC.DOC  Page 6

if you have made no changes at all to the file, or if you have made erroneous
changes and would prefer to have the previous (last saved) version of the
file.  When you use the Save command, a message asking you for the file name
to save will be displayed.  Pressing <ENTER> causes the file to be saved under
the same name (what you retrieved the file as); typing a new name causes the
file to be saved under that name; typing 'X' aborts the Save command and
returns you to the BCF Input Menu.


        WARNING!  If you enter an <ENTER> for the filename, the file in memory
will overwrite the file on disk.  You may want to use a new filename and have
the old file as a backup.


File names may be up to eight alphanumeric characters.  (Refer to your DOS
manual for valid filename characters.) Do not specify an extension.


Edit BCF Data

The Edit command allows you to review and change the contents of the data file
in memory.  You must first "Get" a file before you can "Edit" it.  When you
use the Edit command, another menu will be displayed which lists particular
screens to edit.  You may edit the entire data file or only one particular
screen.

Each time you complete an input screen, the information on it is transferred
into memory.  After you have finished the screens which you indicated for
editing, the Main Menu will reappear.  Choose either additional sections to
edit, save the file and proceed to edit another file, or exit to the other
subprograms.



Enter New Data

The Enter New Data command clears the memory and lets you begin entering a new
set of data for the BCF file.  All of the input screens will appear
sequentially, with blank lines where you should fill in values.  REMEMBER to
store the file in memory before you Enter New Data.  A warning message appears
if data is presently in memory.  


Exit

The Exit command should be used when you want to leave the BCF Input routine. 
The question "Did You Remember to Save Your Files?" will be printed on the
screen.  If you answer 'N' followed by a <ENTER>, you will be returned to the
BCF Input Menu for another chance to save the file.






                              FBLCC.DOC  Page 7

Cautions about Memory

Memory is only temporary.  The data stored in memory is destroyed when you
exit any of the BCF input programs, turn off the computer or otherwise lose
power, or reboot.  Also, only one file can be held in memory at a time.  Thus,
if you replace the file in memory with a different file (either an existing
file with "Get BCF File" or an blank file with "Enter New Data") the file
which was previously in memory will be lost.  (The program issues a warning
message whenever you use the "Get" or "Enter New Data" commands and there is
existing data in memory.) To save the contents of the file in memory, you must
"Save BCF File" before editing other files or leaving any BCF Input program. 

The "Save BCF File" command copies the file in memory to the data diskette in
drive 'B', where it is stored permanently.  Since the disk file is not changed
until you save, if you make many mistakes or accidentally erase a lot of
information while editing, you can always go back to the last saved version of
the file by getting the file again.  


The BCF Input Screens

This section will tell you how to move around within and between input
screens.

The body of the screen is a series of input questions with lines for the data
input.  There may be more than one column for data entry.  The cursor will
move to only those lines where you should input data.  Cursor control is
discussed below.  At the bottom of each input screen is a function key menu,
describing the action resulting from pressing each function key.  This
information is explained in more detail below.  The cursor control and
function key conventions are the same for all LCC and ASEAM2 input data
screens.  They apply both for editing existing and editing new data.


Cursor Control

There are two different types of cursors in the program.  A "smiley face"
cursor is what originally shows on the screen, at the first entry.  With this
cursor you can move between entries.  Once you begin to type an entry the
cursor changes to a blinking underline.  The cursor control keys have
different functions for the two types of cursors.


Smiley-Face Cursor

When you first enter an input screen (through either the "Edit" or the "Enter
New Data" command) the screen will display a list of input questions followed
by either the current values (in the case of edit) or blank lines (in the case
of new data).  A smiley face cursor is in front of the first question.  This
cursor is used to move around the screen, from one input question to another.





                              FBLCC.DOC  Page 8

The following keys are used to move the smiley face cursor:
     Up     - moves up to next entry without error checking

     Down   - moves down to next entry without error checking

     Right  - moves right to next entry (down if no multiple columns)         
               without error checking

     Left   - moves left to next entry (down if no multiple columns)          
               without error checking

     PgUp   - completes error checking for entire screen.  If no errors       
        are found, moves to previous screen.  If an error is found, prints an 
        explanatory message at the bottom of the screen, beeps, and positions 
        cursor at the incorrect entry.  If current screen is the first in the 
        editing sequence, returns to BCF Input Menu.

     PgDn  -  completes error checking for entire screen.  If no errors       
        are found, moves to next screen.  If an error is found, prints an    
        explanatory message at the bottom of the screen, beeps, and positions 
        cursor at the incorrect entry.  If current screen is the last in the  
        editing sequence, returns to BCF Input Menu.  NOTE: after the last
        entry is made on a screen, a message at the bottom of the screen will 
        advise you to press PgDn for the next page.  This message will be
        visible for about 4 seconds.  You cannot execute this command until  
        the message disappears.

     Return - completes entry, performs error checking, moves to next entry if
        data is valid.  If the entry is incorrect, an explanatory            
        message is printed at the bottom of the screen and the cursor        
        remains at this entry.

     Esc    - refreshes the screen.  The data will appear as it was when you  
        first entered the screen.  Any data which was changed will be         
        replaced with the original data.

The function keys may also be used.  These are discussed below.  Any other
keystroke will be interpreted as data entry and written on the entry line.


Underline Cursor

When you begin to type an entry, the cursor changes to a blinking underline. 
What you type is entered on the data entry line.  With this cursor, you move
WITHIN an entry, NOT between entries.  The cursor control keys have different
actions from those for the smiley face cursor.









                              FBLCC.DOC  Page 9

The following keys are used to move the underline cursor:

Up        - completes entry, performs error checking, moves up to previous    
            entry if answer is valid.

Down      - completes entry, performs error checking, moves down to next entry
            is answer is valid.

Return    - same as Down    

Right     - moves cursor right to next character    

Left      - moves cursor left to previous character    

Home      - moves to first character of entry    

End       - moves to last character of entry    

Delete    - deletes the character at the cursor, characters to the right of
the cursor are moved one space to the left    

Insert    - inserts characters at the cursor    

Backspace - deletes the character to the left of the cursor    

Ctrl-End  - deletes all characters to the right of the cursor    

Escape    - clears entry


Any alphanumeric character will be entered as data.  The function keys F9
(help) and F10 (exit) may be used with the underline cursor.  Any other
keystroke will only cause a beep.


Function Keys

The function keys may also be used during the input sessions.  When you have
the blinking underline cursor, only F9 and F10 may be used.  All function keys
are available with the smiley face cursor.  The function keys have the
following actions:

F3 - delete entry at cursor    

F4 - delete column at cursor (only for screens with multiple columns) all     
     other columns move to left    

F5 - insert column at cursor (only for screens with multiple columns) all     
     other columns move to the right
     WARNING:  data in rightmost column is lost (moves off-screen)    

F6 - copy column at cursor (only for screens with columns) copies to column at
     right; if pressed again, copies further right
     WARNING:  data in rightmost column is lost (moves off-screen)    

                             FBLCC.DOC  Page 10

F8 - use default value (if there is one; if not, message appears)    

F9 - help, supplies context-specific message (if there is one)    

F10 - exit to BCF INPUT MENU

     WARNING:  F10 is like a break--editing changes made during this       
screen are not stored.  Every time you PgUp or PgDn out of a screen or are
moved to the next screen or the menu automatically, the information you input
has been stored in memory.  But whenever you use F10 to return to the menu,
the information from that particular screen will not be stored.  If you want
to keep the changes you have made in an input screen, press PgDn before using
the F10 key.

In addition, two other commands may be useful; these can be executed at any
time:

<Alt> H - toggles off and on automatic help messages at the bottom of the
screen.  When the automatic help messages are toggled off, individual help
messages can still be displayed by pressing F9 at the point where help is
needed. (Default setting is 'on'.)

<Alt> P - toggles on and off the automatic screen advance command.  When off
(the default setting), you must press <PgDn> to advance to the next screen. 
When on, the screen is automatically advanced after the last entry on a page
is complete.  (The default setting is 'off' so that you can continue to
examine the screen after completing the last entry.)


Error Checking

Many questions have upper and/or lower numeric limits or other restrictions
(such as number of digits, alphanumeric strings, etc.) imposed on them.  When
you enter an unacceptable value (such as a letter when a number is required),
the computer will beep and an error message will appear briefly at the bottom
of the screen; the smiley face cursor will remain at that line for you to
enter a new value.  You cannot exit from a screen with incorrect or missing
data with the cursor control keys.  If you try to do so, the cursor will be
returned to the erroneous data field.  You can exit from a screen using the
F10 key at any time, but the data you just entered will not be saved and the
previously existing data for that screen will be kept.


Default Values 

Default values have been assigned for many of the input questions.  To enter a
default value, press the F8 key.  If there is no default value, the computer
will beep and a message will appear briefly at the bottom of the screen.  The
cursor will remain at the same entry. 






                             FBLCC.DOC  Page 11