USER.DOC PC/370 User Documentation

Copyright 1987 Donald S. Higgins

Don Higgins
6365 - 32 Avenue North
St. Petersburg, Florida 33710

E-mail CompuServe 73047,1113

PC/370 users:

This is the user documentation for the PC/370 cross assembler,
linkage editor, and emulator for 370 assembly language users.
The PC/370 package provides the capability to assemble, link,
and execute IBM 370 assembler programs on any 80x86 MSDOS 2.0+ micro
computer such as the IBM PC, XT, AT, PS/2, Compaq, etc.

Chapter table of contents:

 1. M370.COM macro preprocessor

 2. A370.EXE cross 370 assembler

 3. L370.EXE cross 370 linkage editor

 4. E370R42.EXE run time 370 emulator

 5. Technical hardware and software specifications

 6. ASSIST extended instructions for student use

 7. DEBUG interactive debugging facility

 8. Floating point instructions and scientific subroutines

 9. XA extended architecture instructions

10. System subroutine library

11. COBOL call interface

12. Reference publications

*********

Chapter 1.  M370.COM macro preprocessor

*********

The M370 macro preprocessor has the following command format:

A>M370 file

where file is the name of a source macro program file which has the
suffix (.MLC).  The source file must be in ASCII text format with
each line terminated by a line feed character.  The only output from
this program is a source basic assembler file with expanded macro
statements.  The suffix of the output file is (.ALC).

Any number of macros can be used by M370 input files and must be
defined in individual source macro files with the file name equal to
the macro name and a suffix of (.MAC).  These macros must be placed on
the default drive for access by M370.  For more speed, these files may
be moved to RAM disk.

*********

Chapter 2.  A370.EXE cross 370 assembler

*********

The A370 assembler has the following command format:

A>A370 file/options

where file is the name of a source program file which has the
suffix (.ALC).  The source file must be in ASCII text
format with each line terminated by a line feed character.
Any number of editors including SEE can be used to create ALC files.
An optional drive and path may be specified such as B:\dir\file.
The options which can be specified are as follows:

  A - alignment option. Default is on.
  C - object code option. Default is on.
  L - produce listing file (.PRN). Default is none.
  T - trace assembler execution. Default is off.
  X - produce symbol and literal cross reference. Default is none.

If an option is on by default, specifying it will turn it off.
For example:

A>A370 B:DEMOPNUM/LX

will read the source file B:DEMOPNUM.ALC and produce the object
code file B:DEMOPNUM.OBJ and the listing file B:DEMOPNUM.PRN.

The A370 assembler conforms to the OS/VS IBM 370 Assembly
Language as defined in the IBM manual GC33-4010 with the
following limitations:

  1.  No continuation lines.
  2.  Maximum control sections and dummy sections is 255.
  3.  Macros and system variable symbols are not supported (see M370).
  4.  OPSYN statement not supported.
  5.  EQU third operand (type attribute) not supported.
  6.  Scale, exponent, and bit length data modifiers not supported.

Extended features include the following:

  1.  Data constant types F and H may use arithmetic expressions.

  2.  Extended ASSIST instruction set including XREAD, XPRNT,
      XDECI, XDECO, AND XDUMP as defined in the book Assembler
      Language with ASSIST by Ross A. Overbeek.  Also 2 more
      instructions XFILI and XFILO are added to allow changing
      default ASSIST input and output files at execution time.

  3.  ASCII character strings may be defining by using double
      quotes instead of single quotes in DC and self defining
      character constants.

*********

Chapter 3.  L370.EXE cross 370 linage editor

*********

The L370 linkage editor has the following command format:

A>L370 file/options

where file is the name of an A370 object code file (.OBJ) and
may specify a specific drive.  The options supported by the
linkage editor are as follows:

  B - create VS COBOL callable subroutine file (type .BIN).
  D - set debug mode for emulator. Default is off.  When option D
      is on, interactive debug is entered at beginning of each
      COM or BIN file execution.
  G - load and execute with no file output. Default is off.
  I - turn off all interrupts from keyboard.
  L - list CSECT addresses and lengths. Default is off.
  M - create 370 code module without COM prefix code.
  O - dump input object code records in hex. Default is off.
  P - force floating point option off even if 80x87 installed.
  X - cross reference of external symbols. Default is off.
  U - allow unresolved external references

For example:

A>L370 B:DEMOPNUM/LX

will read the object code file B:DEMOPNUM.OBJ and produce the binary
command file B:DEMOPNUM.COM, and the listing and cross-reference file
B:DEMOPNUM.LST.  Note that since DEMOPNUM calls the external
subroutine PET, the subroutine library L370.LIB must be available.
The binary command file B:DEMOPNUM.COM may be directly executed by the
MSDOS command:

A>B:DEMOPNUM

When the above command is executed, the program will load at X'0200'
and the fetch routine linked with the program will load the
emulator E370.EXE in high memory and transfer control to it.

The linkage editor uses two concatenated subroutine library
files.  The first file is named file.LIB and may contain
any number of A370 subroutine object modules which are called by the
modules in file.obj.  This file is optional and only called modules
are included.  The second file is named L370.LIB and may contain any
number of A370 subroutine object modules which are commonly used by
multiple programs.  An L370.OBJ file is included with the PC/370
package and contains sample time and date routines.  The MS-DOS COPY
command with option /B may be used to concatenate A370 object modules
in either library file.  Note module references must be resolved in
one sequential pass of library so backward module references may cause
unresolved entry.

The linkage editor listing file (.LST) shows relative entry point
and segment lengths and optional cross reference by segment.  The
last line of the listing contains ENT/LNG which is the 370 relative
entry point of the module and the length of the entire module.

*********

Chapter 4.  E370R42.EXE run time 370 native machine code emulator

*********

The emulator is transparent to the user when using A370 and L370 to
create MSDOS command files.  The emulator is dynamically executed by
the 80x86 COM file prefix generated by L370.  The 370 machine code
starts at X'210' from the beginning of the COM file.  The origin of
the 370 virtual address space for a COM program starts at X'10' from
the beginning of the COM file.  The execution of the 370 machine code
will start at the specified relative start address plus hex 200 with
that absolute address in register 15.  Register 1 will point to
standard MVS parameter list address at location X'80' with EBCDIC text
passed from MS-DOS command line.  Register 13 will point to standard
save area in ASCB and register 14 points to return to detach
instruction in ASCB to exit to MS-DOS.  If a program check occurs, the
interactive debug facility will be invoked and will initially display
the general registers and the program status word at the time of the
interruption.  See DOC\SYSTEM.DOC SPIE supervisor call for facility to
handle program checks.  Also see MAC\MVS.MLC for example of how to run
programs in problem state with your own supervisor shell.

A new facility with PC/370 release 4 is the ability to make the
emulator resident by simply executing it directly.  The resident
emulator reserves about 50k for code and uses an 80x86 hardware
interrupt to transfer control when needed at execution time.  To
remove the current resident emulator, simply execute it directly
again.  Release 4.0 and 4.1 used interrupt hex DC.  Release 4.2 uses
hex 60 within the Micro Focus Extended Memory (XM) real interrupt
handler range of hex 60-6F.  See DOC\PTF.DOC for pathc to change
interrupt in case it conflicts with another user installed software
package.

With release 4.1 a new system queue area (SQA) memory option has been
added to define a memory which can be shared by all COBOL subroutines
and which is allocated in the resident emulator address space.  The
size of the SQA is specified by a single hex parm when making the
emulator resident.  The size is in hex paragraphs and the default is
10 or 256 bytes.  For example, the following command would make the
emulator resident with an 8k byte SQA:

  C>E370R42 200

With the SQA facility, COBOL assembler subroutines can issue standard
file I/O with dynamic buffers allocate from SQA. See BAT\RUNCBL.BAT
for demo.

With release 4.2, PC/370 supports Micro Focus COBOL/2 assembler
subroutine calles in normal MS-DOS mode or in extended memory XM mode.
In both cases the emulator must be resident before starting the COBOL
program via workbench or run time executive with or without XM.  In
XM mode, the emulator still runs in real mode after requesting XM to
mode the called subroutine code (BIN file) and the argument data
segments to base memory area for access in V=R real mode.  This
creates the XM restriction that there must be sufficient base memory
for called BIN file and data segment at the time of the call.  Also,
the emulator must not attempt to access memory beyond end of BIN or
data segments in real memory.  The emulator can use SQA in XM mode.
See BAT\RUNCBL.BAT for demo of XM mode subroutines (requires XM.EXE
and RUN.EXE from Micro Focus).

There are five distinctly different ways to execute the E370 emulator:

  1.  Direct execution to make it resident if not currently resident.

  2.  Direct execution again to remove current resident copy.  If
      another software package is using interrupt, an error message
      will display.  See DOC\PTF.DOC to change interrupt number.

  3.  Execution of a 370 COM module without E370 resident causes
      dynamic loading of E370 in high 64k of MS-DOS memory to support
      execution of 370 code in the COM module.

  4.  Execution of a 370 COM module with E370 module resident causes
      execution of resident copy via cross memory interrupt facility.

  5.  Execution of a 370 BIN module from within Micro Focus COBOL run
      time environment causes execution of resident copy via cross
      memory interrupt facility.  In XM mode, a protected interface
      routine in the emulator is called directly by the BIN module
      which in turn issues interrupt to execute emulator in real mode.


*********

Chapter 5. Technical specifications

*********

   1.  A370.EXE requires 256k memory to execute and can handle source
       programs with over 1000 labels.

   2.  L370.EXE requires 256k memory and can handle load modules up to
       50k bytes long.

   3.  E370R42.EXE requires 50k plus SQA which includes the emulator,
       and the extended SVC support functions, and interactive debug.
       A production only copy of the emulator named E370P42.EXE is
       included which only requires 40k but does not include
       interactive debug facility or the ASSIST extended instructions.
       This version saves resident base memory, but should only be
       used for fully tested programs or programs with their own
       program check handlers for error recovery.

   4.  E370R42 supports all the non-supervisor state IBM 370
       instructions as defined in the IBM/370 XA Principals
       of Operation manual SA22-7085 except the conditional
       swapping feature instructions.  Short, long, and extended
       floating point instructions are supported provided 80x87
       is installed.

   5.  The minimum configuration for PC/370 is as follows:
       a.  80x86 processor.  XM only supported on 80286/80386.
       b.  256k RAM memory which allows execution of 370 program in
           128k virtual address space.  Maximum virtual address space
           is about 512k on 640k machine.
       c.  1 floppy disk drive.
       d.  80x87 only required for floating point instructions.

   6.  A benchmark program consisting of calculating the first
       100 prime numbers was run in interpretive BASIC using
       16 bit integer arithmetic.  It took 67 seconds on a
       4.77 MHZ 8086 system.  The same program was rewritten in
       370 assembler using 32 bit fixed point arithmetic.  It
       took 25 seconds to execute on the same system.  This
       benchmark program is included as a demo called DEMOPNUM.ALC.

       The demo may be run with the following commands:

         A>A370 DEMO\DEMOPNUM/LX  (create DEMOPNUM.OBJ)
         A>L370 DEMO\DEMOPNUM/LX  (create DEMOPNUM.COM)
         A>DEMO\DEMOPNUM

   7.  The following error messages are supported:

       A370/L370

        E01 - DUPLICATE LABEL
        E02 - INVALID LABEL
        E03 - SYMBOL TABLE FULL
        E04 - INVALID OPERATION CODE
        E05 - UNDEFINED OPERATION CODE
        E06 - UNDEFINED LABEL
        E07 - INVALID OPERAND
        E08 - MEMORY FULL
        E09 - EXPRESSION INVALID
        E10 - SELF DEFINING TERM INVALID
        E11 - ARITHMETIC OVERFLOW IN EXPRESSION
        E12 - TOO MANY EXTERNAL SYMBOLS
        E13 - NO BASE REGISTER AVAILABLE
        E14 - LENGTH ERROR
        E15 - OPERAND ERROR
        E16 - DATA CONSTANT DUPLICATION FACTOR ERROR
        E17 - DATA CONSTANT TYPE ERROR
        E18 - DATA CONSTANT LENGTH ERROR
        E19 - DATA CONSTANT DATA ERROR
        E20 - START SEQUENCE ERROR
        E21 - LTORG SEQUENCE ERROR
        E22 - LOCATION COUNTER ERROR BETWEEN PASS 1 AND 2

   8.  IOS LOGICAL ACCESS METHOD USED BY A370, L370, AND E370

      IOS001 - NO DISK SPACE
      IOS001 - FILE NOT FOUND
      IOS001 - NO BUFFER SPACE
      IOS001 - OPEN FAILED
      IOS002 - CLOSE FAILED
      IOS003 - READING UNWRITTEN DATA
      IOS003 - INVALID REQUEST
      IOS004 - ERROR IN EXTENDING FILE
      IOS004 - END OF DISK DATA AREA
      IOS004 - NO MORE DIRECTORY SPACE
      IOS004 - INVALID REQUEST
      IOS005 - INVALID RECORD TYPE
      IOS005 - INVALID RECORD LENGTH
      IOS006 - INVALID RECORD TYPE
      IOS006 - INVALID RECORD LENGTH
      IOS007 - DELETE FAILED

*********

Chapter 6. ASSIST extended instructions for student use

*********

  A.  Overview

      The book, "Assembler Language With ASSIST", by Ross A. Overbeek
      and W. E. Singletary published by Science Research Associates,
      Inc.  in 1976 describes a set of 370 extended instructions to
      greatly simplify input and output for students learning to write
      370 assembler programs.  A new book with also covers ASSIST is,
      "IBM 370 Assembly Language with ASSIST, Structured Concepts, and
      Advanced Topics", Charles J. Kacmar, Prentice Hall, September
      1987, ISBN 0-13-455742-5.

      PC/370 implements these instructions to allow students to
      code, assemble, and execute ASSIST 370 programs on any 80x86 MS-
      DOS based micro-computer rather than having to use an IBM 370
      mainframe.  This was the original objective for which PC/370 was
      developed back in 1981.  The first students to use PC/370 with
      ASSIST were volunteers at the University of South Florida,
      College of Engineering.  The students used a CP/M based Z80
      micro-computer with the original version of PC/370 instead of
      the IBM 3033 mainframe ASSIST system accessed via RJE using
      keypunched card decks.

  B.  ASSIST extended instructions

      1.  XFILI =C'filename'

          This extended instruction redirects input source for XREAD.
          If open, the current input source file is closed.  The new
          filename can be any standard MS-DOS path/filename ending
          with suffix .xxx or a zero byte.  If the filename is CON:
          then the input source is the console with a ? prompt.  To
          set the ASSIST end of file condition code for XREAD from the
          console, use the escape (ESC) key.  See DEMOAST3.ALC for
          demo of redirection.

      2.  XFILO =C'filename'

          This extended instruction redirects the output from XPRNT.
          If open, the current output file is closed.  The new file
          name can be any standard MS-DOS path/filename ending with
          suffix .xxx or a zero byte.  If the filename is CON: then
          the output from XPRNT is directed to the console.  The first
          byte which is printer control code is also printed on
          console.

      3.  XREAD area [,length]

          Read record into area with default length of 80 padded with
          blanks.  If the input is coming from console, the first
          carriage return defines end of record, and single ESC
          character defines end of file.  Note ASCII characters from
          console or file are automatically translated to EBCDIC in
          record area.  Condition code set as follows:

            0 - read successful
            1 - end of file

          Default input source is file named ASSIST.DAT.  If the file
          is not found, the input and output source is switched to
          console.

      4.  XPRNT area [,length]

          Print record from area with default length of 132.  Trailing
          blanks are stripped off.  The first character is used as
          standard ASCII print control character:

           ' ' - space means skip one line
           '/' - slash means skip two lines
           '1' - one means skip a page
           '+' - means skip no lines
           '-' - dash means skip three lines

          Output to console includes print control character.  Default
          output is to file named ASSIST.PRN which is also used by
          interactive debug X logging command and XDUMP.

      5.  XDECI reg,area

          Read ASCII integer number from area and store into register.
          Leading plus or minus signs may be present.  Condition code
          is set as follows:

           0 - number is zero
           1 - number less than zero
           2 - number is greater than zero
           3 - no number found in area

          Register 1 is set to address of first character after number
          read.

      6.  XDECO reg,area

          Convert binary integer number in register to 12 character
          display field with numeric value including sign.

      7.  XDUMP [area start, area end]

          Dump general purpose registers (default with no args) or
          dump area of memory to output file.

*********

Chapter 7.  Interactive Debug Facility

*********

     A.  Overview

     The PC/370 interactive debug facility is designed to provide a
     tool to help debug program errors in either 80x86 code or 370
     code.  The facility provides the basic tools namely tracing
     program flow via breakpoints defined by calls, and displaying
     register and memory contents upon request.  In addition, the
     facility provides a data and address stop option which is very
     useful for locating errors.

     B.  Program Interface

     The PC/370 interactive debug facility is implemented via a single
     module named MMDBUG which is linked into A370, L370 and E370
     programs and is called with a single 3 byte ASCII argument
     located immediately after the near call instruction.   In the
     E370 emulator environment, the interactive debugger can be called
     directly from 370 programs through SVC 9 which must be followed
     by 3 byte EBCDIC argument and a 1 byte filler to keep
     instructions on half word boundary.

     There are several special calling arguments as follows:

     1.   'OFF' - turn off (kill) trace facility for speed
                  (a trace is killed by replacing call with jump over
                  the trace ID to the next instruction)
     2.   'ON ' - turn trace facility back on (stop killing traces)
     3.   'BUG' - force interactive debug mode
     4.   'IOF' - interrupts off (unsolicited keys queued for input)
     5.   'ION' - interrupts on  (any key stroke invokes user
                  interface)
     6.   'IFL' - instruction fetch loop (special trace used in E370
                  to identify next trace id as 370 operation trace to
                  be stored in trace table)

     The first call to MMDBUG in A370, L370, and E370 is with 'OFF'
     unless the trace option was requested via COM file parm or if the
     debug option D was specified on link edit of COM or BIN file.

     C.  User Interface

     When MMDBUG is called without the 'OFF' argument, or when a key
     is hit without the 'IOF' argument being issued previously, the
     user interface mode is invoked and the following commands may
     be entered in upper or lower case from the console:

          A - ADDRESS STOP (PROMPTS FOR ADDRESS, LENGTH, TYPE)
          C - CONTINUE TO NEXT TRACE ENTRY
          D - DUMP MEMORY (PROMPTS FOR ADDRESS)
          F - FIND TRACE ENTRY (PROMPTS FOR TRACE ID)
          H - HELP LIST MMDBUG COMMANDS (THIS LIST)
          I - INSTRUCTION COUNTER WORD
          J - RESET NEXT 370 OR 8086 INSTRUCTION ADDRESS
          K - KILL MODE SET/RESET (kills or restores traces)
          L - SET/RESET TRACE LIMIT FOR Q/T MODE
          M - MODIFY MEMORY (PROMPTS FOR ADDRESS AND DATA)
          N - LIST LAST 20 TRACE ENTRIES (NOTE K,Z  AFFECT THIS LIST)
          P - SET/RESET PRINT COPY OF ALL MMDBUG I/O
          Q - SET QUIET MODE (USED WITH F, L, AND 'BUG' OPTIONS)
          R - DISPLAY REGISTERS (SEE Z OPTION)
          S - SAVE/UNSAVE CURRENT TRACE ID FROM KILL MODE
          T - SET TRACE MODE (USED WITH OPTIONS F AND L)
          W - LIST FREE MEMORY QUEUE
          X - SET/RESET ASSIST LOGGING OF INTERACTIVE DEBUG OUTPUT
          Y - MODIFY 8086/370 REGISTER (PROMPTS FOR REGISTER/DATA)
          Z - SET/RESET 8086/370 MODE
                IN 8086 MODE, R DUMPS 8086 REGISTERS AND D PRINTS
                PRINTABLE ASCII CHARACTERS IN DUMP.
                IN PC/370 MODE, R DUMPS 370 REGISTERS AND PSW
                AND D DUMPS PRINTABLE EBCDIC CHARACTERS IN DUMP.
         <cr> - dump same address again as defined in D command
         <sp> - dump forward until any key hit
         <bs> - dump backwards until any key hit
         <esc>- exit to MSDOS after attempting to close files

     Memory addresses may be entered in xxxx:xxxx or xxxxxx hex format
     without leading zeros required.  In 370 mode, the xxxxxx format
     always refers to the relative address within the current address
     space.  In 80x86 mode, the xxxxxx format refers to the offset
     using the current segment.  The segment:offset is initialized to
     the emulator data segment area containing the 370 registers.

     D.  User Guide

     The PC/370 interactive debug facility can assist you in locating
     errors within your 370 assembler programs.  But first there are
     some more basic things to check:

     1. Are you sure that you are executing the latest version of
        the source program.  To be absolutely sure, code the date
        and time in a print statement at the beginning of the program
        and then reassemble (A370) and relink (L370) and execute the
        program again.

     2. Does the program run to normal termination?  If so then you
        can run the program again specifying a T as the only parameter
        on the execute command to initiate the interactive debug
        facility.  Another way to invoke the interactive debug option
        is to specify option D in the linkage editor.   This method
        should be used if the program requires a parameter other than
        T.

    3.  If the program terminated abnormally, the interactive debug
        facility is automatically initiated along with a display of
        the PSW and the failing instruction.  To calculate the
        relative address of the failing instruction in the program,
        subtract the program load address of X'0200' (Note you will
        have to look at the link edit listing to get the starting
        address if the failing instruction is in a subroutine.

    4.  To trace execution of the program, enter K once or twice to
        restore all traces and then enter T.  To stop the trace at any
        point hit any key.

    5.  To continue execution of the program normally, enter Q.
        For fast execution, use K command to set kill trace mode
        first.

    6.  To dump the current contents of the registers, enter R.

    7.  To dump any 32 byte area in memory, enter A followed by
        the starting address in hex xxxx.

    8.  To continue to dump memory from the current location forward,
        hit the space key.  To dump backwards, hit the backspace key.
        To stop the dump, hit any key.

    9.  To stop the program at a specific address, enter A followed
        by the address in hex xxxx followed by the option code A.
        Then use Q or T to continue execution until the address is
        found.

   10.  To stop the program when a specific data field in memory is
        changed, enter A followed by the address in xxxx followed by
        the option code E for equal data or N for not-equal data.
        Next entry the length of the data compare in hex when
        prompted.  If option E is selected, enter the hex value of the
        data you want to search for when prompted.  Next press Q or T
        to continue  execution until the data compare specified
        triggers debug user interface again.  To stop at a specific
        instruction count in a 370 program, use the I command to
        display the instruction counter word and then use data equal
        address stop on the word.  To obtain detail instruction trace
        up to point of failure, either use Q or T from beginning of
        the program or set address stop at previous multiple of 256
        on instruction count field and then restore traces with K
        command and then use Q or T proceed to point of failure.  At
        point of failure, use N command to list last 20 instruction
        trace points.

   11.  To turn off any address stop option, enter A.

   12.  To list the last 20 instruction trace table entries, enter N.
        If running in 370 mode (option Z toggles mode), only the 370
        instruction traces will be stored and listed via option N.
        In 80x86 mode, all traces will be stored and listed.
        Note that this list may be incomplete if the program
        was running with K option active to kill traces for speed.
        Option K kills each trace entry to debug the first time debug
        is entered for that trace point.  Option K makes the program
        run much faster at the expense of losing repeated trace
        points until K reset is issued.  However, you can use Find to
        locate selected trace id's and use Save to protect id from
        kill mode.  This option allows much faster execution while
        still being able to trace selected id's.  A very useful id to
        save is IFL which will then trace each 370 instruction during
        kill mode while killing all of the lower level ID's for
        reasonable speed yet full visibility of 370 instructions.
        Faster still is to save only one 370 instruction id such as
        TRT.  This is very useful in conjunction with address stop,
        since the address stop overhead is only incurred for the
        selected saved id's.  Note that the trace table only contains
        addresses of instructions, and as a result if instruction
        modification or overlays are used, the data listed for a
        previous instruction may be different from what it was at the
        time it was executed.  In this case it may be helpful to rerun
        program with address stop to see what was in memory at the
        time an instruction was executed.

   13.  To set a fixed limit on the number of trace entries before
        entering debug command mode again, enter L and count in hex
        xxxx.  Next enter Q or T to continue until count reached zero.
        If zero count is entered, the limit is not checked.

   14.  To modify memory, enter M followed by address in hex xxxx.
        Next enter hex data bytes followed by return key.

   15.  To display the 8086 registers, type Z to switch to 8086 mode.
        Now type R.  In 8086 mode, storage dumps translate data to
        ASCII instead of EBCDIC for character display.  In 8086 mode,
        N lists all trace entries instead of just IFL 370 instruction
        traces.  In 8086 mode, Y changes 8086 registers instead of 370
        registers.  To return to 370 mode, type Z again.

   16.  The W command displays free memory in the 8086 data segment
        for 8086 mode and the free memory in the current address
        space in 370 mode.  Note these are two totally separate free
        areas.  The 8086 free area is limited to <= 64k addressable by
        the DS register and uses 4 byte free queue elements
        (next,length).  The 370 free area extends from the end of 370
        code in COM module to the end of free memory and uses 8 byte
        370 format free queue elements (next,length) on 8 byte
        boundaries.  For BIN file execution, the free area is the SQA
        area allocated in the emulator address space.  The first free
        queue element in a 370 address space is pointed to by ASCASF
        field in address space control block located at X'104' in low
        memory (may be zero if no free memory currently available).
        The ASCB for BIN modules can be located by subtracting
        (X'200'-X'104') from the entry point address in register 15 at
        entry (trace ID 370).

   17.  The J jump command may be used to modify either the emulator
        or the 370 current instruction address depending on the
        current Z mode.  In 370 mode, the address entered is a virtual
        address.  In 80x86 mode, the address entered is a code segment
        offset (This is a very dangerous function and not
        recommended).

*********

Chapter 8.  Floating Point Support

*********

  A.  Register formats

    1.  General purpose registers

        The general purpose 370 registers are located at the beginning
        of the data segment of the E370 emulator (DS:0).  They are
        stored in 80x86/80x87 long integer format with least
        significant byte first starting with register 0.  For example,
        the high byte of register 0 is at DS:3 and the low byte of
        register 1 is at DS:4.  This area can be used with address
        stop to detect a specific register value or change in register
        value (although remembering reverse format is always a
        challenge).  This format is used to allow native loads and
        stores without reversing bytes which speeds up register to
        register operations and allows addition of registers directly
        from memory without conversion.

    2.  Floating point registers

        If the 80x87 co-processor is installed, the R command displays
        the four 8 byte floating point register values numbered 0, 2,
        4, and 6.  This is one way (other than 123 /WS screen) to tell
        if 80x87 is installed.   The floating point registers are
        stored in 80x87 temporary real format which is 10 bytes long.
        The first 8 bytes contain the normalized 64 bit unsigned
        mantissa with the high bit always on stored in reverse order
        (like a double long integer with the least significant byte at
        low address.  The last 2 bytes contain the base two exponent
        and the sign stored as an integer.  The 15 bit exponent is
        stored in excess 3FFFH format.  True zero is represented by
        plus or minus sign and all other bits zero.  This format
        exceeds 370 double precision 8 byte format for both mantissa
        and exponent range.  This format is used to significantly
        speed up floating point register to register operations since
        numbers can be directly transferred to/from 80x87 in this
        format.  A conversion routine must be used to convert floating
        point numbers when moved to/from memory to the floating point
        registers.  The conversion routine is quite efficient but does
        involve shifting entire number up to 3 bits left or right to
        convert from normalized base 2 to base 16.  The floating point
        register memory area can be dumped to see the real format and
        can be used with address stop to detect specific value or
        change in value.

  B.  Floating Point Scientific Subroutine Package

    Using floating point 370 instructions plus extended 80x87 function
    SVC's described in SYSTEM.DOC, a set of efficient scientific
    subroutines have been coded in SSP.ALC and are stored in the
    L370.LIB subroutine library.  The argument and result is in F0 or
    R0 unless noted otherwise.  The SSP functions are similar to the
    FORTRAN IV intrinsic functions.

    FUNCTION   DESCRIPTION   RANGE LIMITATIONS           NOTES

    ATAN       ARCTAN
    ALOG       LOG BASE E    0 < F0
    ALOG10     LOG BASE 10   0 < F0
    COS        COSINE
    EXP        E ** X
    REAL       CVT TO REAL   -2**32 <= R0 < 2**32        ARG. IN R0
    INT        CVT TO INT    -2**32 <= F0 < 2**32        RESULT IN R0
    MOD        MOD(F0,F2)                                REMAINDER R0
    PI         PI            3.14159.............
    SIN        SINE
    SQRT       SQUARE ROOT   0 <= F0
    TAN        TANGENT

  C.  Floating point co-processor assisted standard 370 instructions.

      1.  If the floating point option is on and an 80x87 co-processor
          is installed, then it is used to assist the CVB and CVD
          instructions for speed.  In the case of large numbers, the
          speed improvement can be up to 4 times.  For numbers close
          to zero, there is no improvement in speed.  Depending on
          user demand, this type assist may be added for other packed
          decimal instructions in the future.

*********

Chapter 9.  XA Extended Architecture Support

*********

  1.  A370 supports the XA instructions as defined in the
      IBM System/370 XA Principles of Operation manual version
      SA22-7085.

  2.  E370 supports the 6 XA non-privileged instructions
      BAS, BASR, MVCIN, BASSM, IPM, and BSM.  When the emulator is in
      31 bit mode, the PSW format displayed by MMDBUG is extended mode
      with the high address bit on.  The emulator defaults to 24 bit
      mode and the 370 basic PSW format.

  3.  The standard instructions LA, BAL, BALR, EDMK, and TRT
      now support both the 24 bit and 31 bit addressing modes
      as set by BASSM or BSM using the PSW address mode bit.
      Note that in 31 bit addressing mode the LA instruction
      adds all 31 bits of the index and base register plus
      displacement and clears only the high bit of the result.  This
      means the high byte of the index and base must be cleared when
      using 24 bit addresses in 31 bit mode.

**********

Chapter 10.  System subroutine library

**********

The following subroutines are included in the default system
subroutine relocatable library L370.LIB in the root directory:

 #  SUBROUTINE ENTRY   FUNCTION                    ARGUMENTS

 1  DAT                print date and time         none

 2  TIMER              return current time         none
                       of day in R0 in 100th
                       of a second units

 3  PET                print elapsed time since    none
                       last call plus date and
                       time and 370 instruction
                       count interval statistics

 4  DTIME              print time in upper left    none
                       corner of screen in format
                       HH:MM:SS

 5  SYNERROR           print PC/370 input/output   R0 = error code
                       error message based on      R1 = function code
                       return codes passed in
                       registers R0-R1 at entry
                       to SYNAD DCB exit routine

 6  SSP                scientific subroutines
                       (see chapter 8 for entry
                       points to this module)

 7  API                support application using
                       application program interface
                       (API) with IBM PC 3270
                       emulation via interrupt 7A

The 370 source code for all of the above modules is in the LIB
directory, and the BAT\BLDLIB.BAT command file will rebuild library
from the source.  Remember when adding subroutines to a relocatable
library that there cannot be any backward references to prior modules
in the library since L370.EXE uses serial one pass search for external
references in the library.

**********

Chapter 11.  COBOL call interface support

**********

To call a PC/370 assembler subroutine from a Micro Focus COBOL program
requires that the PC/370 emulator E370R42.EXE be made resident by
executing it directly (see BAT\RUNCBL.BAT for demo).  Each subroutine
to be called must be assembled and linked using option B to create a
BIN type file which will be dynamically loaded on the first call.

The interface performs the following functions prior to transferring
control to the assembler subroutine:

  1.  The address space control block at X'104' in the BIN file is
      initialized to a virtual equals real (V=R) region in order to
      address the arguments passed.   The ASCASF free memory pointer
      is initialized to point to the current first free queue element
      in the common system queue area (SQA) memory allocated along
      with the resident emulator.   The SQA is used to dynamically
      allocate buffers for subroutine file I/O and any other dynamic
      memory requests via GETMAIN/FREEMAIN svc's.  Note that SQA is
      shared by all subroutines and each subroutine must release any
      memory it uses prior to exit or SQA will eventually be depleted
      (just like MVS).

  2.  The segment and offset argument addresses on the stack are
      converted into a standard 370 calling list of 32 bit absolute
      addresses located at X'80' in the BIN file (normally the command
      line area).  Up to 32 arguments can be passed.

  3.  The 370 registers are set as follows:

        R1 = absolute address of argument list at X'80' in BIN file

        R14 = absolute return address to exit subroutine at X'102' in
        BIN file via detach SVC.

        R15 = absolute address of entry point (normally X'210' in BIN
        file.   At exit from called BIN module, the low 16 bits of
        register 15 are used to set special Micro Focus COBOL return
        code value called RETURN-CODE.  If emulator is not resident
        when a BIN module is called, a return code of 16 is passed.

  4.  If option D was specified in the L370 link of the BIN module
      being called, the emulator interactive debug facility will be
      invoked at entry with all traces restored.  If option D was
      not specified, execution will proceed without interruption and
      no traces will be restored to provide fast execution of one or
      more BIN modules.

  5.  Note that BIN modules are dynamically loaded by COBOL run time
      system at unknown addresses.  Since BIN subroutines run in
      V=R address mode in order to address COBOL data areas, all 370
      subroutine code must be self relocating.  See CBL\TESTCIO.ALC
      for example of how to relocate any address constants required
      such as subroutine entry points and DCB addresses.  The A370
      assembler lists all relocation addresses in PRN listing created
      with the /L option.

**********

Chapter 12.  Technical References:

**********

   1.  For information on 370 machine instructions see
       IBM System 370 XA Principles of Operation manual SA22-7085.
   2.  For information on 370 assembler language see:
       a.  IBM OS/VS Assembler Language manual GC33-4010.
       b.  Assembler Language Programming by G. W. Struble.
   3.  For information on how the assembler, linkage editor, and
       operating system software works see:
       a.  Systems Programming by John J. Donovan.
       b.  Operating Systems by S. E. Madnick and J. J. Donovan.
   4.  For information on the 80x86 processors see:
       a.  The 8086 Book by George Alexy.
       b.  Intel iAPX 286 Programmer's Reference Manual 210498-003.
       c.  Intel 80386 Programmer's Reference Manual 230985-001.
   5.  For information on the MSDOS operating system and utilities
       see:
       a.  Disk Operating System Version 3.2 Reference 68X2405.
       b.  Disk Operating System Technical Reference 6139658.
       c.  Advanced MS-DOS by Microsoft Press ISBN 0-914845-77-2
   6.  For information on usage of ASSIST extensions see:
       a.  Assembler Language with Assist by Ross A. Overbeek and W.
           E. Singletary.  Published by Science Research Associates,
           Inc., Chicago, Copyright 1976, ISBN 0-574-21085-7.
       b.  IBM 370 Assembly Language with ASSIST, Structured Concepts,
           and Advanced Topics by Charles J. Kacmar.  Published by
           Prentice Hall, September 1987, ISBN 0-13-455742-5.
   7.  For summary article on how PC/370 was developed see ACM
       Sigsmall Newsletter Volume 8 Number 3, August 1982.
   8.  For article on conversion of PC/370 from CP/M to MS-DOS see
       ACM SIGSMALL/PC Newsletter Volume 11 Number 3, August 1985.
   9.  For information on 80x87 see Intel iAPX 286 Programmer's
       Reference Manual #210498-003.  Also book by designer titled,
       "The 8087 Primer" by John F. Palmer and Stephen P. Morse,
       published by John Wiley & Sons, inc. Copyright 1984, ISBN 0-
       471-87569-4.