FIRST.DOC

Copyright 1986, 1987, 1988  by Thomas F. Droege, All Rights Reserved.
Version 1.86 21 August, 1988

                   *******************************
                   *  BE SURE TO READ UPDATE.DOC *
                   *******************************

                               DROEGE

      Design Robot for Origination of Exacting Graphic Engineering

DROEGE is a general purpose program for the design of printed circuit 
photomasters.  Is was created as a demonstration program for our low cost 
precision photoplotter.  As it was developed it became more and more useful as 
a design tool, so eventually the circuit boards and the mechanical drawings 
for our photoplotter were done using this program.  

This is a manual CAD system.  That is, it does nothing automatically like 
schematic capture, wire listing, routing, parts lists, etc..  It does provide 
a computer aided equivalent of a taped master or drawing board with the 
advantage that things are always in perfect registration and one can work on 
selected layers.  

General features are a 65 x 65 inch working area 12 layers deep.  Resolution 
over this area is 0.001 inch.  At least this is the way it is labeled - the 
output can be scaled to anything so what is really provided is a 65000 X 65000 
point working space.  The layers can be turned on and off and assigned to any 
available color.  Lines, Pads (something a photoplotter can do - a small 
object drawn all at once), Symbols (a named collection of other objects), 
Arcs, and Labels can be entered.  The Symbol feature is particularly powerful 
since Symbols can be nested within Symbols to many levels (20) allowing 
construction of very complex objects with a few keystrokes.  

The program being distributed through free channels is very powerful, but is 
missing some of the convenience features of the commercial version.  The main 
differences are lower display resolution, CGA versus EGA; reduced editing 
commands; and less available memory.  We have been able to create very large 
boards with this program, even in its limited form.  If you end up using it a 
for professional work you will want the commercial version as it will pay for 
itself in reduced labor costs.  
  
Depending on how clever one is in conserving space, circuits can be designed 
with ten to twenty chips or about 100 components.  As can be seen from the 
demonstration files,  fairly elaborate designs can be created with the "free" 
version.  The program with full storage allocation will accommodate designs of 
about 300 chip equivalents.  It also allows you to view more of a circuit at a 
time through use of the EGA.  Also supported in the pay version is cursor 
movement by a mouse, and much improved object editing with move, copy, insert 
and move point, and change. 

You will find no appeal to guilt to get you to buy the registered version.  If 
you really use it, it will be in your interest to buy a license.  If you try 
this demonstration version  on something small to test its features you are 
earning what you get by your work,  and helping us sell the product - a fair 
exchange we think.  Print PROD.SUM for details of the advanced software and 
the photoplotter.  Print PRICE.DOC for a price list for preparation of plots 
from the output of this program.  

Print DEMO.DOC for instructions for a quick tour around the facilities.  
TUTOR.DOC directs you through a few simple tasks.  LEARNSYM.DOC works through 
the steps needed to prepare simple printed circuit boards in great detail.  Do 
not underestimate the effort required to learn to use this or any other CAD 
system.  As a member of a CAD selection committee for a large laboratory the 
author has reviewed many systems, it is an awful job.  My current view is that 
one just begins to know the features needed after six months use. 

Note in editing: This above was written in 1986.  My group in the laboratory 
where I work is currently (1988) attempting to purchase a new CAD system.  I 
am mercifully not involved, since I like what I have.  But some who work for 
me are.  While standing around the water cooler yesterday, we added up $10,000 
worth of my group's time just visiting vendors and trying to understand their 
systems.  We are planning to spend about $250,000.  We realize that both the 
evaluation time and the cost of the system are small compared to the cost of 
using it.    My group has been brain washed by using my system so they want 
the powerful symbol features of this $10 program to be available in the 
$250,000 system.   These are really capable people, several have PhD's.  But 
after spending all that time they just don't know what the systems will do.  
The marketing people are really clever.  Their demonstration programs are 
designed to make it look like the programs can do anything.  It is only after 
you come back with your problem job to try to do it yourself that the 
limitations are uncovered.  Use this "free" system a while and you will be a 
lot more expert at finding the limitations of the fancy systems.  These big 
commercial systems are really difficult to learn.  We expect that a good 
designer (some of our designers hold PhD degrees in physics) will just start 
to be able to be facile with the system after six months of 12 hour days.  
While they auto-route, auto-place, schematic capture, rubber band, and 
simulate the circuit; they may not be able to do symbols as this program can.  
The big expensive systems come with a wall full of manuals.  More is better - 
right?  One system we like because it is powerful, requires that you talk to 
it in Unix macro language.  If you know what that means you know what it 
means.  If you don't, then it is worse than your most imaginative nightmare.  

So when you write me letters complaining about how hard this system is to 
learn, and that I don't provide enough documentation, be thankful that you 
have not spent $250,000 for it, that most people can get it running without 
spending two weeks at the factory, and that it did now come with 50 manuals 
that you must read. 

                       ***** SPECIAL OFFER ***** 

For a limited time, if you follow the procedure in PHOTOOL.DOC we will produce 
a phototooling set for your job.  We will plot anything you can get on an 8" x 
10" area of 10" by 12" film, for $25.00 per layer (Since we don't know when 
you will read this, this offer is subject to confirmation, see PHOTOOL.DOC for 
the procedure).  

The following lists the documentation on this disk with a brief description of 
what each file contains.  We suggest you do DEMO.DOC and TUTOR.DOC and don't 
bother to look at much else until you have tried to do a few things.  
ABOUTPC.DOC tells how printed circuits are made.  LEARNSYM.DOC works through 
the symbol process in great detail.  KEYTREE.DOC will help show you where you 
are going in the program: 

The last distribution contained PC-Write page breaks.  We removed them in this 
version so run your printer with whatever page break feature you like.  
Otherwise you will get continuous listings.  It is enough for us to try to 
write this stuff without writing a print program to make it look pretty.  

FIRST.DOC 

This document.  

MANUAL.BAT - PRINTS A MANUAL CONSISTING OF THE FOLLOWING SECTIONS: 
             (You may print individual sections if you wish)

INTRO.DOC 

Introduction and design philosophy.

DEMO.DOC

This leads you through a demonstration of what the system will do.  You 
do not get to do anything, just look.  This is our "gee whiz" demo.  

TUTOR.DOC

This leads you step by step through a few simple tasks.  We have tried 
to start with excruciating detail and gradually tell you less and less 
as you become familiar with our general approach.  

ABOUTPC.DOC

This section tell how printed circuit boards are made.  Please, those of you 
who are experts, don't write me letters telling me the procedure is not up to 
date.  It was written to give the novice some idea of why the various photo 
tooling items are needed.  

LEARNSYM.DOC

This section is for real beginners.  If you are an old hand at printed circuit 
layout and are used to computers, the DEMO and TUTOR sections and the COMMANDS 
appendix may be enough for you.  You can operate on the assumption that the 
program will do what you want it to do and just look up the desired operation 
in the COMMANDS section.  

QUICK.DOC

Quick summaries of how to perform the most common tasks.

HOWTO.DOC

How to do some more complex operations.

APPENDIX.BAT - PRINTS AN APPENDIX TO THE MANUAL CONSISTING OF THE FOLLOWING 
               SECTIONS (Or you can print them separately): 

COMMANDS.DOC

An alphabetical listing of the command keys.  This is the primary reference 
document for all the operations that are available. 

KEYTREE.DOC

Operation of this program is by use of the function keys.  Each key press 
typically reassigns the keys to a new set of values.  KEYTREE.DOC is a "map of 
the cave" showing the route through the menu keys with very brief summaries of 
key operation.  The key menu is presently fourteen layers deep and has 
hundreds of entries, many of them repeated.  A number of the key operations 
are reentrant so that much deeper entry is possible.  The design allows quick 
movement to a menu that will do what you want.  It may be useful to print this 
out and hang it on the wall when you first start using this program to remind 
you of what is available and as an index for COMMANDS.DOC.  We thought this 
would be very useful.  We find it almost impossible to read, but we include it 
because we went to the work to prepare it and it might fit someone's taste.  

ERRORS.DOC

Error messages and their meaning.

STANDARD.DOC

This document suggests a set of standards to get you started.  It pays to 
approach a job in a consistent manner.  This file gives a set of standard 
procedures for producing a design for a two sided plated through hole board.  
If you follow this standard we will be able to plot your job for you with 
minimal hassle.  

PLOTOUT.DOC

How to generate a plot output file with sample file output.

THE FOLLOWING MISCELLANEOUS DOCUMENTS CAN ALL BE PRINTED WITH MISC.BAT 
OR THEY MAY BE PRINTED SEPARATELY:

PHOTOOL.DOC

How to get a set of phototooling prepared from your design.  Read this before 
you prepare a job for us to plot.  

PRICE.DOC

We can prepare phototooling sets from the output of this program.  This list 
allows you to estimate the cost.  We can charge a Visa or Master Card.  

PROD.DOC

A summary of the Environmental Optics products.  Specifications are included 
for our photoplotter, and the the two current versions of the program.  We 
also include some of our future software plans. 

USERS.DOC

We will collect and distribute useful libraries.  This is a form to 
make a submission.

REGISTER.DOC

We do not expect a registration fee.  If you find this program to be useful, 
and feel guilty, then buy the commercial version, $100 post paid.  You will 
enjoy the additional features more than the loss of guilt.  Send this form 
without money and we will keep you advised of new versions.

UPDATE.DOC

Changes and bug fixes by date.  *********Be sure to read this file.*********  
New goodies are described here.  

PRINTALL.BAT

Prints everything.

ORDER.DOC

Order form for photoplotting.

Please forgive inconsistency in this documentation.  It is a big job to edit 
all these words when we make an improvement.  So if words point to something 
that you cannot find, perhaps it was there once.