LEARNSYM.DOC

HOW TO WORK WITH SYMBOLS 

This exercise tells you a little about symbols, and how they are unique to 
this program.  We then lead you step by step in the creation of a symbol, 
which is the normal way to prepare a set of artwork.  We show you how to put a 
symbol on the job or in another symbol.  We show you how to get a plot on a 
printer, how to make plotter files, and how to save your work for later 
additions.    

The symbol feature of this program is very powerful.  We find that systems 
which cost $50,000 and up cannot nest symbols as we do.  This is because they 
have to do schematic capture, simulation, and other wonderful things that you 
may not need to do.  Keeping track of everything through layers of symbols is 
too tough a job for even the big systems.  We have just spent hundreds of 
group man hours reviewing systems from (July 1988) big names like Cadnetix, 
Hewlett Packard, Mentor Graphics, and others and none can nest symbols.  

We are presently involved in the design of a high voltage power supply system 
which has eight high voltage modules which plug into a VME mother board.  We 
designed the plug in board manually using this system as a two layer board.  
Another group designed the VME mother board.  It was done by a big design 
system and uses ten layers.  There are awful errors, like the power bus is 10 
mils wide in several spots, and even a moderately good layout designer would 
have done the job with four layers.  That is what happens when you turn a big 
design system loose with some rules.  When you see the result, you wish you 
had provided a different set of rules, but a live designer would have changed 
his rules when he saw something bad.  But the real problem is that the 8 
identical circuits are laid out eight different ways.  Now we have to test it 
and find that we have eight different sets of problems.  We have discovered 
that there is no real way, on even the largest systems, to duplicate part of a 
layout when it is repeated.  

My guess is that the other design group will do more work than I before the 
job is done.  The big systems do have some nice features.  They make you put 
all the wires in to match your schematic.  People like me that change their 
designs on the fly must keep going back to the schematic section of the 
program if they want to make a change, in the end you are absolutely forced to 
have a correct diagram.  Still, I would prefer the pain of having to keep 
track of which wires I have routed to the helplessness of having the machine 
put things where it wants to.  

For this system, a symbol is any collection of work.  This means lines, pads, 
lettering, arcs, and even other symbols.  The only limitation is that you 
cannot put a symbol in itself.  We sometimes allow ourselves to do this for 
test, the result is like standing between two mirrors, eventually the computer 
runs out of something and dies.  

We find it useful to make a symbol library of common things.  Not just the 
basic symbols for common sized R, C, and IC outlines found on the distribution 
disk as ELEC.LIB, but also common circuits we use, such as amplifiers, timing 
circuits, memory layouts, etc.  

We in fact recommend that you make your entire project a symbol.  

In order to locate a symbol on the job or in another symbol, it must be loaded 
into memory.  If in doubt, you can list the symbols in memory as we do in the 
following example.  You will need to have a printer. 

To start the program put distribution disk 1 in the default drive and type: 

DROEGE (ENTER)  That is type DROEGE followed by the ENTER key.

After you have read the sign on  message hitting any key should get a nice 
blue screen with function key labels across the bottom of the screen and other 
information (see DEMO.DOC) across the top, including the cursor position at 
the top right.  The cursor appears as a blinking square which can be moved by 
the arrow keys.  

Most operations are done by hitting function keys at the left of the keyboard.  
DEMO.DOC and TUTOR.DOC introduce these keys.  This exercise assumes you are 
now familiar with the general ideas.  

Now press the function keys as indicated.  We list here the entire label as it 
shows on the key.  You just have to push the numbered key at the left of the 
keyboard: 

F2FILE          Because that is where we happened to put the command to list 
                symbols. 

If you have not already done so, this is a good place to get a listing of the 
setups.  You will need a printer for the following step.  If you do not have a 
printer skip this step. 

F5LSTSET        A two page table is printed.  Hang this where it is available 
                for reference.  

F2GETFIL        We want to get something from a file
F3LSTSYM        To list the symbols in memory on the printer.

If you don't have a printer the system will say something awful.  Like fatal 
error and some other garbage.  But don't be concerned, it is hard to kill this 
program.  From a freshly started program you will find that you have no 
symbols.  The printer will list one funny symbol called JOB$$SAV.  This is 
where we store the work you do on the job.  We don't automatically load 
symbols because they use up space and we want to give you as much space as 
possible.  To load some representative symbols, for example the library 
ELEC.LIB push function key 2. 

F2LODLIB

To the question answer:

ELEC (ENTER)  

Do not type the extension .LIB or again you will get a nasty error message.  
Just follow the instructions and try again. 

If all goes well, the disk light will come on and symbols will be loaded.  

F3LSTSYM

Will now get a list of about 15 symbols on the printer.  If you don't have a 
printer, you can still do this exercise, but you will have to fly blind.  

Now use the F9 key to get back to the starting menu.

F9BACK
F9BACK  

The bottom menu line should now read:

1ENTER   2FILE   3PLOT   4SETUP   5PATH

If it does not read as above, hitting F9 enough times should get the above 
menu.  If you get lost you can always get to this menu by hitting F9 enough 
times.  Answer "y" when asked if you want to leave a symbol, but "n" when 
asked if you want to leave the job.  If against all our precautions, you 
manage to "break" the program, hitting key pad #9 with caps lock on and num 
lock on and the rest of the special keys off, will usually get you back to 
this starting position.  This is useful if you have done a lot of work without 
periodic saves and then produce a hang.  Honest folks, we have not seen a real 
hang in this version of the program in over a year.  Still, we provide a 
parachute when you fly with us.  

Now let us play with symbols.   

F1ENTER           To go towards entering data
F3SYMBOL          To do something with symbols
F3CREATE          To do something creative with symbols - I had to name it 
                  something.
F5OPEN            To open an existing symbol to change it.

In answer to the question:

IC14 (ENTER) - The name of the symbol we want to work on followed by the 
               ENTER key.  

Symbol names are case sensitive.  That is Ic14 is a different symbol from 
IC14.  If you type wrong you will get a symbol not available message.  Hit F5 
and try again.  We recommend that you run this exercise with the CAPS LOCK key 
on.  This will reduce the chance for a typing error.  In general, unless you 
like naming things in mixed upper and lower case we suggest you pick one case 
and stick to it.  We always run in upper case.  

The system will draw an IC outline at a scale which fills most of the screen.  
We try to follow a convention when we make symbols.  For the most part, the 
symbols in ELEC.LIB were made so they extend horizontally with pin one at the 
lower left, or 0,0 position.  

This symbol is more complicated than it looks.  It has information on five 
different layers.  By using the prepared setups, we can look at the layers 
(levels) one at a time.  Looking at the chart we printed, we see that setup 1 
contains a color assignment for only level 1.  The color assignment column 
indicates what will show when we redraw.  We are presently drawing with setup 
0 which contains color assignments for most layers, so nearly everything is 
showing.   To change the setup assignment we need to find a menu which has a 
4SETUP key label.  This is repeated many places, usually where needed.  But it 
is not on the current menu.  We hit a key to find it: 

1LINE

The new menu contains 4SETUP so: 

4SETUP

The top line now shows that we are in setup 0, and some information about 
setup 0.  There is not enough room on the top line for everything.  The 
advanced version uses the EGA features to display the entire setup table, but 
we will have to be content with our listing.  We want to change the setup so: 

1EDSET

We get a new menu which contains only UP and DOWN  and a key 5 label which 
reads 5*SETUP to indicate that we can change the setup.  Since we want to go 
to setup 1 we go up once.  Many downs would also get there. 

1UP

The second line now reads SETUP 1, LEVEL 1, COLOR GREEN, APER OFF.  This tells 
us that we are now in setup 1, that we are looking at level one of the setup 1 
table, that level one of setup one is displayed in green, and that if we 
attempt to draw a line or pad, nothing will happen as there is no aperture 
selected.  

We can redraw the screen at any time.  This is done with the F10 key.  The 
first press lists a table of previously selected places to look.  We can use 
the menu to select a new area or we can redraw the present area with a second 
F10.  We want to redraw the present area with the new setup so: 

F10REDRAW
F10REDRAW 

The IC is now drawn in green.  Just the pads are drawn.  And we notice they 
are smaller.  When the system last drew the IC it noticed that there were 
things on several layers.  To show this it drew in the "OR" of the colors and 
the size of the largest object.  Since this IC has an eighty mil solder mask 
on level 5, it drew the pads as eighty mils square.  Now it is only showing 
level 1 where the pads are sixty-two mils on a side.  Notice also that the 
package outline drawing disappeared.  It was on level 4.  STANDARD.DOC lists 
our standards for design.  It is not necessary that you follow them, but it 
helps avoid confusion if you send us work.  Otherwise, it is helpful to you to 
set up standard ways of doing a design.  

Let us look at another layer.  

F1UP

This time the second line shows:

SETUP 2, LEVEL 1, COLOR OFF, APER OFF

This is OK as far as it goes.  If we look at the print out we indeed see that 
level one does not have a color assigned to it.  But level 2 does and that 
does not show on the status line.  There is just not enough room to show 
everything.  By backing down one menu level and selecting level for edit, one 
can UP - DOWN through the levels for this setup.  The whole process is awkward 
but it is the best we can do.  Some day we will do this with pull down menus 
and a mouse.  The advanced version is better as you can see everything at 
once. 

F10REDRAW
F10REDRAW

And the pads redraw in red.  This is what is on level two.  Now go to setup 3 
and redraw: 

F1UP
F10REDRAW
F10REDRAW

Looking at the setup listing, we see that setup 3 draws level 3 and 4 at the 
same time.  We put drill spots on level 3 and the package outline on level 4.  
We can easily see both as the drill spots are slightly larger than the line 
used for the package outline.  The drill spots are displayed in green and the 
outline in brown according to the color selections for the two layers showing.  

F1UP
F10REDRAW
F10REDRAW

One more time gets us the outline only. 

F2DWN
F2DWN
F2DWN
F2DWN

Puts us back where we started, at setup 0, where all levels are showing.

Now that we have seen what this symbol looks like, we will close it and look 
at another symbol.  

F9BACK    -  four times.

To leave the symbol.  The system asks "enter y to exit symbol" answer:

Y (ENTER). 

The system tells us it has closed the symbol.  It also does a calculation of 
the size of the symbol at this time so that the next time the symbol is opened 
it can draw it to fill the screen.  

F5OPEN            To open another symbol.
 
answer C (ENTER) to look at the capacitor symbol.  
 
Again the system draws the capacitor symbol to fill the screen.  Again back 
out with an F9.  

F9BACK  answer Y (ENTER)

Now that we have seen what a couple of symbols look like, we will put several 
symbols in a symbol to simulate creating a full piece of work. 

F1NEW 

We are asked to enter a symbol name.  There is no real limit to the entry, but 
sticking to eight letters or less will facilitate later making a library  (DOS 
file) with the same name.  Being an old Smokey Stover fan we name the symbol: 

FOO (ENTER)

We are now asked to locate the symbol origin.  Wherever the cursor is when F3 
is hit will become the 0,0 reference point for this symbol.  When we locate 
the symbol we are creating in the job or another symbol, the work we enter now 
will appear in the same orientation to the point located as it does to the 
origin.  This may seem vague now but a few examples will demonstrate the 
process.  Symbols can be located rotated at 90 degree steps.  Symbols rotate 
around their origin.  So it it best design symbols so you can remember their 
origin and their original orientation.  Sorry, but we have not been consistent 
in the various examples.  ELEC.LIB is mostly done with pin one at the lower 
left for IC outlines, and R's and C's horizontal.  Other libraries we have 
done standing up.  You will develop your own preference.  It does not take 
long to make a library in a style that is pleasing to you.  

Move the cursor near the lower left corner of the screen.  

F3ORIGIN

Note that the value of the cursor position is now 0,0.  We notice that the 
capacitor symbol is still there.  The screen is normally erased only when you 
redraw.  We do that now, though sometimes it is useful to have an old symbol 
left on the screen.  For example, we sometimes make use of this feature when 
we want to make two symbols which connect to each other.  

F10REDRAW
F10REDRAW

We now have a nice clean space and a new symbol "FOO" to create.  We will put 
an IC outline, a bypass capacitor, and a couple of connection lines to make a 
bypassed IC symbol.  

First we get the IC14 symbol that we just looked at and locate it standing up 
at 0,0 where we can remember how it looks.  

We notice that we have the familiar line:

1LINE   2PAD   3SYMBOL   4LABEL   5OTHER

At the bottom of the screen.  When we are in the mode where we can add 
material to a symbol, we get this line just before we can back out of a 
symbol.  Again, if you get lost in the command tree you can always hit F9 
until you get the "enter y to exit symbol" message.  Then hit anything but a y 
and you will know where you are.  We are working on our new symbol "FOO" which 
is at present blank.  We want to add a symbol to it so we select symbol. 

3SYMBOL

We will have to tell the program what symbol we want to enter in our symbol.  
We also need to tell it how we want it oriented.  

F2NAME

We need to name a symbol.  We are asked to enter a symbol name.

IC14  (ENTER)

We notice the second line now reads "enter symbol IC14" to show that we have 
selected a symbol which can be entered into our new symbol FOO.  We could do 
some other things, like rotate our symbol.  For now we will try entering this 
symbol into the new symbol FOO. 

1LOCSYM

We now notice that the bottom line reads:

1FIND   2DELETE   3*MODFY  4SETUP   5REJECT

Whenever we are in a position to enter data, this line appears.  We also 
notice a 7, a triangle pointing to the right, and a happy face in the upper 
left hand corner of the screen.  The 7 is our level in the key tree.  The 
right pointing triangle indicates that the locate key is enabled to locate 
something, and the happy face indicates that we are locating work in a symbol. 

We will locate the library symbol IC14 in our new symbol FOO.  

F7LOCATE       

And the IC14 outline appears.  Depending on where the cursor was placed when 
the symbol origin was located, the outline may be partially off the screen.  
Do not worry, it is not located where we want it anyway. 

F1FIND

We need to find the object just entered to delete it.  With the advanced 
version objects can be moved and copied.  It is enough to do work to "find", 
"delete" and re "locate" objects.  The advanced version is just more 
convenient.  

The information line reads "symbol IC14 found @ above x,y".  The position x,y 
reads 0,0 which is where we just put the symbol so we have found the right 
one.  Later when you have a big job and don't remember where everything is, 
entered objects can be found by positioning the cursor near where the object 
is and noting if the right one is found.  If the wrong object is found, 
hitting the F5REJECT key will cause the search to continue until the desired 
object is found.  Note that sometimes there will be several objects located at 
the same position.  

This is the only object on the screen and it is in the wrong place so:

F2DELETE

And the IC14 symbol disappears.  Actually it is redrawn in background.  This 
means that if several objects were drawn on top of each other then part of 
some of the overlap might disappear.  Two F10REDRAW key hits will always 
redraw what is there.  At the moment our symbol FOO is empty so there is 
nothing to redraw.  

We want to draw our symbol standing up, so we need to get back to the menu 
which allows this. 

F9BACK

Now for our instructional purposes, we want to draw the IC symbol standing up 
with the notch at the top.   The 5ROT=  key allows the symbol to be entered 
rotated in 90 degree increments, starting from how it was created.  Since the 
notch was to the left in the symbol as it is stored, we want to rotate is 3 
steps of 90 degree counterclockwise.  Why counterclockwise?  I hear you ask.  
That is the way mathematicians think of angles.  It could have been done 
either way, but we followed normal math conventions.  

F5ROT=0
F5ROT=1
F5ROT=2

After pushing the F5 key the third time it ends up reading F5ROT=3 which is 
where we want it.  It is also necessary at this point to rename the symbol we 
want to enter.  Sorry, but a peculiarity of this system is that the current 
symbol name is canceled when a delete operation is performed.  We thought we 
had a good reason at the time, but now the logic is so imbeded that it would 
take a major rewrite (which is in progress) to change it.  

F2NAME

Answer IC14 

F1LOCSYM

We are now ready to locate the symbol.  Move the cursor to x=0.0, y=+0.6.  Why 
this location?   Because I am designing this symbol.  You get to design your 
symbols the way you want to.  I have thought out in my mind how I want it to 
look.   I am going to make an IC symbol with a bypass cap at the top and pin 7 
at the lower left hand corner, which will be at zero, zero.  At least the way 
I did it this location is off the screen.  Many systems do not let you locate 
items off the screen.  We often do.  It sometimes saves trying to reposition 
the work on the screen at just the right scale.  We now locate the IC outline. 

F7LOCATE

Part of the IC outline appears.   The rest is off the screen.  No matter.  
Move the cursor to 0,0 which should be the lower left hand pin or pin 7.  This 
is a mess.  We would like our work nicely centered on the screen.   We will 
now create a work area of a scale we like.  The 4SETUP key gets us to menus 
which allow changing all sorts of things about the screen setup.  

F4SETUP
F5SCREN         To work on the screen appearance.
F4REGION        To change the region of the screen we look at.
F3AUTO          To do it in automatic mode.

We have not done things in the right order but purposefully so to instruct 
you.  We are asked for a screen width in inches.  We will enter 2 

2 (ENTER)

The screen redraws.  We briefly see part of one of the pads drawn at the 
screen top before it is overwritten with the status lines.  The screen is now 
blank.  I guess we didn't do it right.  The way auto works, is to draw the 
screen at the entered width with the present cursor position at the upper left 
of the new screen.  We will try again.  We first move the cursor to x=-0.5, 
y=1.2.  Again, I am doing it the way I want to.  You might pick a different 
position for your work space.   

F3AUTO

1.8  (ENTER)

This puts things where I want them.  We might like to remember this location 
so we do not have to fuss the next time we work on this symbol.  We will use 
the memory feature of the redraw command to store this redraw area.  

F10REDRAW

We notice that some of the areas have names, and some are blank.  We could use 
any of them but we will use the up key to select 7 which is presently blank. 

F1UP 6

We note the key label changes to 1UP 7 so we are now selecting the space we 
want.  

F5CHANGE

This will store the present screen view in location 7.  We are asked to enter 
a label for this setup.  Enter anything that is descriptive to you that will 
fit on the screen.  We enter "Nice view of symbol FOO".  We notice that this 
label appears opposite the number 7.  To show how this works, we will redraw 
the screen using one of the old setups.  Use the 2DWN key to get to setup 5. 

F2DWN 7
F2DWN 6

And the key label reads 2DWN 5 to show that we are now pointing at the stored 
view 5.  We select this view by the select key. 

F3SELECT

The screen redraws with the indicated area of 22 by 17 inches.  This is much 
too large to do any work.  We can barely see our IC outline.  So let us go 
back to our stored view.  

F10REDRAW

This gets the list of redraw areas.  We again use the UP DOWN keys to pick the 
area we just made. 

F1UP 5
F1UP 6

And the key now reads F1UP 7 to show that we are pointing to the nice view of 
our symbol.  So we redraw this view.  

F3SELECT

And we are back to the "nice view".  In general this is the way this system is 
designed to move around the work area.  Use the AUTO feature when you want to 
generate a new work view.  Save it as above when you know that you will want 
to come back to it.  

Now we will add to our symbol.  It would be nice to have a bypass capacitor.  

F9BACK
F9BACK
F9BACK
F9BACK

Gets us to the menu that lets us select a symbol name.  We know the menus are 
a little hard to get around at first.  By the time you do a little real work 
you will find that you are moving around the keys with little effort.  If you 
think this system is hard to learn, try one of the big expensive systems where 
similar moves around the system are done with UNIX macro strings.  NO hope to 
learn without going to a school for a long time.  

F2NAME

C (ENTER)

We note that rotation is still at three which is a 270 degree rotation.  
Since this is not where we want it we rotate it one more time.  

5ROT=3

And note that it changes to 5ROT=0

In general, special conditions like rotate are reset to a standard initial 
mode when we leave an operation.  This has advantages and disadvantages.  
Sometimes the system does not remember the current symbol, rotation, etc. when 
we would like it to.  Sometimes it remembers an old condition when we would 
rather it would reset.  We will fix all thin in version 3.  But for now, and 
the free version probably forever, you will have to put up with strange 
behavior.  So if you go to enter a symbol and nothing happens, go back and 
rename the symbol.  We will now enter a bypass capacitor.  

F1LOCSYM

And we see that we have the standard data entry menu.   We move the cursor to 
x=0.050, y=0.8.  To do this we have to change the cursor movement speed.  It 
was moving 0.1 inch per step.  Since we want to move to a .050 step we need to 
change the movement.  

F6SPEED
F6SPEED
F6SPEED
F6SPEED
F6SPEED
F6SPEED

If we have both counted right, the entry ahead of the % sign on the top line 
now reads M  50 to show we are now moving in 50 mil steps.  Use the F6 key to 
go around again if you miss it the first time.  The smallest number in this 
sequence is set by the GRID key.  It can be set at any number.  The SPEED key 
then works on a 1,2,4,5,10,20 multiple of the grid.  The grid is presently set 
at 25 mils.  

Now that we are at the desired location we locate a capacitor.

F7LOCATE

And the capacitor symbol appears where we want it.  It happens to have been 
created lying horizontally so we do not need to rotate it.  

We will now connect the capacitor between pins 7 and 14 with wires on level 1 
and level 2.  Looking at our chart we see that setup 8 will enter 20 mil wires 
on level 1.  We change the setup to 8. 

4SETUP
1EDSET
1 UP  pushed 8 times gets us to setup 8 as shown on the second screen line.

F9BACK pushed 4 times gets us to the line, pad, symbol, label, other menu.

We want to enter lines so we pick:

1LINE         To enter lines.
1LOCLINE      To distinguish from entering points in existing lines

And we now have the familiar find, delete, modfy, setup, reject menu that 
tells us we can enter data.  

Move the cursor to the right end of the capacitor, x=.250, y=.8.  Hit locate
to start a line.  

F7LOCATE

A tick sound is heard to indicate a line has been started.  Now move to 
x=.3, y=.8 and locate an intermediate line point.

F7LOCATE

A green 20 mil line segment appears between the starting point and the current 
cursor position.  Now move to the IC pin 14 x=.3,y=.6 and end the line.  

F8END

A lower pitch sound distinguishes a line end from a line start.  We now have a 
line connecting the right end of the capacitor to the IC pin 14.  For fun, we 
will put the next wire on the other side.  We notice that setup 9 is setup for 
20 mil lines on level 2.  So we select setup 2.  Notice that if none of the 
setups had the line width and level combination that we want, we can edit any 
one of the setups for the desired combination.  We generally try to pre edit 
the setups so we have available the ones we usually want.  We save one, 
usually setup 0, for use when we want something special.  See documentation 
elsewhere for the edit procedure, or just muck around till you figure out how 
to do it.  

F4SETUP
F1EDSET
F1 UP

And we now have setup 9.

F9BACK  twice and we are back at the data entry menu.

Move the cursor to the left end of the capacitor.  x=.05, y=.8 and start a 
line.  

F7LOCATE

Again a tick is heard.  Move to x=.1, y=.8 and locate an intermediate point.  

F7LOCATE

A tick is heard and a red line appears indicating a line on level 2.  Now move 
to x=.1, y=0.0 and place another line segment.

F7LOCATE

Finally move to x=0, y=0 and end the line.  

F8END

A lower pitch sound again indicates a line end.  

This does not seem like a very complicated object but it illustrates most of 
the concepts needed to make very complex boards.  Back out of the symbol now 
by hitting F9 three times and answering y. 

F9BACK three times, y (ENTER)

The system says "symbol closed".  We can now use this symbol.  But first we 
will open it to see what we have made.  Note we created it with "new" but now 
that it is an existing symbol we have to open it. 

F5OPEN

FOO (ENTER) to the question.

Notice that it is now drawn in a scale that fits it to the available screen 
space as best the system can.  Use the redraw command and select "nice view" 
to observe that the system picked its own view of this symbol.  Now use F9 to 
back out of the symbol and answer y to close it.  You now have your very own 
original symbol.   Let us make something even more complicated.  

F1NEW
GOO (ENTER) to create the new symbol goo.
F3ORIGIN  at some convenient place.  

While the new GOO symbol space is empty, our old symbol is still visible.  We 
sometimes make use of this when we want to make two symbols that have to fit 
together.  For now we will clean up the space by hitting F10 twice to redraw 
the clear area.  The cursor is now sitting at 0,0. 

F10REDRAW
F10REDRAW

We will put several copies of the FOO symbol in the GOO symbol.  Suppose, for 
example, that the FOO symbol were all the lines necessary for a memory chip, 
as we indicated in the TUTOR exercise.  We could now make a multi chip memory 
section.  We will put down three of the FOO symbols since that is enough to 
illustrate the idea. 

F3SYMBOL
F2NAME       FOO (ENTER)
F1LOCSYM
F7LOCATE

The FOO symbol appears at 0,0.  Move to 0.5,0 and locate a second copy.

F7LOCATE

Again a third copy at 1.0, 0

F7LOCATE

This is enough for illustration.  Close the symbol by backing out with F9's 
and a y.

Now get a large working space.  

F10REDRAW
F2DWN    six times untli it reads 1
F3SELECT  to select the 10 by 8 inch work space

With this system, you can work with symbols until you have completed your 
task.  For output purposes, the work must be put on something called the 
"job".  The difference between a symbol and the job is that while a symbol can 
be moved, saved and deleted as a unit, the job is a special part of the work 
area which is used for the generation of output files.  The next version of 
this program will allow everything to be done from a symbol which will remove 
one level of confusion.  We just did not think to do it this way at first and 
it is now too hard to change without a complete rewrite.  

We will treat the symbol GOO like it is our complete task.  We will first 
locate it on the job area.  Then we will make a check plot of it and prepare 
files for photoplotting.  First use F9 to back out to the line, pad, symbol, 
label, other menu.  Note that when we do this we are at key tree level 2 as 
shown by the upper left hand corner screen number.  We are no longer working 
in a symbol, work we do now goes in the job.  Move the cursor to 0,0.  Select 
line.  We will first draw a line around the work area so that we can see where 
to put our work.   

F9BACK
F9BACK
F1LINE         To go to enter lines
F1LOCLIN       To locate a line
F4SETUP        We will make this line a different width for practice.
F1EDSET        To pick a different setup.

We note that setup 15 draws a line on four levels at once.  This will 
conveniently put a border on all the layers.  F1 UP six times gets us to setup 
15. 

F1 UP          Six times
F9BACK         Twice gets us to the find, delete, ... menu.

We are still at a move speed of 50 mils.  5 F6SPEED will get us to 1 inch 
moves.  We are already at 0,0.  Let us move to 1,1 and draw a border 1 inch 
inside a possible 10 by 8 inch piece of film.  

Move to x=1, y=1

F7LOCATE

A tick is heard indicating that a line has been started.  Move to x=1, y=7.

F7LOCATE

A tick is heard and a line appears between 1,1 and 1,7.  Continue the border.
Move to x=9, y=7.

F7LOCATE

Move to x=9, y=1

F7LOCATE

Move back to x=1, y=1

F8END

And the border is complete.  

F9BACK      twice to get to the menu which allows symbol selection.

F3SYMBOL    to select symbol entry

F2NAME      to choose a symbol

GOO (ENTER) to pick the symbol we made to simulate a real piece of work.

F1LOCSYM    to locate the selected symbol on the job.

Now we move to x=4, y=3 to locate the symbol GOO.

F7LOCATE    A tick sound is heard and the three chip outlines are drawn.  

We now have a job with some stuff on it.  It is not much, but does illustrate 
how a job might be made.  We can now make a check print to inspect our work.  
Three F9's will get us back to the very first menu where we can select the 
plot menu.  

F9BACK  three times.
F3PLOT  to select the plot menu.

We will first make a plot on the Epson printer.  Since this can take a long 
time, we will select only the part of the layout where there is something of 
interest.  This is the area of the three chips.  First use F6 to select .1 
inch steps so we can accurately bracket the area of interest.  Then move to 
x=3.8, y=4.1.  Now we select the Epson plot mode. 

F2ESPLOT

We are asked to place the cursor at the upper left hand corner and to hit F7.  

F7LOCATE

We are immediately asked to locate the lower right hand corner of the area to 
be plotted.  We move to x=5.5, y=2.8 and:

F7LOCATE

We are now asked for a scale factor.  Entry of 1 would print the design at 
labeled scale.  It would be hard to see the detail.  We pick 2 to get a 2 to 
one plot.  The part of the drawing selected is printed to a new scale on the 
screen and the printer and the printer starts (slowly) printing the screen.  
It there is no printer, or if the printer is not compatible with Epson 
graphics mode 5 there will be a nasty error message but no work will be lost.  
When the print out is complete we notice that the various levels are printed 
out on top of each other.  We can't tell which level is which.  To get 
separate levels, we need to select a setup which prints only one level at a 
time.  We note that Setup 1 is prepared to print only level 1, the parts side 
while Setup 2 is arranged to print only level 2, the wire side.  Setup 3 has 
been arranged to print level 3, the drill spots, and level 4 the parts 
outlines together.  This makes a useful combination.  Repeat the check print 
process with each of the setups selected to get a working set.  

The last thing we will do for this exercise is to make a set of plot files and 
save the work.

We should still be in the plot menu.  

F3PLTFIL

The system asks for a plot file name.  Our convention is that we name the 
files ending in 1,2,3,... to indicate the level we are plotting.  The normal 
procedure for a two sided plated through hole board would be to make 5 plots.  
They are: 

Level 1, the parts side.
Level 2, the wire or solder side.
Level 3, the drill spots.
Level 4, the parts outline, used for a silk screen and parts location.
Level 5, the solder mask.  

We answer

GOO1 (ENTER)

We are asked for a level - we answer

1 (ENTER)

We are asked for the plotter steps per inch.  For 1 to 1 scale on most 
plotters enter 1000.  Here is your chance to change the scale.  If your 
plotter makes 400 steps per inch as do some low cost pen plotters you would 
answer 400.  If you happen to know that your plotter has a scale factor error, 
then a correction could be made here.  We will assume you are sending work to 
us and enter 1000. 

1000 (ENTER)

Now we are asked for offsets in x and y.  You could enter values here in 
thousandths of an inch if you know that you want to relocate the drawing on 
the plotting table.  For example, by giving each plot level a different offset 
you can arrange to have all the levels plotted on a single piece of film.  
Before these last entries are made be sure you have enough room on the default 
disk to hold the plot files.  If in doubt, a fresh formatted disk is in order.  
The system can die a horrible death if it cannot find enough room.  Some 
versions of DOS die in a way that does not let you recover.  Best to be sure 
you have enough room.  

0 (ENTER)
0 (ENTER)

The disk whirrs and a file is created.  Later you will see that it is named 
FOO1.PLT.  Repeat the above process naming the files FOO2 for level 2, FOO3 
for level 3 etc.. 

Finally F9BACK get the menu with 2FILE.

F9BACK
F2FILE
F1PUTFIL
F1SAVJOB

And we are asked for a file name.  We will call this effort GOO.

GOO (ENTER)

The system advises us that it did not remember loading this job.  We are given 
a chance to change our mind.  Entering anything but c will cause the present 
work to be saved.  If we later reload this job we will be back where we are 
now.  Any symbol sets loaded are saved with this job.  Remember we loaded the 
library ELEC.  We will not have to reload it when we restart this job as it 
will be saved as a part of this job.  

(ENTER)

The disk whirrs and the job is saved.  Again, be sure there is room on the 
disk.  Late versions of DOS give you another chance on a full disk.  Earlier 
versions did sometimes.  

Now that the work is saved, three F9BACK will get the question "are you sure" 
We are, and enter y to quit.  

An examination of the disk directory should show 7 new files.  There will be 
five files with names like GOO1.PLT, GOO2.PLT,... These are the plot files.  
Send them and money to us if you want photoplots.  There will be a pair of 
files GOO.PCD, and GOO.PCS which are the files that save your work.  The PCD 
file save all the working conditions, like the redraw areas you have named.  
The PCS file contains all the data you have entered.  

It has taken a lot of words to describe this very simple operation.  But that 
is the way words work.  Most of you will get tired and quit following the step 
by step operations as you pick up on the general idea of this system.  The 
detail is here to help those that are lost .