PROD.DOC

ENVIRONMENTAL OPTICS OFFERS A COMPLETE LOW COST CAD LINE FOR PRINTED CIRCUIT 
LAYOUT.  USE OUR FREE SOFTWARE TO TRY THE SYSTEM, WE WILL PHOTOPLOT YOUR 
DESIGN FOR A NOMINAL CHARGE.  USE THE PROFESSIONAL LEVEL SOFTWARE TO PREPARE 
SOPHISTICATED DESIGNS.  BUY THE COMPLETE SYSTEM, AND GET EVERYTHING NEEDED TO 
PREPARE PRECISION PHOTOTOOLING IN 3' OF LABORATORY BENCH SPACE.  



THE COMPLETE SYSTEM                                             $12,950

Everything needed to prepare precision photooling in 34 1/2" of bench space.  
Includes a 80286 based computer with high resolution color display and a hard 
disk.  The vector photoplotter produces high quality, high precision film and 
is more accurate at 1 to 1 than most pen plotters at 4 to one.  

System Includes:

Environmental Optics Mark VI Photoplotter
        Plots up to 17 1/4" by 23" with a single aperture or 16 1/2" by 22 1/4"
        with all apertures
        Holds film to 20" by 24"
        Size 34 1/2" by 25" by 10"
        No external power required, powered from computer.
        Plotting type, vector.
        Plotting speed, 2"/second, axially.
        Accuracy after shipping and calibration, 0.002" rms.
        16 Apertures range from 0.006" to 0.125", mix of round and square.
        Uses standard low cost litho film, or rapid access line film.
        Light tight box allows operation in lighted room, darkened only for 
        loading film.  Or operate in full daylight with optional film bag.

Computer, 8 MHz 80286 based, similar to IBM AT.
        1.2 MB Floppy Disk
        20 MB Hard Disk
        1 MB Memory
        Printer
        EGA Monitor and adapter
        Keyboard

Software
        DROEGE Manual layout software V 2.175.
        Plotter driver.
        Utility software.
        DOS


PHOTOPLOTTER                                                     $9,950.00

A stand alone photoplotter system to prepare photooling from floppy disks.

System Includes:

Environmental Optics Mark VI Photoplotter
        Specifications as above.
Computer, 8088 based, similar to IBM XT.
        360 KB Floppy Disk
        512 KB Memory
        Mono monitor and adapter. 
Software
        Plotter Driver
        Utility Software
        DOS

ENTRY LEVEL SOFTWARE        DROEGE VERSION 1.85           "FREE" OR $10.00

This is a manual printed circuit system.  It is just like using a layout grid 
and prepared stick-ons.  The advantage of this program is that you don't have 
to take a 2 week training course to learn to use it.  We find most computer 
wise electronic techs just start using it with little reference to the manual.  
Because the program does not do auto-routing, auto-placement, schematic 
capture, simulation, and all the other "wonderful" things available today; it 
doesn't need to know much about the components.  If you are doing high 
frequency work, or simple jobs, or anything else that your fancy CAD designer 
did not prepare for, then the automatic systems are much slower, harder to 
use, and make you do a lot of things that you don't really care to do.  This 
program has powerful symbol manipulation features that we find to be missing 
on programs which cost tens of thousands of dollars.  

This program can be obtained "free" from many bulletin boards.  We will send a 
copy post paid for a $10.00 mailing and duplication fee.  It is also available 
from PC-SIG as their disk numbers 904 and 905.


Features:

1) Multi-color multi-layer display.

2) Maximum layout size 64" x 64" to 0.001" precision.

3) User definable grid of any size from 0.001" to full size.

4) Runs on IBM PC, XT, AT, and anything else that is compatible - we think 
this means anything that will run Microsoft compiled Basic and Assembly code.  
Requires about 400k memory, CGA and adapter, optional Epson compatible 
printer. 

5) Features 12 layers, 15 line widths, entry and deletion of lines, pads, 
symbols, labels, and arcs.  

6) Very powerful symbol concept retains features of groups when nested to many 
levels.  The symbols are stored as master templates so an edit will update all 
the places it is used.  This greatly conserves storage space and is a feature 
found on only the most expensive systems (if at all). 

An item like an IC pad can be made into a first level symbol, then several can 
be grouped for a second level chip layout.  Buss lines added form a third 
level memory chip symbol.  A fourth level would allow a whole memory layout to 
be manipulated with a single edit.  Then a single edit to the basic pad symbol 
would allow changing from round to square pads to suit a vendor preference.  
This concept allows an unlimited number of custom layout patterns to be 
created with very efficient use of storage space. 

7) Symbols can be placed rotated in 90 degree steps, and will rotate in 
rotated symbols to level 20. 

8) Output of design data to any scale on Epson or compatible printers that 
support graphics mode 5 (72 by 72 dots per inch) for check plots. 

9) Easy to learn hierarchical menu structure puts commands within a few 
keystrokes and leaves most of the screen available for work.  Typical users 
never read the approximately 60 pages of documentation on disk. 

10) Zoom and pan to any part of the work area, to any scale from 0.001" per 
screen line to screen display of the full work space.  Fifteen screen views 
can be stored to allow fast switching between work areas. 

11) Stitch function allows moving between any four of the twelve available 
board layers with automatic insertion of vias which can be any user designed 
symbol. 

12) Sixteen user prepared setups allow quick change between layer and aperture 
assignments. 

13) Efficient editing technique quickly finds desired class of item from 
starting screen search point.  Found items are identified i.e. "Red 20 mil 
line on level 5 starting at x= 4.125, y=7.625".  This allows identifying a 
desired item for edit when many items overlap.  

14) Variable size type font for lettering.  Lettering can be drawn with any of 
the available apertures.

15) Complete job parameters are saved to disk so that the exact working space 
is restored when work is resumed.  

16) Summary feature allows counting the total number of symbols, their type and 
symbol level used to provide a parts count.

17) Defined output format matches Environmental Optics Photoplotter, and can be 
easily translated for most plotters.  One sample driver for a pen plotter is 
included. 

                                                                   
PROFESSIONAL LEVEL SOFTWARE   DROEGE VERSION 2.175 (pp Airmail)    $100.00

This version contains all the features listed above plus the following: 

A) Uses available memory up to the 640K DOS limit.  Effectively  10 times 
the available job size as the "freeware" version after loading the usual 
symbol library.  We have designed 16" by 12" boards with over 1000 components 
using less than half the storage space.  About 20,000 items can be handled 
with a 640K DOS machine.  A single line point uses an "item".  Use of a 1000 
component symbol also used one "item".  A scrambled logic board might run out 
of space at 100 chips or so.  A huge multi-layer memory board could be made 
with very little space if layers of symbols are used.  

B) Supports the EGA with a resolution of 640 by 350 lines.  Fifteen colors can 
be assigned to any of the twelve layers. 

C) Setup program allows allocation of memory for best utilization of 
resources. 

D) Powerful editing commands not included in the "freeware" version allow 
move, copy, change, and insert. 

E) Setups can be viewed on the screen without a redraw.  

F) Supports a Microsoft compatible mouse.  

G) Supports line (not drawn at width) drawings on the HP Draftpro.

H) Many small features, like PATH, are supported in this version which have 
not been implemented in the "freeware" version.  There are also additional bug 
fixes.  

I) Defined output format matches Environmental Optics Photoplotter.  Easy to 
translate to other formats, three sample formats provided, including one to 
HPGL. 

J) Indexed manual of about 130 pages.  Tutorial sections with example jobs 
demonstrate most features.  A number of sample jobs are provided.


DROEGE printed circuit design program Version 3.0  (under preparation)

This program now uses floating point arithmetic so there is no longer any 
limit to the size of the drawing.  Well, to be more precise you are limited to 
the known size of the universe after another 100 Billion years of expansion.  
Actually you are limited to about a half mile square to 0.001" precision.  
With this version a math co-processor will be helpful.  

This version does away with the concept of a job.  Everything is a symbol.  
This makes the key structure much easier to learn.  We now do everything the 
right way mathematically so mirror, rotate, and scale work to any level.  This 
will allow a flip redraw mode to make surface mount jobs easier.  Many small 
requested improvements are being added.  This version allows rotation to 
arbitrary angles.  Great for those of you laying out boards which must go in 
round missiles.  Key labels and error messages can be changed by the user 
which makes foreign language versions easy.


PHOTOPLOTTING SERVICE         (Minimum Charge)                      $25.00

Print PRICE.DOC for a price schedule.  A typical 5 film plot set for an IBM PC 
sized board would run a little over $100.    


SPECIAL SOFTWARE

We will attempt any plot file conversion for a nominal or exorbitant charge, 
it depends on how much we want to do it.  We have started conversions programs 
for most popular systems.  So it may not be too bad.  Write with details of 
your plot format.