5

AMS Models

The AMS simulates manned lunar exploration.  Included are one pilot (the
player), eight astronauts, an Orbiting Laboratory (OL), a reusable Landing
Vehicle (LV), a Manned Maneuvering Unit (UN), a Permanent Lunar Habitat (HB), a
Mobile Base (MB), a small Roving Vehicle (RV), and a Portable Life Support
System (PL or PLSS).  Many AMS models and development notes are presented in
this document.  Topics include:

The Moon
Pilot and Astronauts
Power Subsystems
Environmental Subsystems
Damage and Repair
Orbiting Laboratory
Landing Vehicle
Manned Maneuvering Unit
Permanent Lunar Habitat
Mobile Base
Roving Vehicle
Portable Life Support System

The Moon

The moon is modeled as a perfect sphere with a	90ø NORTH
radius of 1738.3km.  The gravitational field    ...............		ÚÄÄÄÄ¿
is a simple inverse square law with a	  ...:	s |	  :...	 ³MOON³
surface acceleration of 1.624m/sý.	   .:	    u |		 :.    ÀÄÄÄÄÙ
Global reference points are the equator .:		 b |		   :.
(0ø latitude) and the subearth	    :		   e |			:
meridian (0ø longitude).  The lunar   :		    a |			 :
solar rotation period is 29.53 days. :			r |			  :
							 :			 t |			   :
The lunar surface has constant	 :			 h |	   equator   :
altitude but is covered with    -90ø:------------------+- 0ø -------------: 90ø
rocks, craters, hills,		WEST:			 m |			   :EAST
mountains, valleys, and rilles.	:			 e 0ø			  :
Actual lunar features larger than    :			r |			  :
about 1ø (30km) are included in the   :		    i |			 :
AMS map between ñ32ø latitude and ñ80ø :		   d |			:
longitude.  Smaller features are	   :.		 i |		   .:    view
derived using a two-step pseudorandom	:.	    a |		 .:	 from
process that generates features as small as :...	n |	  ...:	  EARTH
7.5x15m.  Mountains cover both poles and the    :.............:
antimeridian (ñ180ø longitude).			    -90ø SOUTH

Moon (continued)

Lunar surface features are listed below in increasing order of ruggedness.
Manmade objects, visible only on 4096:1 maps, are assigned other symbols listed
here and in LUNARMAP.DOC.  The dark side of the moon is indicated by a field of
"²" symbols.

SYMBOL  RUGGEDNESS  MEANING				 SYMBOL  MEANING
------  ----------  ------------------------    ------  -----------------------
  " "	  1.0	featureless			    Ž	Landing Vehicle
   ù	   1.1	relatively smooth, rocky	 é	Mobile Base
   ø	   1.3	small, subdued crater	    è	Roving Vehicle
   +	   1.4	moderate, rocky				pilot
   ÷	   1.7	rolling hills			  �	Apollo descent stage
   o	   2.0	medium crater			  ä	Surveyor
   *	   2.5	rugged, rocky			  œ	Luna
   O	   3.3	large crater			   Û	Permanent Lunar Habitat
   ï	   4.0	mountain				  ×	solar array
   U	   5.0	valley				    ê	warning light
   \	   6.7	rille
   /	  10.0	rille
   #	  20.0	major rille

Pilot and Astronauts

The pilot and eight astronauts each have a mass of 80kg.  Three astronauts are
assigned to the OL, three to the HB, and two travel with the pilot.  While the
astronauts are not explicitly included in the simulation, the physiology of the
pilot is modeled.

Injury:  Pilot injury may occur during landing, docking, or EVA, or due to
mechanical failure or lack of oxygen.  Injuries heal slowly with time and
affect pilot efficiency.  The pilot is dead when his injuries exceed 100%.

Sleep:  The pilot requires about 8hr of sleep per day, normally between about
UT 22:00 and UT 06:00.  Lack of sleep affects pilot efficiency.

Rest:  The pilot requires two or three 2hr rest periods per day, during which
he also eats his meals.  Pilot efficiency is substantially restored during
these rest/meal periods.  One rest should be taken after waking up and another
before sleeping.

Consumables:  Each astronaut, including the pilot, requires about 0.8kg of
oxygen and 1.8kg of water per day.  A lack of oxygen very quickly leads to
injury.  A lack of water decreases efficiency.

Pilot and Astronauts (continued)

Metabolic Rate:  The pilot's metabolic rate is a measure of his current level
of activity.  Some activities are very strenuous, e.g., sample collection, and
result in higher metabolic rates than those activities that are less strenuous,
such as resting.  High metabolic rates reduce pilot efficiency.  Avoid
metabolic rates greater than the pilot efficiency.

Efficiency:  Pilot efficiency is a measure of his overall condition.  It
determines the maximum effort (metabolic rate) that he can sustain without
problems.  Efficiency depends on injury, sleep, rest, consumables, and time-of-
day.  Generally, efficiency increases in the morning and early afternoon (UT
03:00 to UT 15:00) and decreases from late afternoon to late night (UT 15:00 to
UT 03:00).  The pilot is also somewhat less efficient while he is wearing a
PLSS.

Power Subsystems

The power subsystems of the OL, LV, HB,	ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
and MB contain solar arrays, batteries,							   ³
fuel cells and hydrogen, oxygen, and  ÉÍÍÍÍÍÏÍÍÍÍ»   ÉÍÍÍÍÍÍÍÍÍ»		    ³
water supplies.  The solar arrays	º Hydrogen ÇÄÄ¶	    º  ÉÍÍÍÍÍÍÍÍÍ» ³
provide electrical power when	    ÈÍÍÍÍÍÍÍÍÍÍ¼   º  Fuel   º  º	    ÇÄÙ
illuminated.  (400W/mý at 30%				    º	    ÇÄ¶  Water  º
efficiency).  Surplus power is used   ÉÍÍÍÍÍÍÍÍÍÍ»   º  Cells  º  º	    ÇÄ¿
to recharge the battery (at 50%	  º  Oxygen  ÇÄÄ¶	    º  ÈÍÍÍÍÑÍÍÍÍ¼ ³
efficiency) or to disassociate	   ÈÍÍÍÍÍÑÍÍÍÍ¼   ÈÍÍÍÍÑÍÍÍÍ¼	  -	 ³
excess water into hydrogen and		    -		   		  ³	 ³
oxygen (1g water/29kJ at 45% efficiency).   ³	   ÉÍÍÍÍÏÍÍÍÍ»  ÉÍÍÍÍÏÍÍÍÍ» ³
Fuel cells supply power and water		 ³	   º	    º  º  Solar  º ³
(3.6kJ/1g water at 25% efficiency) when	³	   º Battery ÇÄ¶	    º ³
necessary to maintain adequate battery	 ³	   º	    º  º  Cells  º ³
charge.							  ³	   ÈÍÍÍÍÍÍÍÍÍ¼  ÈÍÍÍÍÍÍÍÍÍ¼ ³
								    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
The power subsystems of the UN, RV, and PLSS	 ÉÍÍÍÍÍÍÍÍÍÍÍ»  ÉÍÍÍÍÍÍÍÍÍÍÍÍ»
contain batteries that are recharged along with   º		 º  º Recharging º
other consumables (UN nitrogen and PLSS oxygen    º Batteries ÇÄ¶		  º
and water) when the device is stored onboard the  º		 º  º   System   º
OL, LV, HB, or MB.						  ÈÍÍÍÍÍÍÍÍÍÍÍ¼  ÈÍÍÍÍÍÍÍÍÍÍÍÍ¼

Environmental Subsystems

Atmospheric Composition and Density:  The OL, LV, HB, and MB atmospheres are
4:1 mixtures of nitrogen and oxygen at a pressure of one atmosphere or 100kPa.
Atmospheric density is about 1.2kg/m^3.  The PLSS uses a 2:1 nitrogen:oxygen
mixture at 50kPa so that oxygen prebreathing prior to EVA is unnecessary.

Leak Rates:  The leak rate for the OL and HB is normally 0.24l/min (5mg/s).
The normal leak rate for the LV and MB is 0.06l/min (1.25mg/s).  For the PLSS,
it is 0.05l/min (1mg/s).

Depressurization Losses:  Airlocks are used in the OL and HB but not in the LV
or MB.  The residual pressure after depressurization at the start of an EVA is
1.5kPa, leaving a nonrecoverable atmospheric density of 0.018kg/m^3.
Depressurization takes about 3min.

Reserve Supplies:  Atmospheric reserves are maintained in separate nitrogen and
oxygen tanks to replace losses due to normal leaks, cabin or airlock
evacuation, and astronaut usage.  An emergency supply, enough to completely
replace the standard atmosphere in the cabin, is also provided.

Damage and Repair

Damage:  Damage may occur during landing, docking, or movement on the lunar
surface.  Random breakdowns may also occur.  Battery damage increases the
discharge rate.  Damage to fuel cells or solar arrays decreases the amount of
power delivered.  Hydrogen, nitrogen, oxygen, RCS, vacuum, or water subsystem
damage increases the leak rate.  Mechanical structure damage increases the
atmospheric leak rate for pressurized systems and the likelihood of further
breakdowns.  Damage to navigation subsystems increases errors.  Drive subsystem
damage decreases the maximum speed.  Damage to the LV RCS or main engine
increases the likelihood of catastrophic failure.  Docking mechanism or landing
gear damage decreases the chance of successful docking or landing.

Repair:  The pilot may repair subsystems that are accessible to him.  Repairs
may take from less than 5min up to 2hr or more depending on the amount of
damage.  OL and HB damage may be repaired by onboard astronauts.

Orbiting Laboratory

The OL serves as the main transfer point for astronauts and equipment traveling
to and from the lunar surface.  It orbits the lunar			 LV DOCKING
equator at an altitude of 150km and consists of   ÉÑÑÑÑ» -SOUTHÚÄ¿ PORT  ÉÑÑÑÑ»
two cylindrical habitat modules (each 5m in	  ÇÅÅÅÅ¶ ³ ÚÄÄÄÁÄÁÄÄÄ¿   ÇÅÅÅÅ¶
diameter and 10m long), two 5x20m solar power	ÇÅÅÅÅ¶   ³:::::::::³   ÇÅÅÅÅ¶
panels, and supporting structure.  A docking port ÇÅÅÅÅ¶   ÀÂÄÂÄÄÄÂÄÂÙ   ÇÅÅÅÅ¶
for the LV is located on the south side.  OL	 ×ÅÅÅÅ×ðððððððððð³:³ðððð×ÅÅÅÅ×
subsystems include power, environmental,		ÇÅÅÅÅ¶   ÚÁÄÁÄÄÄÁÄÁ¿   ÇÅÅÅÅ¶
consumables, and docking radar.			    ÇÅÅÅÅ¶   ³:::::::::³   ÇÅÅÅÅ¶
										ÇÅÅÅÅ¶   ÀÄÄÄÂÄÂÄÄÄÙ   ÇÅÅÅÅ¶
Power:  Normal power consumption is 34.8kW	   ÈÏÏÏÏ¼	  ÀÄÙ	  ÈÏÏÏÏ¼
during work hours (UT 06:00 to 22:00) and 1kW during sleep	   view from SUN
periods.  The docking radar uses 1kW.  Average power usage is
normally 23.6kW but may be reduced to 1.7kW in emergencies.  The solar array
has an area of 200mý and provides up to 80kW of electrical power.  Fuel cells
deliver 27kW when required.  Battery capacity is 445MJ and can supply emergency
power for 72hr.  The water tank can hold 2920kg, fuel cell production for 72hr.
Hydrogen (324kg) and oxygen (2592kg) are available for fuel cell use.

Orbiting Laboratory (continued)

Environmental:  The inhabitable volume is 196m^3 and requires 235kg of air.
The airlock has a volume of 27m^3 and a depressurization loss of 0.5kg per use.
Reserves are maintained for 360 day leak replenishment (160kg), 100 airlock
uses (50kg), and emergencies (235kg) for a total reserve of 445kg (356kg
nitrogen and 89kg oxygen).

Consumables:  In addition to other supplies, the OL has the capacity to supply
one UN for 30 EVAs (750kg of nitrogen propellant) and the LV for six complete
lunar exploration missions.  Total capacities are hydrogen (11,298kg), oxygen
(69,211kg), nitrogen (1652kg), and RCS propellant (1920kg).

Docking Radar:  The docking radar provides an accurate measurement of the
relative position of the LV with respect to the OL and has a maximum useful
range of 30km.

Landing Vehicle

The LV is an advanced version of those    DOCKINGÉÍÍÍÍÍÍÍ»    -		  CREW
used during the early Apollo lunar		 PORTº³ú³ú³ú³º    ³  UP	 MODULE
exploration missions and is totally  ÉÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍ» 
reusable.  Major components	  ÚÄÁÄ¶úÉÍÍÍÍÍ» ú ³ú ú ú³ ú ÉÍÍÍÍÍ»úÇÄÁÄ¿ TRIAD
include the Crew Module and the  ´ O ºúº    º ú ³ú ú ú³ ú º    ºúº O Ã
Propulsion Module.  Subsystems    ÀÄÄÄ¶úÈÍÍÏÍÍ¼ ú ³ú ú ú³ ú ÈÍÍÏÍÍ¼úÇÄÄÄÙ  LEFT
include power, environmental,	    ºÄÄÄÄÄÄÂÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÂÄÄÄÄÄÄº	 ÄÄÄ
consumables, reaction control,    ÚÄÄÄ¶::::::³ú ú ÚÄÄÄÄÄ¿ EVA³::::::ÇÄÄÄ¿
and navigation.			   ´ O º::::::³ ú ú³ ÀÄÙ ³EXIT³::::::º O Ã
						    ÀÄÂÄ¶::::::³ú ú ÀÄÄÄÄÄÙ ú ú³::::::ÇÄÂÄÙ
Crew Module:  The Crew Module	  - ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹ -
ferries the pilot and astronauts to   º ú ú ú ú ú úÃÄÅÄ´ú ú ú ú ú ú º
the lunar surface and back to the OL, º ú ú ú ú ú úÃÄÅÄ´ú ú ú ú ú ú º
and serves as living quarters during /º ú ú ú ú ú úÃÄÅÄ´ú ú ú ú ú ú º\
missions that do not utilize the    /Åº ú ú ú ú ú úÃÄÅÄ´ú ú ú ú ú ú ºÅ\
MB.  It stands 3.2m tall, has a   /ÅÅÅº ú ú ú ú ú úÃÄÅÄ´ú ú ú ú ú ú ºÅÅÅ\
dry mass of 1611kg, and can	 /ÅÅÅÅ¶ ú ú ú ú ú úÃÄÅÄ´ú ú ú ú ú ú ºÅÅÅÅ\
carry up to 1200kg of lunar	/ÅÅÅÅÅ¶ ú ú ú ú ú úÃÄÅÄ´ú ú ú ú ú ú ºÅÅÅÅÅ\
samples.  A port is provided   /ÅÅÅ/  ÈÍÍÍÍÍÍÍÍÍÍÍÍØÍÏÍØÍÍÍÍÍÍÍÍÍÍÍÍ¼  \ÅÅÅ\
that allow the LV to dock	/ÅÅÅ/  LANDING	  ÃÄÄÄ´    PROPULSION  \ÅÅÅ\
with the OL.			 ÍÏÍÍÍÍÏÍ GEAR	   ÍÏÍÍÍÍÍÏÍ	 MODULE ÍÏÍÍÍÍÏÍ

Landing Vehicle (continued)

Propulsion Module:  The Propulsion Module carries the bulk of supplies required
to perform a lunar exploration mission.  It is 3.8m tall, has a dry mass of
1968kg, and has four legs to cushion landing and to provide support on the
lunar surface.  The main engine burns a 6:1 mixture of liquid oxygen and liquid
hydrogen and can be throttled between 10% and 100% of its rated thrust of
82,240nt.  At full throttle, it uses propellant at 18.9kg/s (16.2kg/s oxygen
and 2.7kg/s hydrogen).  Total propellant capacity is 1809kg hydrogen and
10,854kg oxygen.

Power:  Normal LV power consumption is 1.3kW with three astronauts present and
130W when there are none.  The OL and DSN transponders require 130W each.  The
main engine and landing radar each consume 1kW.  The solar array has an area of
4mý and provides up to 800W of electric power.  Fuel cells deliver 2.7kW when
required.  Battery capacity is 78MJ and can supply emergency power for 168hr.
The water tank can hold 180kg, fuel cell output for 15 days.  Hydrogen (20kg)
and oxygen (160kg) are available for fuel cell use.

Landing Vehicle (continued)

Environmental:  The LV inhabitable volume is 10m^3 and requires 12kg of air.
The depressurization loss is 0.18kg.  Reserves are maintained for 30 day leak
replenishment (4kg), 20 cabin evacuations (4kg), and emergencies (12kg) for a
total reserve of 20kg (16kg nitrogen and 4kg oxygen).  An additional 30 day
supply of oxygen for three astronauts (72kg) is also provided.

Consumables:  In addition to other supplies, the LV carries enough nitrogen to
charge the UN for three EVAs (75kg).  Total consumable capacities are hydrogen
(1829kg), oxygen (11,090kg), and nitrogen (91kg).  The LV can carry up to
1200kg of lunar samples.

Reaction Control:  The RCS consists of eight modules of three thrusters each
(triads) and is used to orient the LV and provide small changes in velocity.
PITCH, ROLL, and YAW commands cause short bursts that change the spin by 1ø/s.
FORWARD/BACK, LEFT/RIGHT, and UP/DOWN commands turn on sets of thrusters to
make small velocity changes.  The translation thrusters have three throttle
settings -- LOW (1%), MEDIUM (10%), and HIGH (100%).  The RCS thrust at full
throttle is 1970nt and uses 0.5kg/s.  A 1ø/s spin change requires 0.07kg
propellant.  The maximum propellant load is 320kg.

Landing Vehicle (continued)

Navigation:  The LV has an INS that provides estimates of position, velocity,
and acceleration.  Orbital parameters may also be displayed.  Major components
of the guidance system are the gyros, accelerometers, DSN and OL transponders,
and the landing radar.

Gyros provide information on the attitude of the LV with respect to local
north, east, and vertical axes.  Accelerometers are used to measure the
acceleration of the LV during main engine and RCS burns.

The DSN transponder provides the INS with a measurement of the position (ñ15m)
and velocity (ñ0.25m/s) of the LV once each minute.  The OL transponder (or
docking radar) provides the INS with more accurate measurements (ñ0.5m position
and ñ0.05m/s velocity) every 10s.  It has a maximum useful range of 30km.  The
landing radar provides the INS with accurate measurements of LV position (ñ1m)
and velocity (ñ0.25m/s) relative to the lunar surface every 2s.  It has a
maximum useful altitude of 30km.

Manned Mobility Unit

The UN is generally used only during an emergency orbital EVA to transfer
between the OL and LV when docking is impossible.  The UN has a dry mass of
175kg.  The pilot and PLSS add 150 kg.  UN subsystems include power and
nitrogen propulsion.

Power System:  The maximum battery charge is 5.8MJ.  At a power consumption of
130W, the maximum EVA duration is about 12hr.  Recharging the battery requires
about 3.5hr.

Propulsion: The UN carries a maximum charge of 25kg nitrogen at 22,700kPa for
use as a propellant.  Small thrusters provide a force of 7nt and use 25g/s.
Acceleration is about 0.02m/sý for a maximum velocity change of about 20m/s.
Attitude control uses 13g for a 1ø/s spin change.

Permanent Lunar Habitat

The HB is the focal point for many lunar surface activities such as materials
processing and equipment maintenance.  It is located just northeast of the
subearth point at 0ø	 ÉÑÑÑÑ»ÉÑÑÑÑ»ÉÑÑÑÑ»	  ÚÄ¿	  ÉÑÑÑÑ»ÉÑÑÑÑ»ÉÑÑÑÑ»
latitude and 0ø		 ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶   ÚÄÄÄÁÄÁÄÄÄ¿   ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶
longitude.  Like the OL,  ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶   ³:::::::::³   ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶
the HB consists of two    ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶   ÀÂÄÂÄÄÄÂÄÂÙ   ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶
cylindrical habitat	  ×ÅÅÅÅ××ÅÅÅÅ××ÅÅÅÅ×ðððð³:³ððð³:³ðððð×ÅÅÅÅ××ÅÅÅÅ××ÅÅÅÅ×
modules (each 5m in	  ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶   ÚÁÄÁÄÄÄÁÄÁ¿   ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶
diameter and 10m long)    ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶   ³:::::::::³   ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶
and six 5x20m solar power ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶ ³ ÀÄÄÄÂÄÂÄÄÄÙ   ÇÅÅÅÅ¶ÇÅÅÅÅ¶ÇÅÅÅÅ¶
panels.  HB subsystems    ÈÏÏÏÏ¼ÈÏÏÏÏ¼ÈÏÏÏÏ¼  EASTÀÄÙAIRLOCKÈÏÏÏÏ¼ÈÏÏÏÏ¼ÈÏÏÏÏ¼
include power, environmental, and consumbles.			    view from ABOVE

Power:  Normal power consumption is 67.6kW during work periods (UT 06:00 to
22:00) and 1kW during sleep periods.  Average power usage is normally 45.4kW
but may be reduced to 1.7kW in emergencies.  The solar array has an area of
600mý and provides up to 240kW of electrical power.  Fuel cells provide 81kW
when required.  The battery capacity is 445MJ and can supply emergency power
for 72hr.  Water capacity is 24,750kg, required to hold fuel cell production
for about 15 days.  Hydrogen (2750kg) and oxygen (22,000kg) are available for
fuel cell use.

Permanent Lunar Habitat (continued)

Environmental:  The inhabitable volume is 196m^3 and requires 235kg of air.
The airlock has a volume of 27m^3, for a depressurization loss of 0.5kg per
use.  Sufficient reserves are maintained for one complete atmospheric purge
(235kg), 360 day leak replenishment (160kg), and 300 airlock uses (150kg) for
a total air mass of 545kg (436kg nitrogen and 109kg oxygen).

Consumables:  In addition to other supplies, the HB has the capacity to supply
the MB for six missions and the LV for one mission.  Total capacities are
hydrogen (4700kg), oxygen (33,200kg), nitrogen (1060kg), and RCS propellant
(320kg).  During the lunar day, oxygen can be manufactured at the rate of
20kg/day.

Mobile Base

The MB can carry three astronauts and up to 1200kg of lunar samples and is
used as the base of operations  ÚÂÂÂÂÂÂÂÂÂÂÂ¿				ÚÂÂÂÂÂÂÂÂÂÂÂ¿
for extended lunar missions of  ³		 ³  MB SAMPLE BOX	³		 ³
up to 45 days.  MB subsystems   ÀÁÁÁÁÁÅÁÁÁÁÁÙ ÚÄÂÄÂÄÂÄÂÄÂÄ¿	 ÀÁÁÁÁÁÅÁÁÁÁÁÙ
include power, environmental,	   ÉÏÍÍÍÍÍÍÍÏÍÏÍÏÍÏÍÏÍÏÍÏÍÍÍÍÍÍÍÍÍÍÍÍÏ»
consumables, and drive.		    º:ÚÄÄÄÄ¿:³: : : : : : :ÉÑÑÑÑ»ÉÑÑÑÑ»ÇÄÄÄ¿
							  º:³    ³:³: : : : : : :ÇÅÅÅÅ¶ÇÅÅÅÅ¶º   ³
Power:  Normal power consumption is  º:³    ³:³: : : :FACE :ÇÅÅÅÅ¶ÇÅÅÅÅ¶º R ³
310W with three astronauts present   º:ÆÍÍÍÍµ:³: : : :ÄÄÄ :ÇÅÅÅÅ¶ÇÅÅÅÅ¶º   ³
and 130W with none.  The drive	  º:³    ³:³: : : : : : :ÇÅÅÅÅ¶ÇÅÅÅÅ¶º V ³
requires 6.4kW at full throttle.	º:³    ³:³: : : : : : :ÇÅÅÅÅ¶ÇÅÅÅÅ¶º   ³
When the battery is fully charged    º:ÀÄÄÄÄÙ:³: : : : : : :ÈÏÏÏÏ¼ÈÏÏÏÏ¼ÇÄÄÄÙ
(94MJ), the MB has a range of	   ÈÑÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÑ¼
100km (at 400J/m) and a 48 hr   ÚÂÂÂÂÂÅÂÂÂÂÂ¿ ³  AIRLOCK  ³ ³    ÚÂÂÂÂÂÅÂÂÂÂÂ¿
emergency supply.  The solar    ³		 ³ ÀÄÄÄÄÄÄÄÄÄÄÄÙ     ³		 ³
array has an area of 6mý and    ÀÁÁÁÁÁÁÁÁÁÁÁÙ		   LEFT   ÀÁÁÁÁÁÁÁÁÁÁÁÙ
provides up to 2.4kW of electrical power.  Recharging the battery takes about
11hr.  Fuel cells can supply 2.7kW when required.  The water tank has a
capacity of 180kg, fuel cell output for 15 days.  Hydrogen (20kg) and oxygen
(160kg) are available for fuel cell use.

Mobile Base (continued)

Environmental:  The MB inhabitable volume is 20m^3 and requires 24kg of air.
The depressurization loss is 0.36kg.  Reserves are maintained for 60 day leak
replenishment (8kg), 35 cabin evacuations (13kg), and emergencies (24kg) for a
total reserve of 45kg (36kg nitrogen and 9kg oxygen).  An additional 60 day
supply of oxygen for three astronauts (144kg) is also provided.

Consumables:  In addition to other supplies, the MB has enough capacity to
supply 20% of one LV mission.  Total consumable capacities are hydrogen
(386kg), oxygen (2540kg), nitrogen (55kg), and RCS (64kg).

Drive:  The MB has a maximum speed of 16m/s.  To improve efficiency, avoid
very rugged areas.

Roving Vehicle

The RV has a mass of 210kg, can carry two astronauts and up to 60kg of
lunar samples, and is used as   ÚÂÂÂÂÂÂÂÂÂÂÂ¿				ÚÂÂÂÂÂÂÂÂÂÂÂ¿
the primary conveyance during   ³		 ³   ASTRONAUT	   ³		 ³
most EVAs.  RV subsystems	  ÀÁÁÁÁÁÅÁÁÁÁÁÙ	  SEATS	   ÀÁÁÁÁÁÅÁÁÁÁÁÙ
include power and drive.		   ÉÏÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÏ»
							  º		 ÚÄÄÄÄÄÄÄÄÂÄÄ¿   ÚÄÄÂÄÄ¿º
Power:  When the battery is fully    º		 ÃÄÄÄÄÄÄÄÄÅÄÄ´   ÃÄÄÅÄÄ´º
charged (14.8MJ), the RV has a	  º		 ÃÄÄÄÄÄÄÄÄÅÄÄ´   ÃÄÄÅÄÄ´º
range of 100km (at 100J/m) and	  º  FACE	ÀÄÄÄÄÄÄÄÄÁÄÄÙ   ÃÄÄÅÄÄ´º    RV
can maintain non-drive systems,	 º  ÄÄÄ	ÚÄÄÄÄÄÄÄÄÂÄÄ¿   ÃÄÄÅÄÄ´ºSAMPLE
consuming 130W, for a 10hr EVA.	 º		 ÃÄÄÄÄÄÄÄÄÅÄÄ´   ÃÄÄÅÄÄ´º   BOX
Recharging the battery requires	 º		 ÃÄÄÄÄÄÄÄÄÅÄÄ´   ÃÄÄÅÄÄ´º
about 8.2hr.					º		 ÀÄÄÄÄÄÄÄÄÁÄÄÙ   ÀÄÄÁÄÄÙº
							  ÈÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑ¼
Drive:  The RV drive has a	 ÚÂÂÂÂÂÅÂÂÂÂÂ¿	    ³		ÚÂÂÂÂÂÅÂÂÂÂÂ¿ 
maximum speed of 8m/s.  To	 ³		 ³	     LEFT	³		 ³
improve efficiency, avoid very  ÀÁÁÁÁÁÁÁÁÁÁÁÙ				ÀÁÁÁÁÁÁÁÁÁÁÁÙ
rugged areas.

Portable Life Support System

One PLSS, with a mass of 70kg, is provided for the pilot and each astronaut to
allow EVAs.  Donning or removing the PLSS requires about 5min.  PLSS subsystems
include power, environmental, and consumables.

Power:  PLSS power consumption is 16W plus a maximum of 64W for pilot cooling.
The battery capacity is 2.9MJ, enough to sustain a 10hr EVA at maximum pilot
effort.  Recharging takes about 1.6hr.

Environmental:  The PLSS carries enough oxygen to sustain a 10hr EVA at maximum
effort (1kg) plus an emergency supply (1kg) and leak replenishment (0.1kg) for
a total of 2.1kg.

Consumables:  The PLSS carries 4kg of water, enough for a 10hr EVA with 8hr
reserve at maximum effort.