BATSET        Set the batterie on HP100LX

Weasel Words:

  I am not a batterie engineer. HP made it very difficult to change the fast 
charge time. I doubt that was by accident. Please make your own decisions about 
what you think this value should be. I just wanted to change it for me, and 
thought some of my friends on CIS might like to also.

Disclaimer:

      Every effort has been made to test thoroughly and verify the functions of 
this program.  However, THIS PROGRAM IS PROVIDED "AS-IS" WITHOUT WARRANTY OF ANY 
KIND.  THE ENTIRE RISK AS TO THE QUALITY AND PERFORMANCE OF THE PROGRAM IS WITH 
YOU, SHOULD THE PROGRAM PROVE DEFECTIVE, YOU ASSUME THE ENTIRE COST OF ALL 
NECESSARY SERVICEING, REPAIR OR CORRECTION. Make backup copies of your important 
files often and use this program at your own risk.

Usage:

  Since the setting of the battery to Alkaline, Nickel Cadmium and charging 
status are reset by a hard reset, I wanted to be able to set them properly in my 
AUTOEXEC.BAT file. BATSET will do these for you.

     BATSET   (  /A  |  /N  |  /C  )

  If you specify /A then the 100 will be set for Alkaline batteries and no 
charging. /N for Nickel Cadmium and no charging. /C for Nickel Cadmium and 
charging.

  In addition BATSET will allow you to change the 6 hour fast charge timer on 
the 100LX. When the AC adapter is plugged in or charging is specified the 100LX 
will charge the batteries at a rate of 100mA for 6 hours. Then it will continue 
to charge at a rate of 45mA.

     BATSET   /T=hh:mm

  Minimum value is 1 minute (00:01), Maximum value is 24 hours and 59 minutes.

  Using normal Nickel Cadmium AA cells usually rated about .400AH they will be 
properly charged from empty in about 6 hours at 100mA. However if you should be 
using high capacity Nickel Cadmiums, they can have ratings as high as .850AH and 
would be much better served by a longer fast charge, on the order of about 12 
hours.

  If you use the parameter to change this fast time, then BATSET will terminate 
and stay resident. That means about 500 bytes of memory will be kept by BATSET, 
and BATSET will chain to the Timer Tick interrupt and do its own counting. It 
will look for the system counter to be reset to 0. This reset will happen when 
the AC adapter is plugged in or it was plugged in but you just specified 
charging. Now BATSET will set the system's charge timer to 1 hour and hold it 
there until BATSET's own timer reaches the specified time. At this time BATSET 
will set the system's charge timer to 6 hours, and the system will notice that 
value and switch to slow charging.

  If you have programs which read this system counter (e.g. Mark Scardina's 
BATT100) you should be aware that with BATSET installed you will only ever see 1 
hour in that field as long as fast charging is active. Then for slow charging 
the number will start from 6 hours. An Example: Say you have BATSET set for 10 
hours, and you run BATT100. BATT100 says you are slow charging and the timer 
says 7:40. That means that you have fast charged for 10 hours and slow charged 
for an additional 1 hour and 40 minutes (7:40 - 6:00).

  BATSET is not a sophisticated terminate and stay resident program. Once loaded 
it will stay there until you reboot. There is no way to remove it. Also do not 
load it while you have system manager loaded, because when you close the DOS 
application the timer tick interrupt will still point to where BATSET was and 
... well ... uhhh. Guess it is reset time. So put it in your AUTOEXEC.BAT file 
ahead of system manager command (100).

  If you regularly keep your 100 plugged into AC, then you probably should not 
need to increase your charging time. You may want to consider decreasing it. If, 
on the other hand, you run your high capacity Nickel Cadmiums down until you are 
getting a low batterie message then you probably want to increase the time to 
about the capacity of the batterie times 150% divided by the charge current 
hours. For example if you have Radio Shack's High Capacity .850AH, multiply by 
150% for 1.275, then divide by charge current .100A to get a charge time of 
12.75 hours. Remember this assumes we start with completely exhaused batterie 
and charge it to 100%. I doubt we would be starting with a completely exhaused 
batterie, but probably pretty low if you getting low batterie messages.

  It appears that there are folks who do not like TSRs for any reason.  To 
accomidate such folks I have added 2 new parameters:

     BATSET    /R   /E 

  The 'R' will reset the system's batterie counter to 0.  So if you run this 
before the 6 hours are up, you will get another 6 hours from that time.  The 'E' 
merely stuffs an escape character into the keyboard buffer so if you run the 'R' 
from APPT you can bypass the PRESS ANY CHARACTER TO CONTINUE message.

  I leave the creation of a system macro to run this in five hours and fifty 
five minutes from the time the macro is invoked as an exercise for the user.

Freeware by Alex Patterson

Enjoy.