--- Repair Procedures for VC II ---

      Section I. of this procedure is for owner replacement of integrated 
      circuit U30, in the event replacement is necessary.  The procedure 
      requires a certain amount of user skill and equipment in unsoldering 
      and soldering delicate electronic devices.  Section II and subsequent
      are reserved for additional repair procedures as I develop them or as
      others wish to add them to this document.

WARNING:   Remove VC power line cord from wall socket before opening unit.

CAUTION:   Accidental shorting of the lithium battery bus on the decoder
           board will cause your seed keys to permanently disappear. Keep
           screwdrivers and other metal objects away from the board. Do not
           place PC board on electrically conductive surface.


I. Replacement of Integrated Circuit chip U30.

   
   A. Remove plastic card cage from rear of VC unit as follows:

      1. Remove two small Phillips-head screws retaining the cage access
         cover on back of VC unit.

      2. Swing cover up and remove it from back of VC unit, revealing rear
         side of black plastic cage.  (If cover is slightly curled around
         back plate of VC enclosure, use screwdriver to pry it free.)
      
      3. Slide cage from back of VC enclosure by pulling on the two plastic
         cage tabs that extend below the bottom of the VC enclosure.  The
         cage is retained only by a pc-board edge connector inside the VC
         unit, so initial force will disengage this connector, and then the
         cage will slide freely.

      
   B. Remove plastic strip (the seal) from bottom center of card cage (which
      immediately voids your warranty) to reveal a security screw that holds
      the two cage halves together.  Note that screw head has a hexagonal
      recess, like an allen-wrench socket, but has a raised pin-like
      obstruction blocking the center of the recess.  Remove security screw
      as follows:

      1. Obtain the proper size Torx-wrench (appears to be size 20), drill 
         a hole in the end of the wrench to clear the pin-like obstruction,
         then use the wrench to remove the screw; or,

      2. Use a small-tipped screwdriver (pocket-type works well) that can be
         tightly wedged between one wall of the screw-head recess and the
         pin-like obstruction.  Pliers may be necessary to apply enough torque
         on the screwdriver to free the screw.


   C. Release seven tab latches around the edges of the plastic cage and
      separate the two halves of the cage.  Maintain a separating force on
      the cage halves as you press each tab, and it will not be too difficult
      to get the cage apart.  NOTE: The two tabs on the edge farthest from
      the PC-board edge connector are not releasable; they merely act as a
      sort of hinge.

   D. Lift the PC board out of the retaining notches in the cage bottom half,
      noting how it must be oriented when it is later replaced.

      CAUTION: Keep PC board away from metal table tops, tools, and anything
               electrically conductive.  Battery power on this board must not
               be shorted.

      TIP: A good work surface is the bottom of a large cardboard box having
           sides cut down to about 2-inches high.

   E. All locating instructions are relative to PC-board orientation as
      follows:
   
          1. Component side of PC board is UP.
        
          2. PC-board edge connector is toward you.


   F. Locate lithium battery on PC board.  This is the cylindrical device
      having a wire lead extending from each end.  It is mounted in the far
      right hand corner of the PC board.  NOTE: In older VC 2000 units, a
      pancake shaped battery was used.  If you are repairing one of these
      units you will not have to remove epoxy, since it was not then being
      used.


   G. Using non-metallic ruler, measure left from battery wire lead 1-1/2
      inches onto surface of epoxy encapsulant.  Mark this point on the 
      epoxy surface and again on the epoxy covering the bottom of the board.


   H. All epoxy between battery and marked point must be removed from both
      sides of the PC board to gain access to integrated circuit chip U30.
      Use either a solvent (make sure you get instructions for using whatever
      solvent you buy) or a heat-gun.

  
   I. If you use a heat-gun (hair dryer doesn't get hot enough), observe
      cautions regarding its use, then proceed as follows:

      1. On top of PC board, shield lithium battery and surrounding
         components from direct hot-air blast.  Use asbestos sheet stock, 
         heavy cardboard, or similar NON-metallic material.

      2. Taper the end of a wooden dowel or stick to use as a scraper.

      3. Apply approximately 500-degree fahrenheit hot air to epoxy for
         10-15 seconds.  This will loosen bonding of surface layer of
         epoxy.  Use wooden scraper to dig-off loosened surface fragments.

         CAUTION:  Do not permit PC board to flex or bend as you apply
                   scraping force.

      4. Continue heating-scraping cycles using minimum heating possible.
         Eventually, you will uncover U30 and reach the surface of the
         PC board.

         CAUTION:  Do not scrape through the copper traces on the surface
                   of the PC board.

      5. Repeat above heating-scraping cycles on epoxy covering marked
         area on bottom of PC board.  Remove enough epoxy for clear access
         to all of U30's 28 solder pads.

      6.  CAUTION: To keep from shorting the lithium battery, do not let
                   soldering iron tip contact more than one pin at a time.

          Using fine-tipped soldering iron and solder-sucker (vacuum type;
          don't use metal wicking braid), unsolder all 28 pins of U30.

          TIP: Pins will likely remain lightly solder-tacked to walls of
               solder pads even after all solder has been removed from the
               holes. Using wood splinter as you apply soldering iron tip
               to the solder pad, apply light freeing force to the pin.
               When the pin releases from the pad, hold pin in center of the
               hole, remove soldering iron, and allow the pin to cool. Pin
               should now be free.

     
      7. After all pins of U30 are free, remove U30 as follows:

      8. Scrape the epoxy from under the end of U30 nearest the edge of the
         PC board to provide an entry point for prying.  Obtain a bakelite
         or hardwood splinter that can be used to apply a prying force under
         U30.

      9. Use heat-gun applied to bottom of PC board directly under U30 for
         10-15 seconds.  Allow heat to conduct through board as you apply a
         light prying force to U30.  Periodically reapply hot air until U30
         starts to pull free.  Check that U30 pins are releasing properly,
         and continue to remove U30.  Work slowly to prevent pulling copper
         traces off the PC board.

     10. Use wooden scraper to clean-up both sides of PC board, making sure
         solder pads are all revealed.

     11. CAUTION: It is not a good idea to solder the new U30 to the PC 
                  board; the solder pads are easily ruined (delaminated)
                  after several unsolder/solder cycles.
                   
         Obtain 28-pin integrated circuit socket and install on component
         side of PC board in place of U30.  Use tape to hold the socket in
         place temporarily. Make sure that all pins protrude through bottom
         of PC board.

     12. Solder socket pins on bottom of PC board using minimum amount of
         solder and ensuring that neither soldering iron tip nor solder
         touches more than one pin at a time.  Remove tape.

     13. Using toothbrush and isopropyl alcohol, clean solder joints of 
         solder flux residue.
     
     14. CAUTION:  Make sure that small U-shaped notch in end of replacement
                   U30 points toward center of PC board.  U30 will be 
                   destroyed if you plug it in with the U-shaped notch
                   pointing toward nearby edge of PC board.
        
         TIP: U30 will be much easier to plug-in if both rows of pins are
              parallel and at right angles to the body of the chip.
          
         Insert replacement U30 integrated circuit in socket.


     15. Carefully inspect U30 to make sure that all of the pins seated
         properly, and that none of them were inadvertently bent under
         the chip body or were bent outward.  This happens all the time
         (even with good technicians) and is often overlooked.


   J. Reassemble PC board and cage halves, reversing disassembly procedures
      given above.  Install cage in VC case, and replace retaining cover
      using the two screws previously removed.


II. (This section to be developed later as other repair procedures become
     known.)

Downloaded From P-80 International Information Systems 304-744-2253