CORRECTION

		FOR PATCH AREAS GIVEN IN FILE NORTPATC.DOC

	The following apply to the Norton Utilities SecMod and DiskLook,
	ver 2.01, files dated 1/2/84  2:01pm. Re: Patching to read up to 
	43 tracks instead of 39.

	See file NORTPATC.DOC.  The offsets given are incorrect for my
	copies which I just received yesterday.  When I ordered the updates,
	I asked Peter if the patches would adversely affect the operation of
	the pgms. He replied that they seemed fine, "but check the offsets".

	Since my copies are dated 1/2/84 and NORTPATC.DOC is dated 12/29/83,
	it would seem that Peter made a change in the pgms for the ver 2.01
	which I received. (I don't know the author of NORTPATC.DOC)

	Use Debug, in the following manner, which will help you avoid a
	mistake and which will give you greater assurance that you have 
	the right locations.  It's only a few seconds slower than that 
	given in NORTPATC.DOC, but much safer.

			   *  *  *  *  *  *  *

	1. Debug in Drive A:.  COPIES of DL.COM & SM.COM in Drive B:
	   Default Drive is A:

	2. You must see what precedes the parens.  If you do not, then 
	   start over. You Enter only what is shown in parens. (Don't
	   enter the parens.)  The  "xxxx"  means any 4 hex digits -- 
	   don't care.

	3. A> DEBUG B:SM.COM <cr>
		
		-E517 <cr>
		xxxx:0517   28.(2B) <cr>

		-E3294 <cr>
		xxxx:0517   28.(2B) <cr>

		-E4BB0 <cr>
		xxxx:4BB0   33.(34) (press space bar) 39.(32) <cr>

		-W <cr>

		-NB:DL.COM <cr>
		-L <cr>

		-E0AE2 <cr>
		xxxx:0AE2   28.(2B) <cr>

		-E3A99 <cr>
		xxxx:3A99   28.(2B) <cr>

		-E7A1B <cr>
		xxxx:7A1B   33.(34) (press space bar) 39.(32) <cr>

		-W <cr>

		-Q <cr>



	The other information in NORTPATC.DOC is correct, including
	the patches for DISKCOPY.COM -- Everything works just fine,
	and you can now access 43 tracks.

	Now, for a little more fun, I worked with Unerase, UE.COM.
	But, we need a little help.   I was able to patch it to work
	to 43 tracks, but when I went to build a file, the logic would
	set the clusters correctly and bomb-o.

	The patches are as follows:

		A> DEBUG B:UE.COM
		-E136D <cr>
		xxxx:136D   28.(2B) <cr>

		-E366E <cr>
		xxxx:366E   28.(2B) <cr>

		-E6232 <cr>
		xxxx:6232   33.(34) (press space bar)  39.(32) <cr>

		-W <cr>
		-Q <cr>

	NOTE: UE will not build a file on the tracks above 39 with only
	      the patches given here for UE.  Perhaps someone can come
	      come up with them.  I formatted track 42 and put data in 
	      Sector 1, side 1.  I then built a file in the standard 
	      manner using the program.  It created wrong cluster nos.
	      Then I "erased" the file in the standard manner, and then
	      "unerased" it, in the standard manner using the program.
	      It made no difference and the file was resurected,
	      incorrectly.  I used CHKDSK /F, which gave "incorrect
	      file allocation, directory entry truncated", but it 
	      didn't fix it.

	      I used SecMod to read the sector, (f7), which it did 
	      correctly.  I made some data changes with it, which it 
	      wrote back correctly.

	3/17/84
	Jim Gainsley
	116 Third Ave. N.
	Mpls., MN. 55401
	(612) 338-6124
	CIS: 70346,457
 
	P.S. For those contemplating the update, we found that the program
	     LPRINT.COM no longer wastes a sheet of paper at the start.  Also,
	     all the programs have been converted from .EXE to .COM formats
	     -- smaller code and faster loading.   
 from .EXE to .COM formats
	     -- smaller code and faster loading.