AR3000 Scanner Control System

                                    Version 1.00

                                    Users Manual













































               Copyright (c) 1990 by Gesmundo Computing & Design, Inc.
                                All Rights Reserved.





                                   COPYRIGHT NOTICE

          The  Scanner Control System is Copyright protected  under  United
          States  law.   First publication of the software  took  place  in
          1990.

          Under   the  copyright  laws,  the  purchaser  of   a   protected
          publication   may   not  duplicate,  reproduce,   or   distribute
          significant  portions of that protected publication  without  the
          express  written consent of the copyright holder,  or  publisher.
          In this case, Gesmundo Computing & Design, Inc. is both.

          We  hereby  expressly grant permission to the  legitimate  retail
          purchaser  of  the system to make two (2) backup copies  of  this
          product,  which copies may only be used for "backup" or  archival
          purposes.   In other words, while such purchaser may make  backup
          copies as herein authorized, the purchaser may not give, sell, or
          otherwise distribute any copies of the software to anyone.

          It  is  our  hope  that  this  authorization  will  protect   the
          legitimate interests of both the purchaser and Gesmundo Computing
          &  Design,  Inc.   We  do not  believe  in  "crippling"  or  copy
          protecting  our products, and encourage our users to make  backup
          copies to protect their investment and their data.

          On the other hand, we are entitled to fair compensation for  each
          new  user of our products, and ask the user to bear that in  mind
          when friends or associates ask them for a free copy.

          The  only  users  who  will receive support  are  those  who  are
          legitimate purchasers, and who have filed a "Registration"  form,
          found in the back of this manual, with us.  Such registration  is
          the  only  way we know of to assure ourselves that a  caller  who
          wants telephone support is a legitimate owner of the software.

          We recommend two backup copies so that you may use one of them as
          your "day to day" working copy and the second for "off  premises"
          storage.   Of course, the master you purchased from us should  be
          stored in a safe place.






                           Gesmundo Computing & Design Inc.
                               10301 E. M89   Suite 303
                               Richland, MI  49083-9347
                               Telephone (616) 629-5801




                            AR3000 Scanner Control System


                                   Table of Contents

          User Manual                                            Page

               Hardware Requirements............................ 1 - 1

               Installation..................................... 1 - 1

               Operation........................................ 1 - 2

               Scanner Control.................................. 2 - 1

               Logging.......................................... 3 - 1

               Spectra Graph.................................... 4 - 1

               Bank Maintenance................................. 5 - 1

               Frequency Data Base Maintenance.................. 6 - 1

               Log Processing................................... 7 - 1

               Configuration.................................... 8 - 1

               Notes on Communication Ports..................... 8 - 3

               Function and Special Key Assignments............. A - 1

               Packing List and Log File Layout................. B - 1

               User Registration Form........................... C - 1


                                Hardware requirements

               An  MS-DOS  PC with at least 256K of available  memory,  one
               floppy disk drive, one serial port, and DOS 2.0 or later.


                                    Installation

               First make a backup copy of the diskette and put the  master
               in a safe place.

               For floppy based systems no further installation is required
               and you may use the backup copy in either drive 'A' or 'B'.

               For  hard  disk systems, place the backup  diskette  in  the
               diskette drive and issue the following commands:


               A:INSTALL  If installing from drive A

                              or

               B:INSTALL  If installing from drive B


               You  will  be  prompted for the source drive  and  then  the
               drive/directory  where  you wish to have  the  software  in-
               stalled.  The  default  is  A, for  the  source  drive,  and
               C:\AR3000,  for  the destination drive/directory.   You  may
               change  the  source drive to B and the  destination  to  any
               drive/directory  you  desire.


                       Connecting the Computer to the AR-3000

               Connect  the DB25S 25 pin connector to a serial port on  the
               computer.  Connect the DB25P to the back of the AR-3000.

                            Connecting the Tape Recorder

               Connect  the 2.5mm plug to the remote jack on the  tape  re-
               corder.   Connect  one of the 3.5mm jacks  to  the  external
               speaker jack on the back of the AR-3000 and the other end of
               the  cable to the auxilary or microphone input jack  on  the
               tape recorder.

          Notes:

               If your computer has 9 pin serial port connectors, then  you
               will  need  a  9 pin to 25 pin serial  cable  adapter.   The
               adapter  can  be obtained from most computer  stores.   When
               selecting  a tape recorder, look for one which has a  trans-
               port  that  starts quickly in order to avoid  missing  audio
               from  the beginning of each call.  Almost any recorder  that
               has a voice activated option will work well.





               AR3000 Version 1.00                         Page 1 - 1


                                      Operation


          Turn  the computer on and wait for the DOS prompt.  Next turn  on
          the  radio.  If you are using a floppy based system,  insert  the
          backup  diskette  in the floppy drive.  If you are using  a  hard
          disk  system,  change  directories to the one  specified  in  the
          installation step above.  Make sure the system date and time  are
          set  correctly  as they will used by the  software  when  logging
          calls.  Type AR3000 and press the Enter key.

          The copyright screen will appear and the software will attempt to
          establish communication with the radio.  If communications cannot
          be established, a message will appear indicating that the attempt
          was  unsuccessful and that the logging and other commands to  the
          radio  have been disabled.  If communication is  not  established
          and the radio is connected properly, see Installation on page  1-
          1.  Then proceed to the configuration screen and ensure that  the
          correct communications port has been selected (see  Configuration
          on page 8-1).

          The  next  screen to appear is the Scanner  Control  System  main
          menu.   From this screen all of the available options  and  addi-
          tional  screens may be selected.  These options and  screens  are
          described in detail in the following chapters.

          The bank data, supplied with the software, is preloaded with  the
          frequencies  that  the factory programs into the radio  prior  to
          shipment.   If you have programmed your own frequency  data  into
          the radio and wish to update the bank data automatically, proceed
          to  the  B)ank  Maintenance screen and use  the  U)pload  option.
          Remember to use the S)ave command when you are finished to update
          the disk file.  See pages 5 - 1 and 5 - 2 for more information on
          Bank Maintenance.


                                   General Conventions


          Each  of the screens has a header, body, and option  select  sec-
          tion.  Upon entering a screen, the cursor will stop at the Select
          prompt  in the option select line.  Entering the letter  code  of
          the desired option, or pressing one of the special keys described
          in  appendix A, selects the option.  Pressing F1 will  display  a
          help message at the bottom of the screen.  See appendix A for  an
          explanation of the function and special key assignments.














               AR3000 Version 1.00                         Page 1 - 2

                               Scanner Control System


          (B)ank Maint   Enter 'B' to select the Bank Maintenance screen.

          (F)req Maint   Enter 'F' to select the Frequency Data Base  Main-
                         tenance screen.

          Process Lo(g)  Enter 'G' to select the Log Processing screen.

          L(o)gging      Enter 'O' to select the Scanner Logging screen.

          (L)ink         Enter 'L' to Link the current bank to the list  of
                         banks to be scanned.

          (U)nlink       Enter 'U' to remove the current bank from the list
                         of banks to be scanned.

                         The list of linked banks is stored as part of  the
                         bank data.  Pressing Link or Unlink sets the  bank
                         edit  flag.   If you Quit the AR3000  program  and
                         have not saved the bank data the following  prompt
                         will be displayed.  Changes made in Banks, Abandon
                         Changes  (Y/N).  Press 'Y' to abandon the  changes
                         or 'N' to save the changes.

          Spect(r)a      Enter 'R' to select the Spectra Graph screen.

          (M)anual       Enter 'M' to switch from scan or search mode  back
                         to the manual mode.

          (S)can         Enter 'S' to select the scan or search mode.

          (T)une         Enter  'T' to tune the radio to a frequency.   The
                         cursor  will move to the frequency column  of  the
                         box  in the center of the screen.  Enter  the  de-
                         sired  frequency, modulation and  attenuator  set-
                         ting.   The  software will tune to  the  frequency
                         upon  completion of the entry.  If  the  frequency
                         entered  is on file in one of the banks or in  the
                         frequency  data  base,  the  description  will  be
                         displayed.

          (D)elay        Enter  'D'  to toggle delay on or off.   When  the
                         Delay  function  is on and a call  completes,  the
                         program will wait for the number of seconds speci-
                         fied for 'Delay time' before stepping to the  next
                         frequency.  The Delay time may be set from 1 to 59
                         seconds in the configuration screen.












               AR3000 Version 1.00                         Page 2 - 1

                               Scanner Control System

          (W)ait         Enter  'W' to toggle the Wait function on or  off.
                         When  the  Wait function is on and a call  is  re-
                         ceived, the program will step to the next frequen-
                         cy  after the number of  seconds   specified   for
                         'Wait  time' if the call has not  terminated.  The
                         Wait  time may be set from 1 to 59 seconds in  the
                         configuration screen.

          Loc(k)         Enter  'K'  to toggle the 'lock' for  the  current
                         frequency.

                                             Scan Banks

                         When 'locked' the frequency will be skipped  while
                         scanning.   In  manual mode the frequency  may  be
                         selected by using the up and down arrow keys.

                                            Search Banks

                         Up to 500 frequencies may be locked out when using
                         a search bank.  Once locked, the frequency will be
                         skipped  in both manual and scan modes.  The  lock
                         table is cleared if you edit the search bank or if
                         you  select  a different search bank.   Note:  The
                         Re(v)iew Locks function is the only way to  unlock
                         a locked search bank frequency.

          P)riority      Enter 'P' to toggle the 'priority' function on  or
                         off.  When priority is on, bank 1 will be  scanned
                         after each  successive bank that is scanned.

          Re(v)iew Locks Enter  'V'  to  Review the  frequencies  that  are
                         locked  out in the current bank.  Entries  may  be
                         unlocked by entering 'N' or left locked by  press-
                         ing Enter.

          (C)onfig       Enter 'C' to select the Configuration screen.

          E(x)it         Enter 'X' to leave the program and return to  DOS.
                         If the Bank, Frequency Data Base, or Configuration
                         data has been changed but not saved, a prompt will
                         appear  indicating which items have been  changed,
                         and ask if you wish to abandon the changes.  Enter
                         'Y'es to exit the program without changes saved or
                         'N'o to have the data saved prior to returning  to
                         DOS.

          Bank nn        Enter a number from 1 to 32 to select a bank.

          Down Arrow     Selects the next frequency.

          Up Arrow       Selects the previous frequency.

          Page Down      Selects the next bank.

          Page Up        Selects the previous bank.



               AR3000 Version 1.00                         Page 2 - 2


                               Scanner Logging System


          The logging system uses the signal strength data returned by  the
          AR3000 to determine call activity.  The software logs the  serial
          number, frequency, mode, attenutator setting, description,  date,
          time  in,  time out and signal strength for each  call  received.
          When  a  frequency  is logged, the software scans  the  bank  and
          frequency  data base for a matching entry.  If a match  is  found
          the  description of the frequency will appear in the  log.   Each
          new  entry appears at the bottom of the window and  the  previous
          entries are scrolled up one line.  The following is a description
          of the column headers at the top of the window.

          S/N            The serial number assigned to the call.

          Frequency      The frequency.

          M              Mode - N for narrow FM, W for Wide FM, A for AM, U
                         for upper sideband, L for lower sideband or C  for
                         CW.

          A              Attenuator - 'Y'es or 'N'o attenuator

          Description    The description entered in bank maintenance or the
                         frequency data base for this frequency.

          Date           The date the call was received.

          Time In        The time when the call started.

          Time Out       The time when the call was completed.

          SS             The signal strength of the call received.

          When  the  AR3000 program is first started, it uses  the  default
          file name AR3000.LOG.  If the file already exists, new data  will
          be appended to the end of the file.  If you wish to use a differ-
          ent file name, go to the Log Processing screen and use the  F)ile
          option to change file names.  The serial number starts at one and
          is incremented by one for each call received.  The serial  number
          is reset to one if you delete, rename, or change log files.


















               AR3000 Version 1.00                         Page 3 - 1


                               Scanner Logging System


          The  cursor  does not sit at the Select option  in  this  screen.
          However,  options  may be selected at any time  by  pressing  the
          letter  of  the desired option.  Since each of the options  is  a
          single  keystroke, you do not need to press the Enter key.


          C)apture       Press  'C' to toggle the capture function  on  and
                         off.  When capture is on, each log entry is  writ-
                         ten to the current log file.

          P)rinter       Press 'P' to toggle the printer on and off.   When
                         the printer is on, each log entry is printed  upon
                         completion of the call.

          R)ecorder      Press  'R' to toggle the recorder function on  and
                         off.   When  the recorder is on, the  recorder  is
                         turned on at the start of each call and turned off
                         on completion.

          S)tatus        Press 'S' to toggle the status line at the  bottom
                         of the screen on and off.

          L)ineprinter   Press 'L' to change printers.

          Loc(k)         Press 'K' to Lock out the current frequency.

          A)log          Press 'A' to begin Autolog.  The Autolog  function
                         logs  the call and then locks out  the  frequency.
                         When  you  have completed scanning  the  log  will
                         contain  a  single entry for  each  frequency  re-
                         ceived.   Note:  Autolog only  works  with  search
                         banks  17-32.   If  Autolog is on  when  you  quit
                         logging, the lockout table will be cleared.

          D)elay         Press 'D' to toggle the Delay function on and off.

          W)ait          Press 'W' to toggle the Wait function on and off.

          Q)uit          Press  'Q' to leave the logging screen.  You  will
                         be returned to the Scanner Control System screen.

          F5             Press F5 to toggle the frequency display on/off.

          Down Arrow     Selects the next frequency.

          Up Arrow       Selects the previous frequency.

          The current status of capture, printer, and the recorder are dis-
          played  in  the  status line at the bottom of  the  screen.   The
          status  of Delay, Wait, and Autolog are displayed at the  top  of
          the screen.






               AR3000 Version 1.00                         Page 3 - 2


                                    Spectra Graph


          Spectra  Graph  uses the search banks, banks 17 thru  32,  to  do
          spectrum analysis. Up to 1000 discrete frequencies can be record-
          ed  in memory at one time.  The display shows 69 steps at a  time
          and  may  be scrolled left or right in single step or  half  page
          increments.  The graph  may be scrolled both during and after the
          search.  You may also print the graph at any time by pressing the
          Print  Screen  key.  The description of the center  frequency  is
          displayed  at the top of the graph if it is on file in the  Banks
          or  Frequency  Data Base.  The software  graphs  signal  strength
          while  performing the sweep/s and counts the number of times  the
          frequency was active.  After stopping the sweep you may press  F7
          to display a graph the counts.  An asterisk in a column indicates
          the  frequency was active but the count is less than  the  lowest
          value  on  the  scale.  Press F7 again to return  to  the  signal
          strength graph.


          Bank nn   Enter the bank number to search, 17 to 32.

          PgUp      Moves the graph right a half page.

          PgDn      Moves the graph left a half page.

          Up Arrow  Moves the graph right one step.

          Dn Arrow  Moves the graph left one step.

          S)weep    Press 'S' for a single sweep of the frequency range.

          R)epeat   Press 'R' for repeating sweeps of the frequency range.

          C)um      Press 'C' for cumulative repeating sweeps of the range.

          T)une     Press 'T' to tune the radio to the center frequency.

          L)og      Press  'L' to log the center frequency  information  in
                    the Log File.  If an entry is logged for which no  call
                    was received the signal strength will be 32.

          F5        F5 toggles the frequency display on and off.

          F6        Change the search parameters.

          F7        Toggles the graph from Signal Strength to Count mode.

          Q)uit     Press 'Q' to leave the Spectra Graph screen.  You  will
                    be returned to the Scanner Control System screen.










               AR3000 Version 1.00                         Page 4 - 1

                                  Bank Maintenance


          There are 16 banks of 100 scan frequencies each and 16 banks each
          containing  2 search frequencies.  In addition to the  frequency,
          modulation,  attenuator, and description, a title for  each  bank
          may be entered.  Also, any one of the 16 scan banks may be  down-
          loaded to or uploaded from any one of the 4 banks in the radio.

          Bank nn   Enter the bank number to edit, Page Down to move to the
                    next page, or Page Up to move to the previous page.

          S)ave     Enter  'S'  to save the bank data.  All  bank  data  is
                    stored in a single file, and entering 'S' saves all  32
                    banks.

          E)dit     Enter 'E' to edit the currently displayed bank.

                                     Scan Banks

                    The  cursor will move to the top of the screen and  you
                    may enter or edit the description for the bank.   After
                    entering  the bank description, the cursor will move to
                    the first frequency in the bank.  You may use the  down
                    arrow  to move to the next frequency, the up  arrow  to
                    move  to the previous frequency, the page down  key  to
                    move  to the next page, the page up key to move to  the
                    previous  page, the F8 key to copy data from  the  fre-
                    quency data base or log, F4 to delete the entry, or you
                    may  enter a frequency between .1 and 2036 Mhz.   After
                    entering a frequency, the cursor will move to the  mode
                    column  which will be preloaded with a default  modula-
                    tion based on the frequency entered.  If the default is
                    acceptable,  press Enter to move to the next column  or
                    enter the desired modulation type.  In the Att  column,
                    enter  'Y'es for attenuator on or 'N'o  for  attenuator
                    off.   In  the Lock column enter 'Y' to  lock  out  the
                    frequency  or  'N'  for no lock out.   Next  enter  the
                    frequency description.

                                    Search Banks

                    After  entering the bank number, select 'E'dit and  the
                    cursor  will  move to the beginning  frequency  column.
                    Enter a frequency between .1 and 2036 Mhz.  The  cursor
                    will move to the Ending Frequency column.  Enter a  the
                    ending  frequency of the range.  Note that  the  ending
                    frequency must be greater than the beginning frequency.
                    The modulation will be defaulted based on the frequency
                    entered.   Press Enter to accept the default  or  enter
                    the desired modulation type.  In the attenuator column,
                    enter  'Y'es for attenuator on or 'N'o  for  attenuator
                    off.  In the Step column, enter the desired step incre-
                    ment.   The step increments may range from .05  Khz  to
                    999.95 Khz in .05 Khz steps.  Next enter a  description
                    for the bank.

                    The valid entries for modulation are 'N' for narrow FM,
                    'W'  for wide FM, 'A' for AM, 'U' for  upper  sideband,
                    'L' for lower sideband or 'C' for CW.

               AR3000 Version 1.00                         Page 5 - 1

                                  Bank Maintenance


                                    Copying Data

                    When you press F8 in the frequency column, the  follow-
                    ing prompt will be displayed.

                    Copy from F)requencies or L)og  _

                    Enter 'F' to copy data from the Frequency Data Base  or
                    'L'  to  copy  data from the Log.   After  making  your
                    selection,  the system will display a page of  frequen-
                    cies from the Frequency Data Base or the Log.  Use  the
                    Page  Up or Page Down keys to move to the desired  page
                    and then the Up Arrow or Down Arrow keys to move to the
                    desired  entry to copy.  Press F8 to mark  the  entries
                    you  wish to copy.  The number of entries that  may  be
                    copied at one time is based on entry number you are  at
                    in the bank when F8 is pressed.  The maximum number  is
                    100  or the number of entries that will fill the  bank.
                    If  you are not on the first empty entry in  the  bank,
                    the copied entries will overwrite the existing entries.
                    After  you  have marked the entries you  wish  to  copy
                    press 'C' to copy the entries or F10 abandon the copy.

          P)rint    Enter  'P'  to print the bank reports.   The  following
                    prompt will appear.

                    I)ndex or B)anks _

                    Enter  'I'  to print the Bank Index Report  or  'B'  to
                    print the Scan Banks Report.  If B)anks is selected you
                    will  be  prompted for the beginning  and  ending  bank
                    numbers.

          U)pload   Enter  'U' to upload frequency data from the  radio  to
                    the computer.  You will be prompted to press F3 to  set
                    the radio on the desired bank and then Enter to process
                    the  upload.   If an uploaded frequency is on  file  in
                    another  bank or the frequency data base, the  descrip-
                    tion will be automatically copied into the bank.

          D)ownload Enter 'D' to download frequency data from the  computer
                    to the radio.  You will be prompted to press F3 to  set
                    the radio on the desired bank  and then Enter to  proc-
                    ess the download.

          O)rder    Enter  'O'  to sort the bank.  After entering  'O'  the
                    following prompt will be displayed.

                    F)req, C)lass or D)escription

                    Enter  'F' to sort by frequency, 'C' to sort by  class,
                    or 'D' to sort by description.

          Q)uit     Enter  'Q'  to leave the Bank  Maintenance  screen  and
                    return to the Scanner Control System screen.



               AR3000 Version 1.00                         Page 5 - 2


                           Frequency Data Base Maintenance


          A  frequency  data base can hold up to 1600  frequencies  and  an
          unlimited  number of data bases may be created.  In  addition  to
          the  frequency, modulation, and attenuator, a classification  and
          description  for each frequency may be entered.  The  entries  in
          the  data  base may be sorted by  frequency,  classification,  or
          description and duplicate entries are allowed.

          Page nn   Enter the page number to edit, Page Down to move to the
                    next page or Page Up to move to the previous page.

          S)ave     Enter 'S' to save the frequency data.

          E)dit     Enter 'E' to edit the currently displayed page.

                    The  cursor  will move to the first  frequency  of  the
                    page.   You may use the down arrow to move to the  next
                    frequency,  the up arrow to move to the  previous  fre-
                    quency, the page down key to move to the next page, the
                    page up key to move to the previous page, the F8 key to
                    copy  data  from  the banks or log, F4  to  delete  the
                    entry, or you may enter a frequency between .1 and 2036
                    Mhz.  If you enter a frequency, the cursor will move to
                    the  modulation  column.  The entry will  be  preloaded
                    with  a default modulation based on the  frequency  en-
                    tered.   If the default is acceptable press  Enter,  or
                    enter the desired modulation type.  Next enter  attenu-
                    tor the setting, 'Y'es for on or 'N'o for off, and  the
                    cursor  will  move to the class column.  Next  enter  a
                    classification for the frequency and then the  descrip-
                    tion for the frequency.

                    The valid entries for modulation are 'N' for narrow FM,
                    'W'  for wide FM, 'A' for AM, 'U' for  upper  sideband,
                    'L' for lower sideband or 'C' for CW.























               AR3000 Version 1.00                         Page 6 - 1


                           Frequency Data Base Maintenance


                                    Copying Data

                    When you press F8 in the frequency column, the  follow-
                    ing prompt will be displayed.

                    Copy from B)anks or L)og  _

                    Enter  'B' to copy data from the Banks, or 'L' to  copy
                    data  from the Log.  After making your  selection,  the
                    system  will  display a page of  frequencies  from  the
                    Banks or the Log.  Use the Page Up or Page Down keys to
                    move  to the desired bank or log page, and then the  Up
                    Arrow  or Down Arrow keys to move to the desired  entry
                    to  copy.   Press F8 to mark the entries  you  wish  to
                    copy.  The maximum number of entries that may be copied
                    at  one time is 32.  If you are not on the first  empty
                    entry  in the data base, the copied entries will  over-
                    write the existing entries.  After you have marked  the
                    entries you wish to copy, press 'C' to copy the entries
                    or F10 abandon the copy.

          P)rint    Enter 'P' to print the Frequency Data Base Report.

          O)rder    Enter  'O' to sort the data base.  After  entering  'O'
                    the following prompt will be displayed.

                    F)req, C)lass or D)escription

                    Enter  'F' to sort by frequency, 'C' to sort by  class,
                    or 'D' to sort by description.

          F)ile     Enter 'F' to change data bases or to create a new  data
                    base.  The cursor will move to the file name at the top
                    left  of the screen and you may enter a new file  name.
                    If  the  file exists, it will be loaded and  the  first
                    page  will be displayed.  If the file does  not  exist,
                    the following message will be displayed.

                    Filename.ext not found - Press Enter to Continue _

                    Pressing  enter will return you to the  select  prompt.


          Q)uit     Enter 'Q' to leave the Frequency Data Base  Maintenance
                    screen and return to the Scanner Control System screen.












               AR3000 Version 1.00                         Page 6 - 2


                                   Log Processing

          P)rint    Enter 'P' to print the log report.

          E)xport   Enter 'E' to export the log in ASCII format.

                    The log is stored in an internal binary format which is
                    not  useable  by  other programs.   The  export  option
                    creates  an  ASCII  file with fixed  field  and  record
                    lengths.   Each  record is terminated with  a  carriage
                    return  and  linefeed.   The file is  created  with  an
                    extension of .PRN and may be read by Lotus 123,  dBASE,
                    word  processors, and many other DOS  application  pro-
                    grams.  The ASCII version of the log is approximately 5
                    times larger than the internal version.  When exporting
                    large  log files, make sure there is enough disk  space
                    available to hold the ASCII file.

          R)ename   Enter 'R' to rename the log file.

                    When  the  AR3000 program is run, it uses  the  default
                    file  name AR3000.LOG.  Use the rename option  to  save
                    the log under a different file name.

          D)elete   Enter 'D' to delete the current log file.

                    After entering 'D' to delete the log file, the  follow-
                    ing prompt will appear.

                    Are You Sure (Y/N) _

                    Enter 'Y'es to delete the file or 'N'o to return to the
                    select prompt.

          F)ile     Enter  'F'  to change log files or to start a  new  log
                    using  a different file name.  The cursor will move  to
                    the file name at the top left of the screen and you may
                    enter a new file name.  If the file exists, it will  be
                    loaded  and the first page will be displayed.   If  the
                    file  does  not exist, the following  message  will  be
                    displayed.

                    Filename.ext not found - Press Enter to Continue _

                    Pressing  enter will return you to the  select  prompt.


          Q)uit     Enter 'Q' to leave the Log Processing screen and return
                    to the Scanner Control System screen.

          Page Down Displays the next page of the log.

          Page Up   Displays the previous page of the log.

          Home      Displays the first page of the log.

          End       Displays the last page of the log.



               AR3000 Version 1.00                         Page 7 - 1


                                System Configuration


          E)dit          Enter 'E' to edit the configuration data.

          S)ave          Enter 'S' to save the changes you have made to the
                         configuration data.

          A)ctivate      Enter  'A' to activate changes in  the  configura-
                         tion.   The A)ctivate option is not  required  for
                         the S)eq or A)ll Linking option, see below.

          Q)uit          Enter  'Q' to quit and return to the Scanner  Con-
                         trol System screen.


          The following is a description of the configuration entries.

               COMn: Port (1-4)  (default=1)

                   Enter the communications port, COMn:, where n = 1 to 4.


               Baud Rate   (automatically set to 4800)

               Data Bits  (automatically set to 8)

               Stop Bits  (automatically set to 2)

               Parity     (automatically set to None)


               Printer Port (1-3)  (default=1)

                    Enter the printer device number 1 to 3.

               Color Monitor  (default is based on installed video adapter)

                    Enter 'Y'es for a color monitor or 'N'o for monochrome.

               Capture Default  (default=OFF)

                    Enter ON to have calls captured to disk while logging.

               Recorder Default  (default=OFF)

                    Enter ON to have calls recorded on the tape recorder.

               Printer Default  (default=OFF)

                    Enter  ON to have the log printed as each call  is  re-
                    ceived.








               AR3000 Version 1.00                         Page 8 - 1

                                System Configuration


               Valid Call Time  (default=0)

                    Enter the time, in hundredths of a second, that a  call
                    must be active in order to be logged.  This option  may
                    be used to filter chop from the log.  The AR-3000 is so
                    sensitive  that frequencys are returned from  calls  of
                    such  a short duration that no audio will be  heard  or
                    recorded.  If you choose to use this option, a value of
                    2 to 4 is recommended.

               Delay Time (default=5)

                    Enter  the time, in seconds, to wait after a call  com-
                    pletes.   When the Delay function is on and a  call  is
                    completed, the program will wait the number of  seconds
                    specified   for 'Delay Time' before moving to the  next
                    frequency.   This function is toggled on and  off  from
                    the Scanner Control screen and Logging.

               Call Wait Time (default=5)

                    Enter the time, in seconds, to wait on an active  call.
                    When  the Wait function is on and a call  is  received,
                    the program will issue a 'down arrow' command after the
                    number of  seconds  specified  for 'Call Wait Time'  if
                    the call has not terminated.  This function is  toggled
                    on and off from the Scanner Control screen and Logging.

               S)eq or A)ll Linking (default=S)

                    S)equential  linking allows groups of contiguous  banks
                    to  be set up for scanning.  For instance, if banks  1,
                    2,  and 3 are linked and banks 5, 6, and 7 are  linked,
                    starting  a  scan in banks 1, 2, or 3 would  result  in
                    banks 1, 2, and 3 being scanned.  Likewise, starting  a
                    scan  in banks 5, 6, or 7 would result in banks  5,  6,
                    and 7 being scanned.  With A)ll linking in effect banks
                    1, 2, 3, 5, 6, and 7 would be scanned.

               Bank File Name (default=AR3000.FRR)

                    Enter  the  Bank  File Name to use  with  the  AR-3000.
                    Multiple  bank files may be created and  maintained  by
                    entering  the the desired file name.  If  configuration
                    is S)aved, see above, the file name entered becomes the
                    default for subsequent sessions.

               Squelch Level (default=1)

                    Enter  the signal strength required to  break  squelch.
                    Any call received with a signal strength less than  the
                    level entered here will be ignored by the software.






               AR3000 Version 1.00                         Page 8 - 2

                                System Configuration


          Notes on communication ports.

               COM1: thru COM4: are supported as follows:

                    Port      Address   Irq

                    COM1:     03F8h     4
                    COM2:     02F8h     3

                    COM3:     03E8h     4
                    COM4:     02E8h     3

                    COM3:     02E8h     4
                    COM4:     02E0h     3

               Since interrupt request lines are shared, only two ports on
               opposite Irq's may be active at any given time.

               The software attempts to find and correctly assign ports  at
               the  addresses given above.  However, the port at 02E8h  may
               not be resolved correctly since it may be assigned to either
               COM3:  or  COM4:.  If COM3: is not assigned  at  03E8h,  and
               COM4:  is  not assigned at 02E0h, then it is  impossible  to
               determine  if  the  port at 02E8h is COM3:  or  COM4:.   The
               software defaults the port to COM4: in this situation.

               You may use a serial port as COM3: at 02E8h by changing  the
               Irq switch on the board to Irq 3, and selecting COM4: in the
               configuration screen.





























               AR3000 Version 1.00                         Page 8 - 3

                        Function and Special Key Assignments

          F1 - Help

          F2 - Re-establish  communications with radio.  Active at most all
               input prompts except in the Logging Screen.

          F3 - Steps the radio to the next bank.

          F5 - Toggles  the  frequency display on and off  in  Logging  and
               Spectra Graph.

          F6 - Change search parameters when using a search bank.

          F7   Toggles  between signal strength and count display modes  in
               Spectra Graph.  (used after sweep/s are completed)

          F10  Exit the current activity

          The following two function keys are only active in the  frequency
          column of Bank and Frequency  Maintenance.

          F4   Delete Frequency

          F8   Selects  the copy option, which is used to import data  from
               the  Banks,  Frequency  Data Base, or Log  File.   Once  the
               screen you are copying from is displayed, use F8 to mark  or
               unmark the entries to be copied.


          Data Entry


          Home           Moves  to the first character of the entry, if  at
                         the  first character, moves the the first  column,
                         if at the first column, moves to the beginning  of
                         the  page, if at the beginning of the page,  moves
                         to  the  beginning of the Bank or  Frequency  Data
                         Base.

          Ctrl+Home      Moves  to the beginning of the Bank  or  Frequency
                         Data Base.

          End            Moves  to  the end of the entry, if  at  the  last
                         character of the entry, moves to the last  column,
                         if  at the last column, moves to the end of  page,
                         if  at the end of  the page, moves to the  end  of
                         the Bank or Frequency Data Base.

          Ctrl+End       Moves  to  the end of the Bank or  Frequency  Data
                         Base.










               Scanner Control System Version 1.00         Page A - 1

                        Function and Special Key Assignments

          Left Arrow     Moves left a character, if at the first  character
                         of the entry, moves left one column.

          Ctrl+Left      Moves left one column.

          Right Arrow    Moves right a character, if at the last  character
                         of the entry, moves right one column.

          Ctrl+Right     Moves right one column.

          Insert         Toggles  the insert/overstrike mode.   Default  is
                         overstrike.

          Delete         Deletes the character under the cursor.

          Backspace      Deletes the character in front of the cursor.

          Up Arrow       Moves to the previous prompt or row.

          Down Arrow     Moves to the next prompt or row.

          PgUp           Moves back a bank or page.

          PgDn           Moves forward a bank or page.

          Alt+C          Clears the current field.

          Alt+E          Clears from the cursor position to end of field.

          Alt+R          Restores the current field.

          Alt+M          Marks the current field for paste/copy.

          Alt+P          Paste/copy to the current field.

























               Scanner Control System Version 1.00         Page A - 2


                          Packing List and Log File Layout


               The following is the list of files supplied on the diskette.

               AR3000.EXE     The Scanner Control System main program.

               INSTALL.EXE    The hard disk installation program.

               AR3000.CFG     The system configuration file.

               AR3000.FRR     The Frequency Bank data file.

               AR3000.FDB     The default Frequency Data Base File.






               Following is the file layout of the exported ASCII log file.


               Position       Length         Description

                 1              5            The serial number of the call.
                 6             11            The received frequency.
                17              2            The modulation type.
                19              2            The attenuator setting.
                21             26            The frequency description.
                47              9            The date received.
                56              9            The time the call started.
                65              9            The time the call ended.
                74              3            The signal strength.
                77              2            The carriage return/linefeed.

























               Scanner Control System Version 1.00         Page B - 1




          Please fill in the following registration form.

          -----------------------------------------------------------------


          Company  ________________________________________________________


          Contact  ________________________________________________________


          Address _________________________________________________________


          City  _______________________  State ____  Zip  _________________


          Phone  ______________________  Serial Number  ___________________


          Signature  __________________________________  Date  ____________

          _________________________________________________________________

          Clip and Mail to:

                            Gesmundo Computing & Design, Inc.
                                10301 E. M89    Suite 303
                                Richland,  MI  49083-9347





























               Scanner Control System Version 1.00         Page C - 1