MPU-401/MT-32 SETUP SAVER v1.2 - by John Barlos - June 1989

 REQUIREMENTS *****************************************************************

	IBM PC/XT/AT or compatible
	MPU-401 MIDI interface or compatible
	MT-32 Sound Module or compatible

 WHAT DOES IT DO? *************************************************************

 MTSS.EXE extracts paramters from the following MT-32 addresses:

	Timbre temp - Parts 1-8         Patch temp - Parts 1-8
	Patch temp  - Rhythm Part       Setup temp - Rhythm Part
	System area - ALL

 11 exclusive messages in all are requested from the MT-32.
 If successfully received, data file will contain 2248 bytes.
 File may later be sent to the MT-32 using 'Quick SEND v2.1' to
 restore saved settings.

 The data received is enough to restore the immediate setup
 of the MT-32. The 64 tone patches in memory group are not saved
 but easily could be, the author of MTSS.EXE does not find it necessary.
 Doing so would increase the size of the data files by 16K.

 FILE CREATION ****************************************************************

 File written to disk will overwrite an existing file with same
 name specification ONLY when user answers "yes" to 'Overwrite (y/n)?'.
 If file name specified already exists on disk in the current
 \PATH\ and MT-32/MIDI communications fails, the file is deleted
 from disk. This will only happen due to USER error (cables not
 connected, MT-32 : OFF, etc...).

 UPDATES **********************************************************************

 ***** Revised v1.1 *****
 Excepts up to 48 char for x:\path\file name.
 User abort successful with keypress while processing.
 ***** Revised v1.2 *****
 User may specify output file name at DOS COMMAND TAIL.
 User timer tick vector (int 1CH) installed to time MT-32/MIDI
 communications response. If MT-32 does not respond 10 sec. after
 1st data request, program is aborted. User may still abort transmission
 with keypress.

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

 DISCLAIMER:
 The author assumes no responsiblity for claimed damages resulting
 from usage of MT-32 SETUP SAVER (MTSS.EXE v1.x).

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

 If you find MT-32 SETUP SAVER to be of ANY use, a donation of $5.00
 or more is requested by the author. Donations assure public release
 of further development from the author, and help fight the high cost of
 commercial software.

 Send $5 donation to:

	John Barlos
	P.O. Box 1118
	Maryland Heights MO.
	63043