SMulator (TM)  (formally 'Overlord')

  by Covox, Inc. - Copyright 1991 - Patents Pending

  Version 0.3á  -- For use with Covox Sound Master II.
                     
  SMulator will allow your Covox Sound Master II, Voice
  Master, and/or the Covox MIDI card to run many pieces 
  of software that do not support Covox products.  
  (Note:  SMulator is not required for Speech Thing and 
  IBM Speech Card emulation).  

  In order to run SMulator, your computer must be a 
  80386SX or above.  SMulator runs as a terminate-and-
  stay-resident (TSR) program.  It captures all sound 
  I/O and redirects it to the appropriate hardware 
  function on the Covox card.  

  This BETA release version currently simulates a
  limited number of applications that are downward-
  compatible with the Sound Master II.  These include 
  the 'Sound Blaster' Card from Creative Labs and the 
  MPU-401 MIDI card from Roland (UART mode only).  
  SMulator does not support 'Sound Blaster' recording 
  or it's compressed file format.  You're better off
  using the Sound Master II for recording and compressing
  sound files.  Other hardware will be simulated as 
  the need arises.

  LIMITATIONS: 

  SMulator is not yet compatible with the Virtual Control 
  Program Interface (or VCPI) standard and therefore will 
  not function with many 386 memory managers such as 
  QEMM.SYS and EMM386.SYS.  Nor will it function with 
  DOS programs that are Dos Protected Mode Interface
  (DPMI) compatible such as SMARTDRV.SYS and HIMEM.SYS. 
  Nor is SMulator compatible with software that accesses
  memory outside of the DOS partition (e.g. most Sierra 
  OnLine and Dynamix games).  A future release of 
  SMulator will overcome these limitations.  Check the 
  Covox BBS for update information (updates are free). 

  With SMulator installed, there is a possibility that 
  your computer might run a bit slower.  We urge you to 
  run SMulator at the fastest clock speed your PC is 
  capable of, especially when emulating the MPU-401.

  This version of SMulator will only work on the factory
  default IRQ, DMA, and port settings.

  --------------------------------------------------------
  QUICK START :

      1. Confirm that the Covox Sound Master II is in your
         computer and configured to the factory defaults.
               
      2. Edit your CONFIG.SYS file and remove XMS, EMS,
         and/or HIMEM.SYS, as well as QEMM.SYS, 386MAX,
         EMM386.SYS, or any other 'protected mode' 
         programs.  Also make certain that all
         drivers are loaded only with the 'DEVICE ='
         command.

      3. Run SM.EXE from the DOS prompt.

      4. From the menu bar select the 'Activate' option
         and the hardware to SMulate (e.g., Sound 
         Blaster or MPU-401).

      5. Run the third-party software.

      6. Reboot your computer to remove from SMulator 
         from memory (not always necessary).

  --------------------------------------------------------
  PROBLEM SOLVING

  If you have problems running SMulator then you should
  first check to make sure you have removed all XMS or
  EMS drivers from your CONFIG.SYS file.  HIMEM.SYS should
  also be removed.  All devices that are loaded in your
  CONFIG.SYS should be loaded only with the 'DEVICE ='
  command.

  If your computer freezes right after SMulator is 
  activated then you should remove all devices from
  your CONFIG.SYS and all TSR's from your 
  AUTOEXEC.BAT file.   Then replace each program one-
  at-a-time until the offending program is found.  
  (We would appreciate knowing all programs that 
  interfere with SMulator.)

  --------------------------------------------------------
  END HELP FILE