Filename: MPUDEMO1.DOC - Description of MPUDEMO1.BAS, MPUDEMO1.EXE

By:   Gino F. Silvestri - CompuServe ID: 71505,1436,  GEnie: SILVESTRI

Date: June 20,1987 14:32:12

While trying to learn to manipulate MIDI data files and communicate with
 MIDI devices, I bought TURBO BASIC, by Borland, as it seemed to be fast
 enough to do the job.  It definitely is!  I probably won't need assembly
 code for programs like MPUDEMO1.  TURBO BASIC ends up having to WAIT for
 the MPU-401 after sending out data - definitely fast enough to keep up
 with MIDI data transmissions.

This BASIC program clearly defines elementary I/O with the MPU-401.

Note that READING ports after a write is usually necessary, so the MPU-401
 knows that data was sent properly.

TURBO BASIC's WAIT command deserves attention.  The statements that use
 WAIT have 3 parameters, for example: WAIT %StatPort,%DRR,%MaskFlip.

WAIT reads the %StatPort I/O port, XOR's the data with %MaskFlip (0FFH),
 and then ANDs it with %DRR (40H).  The XOR is really useful, as I'm waiting
 for the port to go LOW, so the XOR with FF FLIPS the data bits before
 masking for the specific bit being tested.

You might also notice my trick to get BASIC programs to have formatted
 printouts.  I embed a Control-L after a REM Statement where I want a
 Form Feed.  In TURBO BASIC's Editor, you type Control-P to allow entry
 of codes, then type Control-L.  You'll see a light-colored "L" there.

If you're reading this, I presume you've De-Arced it from MPUDEMO1.ARC,
 and that MPUDEMO1.EXE is in your current directory.

To RUN MPUDEMO1, be sure you have a ROLAND MPU-401 connected to a ROLAND
 MPU-IPF card in your IBM (otherwise program will hang up). 

Plug a MIDI synthesizer into your ROLAND MPU-401 MIDI OUT connection,
 make sure the synth is set to receive on MIDI channel 1.  Hopefully,
 the synth is polyphonic, as the second part of the demo plays 3-note 
 chords.  Select a voice with a relatively short sustain, as the scales
 portion of the demo really moves along!

Then just type  MPUDEMO1 and <CR> (Hit RETURN) - MPUDEMO1 will play a
 fast scale from C1 to C6 on your synth, then play some chords.

If you don't have it already, you will want to buy Borland's TURBO BASIC
 so you can load the MPUDEMO1.BAS file, and edit, tinker and compile it.
TURBO BASIC lists at $99.00, but sells at discount for as low as $54.50!
It's really worthwhile.

If you like this, let me know on CompuServe (EMAIL to 71505,1436), or
 MusicForum, MIDI bbs, or on GEnie, username: SILVESTRI.