***** PERFECT.DOC ***** (v 2.2)

              I.   INTRODUCTION:

              PERFECT BOX is a Computer Aided Design (CAD) program for the
         simulation of loudspeaker performance.  PERFECT BOX is a very
         powerful tool for the amateur or professional speaker builder.
              Loudspeaker design is a balance of compromises involving
         enclosure size, low frequency cutoff, and transient response. 
         This program will allow you to model the loudspeaker-enclosure
         combination entirely on your PC.  You are assured of the best
         (lowest in frequency) bass response in the smallest enclosure. 
         You can then build the enclosure with full confidence that the
         final result will not become the new dog house for Fido, but an
         accurate, natural sounding system.
              PERFECT BOX does not deal with midrange or tweeter drivers. 
         It only considers the low frequency driver in a multi-way system
         (or the only driver in a full-range system.)  Since enclosure
         alignments, such as box size, box type, and box frequency  (now on
         refered to as Alignments), effect the woofer response, PERFECT BOX
         models systems covering low frequencies from 10 to 200 Hertz.  The
         mathematical model will hold for higher frequencies, but I have
         optimized the program for the most useful range.

              II.  REQUIREMENTS:

              PERFECT BOX requires certain parameters that uniquely define
         the driver's characteristics.  Some of these parameters have been
         coined as the Thiele/Small (or T/S) parameters.  If you are new to
         loudspeaker design, it isn't important that you understand what
         each value represents, only that you are able to obtain these
         values from the driver manufacturer, or measure them yourself
         (more accurate.)

                PARAMETER                         UNITS
              Free air resonance    (Fs)         Hertz
              Q Electrical          (Qes)
              Q Mechanical          (Qms)
              Q Total               (Qts)
              Volume Equivalent
                   Compliance       (Vas)        Ft^3
              D.C. Voice Coil
                   Resistance       (Re)         Ohms
              Peak Cone
                   Displacement     (Xmax)       Inch
              Effective Piston
                   Diameter                      Inch
              Thermal Power         (P)          Watts, RMS

              NOTE:  Qts=(Qes*Qms)/(Qes+Qms)

              PERFECT BOX allows you to store these driver parameters in a
         data file ("BOXDATA").  This file can store characteristics for up
         to 998 different drivers.  A few sample drivers have been included
         so that you can experiment with PERFECT BOX.  These samples
         represent "real life" units which are currently available at this
         time.

                                 -1-








              III. DEFINITIONS:

              SYSTEM ORDER:  PERFECT BOX uses a classical high-pass filter
         model to simulate a loudspeaker mounted in an enclosure.  The
         order of a loudspeaker system represents the same characteristic
         roll off as that of an electrical filter.  The roll off rate (or
         slope) is:
                        roll off rate=(6 * system order) dB/octave
              or
                        roll off rate=(20 * system order) dB/decade

              PERFECT BOX can simulate both infinite baffle (sealed box),
         and vented (ported) systems.  Each of these systems have a natural
         order in which they resemble an electrical high pass circuit.  For
         infinite baffle, order=2, or that is to say that they are of 2nd
         order.  And for vented systems, order=4.  It seems that each kind
         of enclosure has pros and cons associated with them.  In general,
         both systems, if properly aligned, perform with the same low
         frequency response.  In practice, an infinite baffle system is
         easier to build, and possibly has better transient response.  The
         vented system offers slightly higher efficiency (2.9 dB), and good
         cone dampening near the vent frequency (but less below Fb.)  My
         preference is for 4th and 6th order systems.

              SYSTEM CUTOFF FREQUENCY:  This is the frequency at which the
         system amplitude response is exactly 3.0 dB less than at a
         mid-band reference frequency (where response is basically flat at
         0 dB.)  This is a standard point of interest that can be used to
         compare with another system's low frequency response data.  This
         point represents the "half-power" amplitude, as compared to the
         amplitude at the mid-band reference frequency.

              OTHER ORDERS:  As you are problably aware, a Graphic
         Equalizer can make a tremendous effect on the way your speaker
         system sounds.  The bad news is that an equalizer (EQ) usually
         doesn't have a control exactly centered on the proper frequency to
         properly extend low frequency cutoff, and thus will typically make
         matters worst.
              PERFECT BOX can incorporate the effects of either a 1st or
         2nd order, ACTIVE EQ into the loudspeaker model.  This mini EQ
         consists of a simple active high-pass filter, having a low
         turn-over (cutoff) frequency (typically 20-60 Hz), which actually
         has a slight boost (peak) in its amplitude response above its
         cutoff frequency.  If the amount of boost and cutoff freq. are
         suitably chosen, the total system response typically is extended a
         half-octave or more, while providing infrasonic (rumble) filtering
         to boot!
              In 2nd-order EQ's, the boost is controlled by the "D"
         parameter (D=1/filter Q, for you filter buffs.)  Typical values of
         "D" range from 0.3 to 1.414, giving most to least amount of
         amplitude boost.  A "D" of 0.52 gives approximately 6 dB of boost,
         the most used value.  The EQ frequency and the "D" factor should
         be juggled for the flatest, most extended low frequency response.


                                 -2-










              A word of caution:  using large amounts of boost may tax
         small power amplifiers (less than 50 Watts,RMS) beyond their
         limits.  A properly designed 3, 3.5, 5, or 6th order system will
         not over tax your amplifier unless you listen to music either :  
         1.  at extremely high SPL levels, 2.  with heavy organ pedal
         notes, or 3. use other signal modification equipment such as an
         extremely low-end boosted Graphic Equalizer (Stupid), or Sub-Sonic
         Synthesizer (Harmonizer.)
              The EQ can be inserted into the signal path of your system at
         either a "Pre-amp out/Amp in" loop, or "tape monitor" connection. 
         A simple design for a 2nd order EQ is provided with PERFECT BOX: 
         type EQ2  at the DOS prompt to execute this option.  You must have
         a graphics mode in order to run EQ2 because the electrical
         skematic is drawn on the screen after all the circuit values are
         calculated.  You may execute a screen dump (PrtSc) for a hardcopy
         (as with all screens in PERFECT BOX.)

              IV.  RUNNING PERFECT BOX:

              PROGRAM EXECUTION:  Before you start PERFECT BOX, you must
         execute your DOS command GRAPHICS.COM.  This command sets aside
         memory for doing graphic dumps of your CRT to your graphics
         printer.  I have created a simple batch file called GO.BAT, which
         will do this for you.  Of course you must have either GRAPHICS.COM
         on the program disk or in the current DOS path.  The actual
         program file is BOX2_2.EXE.
              1.  Insert the PERFECT BOX program disk into your default
         disk drive, and type GO <Return>.  You should see the PERFECT BOX
         opening screen.  After about 5 seconds, you may press RETURN to
         continue.  Note:  All questions requiring operator input that have
         default values will have those values prompted between
         parenthesis.  Just press RETURN for the default.
              2.  The next question asks which drive the "BOXDATA" file can
         be found.  Enter the drive letter or simply press RETURN to denote
         the current DOS default drive.
              3.  At this point, you need to choose either ;
                   1.  for Automatic Parameter Entry  or,
                   2.  for Manual Parameter Entry.
              If you choose 1., you can list, reload, edit, or save driver
         parameters using a driver record number.  Option 2. will ask you
         to enter each driver parameter and box characteristic, one at a 
         time.  This choice is good if you only want to run a driver
         through PERFECT BOX once, with out saving the parameters.  Since
         you can store up to 998 different drivers in the data file, I
         rarely use this option!
              Choose "Automatic", and then choose "LIST current Drivers in
         database.  You should see a list of drivers with a record number
         for each.  You may choose a particular driver from this list by
         entering the record number, and then press RETURN.






                                 -3-










              5.  Or, choose "LOAD a Driver by Record Number," and enter
         the record number you had memorized in the "LIST" step above.  The
         model and manufacturer will now appear.  If this wasn't the driver
         that you originally wanted, you can go back by answering "N" to
         the question; "Is this the right driver?"  In this case, press
         RETURN to choose the default of "Y", and the rest of the
         parameters for the driver will appear on the CRT.  Again, you will
         be prompted if these are the right parameters or not.  A "N" will
         take you back to "Enter Driver record number."
              6.  At this point, PERFECT BOX will calculate the "Ideal Box"
         volume, the port frequency for that ideal box volume, and the
         cutoff frequency (-3dB point.)  The ideal box volume is the
         smallest enclosure that provides the flatest, deepest low
         frequency response.  The cutoff point will give you a general idea
         of how low the driver will perform in any box design (best case.) 
         The port frequency (box frequency) must be set as calculated to
         obtain the cutoff predicted.
              7.  Now you must choose the system order.  If the driver Qts
         is 0.5 or greater, I would try infinite baffle (order=2) systems
         first, otherwise, use order=4, with the ideal box size and
         frequency.  Save the other order options for later.  PERFECT BOX
         will also recommend an order to you.
              8.  Enter the box volume in cubic feet.  I suggest that you
         use the ideal box size and box frequency (for 4th order up) as a
         starting point.  Then, on the next pass, change one of the box
         alignments and check how the response was affected.
              9.  PERFECT BOX will now calculate :   1. Amplitude,  2.
         Maximum Power, and 3. Maximum Sound Pressure Level, at each
         frequency cycle between 10 and 200 Hertz.  Then an Output Menu
         will be presented.
              Option 1. will plot the classical Bode (pronounced BO DEE; or
         Frequency Response) plot.
              Option 2, SPL & Power vs. Frequency, will give you an picture
         of the system driven at maximum power.  This plot gives the Sound
         Pressure Level (in dB) and the input power required to reach the
         excursion limit (Xmax) of the driver.
              Option 3. will list on the screen, all calculated data,
         between the frequency limits of your choice.
              Option 4. prints option 3. on your printer with the same
         limit choice.
              Option 5. produces on your printer, a worksheet which gives
         you a handy reference table to use as you change the different
         alignments about your system.  Each block can be filled from data
         printed on the bode plot option.  I suggest that you do this
         option first (only if you have a printer on line.)
              Option 6. (or RETURN) will take you to the Change Menu.  At
         this point you may choose what parameter to change in an attempt
         to optimize the frequency plot, or what ever else you are trying
         to acheive.






                                 -4-










              After you are satisfied with the current design parameters,
         choose "NO CHANGES" in the Change Menu.  PERFECT BOX will now
         calculate the port lengths required to tune the box to the
         frequency last chosen.  A column for two identical length ports is
         given also.  Dual ports are useful when the box volume is large or
         the MACH speed is too large for a single port.  The MACH number is
         the percent of the speed of sound that will occur at the largest
         port output.  Stay away from large (speed> 0.2) port MACH speeds
         as they will cause unmusical whistle noises from the port.  Also,
         ports that are longer than the box depth, can be curved inside the
         enclosure with PVC swept elbows.

              V.   DESIGN HINTS:

                If the ideal box volume is too large to be realistically
         built, PERFECT BOX will allow you to see just how the loudspeaker
         performance will suffer, as you down size box volume.  It is this
         iterative design process that PERFECT BOX is designed for.  By
         changing either box volume, port frequency, or in EQ cases, EQ
         frequency and boost, a "perfect" frequency curve can be obtained. 
           At this point you can tell how good a driver really is because
         sometimes another driver will out perform others in half the
         enclosure volume!
              The port frequency is set by the area and length of the port.
         PERFECT BOX will calculate the port for you, but the length is
         typically 10-15% off, so add an inch to the calculated value, and
         measure it yourself (or have a friend do it.)  The system will not
         perform as calculated if you miss the port frequency by as little
         as 1 Hz.  Also, after you have reached a final box size, increase
         the box volume by as much as 20% to account for volume used by the
         drivers, bracing, and crossover network.
              To find box diminsions from the box volume, take the volume
         in cubic feet, multiply by 1728 cubic in/ft^3, to get in^3.  Then
         take the cube root (or raise it to the 0.3333334 th power.)  Now
         this number is the width in inches.  Multiply the width by 1.62
         for the height, and multiply the width by 0.62 for the depth.
                   volume (ft^3) * 1728 = volume (in^3)
                   width  (in.)   =   (volume (in^3))^0.3333334
                   height (in.)   =   width * 1.62
                   depth  (in.)  =   width * 0.62
              NOTE: All diminsions are internal, not external!
              This will give the box a "typical speaker look" and also set
         the diminsions up for minimum internal reflections.  PERFECT BOX
         calculates these diminsions for you and prints them in the port
         length table.










                                 -5-










              VI.  REFERENCES:

              This document and the program PERFECT BOX are only tools for
         the speaker designer.  One must know how to use these tools
         properly before judging the usefulness of PERFECT BOX.  I suggest
         that you read any of the following publications on the finer art
         of speaker building.

                     SPEAKER BUILDER MAGAZINE (6 times a year)
                      Edward T. Dell, Jr., Publisher
                      PO Box 494
                      Peterborough, NH 03458

                     "The Loudspeaker Design Cookbook"
                      by Vance Dickason
                      Distributed by:
                      Old Colony Sound Lab
                      PO Box 243
                      Peterborough, NH 03458-0243

                     "How to Design, Build, & Test Complete
                      Speaker Systems"
                      by David B. Weems
                      Library of Congress # TK9968.W43
                      Published by:
                      TAB Books
                      Blue Ridge Summit, PA  17214
                      No. 1064

              VII. VERSION 2.3 ADDITIONS:

              The latest version of PERFECT BOX, v2.3, adds the following
         options to the previous versions.

              1.   The ability to change the path to the boxdata file. 
         This allows you to have multiple boxdata files, each in separate
         subdirectory, or disk.  The current path is now displayed at the
         opening menu.  The default DOS path is the initial drive path.

              2.   The ability to save the current alignment (box volume,
         box frequency, order, EQ frequency, and D,) to the BOXDATA file.  
         This allows you to save your favorite box alignment for each
         driver.  You may also load previously saved parameters for a
         starting point on a new design.

              3.  Dual driver systems are now handled.  You may now choose
         from three different configurations in series or parallel:
                Standard --Drivers side-by-side, sharing the same box.
                Push-Pull--Same box, mounted back-to-back or               
                           front-to-front, wired out of phase.
                Isobaric (constant pressure) systems--Drivers close-coupled
                           by a small air-tight tunnel.
              See "The Loudspeaker Design Cookbook" for more information on
         these variations in system design.

                                 -6-










              4.   A BOXDATA file print option which makes a complete
         hardcopy of the current BOXDATA file drivers, including all
         parameters.

              5.   Maximum SPL and minimum power values above 20 Hz. are
         denoted on the Excursion limit plot, for quick reference.  Also
         these values are helpful when designing dual-driver or very heavy
         power rated systems.

              6.   One of the prompts in the LOAD driver sequence has been
         deleted to speed up the process of parameter loading.

              VIII.  ERRATA:

              PERFECT BOX is under constant scrutany for improvement.  If
         you have any ideas for new features/functions, send them to me at
         AUSTIN ACOUSTICS.  Your suggestion could be included in the next
         revision of PERFECT BOX, of which you will recieve the first copy!
              By registering your copy, you will be notified of major
         PERFECT BOX revisions, with new BOXDATA file parameters.  If
         you send a disk, I will update to the present version, and append any
         BOXDATA parameters I have recieved from others to your disk.  Please
         send a COPY of your PERFECT BOX program disk (5.25 or 3.5) in a U.S.
         Post Office approved disk envelope, and $40 (US) (or $51 for
         Overnight Express Return.) Or, just send $40 (US) to me for program
         registration instructions. 
              Please note that a registered user will not have to see the
         annoying "Please Register" boxes that are sprinkled throughout the
         program.  But this doesn't mean that the un-registered copy is
         "crippled" in any way, because it isn't.  All PERFECT BOX
         functions are available on the un-registered program.

              Please make checks payable to:

                             WARREN MERKEL 
                             9874 LANCEWOOD STREET
                             ORLANDO, FL  32817-4251

            12/87            *** End of Document ***
















                                 -7-