------------------------------------------------------------------------------

Initialization routine
----------------------

Declaration:

short pascal far PVOICE_INIT(void)


This must be called once before any of the other routines are called. It hooks
the interrupt service routine into the timer tick interrupt vector.


Return value        Meaning
------------        -------
     0              success
     1              voice package already initialized
     2              wrong CPU, won't run on 8088 or 8086

NOTE:  PVOICE_INIT installs a Control-Break (Int 23h) handler which makes sure
       that the 8253 timer chip and the timer tick vector are restored to
       their original state before program termination. If your program
       installs its own Int 23h handler, then (a) It should be done after
       the call to PVOICE_INIT, and (b) It must call PVOICE_CBREAK before it
       allows the program to terminate. Failure to do this will result in
       a system crash.


------------------------------------------------------------------------------

Cleanup routine
---------------

Declaration:

short pascal far PVOICE_CLEANUP(void)


This restores the timer tick interrupt vector to its previous state. This
routine must be called before the main program exits to DOS, unless the main
program is memory-resident.


Return value        Meaning
------------        -------
     0              success
     1              voice package was not in the initialized state



------------------------------------------------------------------------------

Start routine
-------------

Declaration:

short pascal far PVOICE_START(blockaddr,blocklen,
                              fileread,handle,datalen,startpos)
unsigned char far *blockaddr;
long blocklen;
unsigned short fileread;
unsigned short handle;
long datalen;
long startpos;


This call initiates a voice output operation. It returns to the caller
immediately. Voice output will continue asynchronously (background).


Parameter   Size   Description
---------   ----   -----------
blockaddr     4    A far pointer to the memory block used for voice data.
blocklen      4    A dword indicating the length of the memory block.
fileread      2    A flag word. If this is 1, then data will be read from
                    a file. If it is 0, then the data is assumed to be
                    already present in the memory block.
handle        2    An open file handle. This is ignored if the flag word
                    is 0.
datalen       4    A dword indicating the number of bytes of voice data
                    to be played. If the flag word is 0, then this number
                    must not be greater than the length of the memory
                    block.
startpos      4    A dword indicating the offset within the memory block
                    where playback is to begin. This value must be less
                    than blocklen.

Return value        Meaning
------------        -------
     0              success
     1              data length greater than block size but no file read
     2              block size is too small (datalength > blocksize and
                     blocklen < 8192 and file read = yes)
     3              unable to read from file
     4              voice playback is already in progress
     5              startpos is not less than blocklen



------------------------------------------------------------------------------

Catch-up routine
----------------

Declaration:

short pascal far PVOICE_CATCHUP(void)


This must be called frequently from the main program if file reading is being
used and the length of the data to be played is longer than the length of the
memory block. The routine checks the progress of the address pointer in use
by the interrupt service routine and fills in more data from the file if
necessary.


Return value        Meaning
------------        -------
     0              success
     1              error while reading file


------------------------------------------------------------------------------

Stop routine
------------

Declaration:

void pascal far PVOICE_STOP(void)


Calling this will terminate the voice output operations immediately, before
the end of output would have normally occurred. It is not necessary to call
this routine unless it is desired to terminate voice output before the
specified number of data bytes have been played.



------------------------------------------------------------------------------

Status routine
--------------

Declaration:

short pascal far PVOICE_STATUS(pcount,pindex)
long far *pcount;
long far *pindex;


This will report the status of voice operations, including whether the
output operation has completed, whether all the necessary data has been
read from the file, and the current count of data bytes played.


The first parameter is a far pointer to a dword which will receive the number
of bytes which have already been output to the speaker.

The second parameter is a far pointer to a dword which will receive the
offset within the memory block of the next byte of data to be played.


The return value is a flag word in which the lowest two bits are
significant:

Bit #      Meaning if 1
-----      ------------
  0        playback is still in progress
  1        unread data remains in file