QRT Users Manual
        
        
        INTRODUCTION
        
        QRT (Quick Ray Tracer) is an easy  to use image generation system
        that uses a ray tracing algorithm  for image rendering.  Versions
        exist for the Amiga personal  computer  and Data General MV10000.
        QRT overcomes many of the problems of other ray tracing packages,
        and is designed to operate nicely in a multi-tasking environment.
        
        
        COMPARISON TO OTHER SYSTEMS
        
        QRT was developed on the Amiga  personal  computer, so it will be
        compared to other Amiga ray tracers.  There are, to my knowledge,
        five other Amiga ray  tracers,  each  with  its own strengths and
        weaknesses.  I will describe each  system briefly, and compare it
        to QRT.  All the  Amiga  ray  tracers  can  operate  in HAM (4096
        color) mode.
        
           RT: RT was the first ray tracer written for the Amiga, by Eric
               Graham.  It will model a universe  made of only spheres, a
               sky, and a checkered or  solid  ground.   It is relatively
               fast, but not  generally  useful  for  realistic  modeling
               because of the sphere  limitation.   The input language is
               cryptic, although some error checking is done.  The system
               will only generate low resolution images.
        
          SILVER: I have never seen  SILVER,  so  I cannot say much about
               this system.
        
          SCULPT-3D: This package incorporates  an interactive editor for
               creating objects, and is  capable  of quickly generating a
               preliminary image of  the  scene  by  using hidden surface
               techniques.  However, every primitive is made of polygons,
               and some primitives such as  spheres  require  hundreds of
               polygons for a smooth texture,  so the ray tracing is very
               slow.  Also, the package takes a large amount of memory to
               run, and is prone to system crashes.  Its chief feature is
               the ability to  create  arbitrary  shaped  objects using a
               series of triangles.  Mirrored, dull, or shiny objects are
               supported.
        
          CLIGHT: This ray tracer  also  has  an  interactive editor, but
               produces very poor quality  images.   It is not capable of
               any patterning or reflection characteristics.
        



        QRT Ray Tracer               Page 1                   User Manual












          DBW: This is possibly the  most  complete  ray  tracer  for the
               Amiga.  It will support objects  with arbitrary degrees of
               reflection  and  gloss,   depth  of  field  effects,  some
               texturing, wavy surfaces, fractals,  transparent surfaces,
               diffuse propagation of light from  object to object, and 5
               primitive types (sphere, triangle, parallelogram, fractal,
               and ring).  The input language,  however, is so cryptic as
               to be nearly  incomprehensible,  and if there is any error
               in the input file, it will  crash  the system.  It is also
               painfully  slow;  some  images  take  16  to  24  hours to
               complete.
        
        QRT is meant to be  a  compromise  between  the  fast, simple ray
        tracers and the slow powerful systems.   It compares favorably in
        speed to RT, and in power  to  Sculpt-3d  or  DBW.  It has a very
        friendly input language with extensive  error checking.  Here are
        some features of QRT:
        
            o  Multiple primitive types, including user defined quadratic
               surfaces
        
            o  Arbitrary   levels   of   diffuse   reflection,   spectral
               reflection, transmission, ambient lighting, and gloss
        
            o  User defined pattern information for objects
        
            o  Bounding boxes for groups of objects
        
            o  Shadows
        
            o  Multiple light sources with different characteristics
        
            o  Arbitrary Phong spectral reflection coefficients
        
            o  Color dithering to increase the apparent number of colors
        
            o  Easy  to  use,  free  format  input  language  with  error
               checking.  Parameters are by keyword and may appear in any
               order.
        
            o  Supports medium resolution (128k dots/screen)
        
        Each of these features of QRT will be discussed is greater detail
        in this document.
        
        
        
        THE QRT WORLD
        
        QRT constructs an  image  of  the  world  by  performing  certain
        manipulations  on  an  internal  representation  of  a  group  of


        QRT Ray Tracer               Page 2                   User Manual












        objects.  You must provide a description  of these objects to QRT
        through the QRT input language.
        
        QRT writes a machine independent bitmap file which can be read by 
        a computer specific post  processor.   The  post processor either
        displays the  image  or  converts  it  into  the  proper form for
        display  by  system   programs.     (See  the  Machine  Dependent
        Information section of this manual for details).
        
        QRT is capable of dealing  with  5  types  of  primitive objects:
        spheres,   parallelograms,   triangles,   rings   (annulus),  and
        quadratic  surfaces.   The  latter  can  be  used to model cones,
        oblong spheroids, and other interesting  surfaces.  Each of these
        objects can have an arbitrary orientation in space, and arbitrary
        surface characteristics.
        
        
        
        QRT INPUT LANGUAGE
        
        The QRT input language is free  format,  in  that commands may be
        placed anywhere on a line,  and  newlines  may  be  placed at any
        point.  This makes it easy to use indentation.  Comments are also
        supported by surrounding  text  with  curly  braces  '{' and '}'.
        Comments may span lines.
        
        Once a file with QRT commands is built  (using any available text
        editor), qrt can be made to process these commands:
        
            QRT <commands.qrt
        
        where "commands.qrt" is the file containing  the input.  QRT also
        produces some statistics, so this  output can also be redirected.
        Since QRT runs for a long time, you  will probably want to run it
        as a background task with a low  priority.   So,  the full set of
        commands to run QRT would be:
        
            SetTaskPriority -5
            run QRT <commands.qrt >qrt.out
            SetTaskPriority 0
        
        This set of commands is specific to  the Commodore Amiga; see the
        Machine Dependent  Information  section  of  the manual for other
        operating systems.
        
        QRT will write a very large file, which may be anywhere from 400K 
        to  4  megabytes  depending  on  the  specific  computer  display
        resolution.  (See the Machine  Dependent  Information  section of
        this manual for the exact file  size).   There should be at least
        enough room on your disk to  accommodate  this  file. I recommend
        sending the output to a RAM disk,  so that the physical disk does


        QRT Ray Tracer               Page 3                   User Manual












        not get used for 60 minutes while QRT computes the image.
        
        A typical QRT  command  to  create  a  sphere  using  the default
        surface attributes would, be:
        
            SPHERE ( loc = (5,10,100)     { this is a white sphere }
                     radius = 12.5
                   )
        
        For comparison, the sphere command for DBW looks like this:
        
            s 0 0 0 1 0 0 0 .2 .2 .2 .8 .8 .8 5 10 100 12.5
        
        Or, in RT, the command would be:
        
            <1,1,1> 2 (5,10,100):1;
        
        The QRT input should be much  easier  to understand.  If QRT sees
        an error in its  input  file,  it  will  stop  and print the line
        number of the offending  line,  along  with  a  descriptive error
        message (ILLEGAL PARAMETER, etc).
        
        The QRT input language is not case sensitive.  A full description
        of the language and a shorter, context  free grammar can be found
        elsewhere in this manual.
        
        
        
        THE QRT ILLUMINATION MODEL
        
        Before meaningful images  can  be  created,  the QRT illumination
        model must be understood.  The  light  that  reaches the observer
        from each object is composed of several components:
        
           o  Diffuse light      - The "color" of the object
        
           o  Ambient light      - The color of the light that falls on
                                   the surface of the object if no lamps
                                   are shining on this spot.  Note that
                                   this specifies the color of light, not
                                   the color of the object itself.
        
           o  Reflected light    - If the object acts as a mirror, some
                                   light is reflected.
        
           o  Specular highlights - The "bright spots" of a shiny object
                                   viewed in a light.
        
           o  Transmitted light  - The object may transmit some of the
                                   light that strikes the back of the
                                   object (glass surfaces)


        QRT Ray Tracer               Page 4                   User Manual












        
        All of  these  light  characteristics  can  be  specified for any
        object.  If none are specified, the current defaults are assumed.
        These defaults can be changed (see  DEFAULT in Language Reference
        Guide).
        
        Most of these  light  characteristics  deal  with a percentage of
        light.  For example, a  light  may  reflect  80% of the red light
        that strikes it, 20% of the green,  and 40% of the blue.  This is
        the "color" of the object (diffuse light), and would be specified
        in QRT by the following syntax:
        
                      diff = (.80, .20, .40)
        
        In QRT, 1.00 is 100%.  The  language  is also free-format, so the
        above is equivalent to:
        
                      diff = (.80,
                              .20,
                              .40 )
        
        The commas between parameters  are  optional,  but make the input
        easier to read.  Semicolons can also be used.
        
        Ambient light is specified in a similar manner:
        
                      amb = (.20, .20, .20)
        
        The ambient light  values  should  be  fairly small.  Most of the
        light hitting the object comes from  lamps, but some parts of the
        object may be in the shadow  of  another  object.   If no ambient
        light is specified,  these  shadows  will  appear  totally black,
        which looks unrealistic.  Ambient light will give the affect of a
        small amount of light hitting areas in a shadow, producing a more
        realistic looking image.
        
        Reflection is specified using the MIRROR attribute:
        
                      mirror = (.90, .90, .90)
        
        If a true mirrored surface is  desired,  the mirror values should
        be fairly high.  If one of the values has a higher value than the
        others, the mirror will appear red, green, or blue.
        
        Transmission is specified as follows:
        
                      trans = (.80, .80, .80)
                      index = 120
        
        Note the addition of another parameter,  the index of refraction.
        An explanation of the index of refraction for an object is beyond


        QRT Ray Tracer               Page 5                   User Manual












        the scope of this document - see a  book on elementary optics for
        details.
        
        In  addition,   specular   highlights   are  specified  with  two
        parameters:
        
                      reflect  = .50,
                      sreflect = 45
        
        "REFLECT" is the percentage of  light  reflected  in the specular
        highlight,  and  sreflect   is   the  Phong  spectral  reflection
        coefficient.  Again, an  explanation  of the Phong coefficient is
        beyond the scope of this  document;  however,  a higher value for
        the coefficient will result in smaller,  tighter highlights for a
        more metallic looking object.  Lower values of sreflect should be
        accompanied by lower values in  reflect,  and will produce duller
        looking surfaces, such as paper.
        
        QRT also accepts a dithering amount for each object:
        
                      dither = 3
        
        Dithering is a mechanism for  simulating  colors not available on
        the display by blending  other  colors.   The  default  dithering
        coefficient is 3; it should be kept  small.  Values of 1 to 6 are
        good.  Larger objects should employ  more dithering, and mirrored
        or glass objects should have little or no dithering.
        
        QRT also accepts an attribute "FUZZ", but this is not used in the
        present implementation.  In a future  implementation of QRT, FUZZ
        will effect small, random perturbations of the normal vector at a
        given location on an object.  This  will simulate rough surfaces,
        matted glass, or imperfectly reflecting mirrors.
        
        All of the above  light  characteristics  may  be attached to any
        object.   The  default  is  for  a  white,  non  reflecting,  non
        transmitting dull surface with an average amount of dithering. In
        addition, any of  the  above  color  information  (which  will be
        referred to from now on as  COLORINFO)  may also be attached to a
        pattern structure (see the PATTERN section of this document).
        
        
        
        LIGHT SOURCES
        
        Light sources in QRT are called  "LAMPS".   The lamp structure is
        simple:
        
                     LAMP ( loc = (12, 34, 56),
                            dist = 50,
                            radius = 10 )


        QRT Ray Tracer               Page 6                   User Manual












        
        The default is for a bright white lamp, but if you wish to change
        this, you can  specify  different  values  for the lamp's ambient
        light.  The radius value  is  ignored  by  this implementation of
        QRT, but it must be supplied.   In  a  future version, the radius
        may be used to  implement  penumbral  shadows.   I didn't include
        them in  this  version,  since  they  take  a  very  long time to
        compute, and don't add much to the image quality.
        
        The "dist" entry in the lamp structure specifies at what distance
        the light from the lamp is at full intensity.  Beyond this value,
        the light will decrease in  intensity.   This value should be set
        so that the nearest object  in  the  scene  is slightly more than
        "dist" distance units from the  lamp.   This  does not have to be
        exact. If objects are nearer  than  dist"  units, they will be so
        bright that shading will not  take  place.  Objects very far away
        will be dimly illuminated.
        
        By the way, QRT distance  units  are  not  tied to any real world
        unit.  They can stand for feet,  nautical  miles, or furlongs, at
        your choice.
        
        
        
        THE OBSERVER
        
        After defining the world,  you  must  tell  QRT  the position and
        orientation of the observer.  This is done as follows:
        
                 OBSERVER ( loc     = (0, 10,  20),
                            lookat  = (5,  5, 120),
                            up      = (0,  1,   0)
                          )
        
        The x,y, and z are the location  of  the  observer.  The "lookat"
        variables give a location in  space  that the observer is looking
        at.  Most ray tracers  require  you  to  give  two angles for the
        observers view  direction,  but  it  is  MUCH  easier to know the
        location of an object or point in  space you wish the observer to
        look at.  This will be the center of your scene.
        
        The "up" variables define which  direction  is  up.  Usually, you
        will wish to use the values  given  above.  QRT uses a right hand
        coordinate system: positive  y  is  up,  positive z is out of the
        screen, and positive x is to the right  if you are looking in the
        negative z direction.   The  "up"  parameter  is optional, and if
        omitted, defaults to (0,1,0).
        
        QRT will generate an error message if no observer is defined.
        
        


        QRT Ray Tracer               Page 7                   User Manual












        
        OUTPUT FILENAME
        
        QRT places its output in a file, so  you must give it the name of
        this file:
        
                      FILE_NAME = outfile.tmp
        
        This file must  observe  any  file  naming  restrictions  of  the
        operating system and  computer  you  are  using.  See the Machine
        Dependent Information section  of  this manual for information on
        file naming restrictions.
        
        
        
        FOCAL LENGTH
        
        This is the focal length  of  the  "lens"  used  by the observer.
        Think of it as a 35mm  camera  lens  -  higher  numbers produce a
        telephoto effect, and smaller numbers  are for wide angle lenses.
        Note that small numbers may produce some distortion of the  image
        around the edges.
        
                      FOC_LENGTH = 60
        
        
        
        SCAN RANGE
        
        If you do not want QRT to produce  a whole image, you can specify
        the first and last scan  lines.    The  parameters should be less
        than the maximum Y resolution of your display.
        
                      FIRST_SCAN = 100
                      LAST_SCAN  = 300
        
        This is useful for quickly generating part of an image.
        
        
        
        SKY AND GROUND
        
        QRT has facilities for generating  the sky and ground.  To define
        the sky, you must give it two  colors  - one for the sky overhead
        (zenith), and one for the horizon:
        
                      SKY ( zenith  = (.10, .2, .4),
                            horiz   = (.10, .2, .65),
                            dither   = 6
                      )
        


        QRT Ray Tracer               Page 8                   User Manual












        This will produce a blue  sky,  with  a  brighter  color near the
        horizon.  (The sky need not  be  blue  -  it  could be red or hot
        pink, or vary from red to  green).   QRT  will smoothly blend the
        colors from the zenith  to  the  horizon.   Since  the  sky is so
        large, you may want to specify  a  greater amount of dithering to
        compensate for the displays color resolution limit.
        
        The SKY structure will also produce sky colors below the horizon;
        any ray that does not strike an  object  will strike the SKY.  To
        fix this, define a ground.  There is no dedicated GROUND command,
        since you can define a  very  large  parallelogram  with the same
        effect.  You can make it  brown  with  patches  of  green using a
        PATTERN, or checkered green and yellow in the classic ray-tracing
        ground pattern.
        
        
        
        BOUNDING BOXES
        
        QRT supports the use of  bounding  boxes to speed the ray tracing
        process.  For images  composed  of  only  a few (1 to 3) objects,
        bounding boxes will not do much to  increase speed.  However, for
        images where there are groups of objects physically close to each
        other, they can greatly reduce  execution  times.  A bounding box
        is a conceptual structure that encloses a group of objects.  When
        the ray tracer is finding  line/object  intersections,  if a line
        does not strike a  bounding  box,  it  cannot possibly strike any
        objects within that bounding box.   This saves the ray tracer the
        trouble of  checking  intersections  with  all objects within the
        box.  In the  case  where  the  ray  DOES  enter  the  box,  some
        additional overhead  is  incurred;  however,  this cost is easily
        justified by reduced times for negative tests.
        
        Bounding boxes can occasionally  be  useful  for complex objects,
        such as quadratic  surfaces,  when  the  object  is fairly small.
        Since the time to find the intersection  with a quadratic surface
        is large, but bounding box intersections are fast, the ray tracer
        can save time for all the negative tests.
        














        QRT Ray Tracer               Page 9                   User Manual












        Bounding boxes can contain  other  bounding boxes, in a recursive
        manner.  This recursive structure defines an "object tree". There
        are two keywords that define the beginning  and end of a bounding
        box: BEGIN_BBOX and END_BBOX.  Here is an example:
        
        
            { ** QRT Code for a chessman ** }
        
            BEGIN_BBOX
        
                QUADRATIC (  { ** quadr defn ** }
                          )
        
                QUADRATIC (  { ** quadr defn 2 ** }
                          )
        
                SPHERE    (  { ** sphere defn ** }
                          )
        
                BEGIN_BBOX
        
                    SPHERE ( )    { ** two spheres ** }
                    SPHERE ( )
        
                END_BBOX
        
            END_BBOX
        
        This structure may be nested to an  arbitrary level; if you had a
        closely spaced group of  chessmen,  you could enclose all of them
        with a bounding box.
        
        
        
        PATTERNS
        
        QRT permits user  defined  patterns  which  can  be mapped to the
        surface of any  object.   A  pattern  is  basically  an organized
        method for changing  an  object's  COLORINFO  over the surface of
        that object.  For example, a checkered surface can be created, or
        a surface given the  appearance  of  brick  or tile.  The current
        patterning in QRT is  limited,  yet  powerful  enough to describe
        many common patterns.
        
        A  pattern  is  composed  of  a  series  of  sub-patterns.   Each
        sub-pattern defines a region on  the  surface  of an object which
        will contain a  given  COLORINFO.   These  regions  are presently
        limited to  rectangles,  but  this  may  be  expanded in a future
        implementation of QRT.
        



        QRT Ray Tracer               Page 10                  User Manual












        A pattern can be defined once,  and  used  for many objects.  For
        example, a brick pattern might be defined:
        
                  PATTERN ( name = BRICK,
                            { ** other pattern info here ** }
                          )
        
                  SPHERE  ( { ** sphere definition ** }
                            pattern = BRICK
                          )
        
                  PARALLELOGRAM ( { ** parallelogram definition ** }
                                  pattern = BRICK
                                )
        
        This example ignores what is  actually  in the pattern definition
        to demonstrate how patterns are  attached  to objects.  A pattern
        must be defined before it can be used.   It is given a name, such
        as BRICK, and any object can specify this pattern with "PATTERN =
        BRICK".  There are  no  practical  restrictions  on the length of
        pattern names (if your computer has 1 megabyte of ram, you cannot
        have a pattern name longer than 1  million characters).  Multiple
        patterns may be defined at the top of an input file, and used for
        any object in the file.
        
        What exactly makes  up  a  pattern,  you  ask?   A pattern can be
        viewed as a rectangle that  is  repeated  over  the surface of an
        object.  If the pattern size is  10  x 10, and you have an object
        (say a parallelogram) that is 50 x  50, the pattern will repeat 5
        times in each direction.   Within  this  repeating rectangle, sub
        patterns can be defined.  A sub-pattern  is a rectangle or circle
        within the pattern rectangle with a certain COLORINFO. Any number
        of  these  sub-patterns   can   be  created  within  one  pattern
        definition. To create a  brick  wall,  you  might  define several
        sub-patterns, each with  a  slightly  different  color  of red or
        brown.  The sub  patterns  need  not  cover  the  entire  pattern
        rectangle; if they do not,  the  COLORINFO  you  defined  for the
        object is used instead of the pattern  COLORINFO.  If you defined
        sub-patterns for bricks, the  area  not  covered would be mortar,
        and the objects COLORINFO would  define  the color of the mortar.
        An actual brick pattern is  given  in appendix C.  The proper use
        of patterns can be very effective  in producing realistic looking
        scenes.  However, complicated patterns  will slow image creation,
        so it is recommended that you  first  display test scenes with no
        patterns, and then add  pattern  information  when  the  scene is
        right.
        






        QRT Ray Tracer               Page 11                  User Manual












        INSTANCES
        
        Often, several copies  of  a  complex  object  must  be  created.
        Specifying  their  component   primitives   each  time  would  be
        difficult. There is a solution to both these problems: INSTANCES.
        An INSTANCE is a method by which several primitives (actually, an
        arbitrary object tree) can be  grouped  and given a name.  Copies
        of these objects may be easily created with one command.  Here is
        an example of an instance definition.
        
                BEGIN_INSTANCES
        
                    NAME = object1
                    BEGIN_BBOX
                        { ** a bunch of primitives here ** }
                    END_BBOX
        
                    NAME = object2
                    BEGIN_BBOX
                        { ** a bunch more primitives  here ** }
        
                        NAME = spheres
                        BEGIN_BBOX
                          SPHERE ( )  { ** two sphere definitions ** }
                          SPHERE ( )
                        END_BBOX
        
                    END_BBOX
        
                END_INSTANCES
        
        There can be only one of these instance  definitions, and it must
        appear before any  instances  are  used.   However, any arbitrary
        object tree can appear within the  begin/end instance statements.
        Several instances are now available for use.  For example:
        
                INSTANCE_OF (  name = object1,
                               loc  = (100, 10, 20),
                            )
        
                INSTANCE_OF (  name = spheres,
                               loc  = (12.3, 24.5, 999)
                            )
        
        This example shows that any  named  portion of the object subtree
        can function as an instance  (the  "spheres" object is at a lower
        level than the "object1'  object).   The  "offset" parameters are
        required.  They specify a new  position  for the instance (offset
        from the  origin).   In  the  instance  definition  segment,  all
        objects are defined relative to 0,0,0.  They can then be moved in
        the INSTANCE_OF statement with the offset command.


        QRT Ray Tracer               Page 12                  User Manual












        
        In addition, the instance can be given a new size:
        
                INSTANCE_OF (  name    = object2,
        
                               loc     = (200, 100, 50),
                               scale   = (1.5, 2.0, .25)
                            )
        
        The scale factors are optional,  and  are given the default of 1.
        The instance will be resized by  the  indicated amount in each of
        the directions.  Note that  there  are some restrictions to this:
        if spheres are given a different scale  factor in each direction,
        they will remain spheres (not  change  to  QUADRATIC types).  The
        new radius will be the old  radius  scaled by the smallest of the
        scale factors.
        
        
        
        DEFAULTS
        
        Each object  in  QRT  is  given  certain  default  surface  light
        characteristics (see the section on surface characteristics).  If
        these defaults are  not  suitable,  they  can be changed with the
        DEFAULT command:
        
                DEFAULT ( diff = (1.00, .1, .1)
                          no_shadow )
        
        This will make all future objects red unless specified otherwise.
        More than one default  command  can  be  used in a file: each one
        affects all the  objects  created  after  it, but before the next
        default  command.   Any  light  characteristics  can  be  changed
        (MIRROR, DITHER, etc).
        
        In addition, the keyword "no_shadow"  can be included (as above).
        Ordinarily, QRT computes shadow information for all objects. This
        takes a lot  of  time,  especially  for  scenes  composed of many
        objects and many lamps.  The  "no_shadow"  command  causes QRT to
        bypass the shadow routines.   This  will  result in a much faster
        image  generation  time,   but  the  picture  will  not  look  as
        realistic.
        










        QRT Ray Tracer               Page 13                  User Manual












        PROBLEMS WITH QRT
        
        There are several limitations in this version of QRT:
        
            o  Patterning  does  not   work   well  with  some  quadratic
               surfaces.  This is  a  problem  with  the 3d to 2d mapping
               function used for quadratics.
        
            o  Patterns  do  not   support   circular  or  non-orthogonal
               rectangular   sub-patterns.   This   would   slow  pattern
               processing        but increase the utility of patterns.
        
            o  User defined texturing is not implemented - all objects in
               QRT appear  smooth.   I  have  some  ideas  on  how to add
               textures to objects, but  these  have  not been tested and
               are not incorporated into this version of QRT.
        
            o  Some rounded objects such as  spheres  appear distorted if
               they are near the edge of the image.  This is a bug in the
               routine that creates a ray for a given pixel position.
        
        
        
        FUTURE ENHANCEMENTS TO QRT
        
        The following are some things I'd like to add to QRT:
        
            o  Enhanced  patterning   capability.    This  could  include
               arbitrary polygonal  patterns,  and non-orthogonal shapes.
               Also, the ability to use enumerated  (bit-mapped) patterns
               as well as analytic patterns would be useful.
        
            o  Anti-dithering   routines.     These  routines   are  very
               computationally   expensive   (they   can  increase  image
               generation times by a factor of  3 to 5), so they were not
               included in this version.
        
            o  Penumbral shadows.   This  is  also  very  computationally
               expensive for a minimal utility  level, so I didn't bother
               to include this feature.
        
            o  Fractal generation.  Fractals are,  again, computationally
               expensive, but some things,  such  as mountains, cannot be
               modeled with a ray tracer any other way.
        
            o  Wavy surfaces.  This is useful for modeling water, rippled
               mirrors, etc.  I know  how  to  do  it, I just didn't have
               time to add it yet.  It  would  be  nice if the waves were
               user definable in amplitude and  x and y wavelength.  Wavy
               surfaces are very similar in implementation to textures.
        


        QRT Ray Tracer               Page 14                  User Manual












            o  Snowy surfaces.  This is an idea from DBW, which adds snow
               to a surface depending on its slope and altitude.
        
            o  Interpolated  normal  surfaces.   This  is  a mechanism to
               model  arbitrary  curved  surfaces  by  using  a polygonal
               approximation to the surface, and interpolating the normal
               vector between surfaces to avoid angular looking surfaces.
        
            o  Image  plane  object  lists.    This  is  a  technique for
               increasing the speed for positive line/object intersection
               test.  (Bounding  boxes   increase   speed   for  negative
               line/object intersection tests). 
        
            o  Heuristics for  faster  completion  of  images  using area
               coherence.
        
            o  An  interactive  editor.   This  is  another  large  scale
               project in itself, and I can't forsee having time to do it
               for a long time, but it would be useful.  The editor would
               display a preliminary  image  of  the  scene, and when the
               user had placed objects  to  his  satisfaction,  it  would
               write a QRT input file and call  QRT as a background task.
               There are certain problems here - for instance, how do you
               quickly generate the outline  of  a user defined quadratic
               that can take many forms  (cone,  spheroid, etc)?  And how
               can the user  easily  specify  the  object  tree structure
               (bounding boxes) with an interactive editor?
        

























        QRT Ray Tracer               Page 15                  User Manual