How To Build Your Own Electronic Drumset.


INTRODUCTION.....

Alesis has done it again, they've just released the latest in their
never ending stream of state of the art drum boxes. The D4... it's not
a drum machine. It's a drum module. Sorry, no patterns in this guy.
There are however over 500 16 bit sampled kicks, snares, cymbals,
toms, percussion sounds and even effects. Many of these killer sounds
are sampled in STEREO. And many work with what Alesis calls DYNAMIC
ARTICULATION, a process that creates realism that must be heard.
Another feature of the D4 is the reason I uploaded this project...
TRIGGER INPUTS, 12 of them. This project will let you take advantage
of these. I always thought it would add a touch of realism to my midi
music if I could do drum parts in a more conventional way, as opposed
to doing one drum at a time by tapping on a keyboard. I was right,
what a difference. The beauty of this project is you can make it as
basic or fancy as you want. As long as you stick to the basic stuff
that makes this project work. The way it looks is up to you. I'll
explain later.


PARTS.....

As far as quantity and size of the parts go thats up to you, depending
on how many pads you want to make and how big you want them. I'll list
the parts for (1) pad.

(1) Piezo Transducer (radio shack#) 273-073.
(1) Piece of plywood for the base 5/8" thick.
(1) Sheet of aluminum 16 or 18 gauge, about 1/6" thick.
(1) Sheet of pure gum rubber for batter surface, 1/8" thick.
(1) Sheet of "open-cell" foam rubber, for batter cushion.
(1) 1/4" phono jack, for output.
(1) 3/8" T-nut, for mounting the pad to a stand.
(4) 1" pieces of 3/4" velcro, only if mounting pads on a board.


CONSTRUCTION.....

Enclosed in this upload are diagrams of the pad in DEGAS .PI3 for high
rez. There are many programs on GEnie that can view and print PI3
format pictures if you don't have DEGAS.

What you want to start with is to deside the size and shape of your
pad. First I'll tell you what I did and why. Because I'm not a real
drummer I desided to make the pads rectangles about 6" by 8". I also
desided to mount them together, instead of mounting them on separate
stands like a real drumset. So basically it looks like a large Roland
Octapad with added brackets for the snare, high hat, and xlow tom. Now
this works great for me but a friend of mine who is a "real" drummer
came over to check it out, and he said the spacing was too close for
him. Only because he's used to a real drumset. So if your a real
drummer and your used to the spacing of real drums, try for larger
pads, maybe a six sided shape and a wider spacing between pads.

First when you purchase the transducers you'll find they're in a
plastic case. You must pry open the case and remove the sensor. It's
not easy. The sensor is a thin disk of brass with two wires attached
to it. If the wires come off while doing this it's ok, don't panic,
they can be soldered back on. Use a 15 watt soldering pencil and work
quickly. Don't let the pencil stay on the disk too long.

After you've done this cut all your pad bases, rubber sheets, aluminum
sheets and foam sheets. All the same size and shape as the pad size
you have chosen. Use your pad base as a template. Make sure the gum
rubber sheets are not smaller than the aluminum sheets, you can always
trim the rubber later.

Now you want to get some rubber cement or glue just for gluing rubber
to metal. Glue the rubber batter sheets to the aluminum sheets. When
the glue is dry, turn it over so the rubber faces down. Next draw a
line from corner to corner and find the center. NOTE... The bass drum
pad is the only pad you don't want the sensor to be in the center. A
bass drum pedal hits the pad with alot more force than a stick.
Mounting the sensor off center on this pad works much better. After
you've found the center of your pad. Use some silicon glue and glue
the sensor to the plate. Be sure to put enough glue on the plate so
that it oozes out from behind the sensor on all sides. But not onto
the top of the sensor.

Now grab your pad bases, the 5/8" plywood. Your going to need a spade
bit drill to make a hole between 7/8" and 1" into the base, not quite
all the way through. After that drill a 3/8" hole through the rest of
the way, for the 1/4" output jack. You could, if you like, use RCA
jacks which will require a 1/2" hole or even hard wire a cord right to
it. I don't recommend that though. I used 1/4" jacks. NOTE... Do not
drill this hole in the center. Put it off center, out of the way. If
you're using RCA jacks, You'll need a plate about 2" square with a
1/4" hole in the center and (1) hole in each corner to fasten it to
the base.

If you've desided to mount "all" your pads on a board you can forget
this next part. But if you want to mount some or all on some kind of
stand then read on. Find the center of the bases the same way you did
on the aluminum and mark the center. This is where your putting in the
3/8" T-nut. A T-nut is threaded metal insert that can be found at any
hardware store. The reason you can't use a regular nut here is that
you run the risk of damaging the sensor when putting it on a stand.
You might even want to recess the T-nut with that 1" spade bit drill.
I believe the proper size hole for a 3/8" T-nut is 7/16", check it to
be sure. drill the proper size hole in the bases and insert the T-nut
so the flat end is on the inside of the base. Then give it a good wack
with a hammer to set it into place.

Next, get the 1/2" foam rubber. You have to cut the center of the foam
out so it doesn't touch the sensor. The sensor is about 1" in
diameter. So make the hole about 1 1/2" to 2" in diameter.

Now your ready to assemble the pads. Take a look at the diagrams if
your not sure of the order of the layers. The way you hold it all
together can be done many different ways. The easiest way is to use
wood or machine screws and just drill some holes through the rubber
and sheet metal. Then just screw them into the base. But in my opinion
this looks like hell. What I did is described in the diagrams. It took
a while to do it, but the results are worth it.

This next section is only for those who are mounting multiple pads on
a board. This is where the velcro comes in. When you mount two or more
pads on a board or on a single stand for that matter, you get what is
called "cross talk". Cross talk is when you hit one pad and the pad
next to it also responds. (Not a good thing.) I needed a way to mount
the pads securely and still have them immune to vibrations from the
other pads on the board. With much experimenting yet another use for
velcro was born. Attach a piece of velcro to each corner of the pad
and just mount it where you want it. You still occasionally get a
little cross talk but now it's manageable with the D4 settings without
loosing performance.

If your mounting your pads on a stand or stands, you'll need something
like Roto-Tom stand. After shopping around, I've found you'll be
shelling out some big bucks for these things.

Let me mention something about the bass drum and hi-hat pedal I built.
I'm including the diagrams just for an idea of what can be done. The
hi-hat pedal can really be just a momentary switch mounted on a board.
And the bass drum pedal can be real bass drum pedal mounted on board
with your pad mounted vertically, so it hits the pad the same as a
real bass drum. A note of caution... Don't let the beater hit the pad
exactly where the sensor is. It hits to hard and can damage the pad.

There's not much more to it. Just plug it in and go. Also I want to
say, these pads will probably work with other units that can be
triggered with piezo pads.

If you have any questions, drop me GEmail... M.BOMBARD

Enjoy,
Mark Bombard