Electronic Cymbals
                      Designed by Mark Bombard


This project is an update to my previously uploaded file
"DRUM_PAD.LZH". In the quest for a more conventional setup for my
electronic drumset, I came up with this project to simulate cymbals.
These cymbals, although made of wood, can be mounted on a conventional
cymbal stand and are quite easy to build. Much easier in fact than my
DRUM_PAD project.

There are two different types of cymbals in my illustrations. Crash
cymbals and ride cymbals. Either design can be used as a high hat
cymbal, depending on whether you use the edge or top of the high hat.
You could of coarse make all your cymbals with both top and edge
batters. By doing this, one size fits all, so to speak. 

Materials for this project are simple and fairly easy to get. You'll
need a sensor (radio shack #273-073), a 1/4 inch jack, about 10 inches
of wire, gum rudder or neoprene depending on which type you're planing
to build and something to make the body of the cymbal out of. You'd be
surprized at the variety of materials you can use for this. I used 1/4
inch 5 ply birch plywood. I bought a 5 foot by 5 foot sheet for about
$40.00. But you can use just about any 1/4 inch plywood you can find.
Oh, and a 9/16 inch flat blade drill bit comes in real handy to
countersink the hole for the nut that anchors the 1/4 inch jack.

One thing I like about this project is that you don't have to pry the
sensor out of the plastic case like in my DRUM_PAD project. The sensor
works fine right out of the card. But don't use "hot glue" to attach
it to the cymbal body. The bottom of the sensor case warps, and this
could damage the sensor. I used 5 minute epoxy. Attaching the gum
rubber to the body can be easily accomplished by using a spray
adhesive. It's easy, fast and a clean way to do it. Gluing the
neoprene to the edge of the body can also be done with 5 minute epoxy.
The illustrations pretty much speaks for themselves. That's how easy
this project is.

If any questions need answers I'm available via Email... M.BOMBARD