****** The FAST!FFT Pseudo-realtime Spectrum Analyzer ******

                PROGRAM by Phil McCandless


INTRODUCTION:	

	The Fast Fourier Transform (FFT) is a complex mathematical
analysis of any conventional audio time-domain signal converted
into it's frequency constituents.  The FFT is very similar to the
multi-bar display seen on home high fidelity graphic equalizers,
but this one is much more accurate.  The FASTFFTx.PRG provides a
continuous line display, rather than the typical discrete
frequency band display.  

   This FFT program only works with the SOUNDOFF! cartridge which
is a very low cost 8-bit analog to digital converter for the
ATARI ST computer. I made this program for personal use in my
research laboratory and have used several parts for hearing aid
analysis. It's a little slow, (that's why I call it a Pseudo-Real
Time FFT analyzer), but the end result has yielded a reasonably
accurate test bench tool for audio analysis.

	The frequency accuracy has been crosschecked with an in-lab
150MC digital frequency counter. They have agreed within + or -
0.1 percent!  It's frequency response was measured to be within +
or - 1.5 dB from 100 to 14KHz and + or - 3 dB from 25 to 18000
Hz.  I cannot guarantee that this instrument is will be as
accurate for you, but it has served me well.  

	Only one small solder modification is necessary to make the
SOUNDOFF! cartridge meet these specifications. If you like this
program, you may want to keep an eye open for Frank Pawlowski's
FFT programs which the data saved from this program can be
imported into his programs for analysis.

   

ABBREVIATED OPERATION INSTRUCTIONS:

	I know you want to get started using the Fast!Fourier
Transform Analysis program as soon as you can, so for those of
you who can't wait to read the entire doc's, here's a quick
guide. 


1) Insert the SOUNDOFF! cartridge into the cartridge port and
turn the computer ON.  

2) Double-click on FASTFFT1.PRG. 

3) Place an audio source of pure tones or noise into the RCA
input jack. 

4) Make sure that this is a low-level (preamplifier) input
signal.  

5) Select "GO" from the ACQUIRE pull-down menu.  

	The program will automatically take a small sample of the
input signal through the A/D converter, then mathematically
convert the data from time domain information to frequency domain
data, and plot the those results to the screen.  Use a quality
screen capture program such as Michtron's "SNAPSHOT.PRG" or print
the screen to your printer using the [alternate/help] keys. A
control panel change may be necessary to properly set your
printer. 

	Hold the right mouse button to scroll the cursor across the
screen, and press both keys simultaneously to return to the menu
for another analysis. That's all there is to it!


 
   *********** DETAILS, DETAILS, DETAILS ************


SYSTEM REQUIREMENTS:

1) ATARI ST or equivalent. The accuracy of the FASTFFTx.PRG has
not been demonstrated with accelerator boards, but it should
considerably alter the accuracy.  If it works, Please let me
know.

2) Minimum memory size -- Unknown, because I have a two and a
four megabyte machine, I don't know how well this program will
work on a smaller machine. I can only estimate that the program
will work on a 520. Please let me know if it works. 

3) SoundOff! A/D converter cartridge.


   --PERIPHERALS AND OPTIONS--

1) Pink or White noise generator

2) Pure tone generator

3) Screen-Dump Program for saving to DEGAS or other drawing
program



PULL-DOWN-MENU'S:

	The pull-down menus have an asterisk in many columns to
indicate the default settings. The asterisk is fixed and does not
change when a menu item is selected, instead the small status
line at the bottom of the window gives current configuration
information.  The pull-down menu includes:

1) Desk = Just the INFO box available here....

2) File = These options include IMPORT FFT data, EXPORT FFT data
and SAVE...only QUIT and EXPORT FFT works at this time. The file
is saved as a FFT file, which can be directly read by Frank
Pawloski's FFT program.

3) SampSize = SampleSize lets you select the number of "sample
bins" or "memory locations" that is included in each "snapshot".
The greater the sample size, the greater the accuracy of the FFT.
But this comes at the expense of processing speed.

4) Speed = The speed is how quickly the sample is acquired and
placed in the sample bins. Speed is in Hertz (Hz) or in
microseconds given by:

                          1
          Speed = ________________
                  sample frequency

	Speed is independent of the rate and determines the highest
frequency to be plotted. If a speed of 20KHz is chosen, the
highest audio frequency that can be analyzed is 1/2 of the sample
speed, or 10KHz.  If a sample speed of 10KHz is chosen, the
highest sample frequency that can be plotted is roughly 5KHz.  

5) Sweeps = Multiple sweeps are acquired one after another and
have a "smoothing" effect on the final plot.  Multiple sweeps
also slightly increase the signal to noise ratio.

6) Plot = Look at the "time domain input signal, or switch to FFT
analysis.  The auto scaling option works only in the frequency
domain.

(Hint...If you choose "TIME DOMAIN", increase your sweeps while
you make adjustments to the input level and DC bias. See below
for details.)

7) Window = The shaping envelope used to avoid abrupt transient
at the start and finish of the sample. These transients
contaminate the FFT by "splashing" frequencies in the analysis
that are not really present in the signal. Currently, only the
COSINE 2 option functions at this time.

8) Acquire = GO starts the sampling process.



MODIFICATIONS TO SOUNDOFF! CARTRIDGE:

I have found that the SoundOff! cartridge works very well in most
cases, except that it has a very poor low frequency response in
it's stock form.  The problem is related to the decoupling input
capacitor which is too small. The solution is to solder a larger,
.2 microfarad (or larger) non-polarized capacitor in parallel
with the input capacitor.  You can even remove the original
capacitor if necessary. You can find this capacitor easily, as it
is the first component soldered to the positive terminal of the
input jack.


I have the older SoundOff! cartridge.  It has a volume control,
and a DC bias offset potentiometer inside the case.  Adjustment
of this potentiometer is necessary to give a proper frequency
response.  Here's how to adjust this potentiometer on the older
SoundOff! product:

1) Remove case off the SoundOff! A/D converter

2) Run FASTFFT.PRG

3) Select "INPUT MONITOR" from the "PLOT" pull-down menu.

4) Select "OTHER" from the "SWEEPS" pull-down menu.

5) type <100> and press the <return> key.
 
6) Select "GO" from the "ACQUIRE" pull-down menu.

7) increase any signal to the point of clipping and adjust the
potentiometer to show symmetric peak clipping.  This is the DC
bias adjustment.

     The newer SoundOff! cartridges (with output capabilities)
have the
DC bias set and adjustment is not possible...  Unfortunately, I
do not have one of these units yet, but I plan on making
suggestions with future updates.



CALIBRATION.


     The FFT graph is represented in a LOG Frequency on the
abscissa and in dB Volts along the vertical ordinate. These
values differ from other FFT programs because the FFT was
designed to mimic more conventional frequency plots used in Audio
circles. The conversion time is increased converting to LOG
scales, however the tradeoff is usually worth it, because the
final plot format is widely accepted. 

     The ordinate is in dB or Decibel values referenced to the
threshold of peak clipping on the SoundOff! cartridge.  These
levels need to be calibrated if accurate results are desired. The
calibration involves dB volts per ____ unit measure. Changing the
volume potentiometer changes the calibration. The FASTFFT! is
designed to give 0dB volts at the threshold of peak clipping of
the SoundOff! cartridge. Each dB value below this point is "x dB"
lower than the maximum voltage. This peak input voltage can be
measured on a volt-ohm meter. and is thus the reference voltage. 
(Caution... Most meters are RMS instruments and don't measure
Peak-to-Peak values).

	DC bias should be set if you have one of the older SoundOff!
cartridges. To do this, open the SoundOff! cartage and look for
the second potentiometer. Run the program in the time domain mode
and input a large signal. The peaks should clip symmetrically
about the 0 volt line.  There is no DC bias adjustment on the
newer SoundOff! cartridges. 

READING THE GRAPH.

	FREQUENCY PLOT...
 
	The frequency plot has decibels (dB) on the vertical axis,
and has a fixed reference of 0 dB referenced to the maximum input
level accepted by the SoundOff! cartridge. The gain of the
cartridge can be changed by adjusting the gain of the
potentiometer on the SoundOff! cartridge.  

	The horizontal axis yields frequency information.  At the
left of the screen in bold letters is the minimum frequency
(0Hz). The first frequency to the right of this point is
typically identified by a short vertical tick approximately 3/16"
high. The first small tick represents the resolution of the
frequency analysis. The first dashed vertical line represents
octave steps (a doubling of frequency).


	TIME PLOT...

	The time plot is not scaleable. The vertical axis represents
the real voltage. The horizontal axis shows time, scaled to the
appropriate number of bins selected.  



SPRITE CURSOR

	Pressing the right mouse button moves the mouse to the
right. Pressing both mouse buttons simultaneously restores the
menu for another analysis to begin. The frequency and dB value
corresponding to the cursor location are displayed at the bottom
left hand of the screen. 



COPYRIGHT NOTICE:

	The Fast! Fourier Transform Analysis Program is Copyright
1993. This program is FREEWARE and may be distributed on BBS
systems as long as this file accompanies the FASTFFTx.PRG. 
However, in spite of being freeware, all rights and privileges
still belong to the author:


     Phil McCandless, Ph.D.
     Joule Electronics, 
     Jackson, Mississippi 39211


	Certain limited rights belong to the coauthors, consultants,
and authors of the programming language itself (GFA BASIC) :
(Many thanks to Frank and Joe for their efforts!)


	Frank Pawloski (NH) and 
     Joe Andrews (FL)
     GFA Software Technologies


	The author declares no responsibility or claims of any kind
to the accuracy or suitability of this software. No liability
will be assumed from mechanical or electrical damage resulting
from the use, misuse, or modifications of the hardware or
program.




IF YOU LIKE THIS PROGRAM -- DON'T SEND MONEY!!!

	If you like this program, don't send money. Heaven knows I
have spent a good deal of the better part of my life working on
this &%$#! program.  Late nights, blood-shot eyes, and personal
satisfaction are all I expect to receive from this program.
However,  I would like to know how much money I COULD HAVE MADE
IF I MADE THIS PROGRAM SHAREWARE!  <GRIN>  

	Seriously, if anyone is using this program and actually
likes it, drop me a postcard or send me E-MAIL at P.MCCANDLESS at
GENIE.  Knowing that I am not the only person on Earth using this
program is reward enough.  My mailing address is:


              Phil McCandless, Ph.D.
              Joule Electronics
              600 Northpointe Parkway A-23
              Jackson, Mississippi 39211



Enjoy.. and PLEASE DROP ME A CARD or E-MAIL! P.MCCANDLESS (GENIE)