MT32 Editor Librarian Version 3.9 - January 1993

1.0	General

This Atari ST/TT GEM program/desk accessory can be used to effectively editor 
all available parameters for the Roland MT32.  The program stores the presets
and general settings, and creates configuration files which can be easily
uploaded  to the MT32.  A sequencer capable of playing standard MIDI files is
also included  in the application which can be run while presets are selected
and the parameters  are being edited.

The program was written to be used as a desktop accessory (ACC) so it doesn't 
make use of any pull down menus.  The program version (PRG) functions exactly 
the same as the accessory version, except in the way it allocates memory for the
 sequencer files. The files that should all be included with this program are
the  following :

MT32  EDT.PRG	The desktop/accessory program

MT32  EDT.DOC	The documentation file for the program

MT32  FAC.MTM	The preset file containing all the factory sounds

MT32  TST.MID	The example of a standard MIDI file - scale

MT32  MLT.MID	An example multitimbre midi file - song

MT32  MLT.MCG	An example configuration file used with MT32  MLT

MT32  DMP.ACC	Quick dump accessory/program



1.1	Changes to Program

The program has undergone the following changes. 

1.	The program now uses a window which can be sized an moved around the screen.

2.	You now have access to any desk accessories when using the program.

3.	A pop up window is available by pressing key "Control k" from the main and
secondary editing screens which allows notes and midi controls to be played with
the mouse.  The midi note and controls can then be repeated with the key "F1"
from within the other editing screens. 

4.	The resource file has been eliminated and made general for the medium and
high resolution screen modes.

5.	Changes to the envelope editor.  The editing must end with a click.

Major changes in the program will be designated in the documentation with a "**"
symbol. 

2.0	Registration Terms

This "shareware" program is directly registered to you for the use on "one" 
computer system.  The program is not copy-protected and you are free to make  as
may copies for your own personnel use using standard copy routines.  It is 
illegal and immoral to give away or sell this software without the consent of
the  copyright holder.

I have tried to test out the program as thoroughly as possible to give myself
and  you some confidence in making full use of it in your MIDI applications.  I
cannot  however be responsible for any problems that may result from the use of
this  program.  Please take whatever precautions are necessary such as saving
your  song sequences before entering the desk accessory version of the program
for  editing or configuring presets.

If you discover any problems with the programs operation please forward them  on
to me for my updating.

3.0	MIDI Connections

To provide MIDI communication between the ST/TT and the MT32 the midi  OUT of
the ST/TT should be connected to the MIDI INPUT of the MT32.  The  program is
normally set-up to only download data to the MT32 but some modes  of operation
"may" require the MT32 MIDI output to be connected to the ST/TT  MIDI IN.  This
isn't necessary, but can be advantageous for direct reading of data  from the
MT32.

I recommend using a MIDI "merge" device which takes the output stream of the 
MT32 and merges with the MIDI data from any other controller device such as a 
keyboard or MIDI guitar.  The output of the merger is then connected to the 
ST/TT MIDI IN.  Either that or change the connections if required.

WARNING : The program makes use of user presets memory  locations as a workspace
area for editing.



4.0	Running the Editor Desk Accessory and Program

** The MT32 editor program runs as a desk accessory (.ACC) or as a a program 
which can be run directly from the ST/TT desktop (.PRG).  All that required is
to  "rename" the program using the desktop information function (or equivalent),
 changing the file extension to ACC or PRG, depending on how you wish to use 
the program.  

**There are no longer resource (RSC) files to be loaded.

4.1	Desk Accessory (.ACC)

The .ACC program should be copied to the boot drive of the ST/TT, this is 
normally the A drive in a floppy disk situation and the C drive when booting
from  a hard disk.  When the ST/TT is reset or cold started after powering down
it will  read all the DA's that are residing on the boot disk. To keep the ST/TT
from  loading the DA the file extension .ACC should be changed to just about
anything  else, for example .ACX.

The DA stays resident in memory and can be accessed by selecting them from the 
left most menu position, from the desktop or from within programs which support 
menus.  The ST/TT does not allow DA's to use pull down menus so this editor  was
written to only use mouse clicks on buttons to access the various functions.  
This makes it much more cluttered on the display than necessary, but does allow 
fast access to the various functions.  Since the ST/TT doesn't currently support
 multitasking, the DA approach also allows you to keep different programs active
 in the computer at the same time.

The DA will allocate a user defined amount of memory in case the application 
that it is working in grabs all the remaining memory and won't give any back.  
The ability to auto run programs when booting up the ST/TT should be avoided 
when using the DA since parameters don't settle down with the new application, 
and the DA must allocate some initial parameters to normally work properly 
within a program.  It is best to let the desktop open up and all file load
before  running the new program.

I generally use the editor/librarian within the Master Tracks Pro sequencer to 
audition and edit new presets, instead of exiting the sequencer and loading in
the  editor and then exiting and reloading the sequencer.  This of course
assumes you  have a fair amount of memory in your system.

4.2	Program (.PRG)

The desktop .PRG version can be placed anywhere on a disk drive or within file 
directories.  It is run by the standard double click method.

** The program can now be configured with the "Install Application" function, 
available on TOS 1.4 and higher.  Click on the program, select the desktop 
"Options" function, and select "Install Application".  Designate the Document 
type value as "MTM", and select the Parameter as "Full file" path.  Then click 
on "Install".

Using this set up the program will automatically run when a file with an
extension  of MTM is double clicked, and the preset file will be loaded into the
program,  even if a preconfigured file has been defined for loading.  Sort of a
MAC like  function, for those Apple lovers out there.

4.3	Quick Tour

WARNING : See section 11 on User Preset Configurations if you  have any custom
presets in the user memory and wish to save them.   If they are standard
presets, you should already have a file containing  them, so there is no risk of
overwriting them.

1.	Load the program - select "MT32 Control" from menu for DA or  double click on
the desktop program. 

2.	On the opening screen click on OPEN. 

3.	Click on the file named "MT32  FAC.MTM". 

4.	The librarian screen will open.  Click on any preset "name". 

5.	Click on the EDIT button. 

6.	The main edit screen will open.  The preset is now available for  editing. 

7.	Play around with clicking on objects (just don't save anything) and  click on
EXIT when complete.



4.4	Example of Config  and Sequence File

1.	Reload the program.  The opening dialog should appear. 

2.	Click on the CONFIG button.  Then click on the LOAD button. 

3.	Select the MT32  MLT.MCG file.  When the "Configuring File" dialog box
appears Click on OK (or hit Return Key).  The MT32 should now be loading with
new presets to the starting memory     location displayed.   

4.	The opening dialog will reopen.  Click the SELECT function.  This will
display the presets that were loaded.  Now select the SEQUENCE function.  

5.	When the Sequencer dialog box is open, select the LOAD function. 

6.	Select the MT32  MUL.MID file.  The dialog will reopen with    updated
information on the sequence file.  Selecting START will    begin  the sequence
playing.  Selecting DONE will reopen the library.  Try  selecting different
presets while the sequencer is running.

7.	When completed, hit the "Space Bar" to stop the sequence. 

8.	Exit the program.



5.0	Opening Screen

The opening screen provides the operating options you initially want to enter.  
This is provided for quick access when working as a desk accessory, but also is 
effective for a program version.

Open:	Opens the file selector to load and display a preset file.

Update:	Opens the main editing screen and reads the current user  preset into
the editor.  The MT32 MIDI OUT must be  connected for this to work. 

Select:	Opens the main librarian screen and displays the loaded  presets.  As a
desktop accessary this file will be available  until a new one is loaded.  This
allows direct access to  audition and load any presets or master settings.  (Can
be  auto loaded). 

Config:	Opens the configuration loading or saving function.  As a  desk
accessory this allows direct loading of  the configuration  files and quick exit
when completed. 

System:	Takes you directly into general system settings screen. See  Section 9
for details. 

Cancel:	Exits the program with no action.



5.1	**Windowing Screens

The editing screens use a window which can be resized and moved.  To resize the
window click and hold the mouse on the lower right corner of the window and drag
the mouse until the correct size.  To move the window, click and hold the mouse
on the title bar and move the mouse to the new positon.  To return the window to
the full size click the mouse on the top right window button.  Clicking the full
button a second time will adjust the screen window to the previous postion and
size.  To exit the program you can click on the upper left corner window button.

You have access to external desk accessaries from all screens except the opening
selector screen.  You can move the desk accessory windows anywhere around the
screens (if the program lets you).  You can go back to the editor either by
clicking on the editing window (depending on program) or quitting the external
desk accessory.



6.0	Main Editing Screen

The main editing screen provides access to all the main preset parameters and a 
variety of tools to edit them. The symbol "Internal" or "External" in the top
left  corner indicates whether the preset was selected from the librarian or was
read in  from the MT32.

See the "Edit" function in the Preset Librarian section for a further
explanation of  the effect of editing in the internal and external modes.

NOTE : If the program ever appears to lock-up waiting for the MIDI  data, hit
the space bar once or twice to recover from the routine.

The parameter editing is accomplished by clicking on the parameter with the 
mouse, which should cause a selection box to be formed around it.  The value can
 be modified within its range of values by selecting the scroll bar on the
extreme  right of the screen and either clicking and dragging it up or down to a
new value  or clicking and holding down the mouse above or below the selector
box.  The  "up" and "down" arrows on the range selector will adjust the value
accordingly,  as will the keyboard up and down keys.

Holding the shift key down while clicking on the parameters will enable 
multiple selection which will be used by a number of operations.  If the 
parameter is already selected it will be deselected.

You may also notice that some parameters are disabled on the edit screen.  This 
means that you will not have any effect on those parameters based on the setting
 of the structure control parameters (e.g. synth mode and PCM mode - S or P).

The "Undo" key can be used to undo parameter value changes which result after 
initially selecting the parameter, pasting, and random functions. Pressing Undo
a  second time will return the previous values.  The MT32 parameters are also 
updated with each undo.

Clicking on the preset "Name" will open up a dialog box which will allow 
changes to the name.

The "Open" function loads a new file into the librarian and opens the display.

The "Save" and "Save As" functions will save the presets and master settings 
currently stored in the librarian as the last file name or as a new file name. 
The  file extension of MTM is always given to the file name by the program, even
if  an extension is entered.

The "Select" function opens up the librarian display function with the currently
 loaded file.

The "Store" function will store the currently edited preset in the librarian.  A
 dialog box will appear momentarily to confirm the preset that is being stored. 
Up  to 140 presets can be stored.  Duplication of preset names are allowed and
can  always be removed.  See section 10 on the Librarian operation for details.

The "Update" function will switch the mode from internal to external and attempt
 to read the preset directly from the MT32.  The top left corner of the main
editing  screen will display the new mode.

The "Copy" function will place All the selected parameters into a buffer which 
can be pasted into the existing or new preset.

The "Paste" function will place all the copied parameters into the location 
associated with alternate primary or secondary preset parameters or into the
same  parameters.  This can be useful for copying a good sounding preset value
between  primary and secondary parameters.

The "Random" function will result in the All selected parameters to be replaced 
with a new value within its range.

The "Group" function will select the parameters in logical groups for any
further  required selection based manipulations such as randomizing or copying.

The "Deselect" function will deselect All currently selected parameters.

The "Configure" function opens the configuration loading and saving function.  
This is fully defined in Section 11.

The "Output" function will output the currently edited preset to a new preset 
memory location and the patch assigned to that location.

The "Channel" function displays the current MIDI channel.  Clicking on the 
displayed value will open a dialog box which allows editing of the channel.  The
 program automatically adjusts the incoming MIDI data to this channel.  This 
normally doesn't need adjusting and corresponds to the "Internal" workspace 
channel value.

The "Sequence" function allows loading of sequence files for playback during 
the editing session.  See Section 8 on  the Sequencer for operation details.

The "Envelope" and "System" buttons will open screens to the various editing 
screens.  These will be described in the following sections.

The "Exit" function will exit from the program.  No prompts are given for 
unsaved data, so be sure you do want to exit.  This is not a problem as a desk 
accessory since everything is intact when you reenter the program.

The "Unit No." function displays the current MT32 Device unit number that is 
being communicated with.  Clicking on the displayed value will open a dialog box
 which allows editing of the unit no. This must match the value set for the MT32
 that is being edited or no operations will be made by the MT32 in response to
the  program.  This can be used to edit a number of MT32 units with the same
MIDI  set-up.

The "Top right" corner of the main editing screen contains a box indicating SYS 
CONF.  Clicking on the box will open the program set-up mode dialog box.  See 
Section 12 for details.

Clicking on the "Timbre No" in the INTERNAL mode will open up a dialog  box
containing the presets which are in the workspace area 1-16. The first 8 
presets are displayed.  Select the button 9-16 to display the remaining presets.

Click on the preset to be edited and hit the RETURN key or click on the OK 
button to exit the function.  The parameters for the chosen preset should be 
displayed.

Clicking on the "Timbre No" in the EXTERN mode will open up a dialog box  which
allows you to select a preset number which will be loaded from the MT32.  The
MIDI OUT of the MT32 will have to be connected the MIDI IN of the  ST/TT for
this to be successful.

7.0	Envelope Function

The "Envelope" function is used to display and edit the primary, secondary, and 
auxiliary envelopes.  By clicking and "holding" on the envelope point and 
dragging through the available range limits, the envelope values can be
modified.

**  Clicking on the envelope point will display a small box around the selected 
point for easy identification, especially with monochrome screens.

**  If the structure mode for the partial is set for synthesis then the display
box  over each envelope will be normal.  If the structure mode for the partial
is set for  PCM then only the amplitude envelope will be normal and the
remaining display  boxes over the envelope will be disabled.  Setting the new
partial point will update  the envelopes, as well as the display mode state.

If the value cannot be selected it may be an unalterable parameter of the
envelope  or there may be an overlapping of parameter values.  If the values
overlap, click  on the desired "Select Point", which should highlight the point
with a small box  on all envelope types.  If should now be possible to select
the point in the  envelope and drag it into a new position. When exiting the
envelope function the  new parameters are updated in the main edit display.

8.0	Sequencer Function

The sequencer function has been totally overhauled from the earlier version. The
 program now allows you to read standard MIDI type 0 format files and play  them
back.  There is no recording capability currently provided.  Two example  MIDI
files are also included with the program.

This function allows you to record your sequences on your favorite sequencer 
program, edit them down, and play them back while adjusting the MT32 user 
presets and their parameters.  The sequencer operates at around 60 ppq and will 
give you a very good idea of the final sound mix, even when driving other synth 
modules in the process.

The "Start" and "Stop" buttons can be used to start and stop the playback 
sequencer.  It starts at the very beginning and loops back when it reaches the
end.  To Activate the sequencer on most of the other screens hit the Space Bar,
and a  dialog box will momentarily be displayed to confirm sequencer activation.
 To  deactivate playback hit the space bar again.

The "Load" function will open a file selector with a .MID file extension. This 
extension value can be changed using the program set-up function described in 
Section 12.  The program will determine if it is a standard MIDI file and will 
display the MIDI channels which are active in the file, and the remaining ones
are  disabled. You can mute the channel at any time by clicking on the number. 
This  will deselect the button.  To hear the channel again, click on the MIDI
channel  button again.

The program checks to see if there is more than one MIDI channel used by the 
sequence.  If only one channel is used the "Channel Lock" will be selected.  The
 sequence will output all the MIDI information to the one working channel. This
is  useful for testing purposes and allows you to record and playback the
sequence  and not have to worry about which channel was used.  If multiple
channels are  used you can also select this option by clicking on the button,
with the result of all  the output sent to the working channel.

To exit the function click on the "Done" button or hit the Return key.  Upon 
editing some parameters you may notice some "stuck" notes.  These can easily be 
controlled by turning the sequencer on and off with the space bar to generate 
"Notes Off" commands to the MT32.



8.1	**Midi Note Out

Within the Main and Secondary Editing screens you have access to a Midi Note
Window.  By pressing the "Control K" key the window will pop up.  You can move
the window anywhere within the working area of the screen by grabbing the top
window bar with the mouse, holding and dragging it to the desired position, and
releasing.  The window will "pop up" in this new position the next time it is
opened.

To close the window either click the mouse on the top left window button or
click the mouse anywhere outside the window on the editing screen.

To play a note, simply click the mouse on the displayed keyboard.  The value of
the note is displayed in the indicator boxes on the left side of the keyboard. 
Pressing "F1" within the Midi Note window or any of the editing screens plays
the last selected note.

Clicking on the arrows next to the "octave" indicator will increment and
decrement the octave of the note played.

The duration of the note is controlled with the horizontal bar.  Clicking
anywhere along the bar will reset the duration and play the note at that new
duration.

The vertical bar sets a number of possible midi controls.  The "Volume" is the
start up default and is displayed in the box in the right top section of the
window.  Clicking within the vertical bar will set the new value and play a note
with that value.

Clicking the mouse on the indicator box initially showing "Volume" will bring up
another box which allows setting the control for Volume, Pan, Aftertouch,
Modulation, Pitch, and any desired Controller value.  This is set by typing in
the controller number in the "number" area on the box.  The "Reset" button will
bring all the control values to zero and set the volume to maximum.

All of the controller types are independently set and are accumulative when
played for the selected note.  Clicking on the controller type will exit the box
and reset the vertical control to the last set controller value.

The indicator box shows the new controller type.  Clicking on the vertical box
will control that midi event type.



9.0	System Parameter Editing Screen

Clicking on the "System" function in the main editing screen takes you into the 
system parameter editing screen.  This will allow updating of the parameters 
associated with pan, reverb, volume, and modes.

If the system parameters are "Not available" in the currently edited file, then
the  data will attempted to be read from the MT32.  Ensure that the MT32 midi
OUT  is connected for this transaction.

As previously used, the "Update" function will switch the mode from internal to 
external and attempt to read the system data from the MT32.

The "Store" function will save all the displayed system parameters in the
library  buffer.  This sound will be saved on to a file as part of a preset and
configuration  file.  If there already are master table values in the library
buffer, these will be  overridden by these new tables.

The "Edit Patch" can also be read and displayed in this function.  The data can
be  manipulated to set up the patch for various parameters.

The "Done" function can be used to exit the editing screen.



10.0	Preset Librarian

The "Select" function on the main and secondary editing screens will open the 
library function.  If a file hasn't been opened then the "Open" function should
be  used to select one.  The librarian can hold up to 140 presets for quick
selection.

I the librarian function the presets names are displayed on screen pages.
Clicking  on the name will load the preset into the workspace, which is set up
as preset user  locations 1-64.  The midi channel also is set up by the
corresponding workspace.

Make sure there isn't a preset you haven't saved in one of these workspaces if
you are manipulating the presets in the librarian function.

Clicking on "Next" will increment through the display pages of presets. 
Clicking  on the "Back" will work back through the display pages.

By clicking on the "up" and "down" arrow next to the Channel name you can 
change the workspace location and the corresponding midi channel.  This should 
be visible on the MT32 display.

By clicking on the "up" and "down" arrows next to the Memory name you can 
change the selected preset.  This will also be the location that the new loaded 
preset will be output to.  When the "Channel Lock" is selected the incrementing 
and decrementing of the channel value will also increment and decrement the 
preset value.  This allows easy placement to new preset locations for a MIDI 
channel.  Clicking on the Channel Lock button will select or deselect the
function.

Clicking on the "workspace name" will store that preset in the library.  This is
a  useful function for transferring presets from other files into a new library
file.  All  16 workspaces can be used.  A dialog box will momentarily be
displayed to  confirm the preset that is being stored.

The "Edit" function will load this preset into working memory and the MT32 user 
preset location, and open the main editing screen (the indicator should be 
"Internal").  In this mode of editing all the parameters are manipulated
internally  to the program and will not read the MT32.  Clicking on the preset
number in the  main editing screen will open the corresponding internal
workspace, which could  be empty if no preset has be loaded.

**  Double clicking on the "preset name" will now initiate the edit function for
 that preset.

The "Cancel" function will move you back to the previous display screen.

The "Remove" function will remove any selected presets.  The shift key can be 
used for multiple selections.  A dialog box will appear to confirm if you really
 want to remove the presets.  The removal operation may take a few seconds if 
the file contains a large number of presets.

The "Clear" function will allow the entire preset buffer to be cleared.  A
dialog   box will appear to confirm that you really want to clear the buffer.

The "Rename" function will allow easy renaming of any selected presets. The 
shift key can be used for multiple selections.  A dialog box will open which
will  allow change to the existing name.

The "Move" function will allow movement of the preset position in the file. The 
preset to be moved should be selected (no multiple sections are allowed), and
then  click on the Move button, which should select it.  Then click on the next
preset, at  any page in the file, which you want the old section to follow. 
Clicking on Move  again will perform the result.

The "Open", "Save As", and "Save" functions allow you to read and save the 
preset files.  If a file has been modified through operations such as rename,
move,  storing, then the Save button will be highlighted.  You will not be
prompted for  saving a modified file, so use this indication before exiting or
opening a new file.   The SaveAs function will request which file type you wish
to save the file as.   This results in a MTM or MCG file extension to be used on
the file types, even if  a file extension is entered.

The "Exit function will EXIT you from the program.

The "Print" function allows printing of the basic parameters of all the presets
on  the displayed file.  The parameters printed are the preset name, the number
of  partials, and the memory position of the preset value.

The "Configure" function allows you to output the currently loaded presets and 
system tables to the MT32.  See Section 11 on User Preset Configurations for 
more details.

The "Output" function allows you to output the selected preset to any desired 
user preset memory location and the patch to be associated with that memory 
location.  This will effect any patch already assigned, so some reallocation of
the  patches may be necessary.  Use the "System" patch function to see how they 
map.  Clicking on the memory or patch value and then on the increment and 
decrement buttons will adjust the value accordingly.

The "Sequence" function allows access to the system sequencing application.

The "System" function allows editing of the volume, pan, reverb, and partial 
parameters of the MT32.

11.0	User Preset Configurations

One of the most useful functions of this program is the ability to store preset
and  master table configuration files. Using the main editing "Configure"
function or  the start up screen function you can "Load" or "Save" the
configuration files.

With the "Save" function you can create a file or display the configuration data
 load from the MT32.  As previously discussed the MT32 midi OUT should be 
connected to achieve this function.  The dialog box indicates which parameter 
tables and the range of presets that you request.  If "Display" is indicated
then the  librarian function will open and you can see what was loaded.  This
can then be  saved to a file for permanent storage.  The file extension .MCG is
always used for  the configuration file types.

The "Append" function will allow you to add to the currently loaded preset file,
otherwise the library is initially cleared before storing the new presets.

NOTE : Some problems may be experienced in working as a desk accessory  within
some MIDI programs, since the programs may take over total control of  the ST/TT
midi port.  The program does disable some interrupts associated with  "Master
Tracks Pro" but it still doesn't function on receiving the midi data.  If these
problems are experienced, it is recommended that the configuration save 
function be used outside of the main program.  The "Load configuration" function
should have no difficulties working within another program.

With the "Load" function you can take a file containing preset and master
setting  data and dump it to the MT32.  The dialog box will indicate if any
master setting data exists on the file or any preset data and gives you the
option to "not" load it  by deselecting the indicator button, otherwise it will
be loaded.  If you only require the master tables dumped and none of the
presets, then the preset indicator  should be disabled.  See the example file
included with the program to see how the function works.

11.1	Tips on Configurations

There are two ways to build a preset configuration file.  You can output any 
number of presets to the user locations, use the ones you want in your sequence,
 and then use the config save function to read them all back in.  The "Remove"
and "Move" function can be used to clean up and arrange the ones you want to 
keep.  The sequence MIDI program changes will have to be updated to  accommodate
the new preset locations.  This process can also be used to read the current
master setting, tuning tables, and program table values directly from the  MT32.
Unfortunately this requires you to have the output of the MT32 MIDI'ed  back to
the input to the ST/TT, which means cable swapping unless you have a  merger or
a MIDI patch device.

You can also build your configure files directly in the library function.  This
is  done by opening the files you want, select the preset you want, and storing
them  in the preset channel workspace 1-16.  Increment the channel number and
select the next preset out of the same file or from another file.  Continue this
until you have all the presets you want in the workspace memory.

Then use the "Clear" button to clear the preset memory and adjust the channel 
button until the first preset you want is displayed.  Clicking on the display
will  store that preset in the file.  Continue to select the channels and store
the presets in  the order you want or use the "Move" button to rearrange them.

If the master settings are non standard you should go to the master screen and 
adjust them to what is required.  Then use the store function to save it as part
of  the preset file.  You should then go to the librarian screen and use the 
"Configure" function to output all the current presets and setting to make sure 
the MT32 will be set up to your liking.  Use the "SaveAs" function to save the 
memory as a CONFIG file.  This can then be easily accessed from the initial 
opening menu when the program is first run.

11.2	Quick Dump Utility

**  A new program is included which provides for quick loading and saving of 
configuration presets and master settings, as described in Section 11.  This
utility is a much smaller program, and is therefore more useful for users which
do not  have much memory to spare, but want access to a desk accessory function.

The program allows the selected MT32 information (i.e. presets, master setting, 
tuning tables) to be saved to a file name with extension MCG.  The file can then
 be read and the appropriate MT32 information can be loaded to the MT32.  You 
should proceed to read the file into the full program and then resave them with 
your MT32 configuration.

The program can also be configured using the "Install Applications" of the new 
desktop (see Running a Program - Section 4.2).  You should use a Document  type
of .MCG and a full file path.

12.0	Program Set-up Mode

The system configuration function can be accessed by clicking on the editing 
mode name in the top right corner of the Main editing screen.  The should open
up  a dialog box which contains a set of running mode parameters and boot up 
parameters.

The boot functions allow you to define which preset and sequence files should be
 automatically loaded when the program is initially booted up. Click on the name
 of the preset file (or the blank space if nothing is displayed ) and choose the
file  using the GEM file selector.  The name of the chosen file should then be
displayed  in the area.  The sequence file can be chosen with the same
operation.  If you wish  to clear the file so nothing will be loaded  on boot
up, click on OK with no file  name defined in the "file selector".  The display
will be now blanked out for that file value.  The file extension used in the
standard midi file selection can be edited  and stored.  For the DA version the
amount of memory that is initially allocated can also be edited and stored. 
This will not take effect until the next time the  computer is booted up and the
DA reloaded.  The program version will load any  size sequence file, if  working
memory is available.

The "Save" function can be used to save this file to the disk. Made sure the
disk  that the original Desk accessory or program is on is used, since it will
be read by the program the next time the program is initialized.