CONVERTING COLOR IMAGES TO MONOCHROME

                           Michael A. Long

There has been some discussion in the programming RT of the best method of
converting color images to monochrome. While there are a number of programs
available to convert images, there is little information available on how
these programs work. This file is my attempt to dispell a little of the
darkness.

In general, there are two steps involved in converting from color to
monochrome. First, we need to map some number of colors (RGB) to some number
of shades of gray. Second, we need to display the gray shades on a display
with only two colors. I will discuss each step separately.

I. CONVERTING FROM COLOR TO SHADES OF GRAY

The easiest way to convert from color to shades of gray is simply to average
the three RGB values and use the result as the gray shade. This works fairly
well most of the time.

In some cases averaging results in poor separation of colors. Two distinct
colors may map to the same, or a very similar, shade of gray. This is more
common than you might think. One solution to this problem is to use a
different mapping which distorts the colors somewhat, but separates the
colors better. The method used to convert color television images to black
and white is called YIQ conversion. We can use a simplified version of this
method by calculating Y and using it for our gray shade. The formula is:

          Y = R * 0.30 + G * 0.59 + B * 0.11

This is essentially a weighted average. The floating point calculations can
be removed by using the following formula:

          Y = (R * 30 + G * 59 + B * 11) / 100

Both of these methods give better results if the number of possible RGB values
and gray shades is large. SHOWPI1.C converts the 9-bit ST RGB values to
24-bit RGB values and maps to 8-bit gray shades (256 shades).

Other mappings might work better in particular cases, but one of the preceeding
will work fairly well most of the time.


II. DISPLAYING SHADES OF GRAY

The simplest and most common way to display multiple shades on a two color
display is to use an ordered dither. This technique works by taking a
square 'dither matrix' and filling the matrix with the integers from 0 to
the number of shades - 1, in a pseudo-random order. For example, a 4 shade
dither matrix might be:

                         0 2
                         3 1

To display a pixel, take the remainder of the x coordinate / size of the 
matrix and the y coordinate / size of the matrix and use these values as
indices into the matrix. If the value of the pixel is greater than or equal
to the value of the matrix at this point, the point is white. Otherwise, the
point is black. For example, if pixel (16,13) has a value of 2 we proceed
as follows:

     - The remainder of 16 / 2 is 0.
     - The remainder of 13 / 2 is 1.
     - The value of the pixel is 2.
     - The value of the matrix at [0][1] is 0.
     - 2 > 0 so the pixel is colored white.

The result is that very dark pixels are usually colored black, very light
pixels are usually colored white, and gray pixels are colored black about
half the time and white about half the time.

This technique works better if the number of shades is large. SHOWPI1.C uses
a 16 X 16 dither matrix which can display 256 different shades of gray.

The drawback to the ordered dither technique is that it overlays an obvious
pattern on the image, especially in large areas of one color. A pronounced
improvement can be made by using Floyd-Steinberg half-toning instead of
dithering. The Floyd-Steinberg technique is quite simple. At each pixel we
calculate the color we would LIKE to display, display the closest color we
have, and distribute the error to neighboring pixels. The original algorithm
distributes the error 3/8 to the right, 3/8 down, and 1/4 down and to the
right. For example, if pixel (16,13) has a value of 195 (out of 256 shades)
we proceed as follows:

     - 255 (white) is the closest value we can display so we display a
       white pixel at (16,13).
     - The value we displayed is too bright by 60, so we need to darken the
       neighboring pixels to make up for it.
     - We subtract 22 (about 3/8 of 60) from the value at (17,13).
     - We subtract 22 (about 3/8 of 60) from the value at (16,14).
     - We subtract 15 (about 1/4 of 60) from the value at (17,14).

Note that the neighboring pixels that are adjusted all occur LATER in scan
order than the pixel we are currently drawing. If we draw the image in
scan-line order (top to bottom, left to right) we can perform the correction
in one pass over the image, without backing up.

The Floyd-Steinberg algorithm results in much smoother shading of the image
with much more apparent detail in the resulting image. Some objectionable
patterning occasionally occurs, particularly in large areas of one color, but
the results are generally far superior to the result obtained from dithering.

This technique also works better when the number of shades is large. The 
weighting of the error distribution can also be adjusted to obtain slightly
different results. The algorithm used in SHOWPI1.C distributes the error
as follows:

     - 7/16 to the right
     - 5/16 down
     - 1/16 down and to the right
     - 3/16 down and to the left

III. SHOWPI1.C

SHOWPI1.C displays a DEGAS .PI1 (low resolution) image on the Atari monochrome
display using all of the above techniques. The default is to use YIQ color
conversion and Floyd-Steinberg half-toning. The -d flag allows the image to
be displayed using an ordered dither, and the -a flag allows color averaging
to be used. The syntax is:

     showpi1 [-da] <inputfile>

Examples:

     showpi1 mypic.pi1     - display mypic.pi1 using YIQ conversion and
                             Floyd-Steinberg half-toning

     showpi1 -d mypic.pi1  - display mypic.pi1 using YIQ conversion and
                             ordered dithering

     showpi1 -a mypic.pi1  - display mypic.pi1 using color averaging and
                             Floyd-Steinberg half-toning

     showpi1 -da mypic.pi1 - display mypic.pi1 using color averaging and
                             ordered dithering

Two sample image files are included, trex.pi1 and ceratops.pi1. These are
digitized video images of dinosaurs (my son likes them). I would like to
give credit to the source of the images, but I can't remember where I got
them. Thanks are due to someone.

IV. RECOMMENDATIONS

If you are seriously interested in computer graphics I highly recommend:

     Procedural Elements for Computer Graphics
     by David F. Rogers
     McGraw-Hill

All of the techniques discussed here are discussed in this book, along with
a LOT of other useful techniques. If you have already worked through another
graphics text, and are looking for more information, this book is very good.

Also recommended is the AIM (Atari Image Manager) image processing software
available in the RT. This package will convert DEGAS color images to
monochrome using an enhanced Floyd-Steinberg algorithm, as well as doing
lots of other enhancements.