Probably the best way to learn tbxCAD is to plunge right in.
Let's start with a common CAD project, a simple floor plan.
In this example we will draw a 10' by 15' office, with door
and furnishings.

In this tutorial, the following conventions are used. A key
on the keyboard is written between square brackets, like
[Esc]. Menu commands are written between curly brackets,
like {Set-up}. Menu commands are also strung together within
curly brackets, like {Setup-Grid Options-Snap On}. This
means: select the {Set-up} menu; when the next menu appears,
select {Grid Options}; when the next menu appears, select
{Snap On}.

Throughout the tutorial, please take note of the command
line at the bottom of the screen. You will find it to be a
reliable guide.

1. Load tbxCAD by double clicking on its icon. You will see
a blank screen, with a menu bar across the top and a black
line with a '>' symbol at the bottom. Dead center on the
page is a heavy '+' symbol.  This is the origin of the
drawing (0,0).

2. Let's set up the grid first. Under the {Set-up} menu,
choose {Grid Options} and then {Grid Spacing}. Enter '12' on
the command line when prompted. Now each grid mark will be
12 units. We can think of the grid marks as feet, and the
units as inches. Also, turn the grid on by selecting {Show
Grid} and turn snap on using {Snap On}. Checkmarks will
appear in front of these commands to indicate that they are
active.

3. Choose {Tools-Rectangle} and click on the origin point of
the drawing (the heavy black + sign). This is just for
convenience - there is no real need to start your drawing
here.  Stretch the box up and to the right until the
coordinate display in the upper right corner of the screen
reads X: 180.0 Y: 120.0.  Note that with snap on, the
coordinates jump in increments of 12 units. Click the left
button to fix the rectangle in place, and click with the
right mouse button to exit this drawing mode (note that you
can keep drawing rectangles one after another, until you
exit the drawing mode).

4. Let's double check our work. Choose
{Extras-Measure-Length of Line}.  Click near one of the
horizontal lines - the command line should report 180 units.
Click near a vertical line - tbxCAD should now display 120
units. If you have not quite gotten this right, just choose
{File-New} or press [Undo] and try step 3 again. Later,
we'll show how to edit and move lines, instead of clearing
the drawing and starting over.

5. Turn snap off by selecting {Setup-Grid Options-Snap On}.
The checkmark will disappear.

6. Now, let's put a door in the lower right hand corner of
the office.  First, use {Extras-Zoom-Zoom In} to enlarge the
area of interest by drawing a box over the lower right
quarter of the office. We will put the door opening in the
vertical line. This will be 30 units (ie. inches) wide, and
will start 6 units from the corner.  Select
{Tools-Line-Break-Break to Length}. Digitize the vertical
line by clicking near it. Notice that the line is redrawn as
a dashed line and the Specific Locations menu appears.
tbxCAD is asking you to select the break points. There are
several ways of doing this, but the easiest is to simply
enter a '6'.  A temporary mark is drawn to conform the
location of the break. tbxCAD is now ready to break another
line. Select the longer vertical line by clicking above and
top the left or right of the last break mark. Now enter
'30'. A second mark should appear (it it doesn't, you may
have zoomed in too much on the corner, and the break may be
off-screen).  Click the right button to exit this mode.
Press [Esc] to return to the main menu. Hey, the marks
disappeared! (I did say that they were temporary).  Now
select {Edit-Delete-Digitize} and click near the door
opening. The door-sized segment should be highlighted.  If
you get the wrong one, hit [Esc] and try again. When you
have the right one, click the right button to stop the
selection process, and select Proceed to complete the
command. If you make an error at any time, press [Undo] and
try again. Press [Clr-Home] to redraw the screen.

7. Let's add some thickness to the walls. We'll make then 4"
(units) thick. Select {Tools-Line-Horizontal} followed by
{Specific Location-End of Entity}.  Digitize near the upper
edge of the door frame. When prompted for length, enter 4.
When prompted to digitize the direction of the line, click
anywhere to the right of the vertical line. A short line
segment should appear. We now need another line just like
this for the lower door frame. Choose {Edit-Copy}. Digitize
the upper door frame line (if you get the wrong one, hit
[Esc] and start over. Depending on where you digitized,
tbxCAD may find two entities at that location - the vertical
and horizontal lines. You can cycle through the chosen
entities by choosing {Next Entity}, and when you have the
right one, {Select This Entity}.) When you have selected it,
click the right mouse button to end the selection process.
tbxCAD will now ask you if you want to Drag or Digitize. For
maximum accuracy, choose {Digitize}. You will now need to
select an origin for the copy - that is, a reference point
on the entity to be copied. Select {Specific Location-End of
Entity} and select the left end of the line segment.  Now
you need to select the destination.  Choose {Specific
Location-End of Entity} and select the end of the 6 unit
vertical segment. A copy will be placed exactly.

8. To complete the walls, first do {Extras-Zoom All} and the
drawing will fill the screen. Now draw a vertical line of
length 88 from the right end of the upper door frame line
towards the top right corner of the office, using
{Tools-Line-Vertical}, then {Specific Location-End of
Entity} to select the end of the horizontal line. Type in
the length directly and digitize the direction of the line.
The right mouse button exits the drawing mode. Using a
similar procedure, draw a horizontal line of length 188 to
the left, a vertical line down of length 128, and another
horizontal line of 188 units to the right. You should now
have a short vertical line segment of 10 units to draw to
complete the walls. Let's try something different. Choose
{Tools-Line-Simple}. Use the {Specific Location-End of
Entity} option to choose the right ends of both the lower
outside horizontal wall and the lower horizontal door frame
segment.  A line will be drawn exactly joining these two
ends. Remember, while drawing, you can usually hit the
[Space bar] to access the Specific Locations pop-up menu.

9. Whew! The walls are complete. It takes a lot more to
explain it than to actually do it. To add a finishing touch,
let's crosshatch the walls. You may be a little too close to
the edges of your screen, so choose {Extras-Zoom-Zoom Out},
and draw a box about half an inch smaller than the working
screen. The drawing should now be nicely positioned on the
screen.  {Select Tools-Xhatch-Enter Xhatch-Window}. Draw a
window around the entire office and the walls will be
immediately crosshatched. Is the spacing too wide ? Try
{Xhatch-Delete Xhatch-Window}. Then use {Xhatch-Xhatch
Spacing} to change the spacing to 5 from the default value
of 20. (You can also try out the {Xhatch-Angle} command if
you wish.) Then {Enter-Xhatch} again. That's better! Press
[Clr-Home] to redraw the screen.

10.   Save it! Choose {Files-Save} and enter the name of
your choice.  An extension of TBX will be added
automatically.

11.   Let's add the door. We'll do this one freehand. Zoom
In on the area of the door using {Extras-Zoom-Zoom In}. Use
{Tools-Rectangle} to draw a thin rectangle in the door
opening (say about 2 units thick). It's usual to show the
door open and with an arc to trace its path. Use
{Edit-Rotate-Single Rotation-Window} and draw a rubber band
window around the door. Fully enclose the 4 door line
entities only (you can digitize if you prefer).  Now the 4
lines should be shown as broken lines on screen.  Select a
point of rotation. How about the lower left corner of the
door (where the hinge is)?  Use a speck (specific location)
to locate it. Hit [Space] and select {End of Entity} to
digitize the corner. Now enter 60 for the angle.  When you
select {Proceed}, the original door rectangle will be erased
and the new one drawn in position. {Zoom All} to examine
your handiwork.

12.   To draw the dashed arc, first select {Setup-Line
Style} and choose a dashed line (not the change in the line
style display box in the menu bar at the top right of the
screen). Now select {Tools-Arc-Standard}.  Choose specks
when prompted for the four points required to define this
arc. First select a center point...that's the door hinge
again. Then a radius is required...the line representing the
door width will do fine.  Now the starting point of the arc.
Remember, arcs are always drawn counter-clockwise from the
starting point to the end point.  Choose the top inside
corner of the door opening. The end point is the top outside
corner of the door. The arc will be drawn to show the swing
of the door.  Select {Setup-Line Style} and choose the solid
line again.

13.   The permanent features of the office are now complete.
{Zoom All} to see your handiwork and save it! So far, we
have been drawing on the default layer, Layer 0. We will
add the furnishings on layer 1. Choose {Setup-Layer
Options-Working Layer} and enter '1' at the prompt.
Alternately, press [F1]. Notice that the Layer display at
the top right of the screen now says "Layer:1".

14.   In this segment of the tutorial we will not be
striving for accuracy. Start by drawing a round conference
table. Choose {Tools-Circle-Standard} and digitize a center
point somewhere in the middle of the office (we'll move it
around later). Then enter the radius...this is a 36"
diameter table, so enter a radius of 18 units. Now draw a
chair. A rectangle drawn to approximate size is fine. Now,
choose {Edit-Delete-Digitize} and digitize the top line of
the rectangle; right click to end selection and choose
{Proceed}. Now select {Tools-Arc-3 Point Arc}. Use the
specks at the open ends of the rectangle as start and end
points (remember, arcs are drawn counter-clockwise).
Digitize the third point about midway between the upright
line segments and above their ends. The intended result is
shown in the figure below.

15.   Now, select {Files-Block Save-Window}. Draw a window
around the entire chair. A file selector will appear...type
in CHAIR. The file extension BLK will be added
automatically. We have just started a library of standard
design elements that can be loaded into this and other
drawings.

16.   Let's move the chair to the conference table. Select
{Edit-Move-Window} and draw a window around the chair.
Choose {Digitize} to select the reference point for the
move. This will be the center of the bottom line of the
chair ...  select it using {Specific Location-Centre of
Entity}.  The destination speck will be a point just a bit
above the top of the table (the 12 o'clock position). This
will illustrate how to combine a number of specks to define
the point you want. When asked for the location of the
move, first select {Specific Location-Relative to Loc}, and
then select {Specific Location-Centre of Entity} and
digitize the circle. The center of the circle will be
marked. Now select {X,Y} and enter 0 for the x coordinate
and 19 for the y coordinate. The chair will then snap to a
position 1" from the table.

17.   Hmmm...we could use a few more chairs. Select
{Edit-Rotate-Multiple Rotation-Window} and draw a rubber
band around the chair. The center of rotation is the center
of the circle ... select it using {Specific Location-Centre
of Entity}. When asked for the angle enter 90; enter 3 for
number of copies. You should now have 4 chairs around the
table at 0, 90, 180 and 270 degrees. Now choose
{Edit-Move-Window-Drag}, capture the chairs and table and
move them to the upper right corner of the office.

18.   Add more furniture, such as a desk, bookcase or plant.
You can load the chair we saved earlier using {Files-Block
Load}.

19.   Now let's add some labels. Choose
{Tools-Label-Height}.  Enter 6.  Now choose {Insert Label}.
Digitize an insertion point on the left side of the
conference table and type in "Conf", press [Enter], type in
"Table" and press the right mouse button. The label will be
inserted.  If you want to adjust its location, choose {Move
Label} and digitize the label and the destination point. The
label will be moved immediately.  Experiment with adding
more labels and modifying them.

20.   Now, choose {Tools-Dimension}. tbxCAD will give you
the option of automatically determining the dimension size
(this only happens when there are no other dimensions on
the drawing) ... select {Yes}. A new menu bar will appear
at the top of the page. Now choose {Insert Dim-Parallel}.
Digitize  a horizontal inside wall line, and then choose a
location for the dimension.  Experiment with other
dimensioning features.

That's it for the tutorial. You're ready to tackle you own
drawings.  Good luck!