PANASET Version 3.10

                        Desk Accessory and Utility Program

                              copyright (c) 1992 by

                              Leonard A. Kaczorowski
                                 January 24, 1988

                                   Version 3.10
                                  April 18, 1992


        PANASET is a utility for setting some of the most often used print 

        characteristics  and functions for  the  Panasonic KX-P1091i  line 

        printer.  It works in "Epson" or "IBM" mode, and might possibly be

        able to be used with some IBM or compatible printers,  but it  has 

        only been tested with a Panasonic KXP-1091i.


        Please feel free to copy and distribute the software,   but it may

        not be sold, and the copyright notice must be included, naturally.


        PANASET  was  compiled  and  linked  using  "LASER C"  by MEGAMAX.

     
        The following files should have been obtained from the  "Archived"

        file "PANASET.ARC":


                PANASET.ACC          The EPSON default desk accessory
                PANASET.C            The source code for PANASET
                PANASET.DEF          The resource file definitions
                PANASET.DOC          This document
                PANASET.H            The resource include file
                PANASET.PRG          The EPSON default program
                PANASET.RSC          The resource file
                PANASRSC.C           The resource file source code
                PANIBM.ACC           The IBM default desk accessory
                PANIBM.PRG           The IBM default program
                READ.ME              Explanation of changes








                                      Page 1









        The desk accessory and program are executed in the normal  manner.  

        Upon execution,   a dialog window  will open to allow selection of

        several characteristics as follows:


        L-R ONLY (OFF or ON)

                Selecting the "ON" button causes the printer to print only

                from left to right.  "OFF" allows bi-directional printing.


        BOLD (OFF or ON)

                Selecting  the  "ON" button causes the printer  to  double 

                strike all lines of print.   The "OFF" button returns  the 

                printing to normal single strike.  Bold printing cannot be

                selected along with "CONDENSED" printing.


        EXPAND (OFF or ON)

                Selecting the "ON" button causes the printer to expand the

                character  size  to double its  normal width.    The "OFF"

                button returns the printing to the normal character width.


        PERF (CONT or SKIP)

                Selecting  the "CONT" button causes the printer to print a

                continuous form.   The "SKIP" button causes the printer to

                skip the paper perforation at the bottom of the page.


        LINES (1/6" or 1/8")

                Selecting  the 1/8"  button causes the  printer  to  print
 
                eight lines per inch.   The 1/6" button causes the printer 

                to print Six lines per inch.






                                      Page 2









        MARGIN (0" or 1")

                Selection the 1"  button sets the left margin at  1"  from 

                the  normal  left starting  position.   Selecting  the  0" 

                button  returns  the  left margin to  the  leftmost  print 

                position.


        MODE (EPSON or IBM)

                Select "EPSON" or "IBM" to tell the utility which mode  is
 
                selected by the "DIP" switches on the printer.

      
        PICA

                Selecting the  PICA button causes the printer to print  in 

                Pica pitch, Ten characters per inch.


        ELITE

                Selecting the  ELITE button causes the printer to print in

                Elite pitch, Twelve characters per inch.


        CONDENSED

                Selecting the CONDENSED button causes the printer to print

                in Condensed pitch,  Seventeen characters per inch.   Bold

                printing cannot be used with CONDENSED pitch.


        PROPORTIONAL

                Selecting  the  PROPORTIONAL  button causes the printer to

                print PICA pitch with proportional spacing.   PROPORTIONAL

                spacing cannot be used in IBM mode.








                                      Page 3









        LETTER

                Selecting the LETTER button causes the printer to print in

                the currently selected pitch using the Near Letter Quality

                character set.


        CANCEL

                Selecting the  CANCEL  button causes the utility to return

                to the "Desktop" without making any printer setup changes.


        FORM

                Selecting the FORM button causes the printer to feed paper

                to the top of the next form.


        DONE

                The  DONE  button sends the escape codes for the selected

                print characteristics,  rings the bell,  and  closes  the 

                dialog window.





        If any problems or bugs should arise,   I can be reached on GENIE

        occasionally.  My mail address is LKACZOROWSKI.   I cannot always

        guarantee swift responses, but I will try.



        Enjoy the software!












                                      Page 4