* UPGRADING YOUR 520ST TO 2 OR 4 MEGABYTES *
                        Copyright 1991, Mark L. Dodge


                   SHAREWARE PLEA and OTHER RELATED ISSUES
                   ---------------------------------------

By the time you finish printing out all of the text and .PI3 files, you'll
have to agree that _M A N Y_ hours of work went into this procedure.  I
spend numerous hours on GEnie and have witnessed the heartache that so many
ST users encounter trying to enhance their computers with more memory.  I
have encountered such heartaches with a couple of my own ST systems.  So I
did quite a bit of homework in this area.  And the procedure that you see
before you is a rock solid, permanent installation of extra memory.  (Once
it's installed, it's not extra any more!  You'll use it!)

I realize this is not a program, but just the same, I slaved over the drawings
trying to provide accurate and useful diagrams.  And I believe these are what
make this procedure so achievable.  Together with the text files, I don't
think you'll find a more complete procedure out there.

I drew all of the diagrams in monochrome mode because I was able to attain a
more accurate depiction of what goes where.  If you are converting the files
over to color, you will probably lose some of the details.  So if you can,
print them in their original format.

Included are two digitized pictures (.PI3 format) to provide you with some
sort of an idea as to what the upgrade looks like installed.  The color
pallette (mono) will reverse on you when you load up the files.  Print them
which ever way you desire.

I am asking for a $20.00 donation to compensate me for all of the hours spent
on this project.  If you desire telephone support or support over GEnie mail
then include a $25.00 donation.  My GEnie address is M.DODGE2.  You can reach
me at J & M Computer Specialties between the hours 6:00pm to 9:00pm, Monday
thru Thursday (512) 923-2811, and occasionally on the weekends.

Please send all donations payable to Mark Dodge at:

J & M Computer Specialties
907 DODIC PLACE
SAN ANTONIO, TX  78221

I encourage everyone to upload this to other privately owned BBS's so that
others may benefit.  But I sure would appreciate you giving me a call first.

Thanks,  Mark


                          * RECOMMENDED READING *

    Before attempting this upgrade, I strongly recommend that you read this
document in its entirety.  I'll be referring to several of the figures that
are included with this procedure to briefly describe the nature of how the
memory is manipulated.  I will not go into detail as far as clocking pulses,
timing tables, etc. to explain how this is achieved.  But I will explain
the necessary functions enough to help with trouble isolation in case the
computer does not work initially after the upgrade is installed.  DON'T
WORRY!  I've included some very useful troubleshooting tips that should get
your machine up and running in a relatively short period of time.


                 * BECOMING FAMILIAR WITH THE MEMORY LAYOUT *
                        AND BASIC MEMORY FUNCTIONALITY

       (Note:  Not all motherboards may be labled in the same manner.)

    Take a look at Fig. 1.  What this illustrates are all of the locations of
the 41256-12 Dynamic Random Access Memory (DRAM) chips on the 520ST
motherboard.  They have been installed in one long row.  The lowest (U16)
being to the left.  And the highest (U45) being to the right.  All 16 of these
chips will need to be removed in the first part of the upgrade (To be
performed later.  First read the rest of this.)

    The Memory Management Unit chip C025912-38 (MMU CHIP U15, FIG. 2)
addresses the DRAM basically in "BANKS" of eight chips each.  Two "BANKS" make
up a "ROW".  The 520ST has one "ROW" of DRAM'S to make up roughly 512K of
usable memory.  As the MMU chip reads and writes to the DRAM'S, it addresses
each of the chips by use of several "control" signals.  Two of which are named
Column Address Strobe 0 Low (CAS0LOW) or Column Address Strobe 0 High
(CAS0HIGH).  The CAS0LOW strobes the lower eight DRAM'S (BANK 0-The 8 DRAM'S
to the left.)  The CAS0HIGH strobes the upper eight DRAM'S (BANK 1-The 8
DRAM'S to the right.)  In addition, the MMU chip uses a signal that "strobes"
all 16 of the DRAM'S at the same time.  This signal is called Row Address
Strobe 0 (RAS0).  There is another signal that provides "control" over the 16
DRAM'S.  It is referred to as Write Enable (WE).

    Now notice that I am not going into explicit detail as to the exact nature
of how the signals are timed and sequenced, etc.  That portion isn't really
necessary to complete the upgrade.  But it is important to know these signals
are used by each of the DRAM'S.  They all need these "control" signals to
perform for the MMU chip.  And all of these signals are absolutely necessary
for the DRAM'S to share.

    The DRAM'S also share the data bits.  My drawings refer to them as
"ADDR0 thru ADDR9".  These are the signals that carry the data bits in and out
of the DRAM'S.  And all 16 of the DRAM'S need to share these signals as well.
Unlike the CAS0LOW, CAS0HIGH, RAS0 and WE signals, the ADDR signals are not
really "control" signals.  The table below illustrates all signals common to
the 16 DRAM'S;

 CAS0LOW common to DRAM'S>  U16, 17, 18, 24, 25, 28, 29, and 30 (leftmost 8)
CAS0HIGH common to DRAM'S>  U32, 33, 34, 38, 42, 43, 44, and 45 (rightmost 8)
    RAS0 common to DRAM'S>  ALL
      WE common to DRAM'S>  ALL
 ADDR0-9 common to DRAM'S>  ALL

    Now there are two more signals that I haven't mentioned yet.  Those being
the DRAM Data In (DIN) and Data Out (DOUT) signals.  These are actually data
paths that eventually end up at the video shifter chip.  I'm not going to
waste your time (or mine) attempting to explain the video shifter chip
operation.  It isn't necessary for this upgrade.  Just remember that all the
data will eventually end up at the video shifter chip.

    The DIN and DOUT signals are not shared with "neighbor chips".  These
signals are particular to each individual chip with their own data paths.  In
Fig. 3 you will note that I illustrate ideal areas to "open" or "cut" the
signal traces to accommodate the 1MB DRAM'S (more on that later, just wanted
you to take a look).  But it does illustrate that each chip has its own
dedicated data path. It is very important that these DIN and DOUT paths are
kept separate from each neighbor DRAM chip.

    You might be asking yourself, "Well, how does one fit 4MB of memory into
this machine?"  It's easy.  Study figure 2 for a moment.  Notice that on pins
18, 21, and 22 there exists RAS1, CAS1LOW and CAS1HIGH.  These three "control"
signals support an upper row of 16 1MB DRAM chips.  So when you finish
installing the bottom 16 chips and they check out okay, this procedure will
instruct you as to the installation of the upper 16 1MB chips.  All signals
are shared between the upper and lower "ROWS" of memory with the exception
of the RAS0 and RAS1, CAS0LOW and CAS1LOW, CAS0HIGH and CAS1HIGH signals.


             * LET'S COMPARE A 256K DRAM CHIP TO A 1MB DRAM CHIP *

    Look at Fig. 3, upper left corner.  You will see a representation of a
256K DRAM and a 1MB DRAM.  Note that the 1MB DRAM has two extra pins on it.
Pin number four on the 1MB DRAM is not connected.  Pin number 15 on the 1MB
DRAM is ADDR 9 (an extra DATA BIT!!!).  If you look at these two DRAM chips
long enough, it might suddenly dawn on you that a person could just about plug
one of the 1MB DRAM'S right into the motherboard where the 256K DRAM is.
Essentially, that's what you are going to do!  But some slight modification to
the 1MB DRAM'S are necessary.  And a few "new" data paths must be put in place
to allow proper operation of the 1MB DRAM'S.

    What will be happening is, some of the pins on the 1MB DRAM'S will be bent
in an upward fashion so that the chip will fit into the existing sockets.  New
data paths will be connected via the bent pins.  This will all be done so that
if you choose to upgrade your computer to a full 4MB, you can "piggy-back" the
upper 16 1MB DRAM'S with minimum effort.

    Now, before you start questioning my sanity with, "Is this guy crazy?
Bending pins on chips?!!!  Expensive chips!!??!!  Piggy-backing 1MB
DRAM's??!!  Believe me.  It works.  And it works very well!  I have
performed this upgrade on four different revisions of 520ST motherboards with
excellent success.  (Not to mention several 520/1040STfm's.)  Two of the 520ST
systems I did have been running for over 18 months without a glitch of
trouble.  The other two 520ST systems have been running flawlessly for just
under a year.  All without excessive drain on the power supply causing
premature failure in that area.  And no excessive heat inside of the Radio
Frequency (RF) shielding causing solder joints to become "weak" (as I've heard
from a few novices).  Most of the "plug-in" memory expansion modules (all of
them that I know of, personally) draw their power from the original ST power
supply.  And all of them (in some way) plug into the video shifter socket.


         * SOME PROBLEMS I'VE EXPERIENCED WITH MODULAR UPGRADES *

1.  Most expansion modules plug into the video shifter socket.  Without solder
connections here, the possibility for a "weak" connection is relativley high
after a period of moderate to heavy use.  The contacts expand and contract as
the temperature fluctuates during periods of being energized and de-energized.
One of the key indications that the connections are weakening, is the screen
developes "noise spots" or "drop outs" when the computer is first turned on or
after the computer has had ample time to heat up.  Soldering the module into
the video shifter socket, most cases, will fix the problem immediately.

2.  Most expansion modules use some sort of a "pin-grid" that plugs into the
MMU chip socket.  (Not a good place if you ask me.  But that's my opinion.
And my opinion is worth what you paid me for it! <grin>.)  But you end up
having the same type of problem in this area as with the video shifter set-up
due to the heat.  And if you notice, by looking at your motherboard, Atari
installs retaining devices over the MMU chip because they most definitely DO
NOT want that baby coming loose!  So it makes good sense to me not to tamper
with it.

3.  Most expansion modules carry additional components to function properly.
Namely, 10-33 OHM resistors, 3-68 OHM resistors, and 34 assorted capacitors.
Now if that doesn't put an additional strain on the computer power supply!
Not to mention the heat dissipation from the resistors!  The additional
components you'll need for this upgrade project (excluding DRAM chips) total
four.

4.  Most expansion modules require removal of the RF shielding around the
video shifter chip and associated circuitry.  This allows noise into, as well
as out of, this noise critical area.  In fact, some of the wires that connect
the expansion modules to the rest of the motherboard can perform like a little
"antenna" that conducts noise transients in and out of the video shifter area.
I have soldered filter capacitors in-line with these wires to reduce the
amount of noise transients on the lines.  It works, but why add MORE
components?

    It would be foolish of me to say that none of these memory expansion
modules work.  Because obviously they do!  And a great many Atari users have
had absolutely no problems at all.  And are very happy with their upgrade
modules.  What it comes down to with me is personal preference.


                             * SOLDERING TIPS *

    If you're soldering talents are good, then skip this section.  But I would
like to mention that Radio Shack sells an excellent iron for this project.
It's their 15 Watt IC Iron.  It is grounded, and not too hot for the DRAM
chips.  I think it runs in the neighborhood of $8.00.  They also sell a good
"Solder Vacuum Pencil" tool that makes removal of the old DRAM'S a snap.  So
pick one up while you're there (this isn't a sales pitch for Radio Shack.
But if you don't want to go out and purchase a Weller, their's works well).

REFER TO THE "SOLDERING TIPS - DIAGRAM 1"

    TIP 1.  When removing the old 256K DRAM'S, be sure to place the solder
            iron tip against the chip leg and the solder pad.  The solder pad
            could also be referred to as the "contact pad".  This is the
            portion of "metal" that connects the chip leg to the motherboard
            and other components via the "data paths" or "solder runs".
            By holding the iron between the chip leg and solder pad for a
            fair amount of time, the solder will become sufficiently HOT for
            the solder vacuum to draw all of the old solder out.

    TIP 2.  Just as soon as the solder iron has been pulled away from the
            point that was heated, quickly place the solder vacuum tip over
            the leg attempting to make a "seal" with the end of the tip
            against the solder pad.  Then actuate the vacuum by depressing
            the release button on the vacuum tool.  Because the solder iron
            tip was left in place for a fair amount of time, the solder
            should remain somewhat in a "liquid" state.  This will give
            ample time for all of the old solder to be extracted into the
            solder vacuum chamber.  If the solder iron is not left long
            enough on the solder pad, the solder will not get hot enough
            through the solder pad, and extraction of the old solder will be
            difficult.  It is very important to remove ALL of the old solder.
            Use a small flashlight to inspect the openings once the solder
            has been removed.  Re-heat, and use the vacuum again if needed.

    TIP 3.  When it is time to solder the new 1MB DRAM'S in place, you may
            want to come back to this TIP.  Place the new solder on one side
            of the chip leg and the solder iron tip on the opposite side.
            Make contact with the solder pad and chip leg with both the solder
            and iron, make contact with the solder pad as well.  This will
            heat everything up so that the new solder will adhere to both
            elements (chip leg and solder pad).  "Feed" the new solder into
            the solder pad area so that it flows around, and down into
            the solder pad filling it up.  It is necessary to feed an extra
            amount of solder so that a slight build up of solder will collect
            around the chip leg on the component side of the motherboard (see
            TIP 4).

    TIP 4.  This illustration simply indicates that it is necessary to use a
            bit of extra solder when putting the first row of 1MB DRAM'S in
            place.  The reason for this, when the second row of 1MB DRAM'S
            are placed over the bottom row (piggy-back style), simply placing
            the solder iron tip onto the top leg will re-heat the extra
            solder causing both legs to bond together.

    TIP 5.  When the top 1MB DRAM is in proper position, it should not be
            offset as shown in this illustration.  With the top chip centered
            over the bottom chip, the legs will bow slightly putting pressure
            on the extra solder.  Once the solder tip is placed onto the side
            of the top chip leg, the solder will melt quickly and the leg will
            "contract" or "press" up closer to the bottom chip leg.  This is
            how you will be able to tell that a good solder joint has been
            formed between the two legs.

    TIP 6.  While heating the top 1MB DRAM leg, try to "capture" a small
            amount of the extra solder with the tip of the iron and drag it
            in an upward manner.  This darn near guarantees an excellent bond
            between the two chips, avoiding the possibility of a "cold"
            solder spot.

EXTRA TIP!  This tip is not illustrated.  But I recommend finding an old
            circuit board with some components on it and practicing with the
            solder vacuum pencil tool.  Remove a few components to get a feel
            for how the tools react when being used.  Once you have removed
            a few components, re-solder them into place using some of the
            tips I've included with this procedure.  I think you'll find
            it's sort of fun.

The remaining soldering tips and techniques are explained on the
illustrations.


                 * FIRST THINGS FIRST.  PREPARE A WORK AREA *

    You're going to need plenty of light.  So position a lamp nearby that
shines brightly on the computer and around the work area you'll be conducting
business in.  If you like headaches, make sure the lamp shines brightly in
your eyes.

    Now some "home brew" projects I've read in the past (i.e. 1987 "Piggy-
backing DRAM'S for 1MEG upgrades") suggest using a towel to work on.  Then
it is recommended placing a piece of foil over the towel.  Well, if you do
this, when you place the motherboard component side up on top of the foil,
the legs will puncture the foil and the foil will end up sticking to the
motherboard (kind of like working on flypaper).  I don't like the idea of
working on a towel either.  Have you ever pulled a towel out of the clothes
dryer and noticed how the socks have this incredible ability to "cling" to
the towel?  STATIC!!!!  So I find that a large piece of CLEAN cardboard,
taped to the table-top works very well.  And for static,  I just take a
L O N G  piece of wire and strip both ends.  Then I wrap one of the stripped
ends to a long screw driver and stick the screwdriver in the ground outside
of a nearby window.  If I'm worried about static ruining one of the DRAM'S,
I just ground myself on the exposed piece of wire that is literally attached
to ground.  (It works just fine!)

    Make sure you have a damp sponge in a dish on your table-top to wipe off
any excessive carbon buildup on the solder iron tip.  I strongly recommend
purchasing some Tip Tinner & Cleaner from Radio Shack (Catolog No. 64-020).
It's kind of expensive, but it does a real fine job cleaning and conditioning
the solder iron tip.  After immersing the tip in the compound, wipe any excess
away on the damp sponge.  Soldering on this upgrade with a dirty solder iron
tip will greatly increase the chances of the upgrade breaking down sooner or
later.  It's kind of like, trying to breathe thru an obstructed nasal passage.
You still get oxygen, just a bit, but not quite what you would normally
require.  Know what I mean?  So give those DRAM chips some air!


                        * OPENING THE COMPUTER *

     (NOTE:  NEVER WORK ON EQUIPMENT THAT IS PLUGGED IN OR ENERGIZED!!!)
           >>>>>>> DISCONNECT ALL POWER BEFORE PROCEEDING <<<<<<<

    Piece of cake!  Turn the computer over so the keyboard is face down.
Locate three phillips type screws near the front of the computer and remove
them.  Now locate three phillips type screws near the back of the computer
and remove them.  Now, holding the computer together with both hands, turn
the computer over so that the keyboard is face up.  Gently lift the top half
of the plastic case up and off of the computer.  Place it aside in a safe
place away from your work area.

    Next you should gently lift the keyboard up and away from its resting
place.  Be careful not to strain the keyboard connector that attaches the
keyboard to the motherboard (right-hand side).  Now follow the wires from the
back of the keyboard to the motherboard and locate the keyboard connecting
plug.  Grasp the plug and pull gently up to disconnect the keyboard.  Place
the keyboard in a safe place out of the area that you are working in.  And
possibly covered so the cat or kids won't see it.

    You will need to use a relatively small pair of needle-nose pliers to
remove the RF shielding around the motherboard.  There should be four (4)
tabs along the front of the motherboard that secure the top of the RF
shielding in place.  Using the needle-nose pliers, straighten the tabs so
that they are in-line with openings just below each tab.  There should be
three (3) tabs along the left and right sides of the motherboard, do the same
to these tabs.  Now there are two (2) tabs along the back of the RF shielding
that are somewhat difficult to get to (that's why you need a relatively small
pair of needle-nose pliers for this job).  Straighten these as you did the
others.

    Okay!  If everything is straight, pull the top of the RF shield off.
Be careful handling the RF shield as it is some what easy to cut a finger
on the edges since it is fabricated out of sheet metal.  Put it aside in
a safe place away from your working area.  Now locate three (3) phillips type
screws along the front of the motherboard and remove them.  Next locate three
(3) phillips type screws along the back of the motherboard (near the ports)
and remove them.  Double check for any additional screws that might have been
missed.  If all of the screws have been removed, gently lift along the front
side of the motherboard as you pull the assembly from the bottom half of the
plastic case.  Set the plastic part of the case away from the area that you
are working in.

    Next, stand the motherboard on any one of its side edges and gently press
the tabs that you straightened so that the bottom portion of the RF shield
begins to separate from the motherboard.  Finish pressing on all of the tabs
so that the RF shield is easily removed.  Put the RF shield aside in a safe
place so that it does not clutter up your work area.


                        * REMOVAL OF THE 256K DRAM'S *

    You might want to wear a set of safety glasses while performing this
procedure.  Solder has a tendency to become airborne at times.  And when
it's hot, it can stick to you like a cactus needle to an eye-ball!  Please
be careful!

    This is the part I dislike the most.  Removing the 256K DRAM chips.  It
takes awhile.  But don't lose patience.  The only pin on each of these chips
that is very difficult at times is pin number 16 (VSS).  You may have to hold
the solder tip on pin number 16 as you extract the chips with a relatively
small pair of needle-nose pliers.  But it works just fine.  Refer to the
Soldering Tips - Diagram 1, TIP 3 and TIP 4 illustrations as well as the
narrative section for help regarding removal.  There are hmmmm.... let's
see.... 16 chips X 16 legs.... that's 256 solder points to undo!  (Sure you
couldn't use a cup-o-coffee first?)

    De-solder all of the pins on each DRAM chip prior to removal of the chips.
This will help to expedite the process.  When you are ready to "extract" the
256K DRAM chips, use a small jewelers screwdriver to sort of "pry" the chip
away from its socket by placing it between the bottom side of the chip and
the top side of the motherboard.  If at first it seems terribly bound up
somewhere, turn the motherboard over and inspect the legs to see if they have
attached themselves to the sides of the solder pads.  Gently pressing on the
side of each leg that appears to be attached to the solder pad will quickly
"snap" the leg free without ruining any of the solder runs on the motherboard
(if all of the solder has been removed first.  See Soldering Tips - Diagram 2,
Tip 3).  If you decide to use a small jewelers screwdriver to pry the chips
loose, don't pry so hard that you crack the motherboard.  Be gentle.  It is
necessary to help the chip out of its place by making certain that all or most
of the solder is removed first.

    Once all of the memory chips are removed, inspect each opening by holding
the motherboard up to a light.  Look for any remaining solder that might
prevent the new 1MB memory chips from seating properly.  Use the solder iron
and solder vacuum to clear any obstructions.


                             * CUTTING TRACES *

    This part can be kind of fun if you're into whittling.  Be sure to use
caution while cutting on the traces.  The copper foil will sometimes cause
the knife blade to bind.  And once the copper gives out as pressure is
applied, the knife will free up and could slip.  This could damage the
surrounding traces or components as well as hands, fingers, etc.

    Look at figure 3.  In this diagram, all of the traces that need to be cut
are drawn in their approximate locations regarding the motherboard layout.
Take a few minutes to study the layout on your motherboard.  Compare the trace
locations to those that have been drawn in figure 3.  If there are any
differences, draw them in on the sheet that figure 3 is printed on.  This will
help later if for some reason the computer does not appear to be functioning
properly and troubleshooting is required.

    The "X" on each trace illustrates the ideal place to cut.  Try to locate
each cut in an area that will not be obstructed by components or wires later
on.  All of the traces lead to little solder pads.  These pads go through the
motherboard onto the bottom side.  Reconnection will occur at these locations.
The only exception will be at U27, pin #16.  This connection runs from pin #2
of memory chip U28.  Notice that pin #2 of U32 is connected to pin #14, U32
and then over to the underside of U33.  The trace under U33 runs along the
top side of the motherboard.  Don't let it throw you later on when you start
re-connecting the DIN and DOUT signals of the 1MB memory chips.

    Remember, DIN is on pin #2, and DOUT is on pin #14 of each memory chip.
The signal traces tie these two signals together for each respective chip.
These signal paths must be opened to accommodate the 1MB DRAM chips.  Later,
when new data paths are installed, this pin #2 of the old 256K DRAM will
become the data path for RAS0.  And the old pin #14 will become the new data
path for ADDR9.


                   * DIN AND DOUT PRELIMINARY WIRING *

    Take a look at figure 4.  With the 256K memory chips removed, and the
DIN and DOUT traces cut, it is necessary to solder a four or five inch piece
of wire-wrap wire at these locations.  If the wires are not put into place
prior to the installation of the 1MB DRAM chips, it will be very difficult
to route the DIN and DOUT signal paths for the five chips illustrated (U30,
38, 43, 44, and 45).  Refer to the Solder Tips - Diagram 2, TIP 4 for
assistance in this area.


                     * PREPARING THE 1MB DRAM CHIPS *
                           (Refer to figure 5).

    Most 1MB memory chips that I have performed this on have very sturdy pins
on them.  But caution is highly recommended to avoid accidental breakage of
the pins.  Use a small set of needle-nose pliers.  If you can gain access to
a pair, use Hemostats.

    Start by ensuring your static level is to a minimum before handling the
chips.  The only pins that require bending are illustrated in figure 5.  They
are pins 1, 4, 17 and 18 (bottom 16 DRAM'S only).  And pins 1, 3, 4, 16, and
17 are modified for the top row of 1MB DRAM chips.  * DO NOT BEND PIN #18 FOR
THE TOP 16 DRAM CHIPS! *  Remember that pin #4 is not connected and should be
trimmed off after the memory chip is installed.  You can trim off pin #4
prior to installation.  But it is much easier once the chips are in place on
the motherboard.

    So go ahead and bend pins 1, 4 and 17 straight up in the opposite
direction as the others.  It isn't real critical to get them perfectly
straight.  Bend slowly to avoid snapping them off.  On pin #18, place which
ever tool you are using just about in the middle of the leg.  Then bend it
slightly towards the under-side of pin #17.  Once you've gotten it there,
bend it so that the end of the pin is straight downward.  You will know when
pin #18 is in the proper position when it lines up under pin #17.  Also, try
inserting the chip into the motherboard so that pin #18 enters into the
opening where pin #16 of the old 256K DRAM chips were.  The signal on pin #18
is VSS.  And pin #16 on the old 256K DRAM chips were VSS.

    Try fitting the chips into the motherboard.  Don't place them firmly until
you are ready to solder them into place.  Orientate the modified 1MB chips so
that pin #2 enters into the hole where pin #1 on the old 256K chips were.
What you should end up with is;

  OLD 256K DRAM OPENING        SIGNAL ON 1MB DRAM       1MB DRAM PIN #
-----------------------------------------------------------------------------
          1                    WRITE ENABLE                pin 2
          2                    ROW ADDRESS STROBE          pin 3
          3                    - - - - - - -      nothing (pin #4 not used)
          4                    ADDR0                       pin 5
          5                    ADDR1                       pin 6
          6                    ADDR2                       pin 7
          7                    ADDR3                       pin 8
          8                    VCC                         pin 9
          9                    ADDR4                       pin 10
         10                    ADDR5                       pin 11
         11                    ADDR6                       pin 12
         12                    ADDR7                       pin 13
         13                    ADDR8                       pin 14
         14                    ADDR9                       pin 15
         15                    COLUMN ADDRESS STROBE       pin 16
         16                    VSS                         pin 18
-----------------------------------------------------------------------------

Note that some of the ADDR bits are not matched up with the old 256K memory
chips.  Don't worry, this has no effect on the operation of the computer.
What will be necessary after the chips are soldered into place is the routing
of two new data paths on the bottom side of the motherboard (RAS0 and ADDR9).
The DIN and DOUT paths will be done individually for each chip by reconnecting
pins 1 and 17 on the top of each chip.  With extra wire-wrap wire, the signals
can then be reconnected to the appropriate locations on the motherboard at
the solder pad locations.


                   * SOLDERING THE LOWER ROW INTO PLACE *

    In case you're wondering, it takes 16 1MB DRAM chips to comprise 2MB of
user memory.  Now in most IBM or IBM clones they use two additional memory
chips to make up 2MB of memory.  (This is for parity reasons).  Just thought
I'd mention it!

    Now insert all of the modified 1MB memory chips into the motherboard.
Be careful not to jam any of them into place where a pin may get bent.  You
might find it necessary to hold each chip by either end (not over the pins)
and gently press the sides with pins against the cardboard you're working
over to straighten them out a little.  Most chips are manufactured with the
pins slightly bowed outward.  This is because most chips are inserted into
sockets.  And by having the pins bowed outward, insures a sufficient amount
of pressure against the sides of the sockets making better contact once the
chips are in place.  After each new chip is in its proper place, turn the
motherboard over so that you are looking at the non-component side and make
sure that none of the 1MB DRAMS have fallen out.

    Refer to soldering tips 3 and 4 in this procedure along with the
corresponding diagrams (Soldering Tips - Diagram 1 - Tips 3 & 4).  This will
help you as each new 1MB memory chip is soldered into place.  Remember to
add a little extra solder for the second row of 1MB memory chips for the 4MB
upgrade.  (If you're not upgrading to 4MB at this point in time, I still
recommend adding a bit of extra solder in case you decide to add the extra
2MB at a later point in time.)

    Continue soldering each of the 1MB DRAM chip legs until all of the chips
have been soldered into place.  When you are finished with the soldering, it
is necessary to check the integrity of all solder points.  So turn the
motherboard over so that you are looking at the component side and prepare
to take continuity readings.


         * CHECKING THE INTEGRITY OF THE NEW SOLDER JOINTS *

    If you don't already have a multi-meter (ohm-meter), Radio Shack sells a
few models for under $20.00.  If you don't have $20.00, then borrow a meter
from school, work, or a friend.  This section is very important.  If you
don't check your work at this point in the procedure, you're asking for quite
a bit of heartache.

    What you will be looking for is what are referred to as "cold solder
joints".  Now it may not be that there are any cold solder joints in your
work.  But when the old 256K DRAM chips were pulled, often the solder runs
leading to the solder pads will crack open causing an "open" so that the
signals can not make good connection.  This will render your computer useless.
Checking for this type of damage is very simple.  And 99% of the upgrades
that don't work initially are due to an open signal path somewhere along the
line.  So let's check it out.

    Refer to figure 6.  Place the scale setting on the multi-meter to RX1K.
Place one of the meter leads on pin 18 as shown.  Place the other meter lead
on the chip at the other end (pin 18) as shown.  Look for a "FULL SCALE"
deflection on the meter.  If you are reading about 1/2 deflection then one
of the meter leads is not on pin 18 and you are reading resistance thru the
chip.  In this particular check, the key readings will be either "FULL SCALE"
deflection (good connection).  Or no reading at all (an open exists at that
point).  Check each chip on pin 18 and on pin 9.

    Refer to figure 7.  Check the pins indicated in this figure.  Follow the
notes referenced in this figure.  Note the method of "bracketing and half
splitting" that is used to narrow down where the open trace is located.  This
method of troubleshooting is very useful for "smoking out" problem areas.
Make any necessary repairs as explained in the illustration.  Once you are
certain that all connections are good up to this point, move on
to the next section.


         * CONNECTING DATA IN (DIN) AND DATA OUT (DOUT) SIGNAL PATHS *

    Refer to figure 3 and figure 8.  Note that all of the new signal paths
are connected with wire-wrap wire.  Both pins 1 and 17 are re-connected to the
solder pads that the original DIN and DOUT signals went to prior to cutting
the paths with an x-acto knife.  Use the wires that were soldered into place
in figure 4 earlier to connect U30, U38, U43, U44, and U45.

    Note that the paths for U32 and U33 cross one another.  When soldering
these into place, make sure that the wires do not touch.  The wire insulation
gets somewhat soft when heated with the solder iron.  If the two wires are
touching, the insulation might melt between the two allowing the metal part
of both wires to bond together.  Thus a short between the two signals will
result.

    One other item to keep in mind while performing this procedure is, keep
the wire runs close to the center of each chip while installing.  This way,
when the top row of 1MB chips are installed (piggy-backed), the wire on the
bottom row will not bond to any of the chip legs on the top row as they are
heated and soldered into place.

    When all of the DIN and DOUT paths are routed and re-connected, check
your work with a multi-meter.  Make sure that none of the new paths are
shorted to any other areas.  Check each connection by placing one of the meter
leads to the solder pad, and touch the other lead to the very top of each chip
leg that the path is soldered too.  This will accurately test each solder
joint for weak or cold solder joints.


              * CONNECTION AND ROUTING OF NEW DATA BIT 9 (ADDR9) *
                             AND WRITE ENABLE (WE)

    Study the pin numbering scheme of the MMU chip U15 illustrated in figure
9.  It is necessary to connect a 33 ohm (1/4 watt) resistor in-line with this
signal path.  Trim one side of the resistor lead shorter than the other.
Leave enough of the lead so that a small loop can be formed that will fit over
pin 64 of MMU chip U15.  Trial fit the resistor.  On the long lead, slide a
piece of heat shrink tubing over it so that ample insulation is achieved from
other components.  Solder the resistor in place as shown in figure 10.

    Now strip one end of the wire wrap wire just enough to expose about a 1/16
inch section.  Solder this to the end of the resistor lead.  Leave the wire-
wrap wire attached to the spool and follow the solder/installation technique
illustrated in figure 10.  When the new signal path is installed, check your
work with a multi-meter.

    Look at figure 10.  Note how the new signal path for the WE signal is
installed.  Locate an ideal spot to place the wire jumper on your motherboard
and install it.  Check to make sure the WE signal is connected properly by
placing one of the multi-meter leads to pin 23 of MMU chip U15 and the other
lead on any pin 2 (or pin 1 on the bottom side of the motherboard) of the
1MB DRAM chips.  Check across all new 1MB DRAM chips to make sure a full
scale meter deflection is achieved.  This will ensure the WE signal is going
to get to all DRAM chips.


                   * ROUTING THE NEW SIGNAL PATH FOR RAS0 *

    Refer to figure 11.  Note that the same technique used to route ADDR9 is
used to route RAS0.  Start by connecting one end of the wire wrap-wire to
pin number 8 of the MMU chip on the bottom side of the motherboard.  Next,
melt away a small portion of the insulation at pin number 2 on U16.  Solder
the wire-wrap wire at this point and the remaining pin number 2's on each
1MB DRAM chip.  It is necessary to route the wire around the pins that it
will not be connected to.  Use caution and make sure the insulation is not
touching any other metal surfaces when heated.  It may bond accidentally
to a location that it is not supposed to.  This will cause problems and the
computer may not work properly.  Remember that in actuality, pin number 2
on the bottomside of the motherboard is pin number 3 on the 1MB DRAM chip.

    After all of the connections are made, double check your work with a
multi-meter.  Again, watch for a full scale deflection on the meter at each
chip.  It is a good idea to check from pin 8 of the MMU chip to each pin 2
of the 1MB DRAM chips.  If you are checking on the top side of the
motherboard, remember that RAS0 is on pin number 3.


                   * PARTIAL REASSEMBLY FOR TESTING *

    You may want to recheck all connections prior to partial reassembly for
testing the first 2MB of memory.  Make sure you clean all of the areas that
were being soldered on with rosin and flux remover.  The spray type usually
works best.  Hold the motherboard so that the DRAM chips are facing towards
the ground.  Spray both the component side and the non-component side.
Allow the remover to "run off" the motherboard away from all of the other
components.  Allow all excessive remover to evaporate COMPLETELY before
re-energizing the computer.  (Refer to figure 12 for tips on cleaning.)

    Insert the motherboard into the bottom portion of the plastic CPU case.
Use one of the small phillips head screws to secure the motherboard in place
along the front side.  Reconnect the computer keyboard at the right side with
the connector.  Observe the orientation of the connector pins and avoid
bending any of them.  Set the keyboard into place so that it rests properly
on the provided stand-offs.

    Plug the power supply connection into the appropriate location at the back
of the computer before energizing.  Connect the disk drive and insert the
disk containing the memory test software.  Connect the monitor and mouse.

    Now plug the power supply into a convenience outlet.  Energize your
monitor and disk drive.  Turn on the computer and observe that it boots just
a little bit slower than usual.  (Particularly if your TOS is version 1.2 or
lower).  Load and run the MEMTEST.TOS file on the disk.  Observe that it
reports "2048Kbytes memory detected".  If the computer does not boot at all,
then remove the motherboard and take continuity checks on every pin of every
1MB DRAM chip using the suggestions included with this procedure.  Refer to
the special trouble-shooting section included as well.

    While taking continuity checks, put one of the meter leads on the
associated pin of the MMU and then the other to the pin on the DRAM that
coincides.  Check across every pin on every chip.  What you are looking for
are "opens" or no delfection on the multi-meter scale.  As you come across
any opening, write down the location so that you can go back and make the
necessary repair.  Once the repairs are made.  Recheck the connection with a
multi-meter.

    99% of the time, if an upgrade does not work initially, it is due to
a bad connection somewhere.  "Bad" meaning, not connected or open.  You should
also inspect everything visually for shorts in the new wiring installed.  And
don't forget to take continuity checks on the new DIN and DOUT signal paths
that were installed.

    Once the first 2MB of memory is working, remove the motherboard and
prepare to piggy-back the upper 2MB of memory.


                   * PIGGY-BACKING THE UPPER 2MB OF DRAM *

    If you haven't already prepared the 16 1MB DRAM chips then do so now by
following the technique described earlier.  Refer to figure 5 for more
details and which pins to modify for the upper row of 1MB DRAM chips.

    Place each chip over the lower 1MB DRAM chips so that the pins line up
nice and even between the upper row and lower row.  If the legs on the upper
chips do not come in contact with the lower chips, then it is necessary to
add a slight bend inward on the upper chip legs.  Now refer to SOLDERING TIPS
DIAGRAM 1, TIPS 4 & 5 for proper solder techniques.  Look at SOLDERING TIPS -
DIAGRAM 3 for further help with the installation of the upper row.  Figures
13 and 14 provide the information regarding new signal paths for the CAS1LOW,
CAS1HIGH and RAS1 signals.

    I have installed 68 ohm (1/4 watt) resistors inline with the CAS1LOW,
CAS1HIGH and RAS1 signals before with no noticable differences regarding
operational characteristics of the computer.  If you are concerned about
"undershoot" (noise getting back to the MMU chip from the DRAM chips), then
you may want to install the 68 ohm resistors inline with these signals when
routing the new signal paths.  I've put in several upgrades without the
resistors and have had absolutely no trouble at all with the computer
operating properly.  Nor have I witnessed any short lived MMU chips as a
result.  My personal opinion is the resistors add an extra load to the MMU
chip which means the chip must drive harder to operate the 1MB DRAM chips.
And on some occasions, I've had to remove the 68 ohm resistors to make the
upgrade operational.  Keep this in mind if your upgrade has a difficult time
coming up.  You may need to go back and remove the resistors.

    Pin 18 of the upper row will line up over pin 18 on the lower row.  Solder
the upper pin 18 to the lower pin 18 at the bend where the lower chip leg
enters the chip package.  (Refer to SOLDERING TIPS - DIAGRAM 3, TIP 3).

    There are relatively large capacitors between each of the DRAM chips on
the motherboard.  It is easy to work around these while installing the upper
row if you move them out of the way by use of a small flat-tip screwdriver.
Just press slightly on one side to give you clearance to one chip.  Then
press on the other side to give you room enough to work on the chip that is
opposite.  Remember, with proper pressure between the upper chip legs and
lower chip legs, all that is necessary is the heating of the upper chip leg.
When the upper chip leg becomes hot, the leg will "sink" into the solder that
is built up around the lower chip leg.  Don't hold the solder iron tip on
the leg for minutes at a time.  But a few extra seconds will allow proper
bonding.

    Follow the suggestions in figure 6 and meter all of the new connections
to ensure they are installed properly.  Make any necessary repairs before
partial reassembly for testing.  Now go back to the * PARTIAL REASSEMBLY FOR
TESTING * section and follow the instructions.  Test all of the new memory
chips for proper operation.

    If you find that the installation is failing, go to the special trouble-
shooting section included with this document.  If it works fine;
****************** CONGRATULATIONS ON A JOB WELL DONE! **********************
It takes a skilled pair of hands, a keen eye, a bit of intellect and a TON
of patience to perform this upgrade correctly.  Give yourself a pat on the
back.  If I were there with you, I'd shake your hand!

    Well, maybe I got a little over zealous there for a second.  You still
need to snip off the excess leg portions that are pointing up towards you so
the RF shielding will fit back into place.  Refer to figure 15 for assistance
on this.  Notice on the lower right side of the figure I've included some
notes on placing electrical tape on the inside of the RF shielding to provied
a little insurance against the chips shorting out on the RF shield.  I
recommend putting a slight bend in the RF shield to give just a bit more
clearance if necessary.  You don't want to bend this shield excessively or
the keyboard won't fit properly.  Trial fit everything first before
installing it permanently.


                             * TROUBLE SHOOTING *

    As I mentioned earlier, the primary reason for a non-operational upgrade
is due to an open, or not connected signal at one point or another.  So
utilize the mulit-meter and take cold checks across each signal path in its
entirety.  Set your multi-meter scale to about the X10 range (ohms).
Locate a starting point at the MMU chip U15.  Start with the WE signal, for
example.  Now place the other meter lead at pin #2 on DRAM chip U45 (component
side of the motherboard).  If all connections are properly made, then a full
scale deflection should be observed on the multi-meter.  If you observe about
a half scale deflection then one of the leads is on a wrong pin number and
you are witnessing the resistive value through the components.  Relocate one
of the meter leads to the correct pin number and observe again.  If a full
scale deflection is not observed, and no movement is obvious on the multi-
meter scale, then there is an open in that signal path somewhere.  So leave
the meter lead at the MMU chip where it is.  And work your way backwards
from DRAM chip 45 to 44, 43, 42 and so on until you observe a full scale
deflection.  As soon as you see a full scale deflection then the opening or
bad connection is between that chip and the one just previously measured.

    Shorted signal paths are a bit more difficult to locate.  It is necessary
to check between nearby pins to determine if the signal paths are crossed
some where along the line.  If you place one meter lead on pin number 15,
use the other lead to check across to the other pins of each chip.  You should
observe about a middle scale deflection.  If you observe a full scale
deflection at any time, then there is a crossed signal path between the two
paths that are being metered.  Visual inspection at this point in time with
a magnifying glass can easily locate the short.

    Figure 16 has some notes and diagrams that should help you out if you are
attempting to trouble shoot the upgrade while it is energized.  But I strongly
recommend "cold checks" as the primary method of trouble isolation.  Use the
suggestions in figure 16 if you are certain that all connections are properly
installed.  Some of the signals may look a bit different than the drawings
in this figure.  And you may experience just a slight difference in some of
the voltage readings.  I've tried to average them based on the number of
different computers that I have tested.