Hey everyone:

Did you ever stop to think that the only other place that could be
worse than the back of the machine for the power switch would be on
the bottom?  My ST is under a shelf that allows for about 3 inches
of clearance, not quite enough to fit my hand under it to turn it
on.  (disk access is still easy)  I got sick of reaching around the
back to turn on the machine, so I developed a remote switch for
it.  This remote switch can be placed anywhere you like, limited
only by the length of the wire you install.  Mine is just to the
left of the ST, like another mouse on the other side.  The
existing switch stays in place but is overridden.  It should cost
about $5-10 to do, and takes about 1 hour.

All the parts are available at Radio Shack.  A small plastic box
(RS 270-230) holds the switch (RS 275-690).  (Rubber feet may be
necessary if it's to be mounted on a surface that shouldn't be
scratched.)  A length of 2 conductor 18-gauge wire runs from that
box to inside the ST.  I ran it through the hole where the RF
modulator would be since my 1040STf doesn't have one.  If you do
that, the wire needs to be 18" long for locating it on the left
side.  It is also possible to run it through the case over the
cartridge port if you don't use that; in that case, a 12" wire will
do.  Heck, if you want the switch 25' away, then that's possible
too!

Turn off the computer and unplug everything leading into it.
Remove the top half of the case and the RFI shielding over the
power supply.  Solder one end of the wire to the two switch posts
on the power supply.  Don't worry about polarity; it doesn't
matter.  If you find it easier, remove the power supply.  Snake the
wire under the RFI shielding and outside the case as described
above.  Install the RFI shielding and put the case back together.

Drill a small hole in the side of the box for the wire to go
through.  A 7/32" bit should do it.  Drill another hole, this time
on the top (plastic side) of the box for the switch.  You'll need
a 5/8" bit for the switch mentioned; if you're like me and don't
have one that big, draw a 5/8" circle and using a 1/8" bit, make a
bunch of holes along the edge and knock out the center and make the
edge smooth.  Put the switch in the hole and pull the wire through
it's hole.  Solder the wire to the switch; again, it doesn't matter
what wire goes to what post.  Put the box back together and install
the feet, if used.

Try it!  Your remote switch is now the master power switch!

I suppose it would be just as easy to run an extension of the Reset
switch.  Though I haven't done that, the procedure is the same
except that removal of the motherboard is probably required to
solder the wire on to the reset switch.  But it's easier to get
to in it's existing location, so I didn't bother.

*note*  The Radio Shack switch mentioned is rated at 6 amps, one
more than what the power supply takes in.  If I remember
correctly, my power supply said: AC in 117V, 5A.

Bob Morrow
(Delphi-RMORROW)
(GEnie-R.MORROW10)