SIO-Driver vers. 1.0

			    by James C. McCormick


	SIO-Driver is a 'stay resident' program that enables the Atari ST to
use an 8-bit disk drive. The 8-bit drive can be accessed from the desktop  
or from an application just as any other drive would be. The program uses 
the ST's printer port to connect to the drive and emulates the 8-bit Serial 
Input/Output (SIO).  

	What you need:
	
		_ Atari 8-bit disk drive (810,1050,Rana, etc.)
		_ XformerII (or similar) cable.

	Contents of SDRIVER.ARC file include:

		_ SDRIVER.DOC - This file!
		_ SDRIVER.PRG - to be placed in auto folder and must be run
				to enable access to 8-bit drives.
		_ SCONFIG.TOS - Format and configure utility for the 8-bit
				disk drive.


1.	How to use SIO-Driver

	This program is very easy to use, and once the program is loaded
(usually from the auto folder), you won't need to run any other programs
to access the 8-bit drive.  (except to format!) You can store ST files to 
your 8-bit drives just as you would your ST drive. 
	I have written this program in hopes that some people, such as myself,
have one or two 8-bit drives around that aren't being used, as well as a 
mountain of 5 1/4" blank floppies. This program will allow you to put 
your old drive to good use.

1.1	Hooking up the system

	You must plug the XformerII (or similar) cable between the Atari ST's 
printer port and the 8-bit disk drive. You can use the cable available for
Darek Mihocka's XformerII or purchase a similar cable from me. 
(ordering instructions later) You may connect additional 8-bit drives by
daisy chaining them through the standard SIO cables. 

1.2	SDRIVER.PRG

	This is the actual interfacing software. When placed in the auto
folder (it can be run from anywhere at anytime though) it will run on 
bootup and look for a file named 'SDRIVER.DAT'. This file is created 
using the configure utility and tells the SDRIVER program which desktop
drive letter, C through P, belongs to which 8-bit drive unit, 1 through 4.
You can have up to 4 drives, each with it's own letter (or icon). 
When SDRIVER.PRG runs, it will tell you which drives are online and which
are offline. This is for your own information only, you can turn on the 8-bit
drive anytime after the program is run and access it. 
	You must note though, that of your auto-boot programs that might
use any of the operating system disk vectors, SDRIVER.PRG must be run LAST.
This is so that the configure utility will be able to sense that the SDRIVER
program is installed. Ramdisks are the main offenders here. To insure that 
SDRIVER is loaded last, use one of the public domain auto folder file sort 
programs.
	This version of SIO-Driver only supports single-sided single-density
disks, but future versions will take better advantage of higher capacity 
drives.


1.3	SCONFIG.TOS

	This program is used to format disks in your 8-bit disk drive and
create the SDRIVER.DAT file. Note that this is the only way to format a
disk since the desktop format command will not work.
	The program is menu driven and fairly self explanatory. The main menu
provides two options, formatting and configuring.

1.3.1	Formatting

	The format menu asks which drive unit to format, 1-4. This has no
connection with what drive letter is associated with a drive, it is just the 
unit number. (the number selected with the switches on the drive). After
formatting the disk, you will be returned to the main menu.

1.3.2	Configuring

	When entering the configure menu, the program will attempt to read 
an existing SDRIVER.DAT file in the current path, if one is not found, 
default configurations will be chosen for each drive. The menu options
include modifying the configuration of drives 1-4. The current configuration
will be displayed. Either a drive letter will be shown, meaning that this
drive unit will respond when you access this letter of drive icon, or an
asterik will be shown, indicating that the drive is not in the configuration.
After choosing which unit numbers will correspond to which drive, you
must select the 'save configuration' option in order to create the new
SDRIVER.DAT file. It will be written in the current path.

1.3.3	Adding the new drive icon

	After you have created the SDRIVER.DAT file using SCONFIG.TOS
program, and you have placed SDRIVER.PRG and the new SDRIVER.DAT file in
the auto folder, you must create a drive icon for your 'new' 8-bit drive. 
This process is the same for adding a ram disk.  Just click once on an
existing drive to highlight it, then select 'Install Drive' from the
options menu.  Type in the letter of your new drive in the space
provided and click on 'install'.  Now that your icon is installed, you
might wish to make it permanent by 'saving desktop' from the options
menu. 

1.3.4   Setup Summary

	_ Run the configure/format utility (sconfig.tos) to configure
	  your 8-bit drives. Be sure to 'save configuration'.
	_ copy the SDRIVER.DAT file (just created with sconfig.tos) as well
	  as SDRIVER.PRG to your auto folder and reboot.
	_ install a drive icon as the drive letter you specified in the
	  configure program and then 'save desktop' from the GEM options
	  menu.
	_ Run the configure program again to format a disk(s). 
	_ Use your new drive!


2	What SIO-Driver will (and won't) do

	With SIO-Driver installed, you can read/write/copy/delete files
on the 8-bit disk drive, just like any other drive. You can do anything
that a regular drive can do except boot from it. The file system used on 
the drive is the ST's file system. IMPORTANT: You can NOT read and write 
8-bit Atari files. The disks used by this program become ST disks. Of
course, no harm will be done by trying, but I don't want anyone to have
any misconceptions about the function of this program. The file structure
that the 8-bit drive will be using is ST only.
	Now the bad news. As you may have guessed, these drives are SLOW. 
Atari SIO runs at 19.2k baud. This didn't seem so bad on the old 8-bit 
machines but now that you have them up against the regular ST drives, the 
slow pace is more noticable. Also, not only can you not use the desktop
format option, but whole disk copies won't work either. You can copy all the 
files from one drive to the other, but you can't drag the disk icon onto
another one.
	You will also notice that while access to the 8-bit drive is active,
your mouse and keyboard is inactive. This is required because the timing
needed to interface to the 8-bit drives is software controlled and must be 
very precise, therefore while accessing, all interrupts are disabled. This
means no mouse and keyboard input. I believe that this is a small price to 
pay since you the mouse is useless in the 'busy bee' state anyway.
	With my 8-bit drives I have successfully copied/deleted files. 
I've run programs from these drives, loaded pictures and text files, and
even ARC'ed files to and from them. In all cases they have performed just
as any other ST drive (except the speed of course). One thing I haven't tried
that is certain to fail, is downloading to these drives. With the 
computer's interrupts disabled on the drive accesses, I feel certain that 
the modem would no longer receive data; try it if you must but don't say
I didn't warn you!

3.	Future plans?

	Of course future plans depend on the interest in this program. I
would like to have a desk accessory to configure and format the disks. Also,
a 'whole disk' copy would make fast backups of both your ST floppies AND 
your 8-bit disks. (one pass copier!) And certainly the ability to use the
Atari XF551 disk drive is on the horizon, as well as any enhanced or
double density drives.

4.	Shareware

	This program is indeed shareware. Upload it everywhere. But if
you find this program usefull, please send a donation. I have listed 
two options for becoming a registered user.

	1 _ Send $10 (or whatever you feel adequate) to the address below 
            and you will receive a disk containing the source code to 
            this program and a new version of the configure utility. 
            As a registerd user, you will be notified of any new versions 
            and utilities which will be available for the price of the disk
            and postage.
	2 _ Send $25 dollars to become a registered user, receiving 
	    everything mentioned above, and I will send you a SDRIVER cable
	    as well.
	    
	Be sure and let me know what kind of disk you want it on. 3.5"
single or double sided, (or even a 5.25")

5.	Feedback

	Please contact me at the address below with any questions, 
suggestions, or (shudder) bugs. I can't fix it unless I know it's broken!

6.	Many Thanks

	Thanks to John Stanley and Doug W. on GEnie for coming to the rescue
and solving a very tricky problem with the mouse.
	Many thanks to Jim Gross of the Huntsville Atari Users Group for 
lending me equipment and pointing out the many 'features' of earlier versions 
for me (some might call them bugs). Thanks to Larry Mears who before running
my code for the first time on his machine, looked from his hard drive, to his
ST, and then to me and said 'Are you sure?' 

7.	Legal

	This document and software are Copyright 1989 by James C. McCormick.
SDRIVER may not be sold. It may be freely distributed however as long as this
document and the accompanying program is not modified.
	I have made every effort to assure that this software runs bug-free,
however I cannot be responsible for any loss of data caused by this 
software.


						James C. McCormick
						P.O. Box 6333
						Huntsville, Alabama
						35824-0333

						GEnie: J.MCCORMICK4

						H.A.U.G. BBS
						(205)-461-7893
						as James McCormick