ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
               º  ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±  º
               º  ±                                             ±  º
               º  ±           DTMF Real-Time Decoder            ±  º
               º  ±      386 and 387 Turbo DEMO Versions        ±  º
               º  ±                                             ±  º
               º  ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±  º
               º                                                   º
               ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
               º    Shima-nized Advanced Utilities - J.M. Shima    º
               º         Copyright (c) 1994-95 by James Shima      º
               º                 All Rights Reserved               º
               º                                                   º
               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                   ÞÞÞÞ   R E F E R E N C E   M A N U A L   ÞÞÞÞ





             ¯ Type DTMF386D at the DOS prompt for a summary of options ®




INTRODUCTION
ßßßßßßßßßßßß

* This program functions as a real-time DTMF decoder.  One application
  where DTMF tones are used is in the standard American telephone dialing
  system.  The standard DTMF tones represent the numbers 1,2,3,4,5,6,7,
  8,9,0,*,# on a standard keypad interface.  The four reserved DTMF tones
  representing A,B,C,D are supported in the REGISTERED version.

* This program is capable of decoding DTMF tones from a Soundblaster
  Version 1.0 - 2.0, Soundblaster Pro, or TRUE Soundblaster compatible
  (16-bit or 8-bit) sound card in real-time.  Soundblaster 16 support
  has been reported to work but is fully untested at this point.

* This 386 version is geared for slower machines that cannot perform
  real-time processing with the 486 version.  HOWEVER, due to the
  streamlining of the algorithm, results MAY NOT be as accurate as
  the 486 version and can be susceptible to more decoding errors than
  the 486 version.

* This program attempts to use your coprocessor for faster floating
  point speed.  If you do not have a coprocessor, use the DTMF386D.EXE
  executable.  Otherwise, use DTMF387D.EXE for coprocessor support.

* The Soundblaster or compatible sound card MUST be connected to port
  address 220h and using DMA 1 (the factory settings).

* The input to the Soundblaster mic or line input can originate
  from any external communication device that supplies DTMF tones
  to the sound card.

* This program accepts COMMAND-LINE ARGUMENTS that are passed to the
  DTMF decoder.

* For a list of the arguments, type DTMF386D at the DOS prompt.

* The DEMO only decodes a maximum of 4 numbers.  Interested
  persons can receive the REGISTERED version with no limitations.


SOFTWARE LICENSE
ßßßßßßßßßßßßßßßß

The 386 DEMO version of the DTMF real-time decoder is shareware, and is free
for personal use only.  This is true as long as the DEMO is
not alterted in any fashion.  Registered users will receive the REGISTERED
version of the DTMF decoder and will receive documentation stating such.



The author offers no warranties on this program.  This program is provided
as is.  Use this program at your own risk.  I assume no responsibility in your
actions while you are using this program.  The author is not liable for any
damage caused to your computer while you are using this program.  Using
the program is your compliance to this statement and the license.


COMMAND-LINE ARGUMENT SCREEN
ßßßßßßßßßßßßßßßßßßßßßßßßßßßß

The program argument screen should look as follows:

Real-Time Dual-Tone Multi-Frequency Decoder, 386 DEMO Version
Shima-nized Advanced Utilities (c) 1994-95 - J.M. Shima

USAGE: DTMF386D  <sample_rate>  switches:[ <-t>number ]

Notes:  <sample_rate> = rate of incoming samples in Hz. The range
                        is 4000 < fs < 12000 for DTMF decoding.
                        The RECOMMENDED value is 4000 Hz for real-time
                        decoding.

** Sound card must be Soundblaster 1.0 - 2.0, Pro, or Soundblaster
** compatible connected to port 220h using DMA 1 (The factory settings).

Switches: -t = Defines the S/N threshold value (in dB) that DTMF tones
               must surpass for proper detection.
               The threshold S/N value can be any real, non-negative number.
               DEFAULT value is 20 dB.


EXPLANATION OF COMMAND-LINE ARGUMENTS
ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

<sample_rate>   -->  Input sample rate.  Must be in the range of 4000 to
                     12000 Hertz (Hz).  For DTMF detection, it is HIGHLY
                     RECOMMENDED THAT YOU USE 4000 Hz for
                     real-time processing.

Switches:
ÍÍÍÍÍÍÍÍ

 -t<number>    -->  The threshold that the DTMF tones must exceed over the
                    noise floor for detection (in dB).  Typically, strong
                    DTMF tones will be 20-40 dB stronger than the noise
                    in the signal.  However, noisy signals lower this
                    signal-to-noise (S/N) ratio.  The threshold parameter
                    allows the user to set the S/N threshold for detection
                    of noisier or corrupted DTMF tones.

                    * NOTE:  If nothing is entered, then the DEFAULT S/N
                             threshold value is 20dB, which is a figure
                             of merit for normal tones.


                    One must realize that dB is a logarithmic scale
                    of signal gain through the equation:
                    dB = 20 * log(signal gain).
                    Thus, a large signal gain represents a small
                    increase in the dB number (i.e. 40dB is a 100x
                    signal gain, while 20dB is a 10x signal gain).


EXAMPLES OF RUNNING DTMF386D
ßßßßßßßßßßßßßßßßßßßßßßßßßßßß

* Program start:  Run the program by typing the executable name.
* Program end:  The program ENDS when ANY key is hit during decoding!

 
DTMF386D 4000            -->   Input sample rate is 4000 Hz.
                               Input S/N threshold defaults to 20dB.

DTMF386D 4000 -t25       -->   Input sample rate is 4000 Hz.  The input
                               S/N threshold is set to 25dB.

DTMF386D 4000 -t15       -->   Input sample rate is 4000 Hz.  The S/N
                               threshold is set to 15dB.


IMPORTANT NOTES
ßßßßßßßßßßßßßßß

Since this is a real-time piece of software, certain rules must be followed
for proper use.

Sampling rate:
                Increasing the sampling rate means that samples are ready
                faster.  Thus, the computer has less time to do what
                is has to before it has to fetch more samples.  So,
                one must make the sample rate as low as it can go
                and still represent the maximum frequency in the signal.
                For DTMF tones, this minimum sampling rate is 4000 Hz,
                (due to Nyquist theorem).  IT BEHOOVES YOU to use this rate.
                Sampling at a rate higher than necessary gains you
                nothing, but INCREASES your computational overhead. For real-
                time operation, make your sampling rate as low as you can
                without violating Nyquist theorem (2x the maximum freq.
                in the signal).  So, for all practical purposes, use
                4000 Hz as your sampling rate.

Real-time processing:
                If your system cannot handle real-time processing, that
                means data will be lost.  While your system is processing
                the old data, it doesn't have time to retrieve the new
                data coming in.  This new data is discarded and the
                computer picks up fresh data when it's done with its
                current task.  Thus, results are inconsistent when real-time
                processing cannot be done.  The probability of detecting
                a given tone depends on where your computer is in its
                processing stage.  You can see that its nearly impossible
                to debug whether or not real-time processing is happening

               or not.  On top of this, your CPU takes care of many other
                housekeeping tasks.  Therefore, I have deemed "real-time"
                on the fact that a DTMF tone does not go undetected as given
                in the DTMF standards.  Closely spaced tones will be detected
                in real-time if your system can run the code in real time.

                Noisy DTMF tones are also error ridden since the processing
                window is so small no noise immunity algorithm can be
                implemented.  Note that non-pure tones may not be detected
                properly!



INCLUDED FILES
ßßßßßßßßßßßßßß

DTMF386D.EXE   -->  DTMF real-time decoder, 386 demo version.
DTMF387D.EXE   -->  386 demo version with 80387 coprocessor support.
DTMF386D.DOC   -->  This file.
REGISTER.DOC   -->  Registration form.
 

REGISTRATION
ßßßßßßßßßßßß

** For registration, please fill out REGISTER.DOC and see the DEMO screen.
   Specify media dispersement.

The REGISTERED version of this program allows unlimited decoding of numbers,
and offers other features including:

1) Automatic logging of the resulting decoded numbers to a log file.
   The session is also time and date stamped.

2) Time monitoring switch.  Allows deciphering of incoming streams of
   numbers if tone activity is not detected for a set number of seconds.

3) Supports the extended DTMF tones A,B,C,D.

4) REGISTERED users will also receive a DTMF generator program.  This is
   a DTMF tone generator which allows you to create any DTMF sequence
   you wish.  The program allows you to specify a DTMF number sequence,
   the sampling rate, and how long you want the pulses to be (in samples).


TESTING
ßßßßßßß

I have thoroughly tested this code and I am not responsible for any mishaps
that may happen when run on your computer.




SOUND CARDS TESTED:

Aztec Sound Galaxy 16 bit
Sound Blaster 8 bit
Sound Blaster ASP 16
Generic SB compatible 16 bit
Sound Blaster 16 VE *

* Some problems with the SB 16 VE have been reported and verified.
  Mic and line inputs for the SB 16 VE gave spurious results.  No
  explanation for this hardware problem has been determined.


TESTING PLATFORM:

The code was tested on an IBM compatible 25MHz 486DX Cyrix upgrade PC
with a Soundblaster Version 1.5 sound card running DOS 5.0.  Tones
were recorded onto a cassette tape and played into a microphone which
was connected to the mic input of the Soundblaster card.  It was able
to run in quasi real-time mode with a 4000 Hz sample rate and decoded
numbers with approximately 90% accuracy.  Real-time mode was
unachievable but gave similar results.  Using this test vector data,
normal dialing was decoded 95% of the time.  Burst dialing was
decoded 95% of the time.  Noisy tones gave inconsistent results.

** NOTE: All captured numbers were correctly decoded, the errors
         stemmed from the fact that real-time decoding was not possible!


Every action has been taken to ensure an error-free program.

Note, incompatibilities may stem from hardware deviations.
For optimal performance, DO NOT launch this program while running under
Microsoft Windows.


For more information,

EMAIL:  shima@eel.ufl.edu

US MAIL:        J.M. Shima
          3800 SW 34th St.  Apt. J-80
           Gainesville, FL  32608


TRADEMARKS
ßßßßßßßßßß

Soundblaster is a trademark of Creative Lab's Inc.
Microsoft Windows and DOS is a trademark of Microsoft.