Just When You Thought You'd Never Find A Better Dialer...


                     /**\
                   <******>
                  <********>   -------Com-Worx
                  <COM-WORX>   S O F T W A R E
                  <********>   --------Systems
                   <******>
                     \**/

         |--------------------------------------------|
         |  The Ultimate In WarGames Dialer Programs  |
         |  ======================== ULTRA-DIAL v5.1  |
         |--------------------------------------------|


Welcome To The World Of WarGames Dialers!  If you are a past user
of  the ULTRA-DIAL series or a new one,  you will find ULTRA-DIAL
version 5.1 to be an utterly different and amazing program.

THIS  PROGRAM  IS OFFICIALLY COPYRIGHTED BY PAUL  LEVY.   I  have
chosen,  though, to distribute this program in the public domain.
Its' limits are as follows:

     (1) ULTRA-DIAL and it's documentation are not to be modified
in any way, shape or form under penaly of federal copyright laws.
     (2)  No  fee is charged for the use of or right to  use  the
ULTRA-DIAL program (in it's .EXE form).
     (3)  This program is not intended for misuse and the  author
takes NO RESPOSIBILITY for it's uses from here forward.


                  *-* TABLE OF CONTENTS *-*

              1.0 - MINIMUM CONFIGURATION
              2.0 - ULTRA.CNF CONFIGURATION
              3.0 - START A DIALING ROUTINE
              4.0 - VIEW AND DIAL SELECTED NUMBERS
              5.0 - ENTER TERMINAL MODE
              6.0 - PRINT A COPY OF FOUND NUMBERS
              7.0 - DELETE FOUND NUMBERS
              8.0 - TOGGLE SOUND MODE
              9.0 - RESET TIME AND DATE
             10.0 - QUIT TO DOS
             11.0 - COMMAND LINE ENTRIES




1.0 MINIMUM CONFIGURATION
-------------------------

     To  operate ULTRA-DIAL v5.1 with  optimum  performance,  the
following equipment is required:

     o IBM PC or XT with 256k
     o One disk drive (floppy or hard/fixed)
     o Hayes 1200 External Modem (internal is questionable)
     o Any brand 80-column line printer

     THE  HAYES MODEM REQUIRES the following switch settings  for
this program to detect and process carriers correctly.

           SWITCH .................... 12345678
           SETTING ................... UUDUDUUD

     If these settings are not maintained during the operation of
ULTRA-DIAL v5.1, errors may occur in all aspects of the program.
     ULTRA-DIAL  v5.1 will now has the possibility of  supporting
other   than  Hayes  modes,   such  as  compatibles  like  Anchor
Automations's  various  models which require  a  special  hang-up
method.

2.0 ULTRA.CNF CONFIGURATION
---------------------------

     Version  5.1 offers the versatility of a configuration  file
for  your convenience.    When you first boot ULTRA51,   you will
be asked  to  create  the  file  ULTRA.CNF,    the  following  is
a description of the questions that are asked.

Communications Port.......... Select COM1: or COM2: with 1 or 2
Baud Rate.................... Open and operate the modem at 300
                              baud or 1200 baud.  I suggest you
                              open the modem at 300 for safety.
Wait Time During Call........ How long to wait per call for a
                              carrier tone to be transmitted.
Modem speaker................ Select Y to have the Hayes modem's
                              internal speaker on, otherwise it
                              will default to your modems normal
                              speaker setting (if any).
Tone or Pulse Dialing........ Select if ULTRA-DIAL should use
                              TONE for dialing or PULSE.
Communications mode.......... Select mode 1 for the normally used
                              ULTRA-DIAL method of hang-up.  Or,
                              if you are using a modem such as
                              Anchor Automation's modems, select
                              2  for an alternate method of hang-
                              up (escape, then ATZ).

      To create a new ULTRA.CNF, simply delete the old one.

*IMPORTANT*  If  you  tell ULTRA-DIAL to open the modem  at  1200
baud, it will only be able to detect 1200 BAUD NUMBERS!  I highly
suggest that you set the baud rate at 300 for the best detection.


3.0 START A DIALING ROUTINE
---------------------------

     This is the primary part of the program.  The following is a
description of the prompts.

Enter prefix............. If you would like a prefix to be placed
                          before EVERY number (i.e. for MCI), you
                          may place that data here otherwise you
                          hit <ENTER> for none.
Enter LOW number......... This is where you enter the low (also
                          called starting) number in the dialing
                          sequence. (i.e. 9861673)
Enter HIGH number........ This where you enter the high (also
                          called ending) number in the dialing
                          sequence.

DO  NOT  USE  HYPHENS IN THE LOW AND  HIGH  NUMBERS!!   You  may,
though,  use  commas is the PREFIX only!   Be careful of what you
enter yet this program is free for experimenting.

There  is a final option for a printer.   If you want all CARRIER
FOUND   numbers  to  be  sent  to  the  printer   for   recording
immdeiately, answer Y to this prompt, else enter N here.
-------------------------------***-------------------------------
The dialing sequence will start now.   You will see at the top of
the  screen  the  numbers  being dialed,  the  bottom  shows  two
function keys:

[F1] - QUIT  - Will exit dialing routine after number in progress
is  completed.   Only  press this key once and then  wait  for  a
reaction.  It takes a few seconds to respond.

[F2]  - PAUSE  - Will pause the dialing routine AFTER  NUMBER  IN
PROGRESS  IS COMPLETED.   Again,  wait a few moments for this  to
respond.

     AT  THE  END  of the dialing routine,  an alarm  will  sound
momentarily  and then it will go into a "wait  mode"...the  first
sixty  seconds  of this wait mode will contain 10 chirps every  6
seconds...after  that the screen will clear to prevent  burn  in.
Hit Any Key during this wait mode to get the main menu.
-------------------------------***-------------------------------


4.0 VIEW AND DIAL A SELECTED NUMBER
-----------------------------------

     ULTRA-DIAL also incorporates a very simple terminal mode for
use  in  quick  testing  of the numbers you  have  found  without
exiting ULTRA-DIAL itself.
     When you select the V)iew and Dial option you will be  shown
the numbers that are in the ULTRA.NBR file.   Only 40 numbers can
be  displayed  so deletion of this file is  recommended  whenever
possible to make room for new numbers.
     Use  <SPACE BAR> to go through the numbers with the pointer.
When  you have the pointer on the number you wish  to  dial,  hit
<RETURN>.  (the <ESC> key will exit this)
     Here,  the  ULTRA-DIAL  terminal  takes over and  dials  the
number for you!

*NOTE*   DUE  TO  THE  SIMPLICITY  OF  THIS   TERMINAL,   CERTAIN
CONNECTIONS  MAY OVERFLOW THE TERMINAL.   IT IS  NOT  RECOMMENDED
THAT YOU USE THIS TERMINAL FOR SERIOUS COMMUNICATIONS.


5.0 ENTER TERMINAL MODE
-----------------------

     This  command  will  simply  put  you  into  the  ULTRA-DIAL
terminal  mode  as described above.   All input goes directly  to
your modem during operation of the terminal.   Use the <ESC>  key
to exit back to the main menu.


6.0 PRINT A COPY OF THE NUMBERS FOUND
-------------------------------------

     This  command  will simply print  out,  in  "ULTRA-official"
form, all of the numbers is the ULTRA.NBR file.


7.0 DELETE ALL NUMBERS FOUND
----------------------------

     This command will delete and set-up the ULTRA.NBR file.   It
is  recommended that you do this often so as to make room for new
numbers to be recorded.


8.0 SOUND MODE TOGGLE
---------------------

     As per a reques by a user,  I have added a "SILENT" mode  to
ULTRA-DIAL.   It  basicly quiets down the dialing routine.   This
can be helpful in coordination with the speaker toggle for night-
time  operation.   The  simples BEEPS that are  heard  when,  for
example,  you  go to dial a number,  are heard regardless of  the
mode.   Simply  press T at the main menu and you can  toggle  the
sound mode you are in.


9.0 RESET DATE AND TIME
-----------------------

     This  one is pretty self-explanatory...It will allow you  to
change  the date and time appropriately just as the DOS DATE  and
TIME prompt would.


10.0 QUIT TO DOS
----------------

     This command is self-explanatory.   You will be placed  back
into DOS where you left off.


11.0 COMMAND LINE ENTRIES
-------------------------

     The  feature  presentation  of  ULTRA-DIAL's  command   line
system!  Now you can run ULTRA-DIAL quickly and efficiently.  The
format for the command reads as follows:

A>ULTRA5 (prefix),<low #>,<high #>,(printer)

     In other words, if you were to enter:

A>ULTRA5 9,9861673,9861690,N

     Ultra-Dial  would take 9 as the prefix,  9861673 as the  low
number,  9861690 as the high number, and that you did not want to
use  a  printer and use it all in a dialing  routine.   In  other
words,  you  can  start  dialing  routines by  entering  all  the
information on your boot line.
     THERE  MUST  BE *THREE* COMMAS IN  THE  COMMAND  LINE!   The
prefix is optional, for example:

A>ULTRA5 ,9861673,9861690,N

     Would  do the same as above except without a  prefix.  Also,
the printer is optional and if it is left out, it will be assumed
as no printer, for example:

A>ULTRA5 ,9861673,9861690,

     Would  also  do  the  same  thing  without  a  prefix.   You
experiment with this feature you you can just boot ULTRA5 without
a  command line.   The feature was added for convience.   It also
justifies the requirement for this program to use an IBM only.


UPDATE NOTE:  THIS PROGRAM HAS ONLY BEEN TESTED FOR USE ON AN IBM
PC  OR  XT  MODEL PERSONAL COMPUTER USING A HAYES  1200  EXTERNAL
MODEM.   SUPPORT  FOR  ANCHOR  OR ANY OTHER MODEM  IS  STILL  NOT
GUARANTEED.    ALSO,  SUPPORT  FOR  ANY  OTHER  COMPUTER  IS  NOT
GUARANTEED AND THIS INCLUDES THE IBM AT.    If you are using  DOS
3.0 and it does not work,  try it out with 2.1 or 2.0 and see how
it works before you ask questions.  Enjoy...