78


                                   CHAPTER 10 - TEMPLATES


             Do you remember when you were younger and you needed to look up a
             word in the dictionary? It would define the word in terms of a
             second word which you didn't know so you would look that up too.
             Most likely that second word was either defined in terms of a
             third word you didn't know or it referred you back to the first
             word.

             This chapter is something like that. The items in the template
             file are interdependent. If you're lucky, everything will be
             clear by the time you have finished the chapter. If not, you'll
             have to reread it.

             There are four different things which operate on the assembler
             instructions which you write - the ASSEMBLER, the LINKER, the
             LOADER and the 8086.

             1) The ASSEMBLER takes your text and turns it into the machine
             code that is used by the 8086. It is complete except that the
             addresses of data and subroutines might change during linking and
             loading. The assembler generates information called HEADER files
             which give the LINKER and LOADER the information they need to
             update these addresses in the machine code. This means that you
             can move the code anywhere in memory.

             2) If your program is made up of more than one file, the LINKER
             links them together. It then makes it ready for running. If there
             is only one file, the linker makes it ready for running. It does
             this by updating the addresses of anything it has moved. It still
             leaves the HEADER files which contain the segment addresses.

             3) At run time, the LOADER, which is part of the operating
             system, decides where to put your program in memory. It loads the
             program, and adjusts any segment addresses in the program to
             reflect where the program actually is in memory. It then gives
             control to the program.

             4) The code is fixed at the time the 8086 takes over. Any
             addresses are constants and are unchangable. 

             Keep this in mind as we work through the template file.


             THE .LST FILE

             The first thing we need to look at is segments. Let's look at a
             slightly modified version of the template file called segs.asm.
             Here it is. 

             ;*********************************** 
             ; segs.asm 

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             Chapter 10 - Templates                                         79
             ______________________


             ; - - - - - - - - - - - - - 
             STACKSEG SEGMENT STACK  'STACK' 
              
             variable4    dw     4444h 
                          dw     100h dup (?) 
              
             STACKSEG  ENDS 
             ; - - - - - - - - - - - - - 
             MORESTUFF SEGMENT PUBLIC  'HOHUM' 
              
             variable2    dw   2222h 
              
             MORESTUFF    ENDS 
             ; - - - - - - - - - - - - -  
             DATASTUFF  SEGMENT PUBLIC  'DATA' 
              
             variable1    dw     1111h 
              
             DATASTUFF    ENDS 
             ; - - - - - - - - - - - - - 
             CODESTUFF SEGMENT PUBLIC  'CODE' 
              
              EXTRN  print_num:NEAR , get_num:NEAR  
              
              ASSUME cs:CODESTUFF,ds:DATASTUFF 
              ASSUME es:MORESTUFF,ss:STACKSEG 
              
             variable3    dw     3333h 
              
             main   proc far 
             start: push  ds    
                    sub   ax,ax 
                    push  ax 
              
                    mov   ax, DATASTUFF 
                    mov   ds,ax 
                    mov   ax, MORESTUFF 
                    mov   es,ax 
              
                    mov   cx, variable1 
                    mov   variable1, cx 
              
                    ret 
              
             main   endp 
              
              
             CODESTUFF    ENDS 
             ; - - - - - - - - - - - -  
              
                 END     start 
             ;***************************

             There is an extra segment put in that has the definition

                 MORESTUFF SEGMENT PUBLIC  'HOHUM' 





             The PC Assembler Tutor                                         80
             ______________________


             There is a variable defined in each segment including the stack
             segment. These variables all have numbers in them, and the
             numbers are in hex so they will be easy to read. There are only
             two external subroutines (neither of which is called). It is time
             to take a look at an assembler listing. 

             ----- THIS IS FROM THE SCREEN -----

             C>masm segs
             Microsoft (R) Macro Assembler Version 5.10
             Copyright (C) Microsoft Corp 1981, 1988.  All rights reserved.   
                           
             Object filename [segs.OBJ]:               
             Source listing  [NUL.LST]: segs
             Cross-reference [NUL.CRF]:         

             -----------                               

             If you don't put a semicolon after the filename with masm, you
             get some prompts. The first asks you if you want the object file
             name to be different from the asm file name. You may change
             either the name or the name and the extension. If you don't want
             to change either, just press ENTER. The second asks if you want a
             listing. Normally you don't, so you just press ENTER. This time
             we do, so we give it the same name as the assembler file. The
             assembler will generate a file SEGS.LST. Finally, it asks if you
             want the information needed to create a cross-reference file. We
             won't cover that. Once again, press ENTER. The assembler
             generates an object file and a listing. Here's the complete
             listing.

             **********************
             Microsoft (R) Macro Assembler Version 5.10                 
             9/2/89 09:50:54

                                                       Page     1-1 
              
              
                                 
                                ; segs.asm 
                                 
                                ; - - - - - - - - - - - - - 
              0000                   STACKSEG SEGMENT STACK  'STACK' 
                                 
              0000  4444             variable4    dw     4444h 
              0002  0100[                         dw     100h dup (?) 
                    ????              
                            ]    
                                 
                                 
              0202                   STACKSEG  ENDS 
                                ; - - - - - - - - - - - - - 
              0000                   MORESTUFF SEGMENT PUBLIC  'HOHUM' 
                                 
              0000  2222             variable2    dw   2222h 
                                 





             Chapter 10 - Templates                                         81
             ______________________

              0002                   MORESTUFF    ENDS 
                                ; - - - - - - - - - - - - -  
              0000                   DATASTUFF  SEGMENT PUBLIC  'DATA' 
                                 
              0000  1111             variable1    dw     1111h 
                                 
              0002                   DATASTUFF    ENDS 
                                ; - - - - - - - - - - - - - 
              0000                   CODESTUFF SEGMENT PUBLIC  'CODE' 
                                 
                                 EXTRN  print_num:NEAR , get_num:NEAR  
                                 
                                 ASSUME cs:CODESTUFF,ds:DATASTUFF 
                                 ASSUME es:MORESTUFF,ss:STACKSEG 
                                 
              0000  3333             variable3    dw     3333h 
                                 
              0002                   main   proc far 
              0002  1E          start: push  ds    
              0003  2B C0                   sub   ax,ax 
              0005  50                 push  ax 
                                 
              0006  B8 ---- R               mov   ax, DATASTUFF 
              0009  8E D8                   mov   ds,ax 
              000B  B8 ---- R               mov   ax, MORESTUFF 
              000E  8E C0                   mov   es,ax 
                                 
              0010  8B 0E 0000 R            mov   cx, variable1 
              0014  89 0E 0000 R            mov   variable1, cx 
                                 
              0018  CB                 ret 
                                 
              0019                   main   endp 
                                 
                                 
              0019                   CODESTUFF    ENDS 

             Microsoft (R) Macro Assembler Version 5.10                 
             9/2/89 09:50:54
              
                                                       Page     1-2 
              
              
                                ; - - - - - - - - - - - -  
                                 
                                    END     start 


             Microsoft (R) Macro Assembler Version 5.10                 
             9/2/89 09:50:54
              
                                                                         
             Symbols-1 
              
              
             Segments and Groups: 
              





             The PC Assembler Tutor                                         82
             ______________________

                       N a m e               Length Align Combine  Class 
              
             CODESTUFF  . . . . . . . . . . .  0019 PARA PUBLIC    'CODE' 
             DATASTUFF  . . . . . . . . . . .  0002 PARA PUBLIC    'DATA' 
             MORESTUFF  . . . . . . . . . . .  0002 PARA PUBLIC    'HOHUM' 
             STACKSEG . . . . . . . . . . . .  0202 PARA STACK     'STACK' 
              
             Symbols:             
              
                     N a m e         Type     Value  Attr 
              
             GET_NUM  .  . . . .     L NEAR    0000 CODESTUFF External 
              
             MAIN . . .   . . . . .  F PROC    0002 CODESTUFF Length = 0017 
              
             PRINT_NUM   . . . .     L NEAR    0000 CODESTUFF External 
              
             START  . . . . . . . .  L NEAR    0002 CODESTUFF 
              
             VARIABLE1  . . . . . .  L WORD    0000 DATASTUFF 
             VARIABLE2  . . . . . .  L WORD    0000 MORESTUFF 
             VARIABLE3  . . . . . .  L WORD    0000 CODESTUFF 
             VARIABLE4  . . . . . .  L WORD    0000 STACKSEG 
              
             @CPU . . . . . . . . . . . . . .  TEXT  0101h          
             @FILENAME  . . . . . . . . . . .  TEXT  segs           
             @VERSION . . . . . . . . . . . .  TEXT  510       
              
              
                  54 Source  Lines 
                  54 Total   Lines 
                  21 Symbols 
              
               48006 + 428261 Bytes symbol space free 
              
                   0 Warning Errors 
                   0 Severe  Errors 

             **********************

             As you can see, the listing, even for a short program, is very
             long. Let's take it apart section by section. The first large
             section is a copy of the text file except that there is
             information on the left. The number on the far left tells the
             offset address (in hex) from the beginning of the segment for
             each label, variable or instruction. In this section:

                                 
              0000  3333             variable3    dw     3333h 
                                 
              0002                   main   proc far 
              0002  1E          start: push  ds    
              0003  2B C0                   sub   ax,ax 
              0005  50                 push  ax 
                                 
              0006  B8 ---- R               mov   ax, DATASTUFF 
              0009  8E D8                   mov   ds,ax 





             Chapter 10 - Templates                                         83
             ______________________

              000B  B8 ---- R               mov   ax, MORESTUFF 
              000E  8E C0                   mov   es,ax 
                                 
              0010  8B 0E 0000 R            mov   cx, variable1 
              0014  89 0E 0000 R            mov   variable1, cx 
                                 
              0018  CB                 ret 
                                 
              0019                   main   endp 

             "start" is at 0002h ,"mov cx, variable1" is at 0010h and "ret" is
             at 18h.

             The second set of numbers is the actual machine instructions in
             hex. These are the what the 8086 operates on. "push ds" is 1E,
             "mov ds, ax" is 8E D8, and "ret" is CB. The instructions can be
             from 1 - 6 bytes long. Notice the "R" after some of the
             instructions. The "R" stands for relocatable. This means that it
             is an address that might be changed by either the linker or the
             loader. We'll talk about that later. In any case, the object file
             keeps track of these so they can be changed if necessary. Also,
             go back to the complete listing and look at the four variables;
             you will see that the values have been put in the object code;
             that is, 1111h, 2222h, 3333h and 4444h.

             If we had had an error, the assembler would have placed an error
             message at the spot of the error in this part of the file. 


             The next part of the .LST file is the segment listing. It tells
             how the segments are defined.

                     N a m e                 Length Align Combine  Class 
              
                 CODESTUFF  . . . . . . . .    0019 PARA PUBLIC    'CODE' 
                 DATASTUFF  . . . . . . . .    0002 PARA PUBLIC    'DATA' 
                 MORESTUFF  . . . . . . . .    0002 PARA PUBLIC    'HOHUM' 
                 STACKSEG . . . . . . . . .    0202 PARA STACK     'STACK' 
              

             We have the segment name, length, and some other information
             we'll talk about later. Notice that 'HOHUM' which is an
             artificial class, is dutifully listed with no complaints.


             Then comes the listing of all labels, variables, and procedure
             names.

                 Symbols:             
              
                     N a m e         Type     Value  Attr 
              
                 GET_NUM  . . . .    L NEAR    0000 CODESTUFF External  
                 MAIN   . . . . .    F PROC    0002 CODESTUFF Length = 0017  
                 PRINT_NUM    . .    L NEAR    0000 CODESTUFF External  
                 START  . . . . .    L NEAR    0002 CODESTUFF  
                 VARIABLE1  . . .    L WORD    0000 DATASTUFF 





             The PC Assembler Tutor                                         84
             ______________________

                 VARIABLE2  . . .    L WORD    0000 MORESTUFF 
                 VARIABLE3  . . .    L WORD    0000 CODESTUFF 
                 VARIABLE4  . . .    L WORD    0000 STACKSEG 


             It shows the segment and offset, whether they are bytes, words,
             processes etc. The "L" stands for label. The variables and
             procedures which are in an external file are so marked. Neither
             print_num nor get_num was called, but the assembler maintains a
             listing for them.

             Finally, some internal info for the assembler.

             @CPU . . . . . . . . . . . . . .  TEXT  0101h          
             @FILENAME  . . . . . . . . . . .  TEXT  segs           
             @VERSION . . . . . . . . . . . .  TEXT  510       

             We will come back to parts of the .LST file, so make yourself
             comfortable with it. 



             SEGMENTS

             It is now time for the nitty-gritty. We need to know what all
             those statements in the template file mean. Remember that there
             are four players in the game - (1) MASM, the Microsoft assembler,
             (2) LINK, the Microsoft linker, (3) the program loader and (4)
             the 8086 chip itself. Who does what to whom is the subject of
             this chapter.

             You will notice that there are three segments in all the template
             files, one for data, one for code, and one for the stack. How
             many segments can a program have? An unlimited number for code,
             an unlimited number for data, and one for the stack.{1}  Although
             you can have an unlimited number of segments, you can use only
             four at any one time - two for regular data (referenced by the DS
             and ES registers), one for code (referenced by the CS register),
             and one for temporary data (referenced by the SS register).

             You don't have direct control over CS. You should NEVER change
             the value in SS. This means that you can only change which
             segments that ES and DS refer to. How do you do that? The 8086
             does not allow you to move a constant into a segment register.
             Therefore it is a two step process. Put the constant into an
             arithmetic register (AX, BX, CX, DX, SI, DI or BP) and from there
             to the segment register. Suppose we have 327 different data
             segments in our file (named SEG1, SEG2, SEG3 ... SEG327) and we
             wanted to reference data in SEG27. The code would be:

                 mov  ax, SEG27
                 mov  ds, ax

             ____________________

                1 Although if you REALLY need more space for a stack it is
             possible, if a little arcane.





             Chapter 10 - Templates                                         85
             ______________________

             This is the standard way to do it, and this is the same as the
             fourth and fifth instructions in the code segment of the template
             files where we are putting the address of DATASTUFF in ds.

             What is that SEG27 in the instruction (mov  ax, SEG27)? It is a
             constant. When the assembler assembles the program, it makes note
             of the fact that you want to have the starting address of SEG27
             in that instruction (you saw the "R" in the listing for the
             instruction 'mov ax, DATASTUFF'). Later the linker makes sure
             there is a SEG27 segment in the complete program, gives it a
             temporary segment address, and puts this temporary address in
             every place that references that segment address. This address is
             guaranteed to be adjusted. You will see why when we look at the
             linker .MAP file.

             Finally, the loader (which is the program that puts your program
             into memory) puts the segment where it wants and updates all
             references to the segment address to reflect where it now is.
             Thus, the program is complete only when this information is put
             in at run time. Each time you run the program SEG27 might be in a
             different place, but the loader will always update the references
             correctly. 

             We named the segments SEG1, SEG2, etc. Does SEG have to be part
             of the segment name? Not on your life. Here are three perfectly
             acceptable segment definitions:

                 CURLY     SEGMENT
                 LARRY     SEGMENT
                 MOE       SEGMENT

             It is good practice to have 'SEG' as part of the segment name to
             remind you that these are segments, not variables, but this is a
             practice only, it is not a law. Any name you could use for a
             variable or a label you could use as a segment name. The reserved
             word SEGMENT after the name tells the assembler that this is the
             beginning of a segment with that name. You tell the assembler
             that you are starting a segment with 'SEGMENT'

                 CURLY     SEGMENT

             and you tell the assembler that you are finished with that
             segment with the reserved word ENDS (END [of] Segment):

                 CURLY     ENDS

             You need to put the name of the segment before the  ENDS
             directive.

             In the template file, the data segment definition reads:

                 DATASTUFF  SEGMENT  PUBLIC    'DATA'

             DATASTUFF is the segment name, but what are PUBLIC and 'DATA'
             there for? To understand this, we need to look at the linker.
             First, let's assemble temp1.asm (our first template file) just
             the way it is. 





             The PC Assembler Tutor                                         86
             ______________________


             ---------- FROM THE SCREEN ----------
             C>masm temp1.asm          
             Microsoft (R) Macro Assembler Version 5.10           
             Copyright (C) Microsoft Corp 1981, 1988.  All rights reserved.   
                  
                     
             Object filename [temp1.OBJ]:       
             Source listing  [NUL.LST]: temp1            
             Cross-reference [NUL.CRF]:         

             ----------
             We have made the listing file so let's look at the segment
             information.


             N a m e                         Length Align Combine Class 
              
             CODESTUFF  . . . . . . . . . . .  000A PARA PUBLIC    'CODE' 
             DATASTUFF  . . . . . . . . . . .  0000 PARA PUBLIC    'DATA' 
             STACKSEG . . . . . . . . . . . .  00C8 PARA STACK     'STACK' 

             You will see that CODESTUFF is Ah (10d) bytes long, DATASTUFF has
             no data and is 0 bytes long, and STACKSEG is C8h (200d) bytes
             long.

             Now let's link temp1.obj and asmhelp.obj.

             ---------- FROM THE SCREEN -----

             C>link temp1+asmhelp      
                     
             Microsoft (R) Overlay Linker  Version 3.61           
             Copyright (C) Microsoft Corp 1983-1987.  All rights reserved.    
                  
                     
             Run File [TEMP1.EXE]:              
             List File [NUL.MAP]: temp          
             Libraries [.LIB]:         

             ----------

             This time we have made a listing file for the link process. It is
             called TEMP.MAP. Let's look at it.

                  Start  Stop   Length Name         Class 
                  00000H 000C7H 000C8H STACKSEG     STACK 
                  000D0H 00540H 00471H DATASTUFF    DATA 
                  00550H 01944H 013F5H CODESTUFF    CODE 
              
                 Program entry point at 0055:0000 

             This is what the map file looks like. There are still only three
             segments in the final executable file, STACKSEG, DATASTUFF and
             CODESTUFF. You will notice that the class name is still there,
             but the PUBLIC is missing. It's job is finished. "Start" says
             where the segment starts in the executable file, "Stop" says





             Chapter 10 - Templates                                         87
             ______________________

             where the segment ends in the executable file, and "Length" says
             the length in bytes of the segment. These numbers are 5 digit hex
             numbers instead of 4. That means that they are showing the total
             address. The segment number is the left 4 digits of 'Start'.

             STACKSEG is C8h (200d) bytes long like before. Although DATASTUFF
             had no data, it is now 471h (1137d) bytes long, and CODESTUFF was
             Ah (10d) bytes long before but now it is a whopping 13F5h (5109d)
             bytes long. What happened? The linker did its work. 

             One of the things the linker does is combine things that we want
             to be in the same segment. It took the DATASTUFF segment from
             temp1.obj and appended the DATASTUFF segment from asmhelp.obj,
             combining them into one larger segment.{2}  It took the CODESTUFF
             segment from temp1.obj and appended the CODESTUFF segment from
             asmhelp.obj, making them one large segment. Why did it do that?
             Because we put the word "PUBLIC" in the segment definition. When
             the assembler sees "PUBLIC" in the segment definition, it passes
             that information along to the linker in a header file.{3}  When
             the linker has a segment which is "PUBLIC", it will append any
             other segment which (1) is "PUBLIC", (2) has the same name (i.e.
             CODESTUFF or DATASTUFF or CURLY etc.), and (3) has the same class
             name{4}. All three things must be true for the linker to combine
             them. We will actually check this out a little later to make sure
             you believe it.

             One other thing to notice is that the linker is allocating only
             as much space as is needed. It could allocate 65536 bytes for
             each segment defined, but it uses only as much as the program
             needs and then starts the next segment at the next segment
             starting address. This is efficient management of memory. 

             What is the advantage of combining the smaller segments into one
             larger segment? For code, there is no big advantage. But for
             data, remember that every time we want to access data, we need to
             have the starting address of that particular segment in register
             ds. We do this by using:

                 mov  ax, DATASTUFF
                 mov  ds, ax

             If we have a number of data segments, every time we access data
             ____________________

                2 The linker always works from left to right. For each
             different type of segment, it starts with the first one it finds
             and then appends each succeeding one it finds.

                3 A header is information for the linker or loader which is
             put in front of the machine code in an object file or an
             executable file. There are typically a number of headers in front
             of the machine code.

                4 Remember that class names are somewhat arbitrary. I use
             'CODE', 'DATA' and 'STACK' for clarity and because they are the
             standard Microsoft class names, but if you are not linking with
             anyone else's programs, you can use any class name you want.





             The PC Assembler Tutor                                         88
             ______________________

             we need to (1) make sure that ds contains the address of the
             correct data segment, and (2) if not, we need to write the code
             to change ds. This entails using a lot of code, can be confusing
             and is certainly error prone. With one data segment, you simply
             load ds with the correct address at the beginning of the program
             and then forget about it. This should be a rule for you. Unless
             you have truly humongous amounts of data (over 65535 bytes),
             ALWAYS put all your data in the same segment. 

             Do you remember those dashes '----' in the assembler listing?
             That was because the assembler didn't have a segment address to
             put there.

                  0004  B8 ---- R                mov   ax, DATASTUFF 
                  0007  8E D8                    mov   ds,ax 
                                 
                  0009  8B 0E 0000 R             mov   cx, variable1 
                  000D  89 0E 0000 R             mov   variable1, cx 

             The linker now has a temporary address for the start of DATASTUFF
             (000D0h) so it will put the segment address (the left four hex
             bytes) in this spot. This is temporary, but will be updated by
             the loader. If variable1 has been moved, it will update that too.

             Why am I sure that these temporary segments will be moved? The
             segment address of STACKSEG is 0000h. The segment address of
             DATASTUFF is 000Dh (13h) and the segment address of CODESTUFF is
             0055h (85d). But the operating sysyem owns the first several
             THOUSAND segments. The loader will load your program in much
             higher memory. They must move.

             So the linker combines all the segments we want to combine, and
             then it looks at the machine code and modifies every reference to
             the segments and to the variables which have been moved. That is
             a lot of work. For instance, when the linker appends asmhelp.obj,
             there are a hundred or so variables which it moves and a thousand
             or so references to those variables which it modifies. The linker
             does that every time you link a file with ASMHELP.OBJ. That's not
             too shabby.