104

                       CHAPTER 11 - ADDRESSING MODES AND POINTERS


             In this chapter we are going to cover all possible ways of
             getting data to and from memory with the different addressing
             modes. Read this carefully, since it is likely this is the only
             time you will ever see ALL addressing possibilities covered. 

             The easiest way to move data is if the data has a name and the
             data is one or two bytes long. Take the following data:

             ; -----
             variable1 dw  2000
             variable2 db  -26
             variable3 dw  -589
             ; -----

             We can write:

                 mov  variable1, ax
                 mov  cl, variable2
                 mov  si, variable3

             and the assembler will write the appropriate machine code for
             moving the data. What can we do if the data is more than two
             bytes long? Here is some more data:

             ; -----
             variable4 db  "This is a string of ascii data."
             variable5 dd  -291578
             variable6 dw  600 dup (-11000)
             ; -----

             Variable4 is the address of the first byte of a string of ascii
             data. Variable5 is a single piece of data, but it won't fit into
             an 8086 register since it is 4 bytes long. Variable6 is a 600
             element long array, with each element having the value -11000. In
             order to deal with these, we need pointers.

             Some of you will be flummoxed at this point, while those who are
             used to the C language will feel right at home. A pointer is
             simply the address of a variable. We use one of the 8086
             registers to hold the address of a variable, and then tell the
             8086 that the register contains the address of the variable, not
             the variable itself. It "points" to a place in memory to send the
             data to or retrieve the data from. If this seems a little
             confusing, don't worry; you'll get the hang of it quickly. 

             As I have said before, the 8086 does not have general purpose
             registers. Many instructions (such as LOOP, MUL, IDIV, ROL) work
             only with specific registers. The same is true of pointers. You
             may use only  BX, SI, DI, and BP as pointers. The assembler will
             give you an error if you try using a different register as a
             pointer.

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             Chapter 11 - Addressing Modes                                 105
             _____________________________



             There are two ways to put an address in a pointer. For variable4,
             we could write either:

                 lea  si, variable4

             or:

                 mov  si, offset variable4

             Both instructions will put the offset address of variable4 in
             SI.{1} SI now 'points' to the first byte (the letter 'T') of
             variable4. If we wanted to move the third byte of that array
             (the letter 'i') to CL, how would we do it? First, we need to
             have SI point to the third byte, not the first. That's easy:

                 add  si, 2

             But if we now write:

                 mov  cl, si

             we will generate an assembler error because the assembler will
             think that we want to move the data in SI (a two byte number) to
             CL (one byte). How do we tell the assembler that we are using SI
             as a pointer? By enclosing SI in square brackets:

                 mov  cl, [si]

             since CL is one byte, the assembler assumes you want to move one
             byte. If you write:

                 mov  cx, [si]

             then the assembler assumes that you want to move a word (two
             bytes). The whole thing now is:

                 lea  si, variable4
                 add  si, 2
                 mov  cl, [si]

             This puts the third byte of the string in CL. Remember, if a
             register is in square brackets, then it is holding the ADDRESS of
             a variable, and the 8086 will use the register to calculate where
             the data is in memory.

             What if we want to put 0s in all the elements of variable6?
             ____________________

                1 LEA stands for load effective address. Note that with LEA,
             we use only the name of the variable, while with:

                 mov  si, offset variable4

             we need to use the word 'offset'. The exact difference between
             the two will be explained later.





             The PC Assembler Tutor                                        106
             ______________________

             Here's the code:

                      mov  bx, offset variable6
                      mov  ax, 0
                      mov  cx, 600
                 zero_loop:
                      mov  [bx], ax
                      add  bx, 2
                      loop zero_loop

             We add 2 to BX each time since each element of variable6 is a
             word (two bytes) long. There is another way of writing this:

                      mov  bx, offset variable6
                      mov  cx, 600
                 zero_loop:
                      mov  [bx], 0
                      add  bx, 2
                      loop zero_loop

             Unfortunately, this will generate an assembler error. Why? If the
             assembler sees:

                      mov  [bx], ax

             it knows that you want to move what is in AX to the address in
             BX, and AX is one word (two bytes) long so it generates the
             machine code for a word move. If the assembler sees:

                      mov  [bx], al

             it knows that you want to move what is in AL to the address in
             BX, and AL is one byte long, so it generates the machine code for
             a byte move. If the assembler sees:

                      mov  [bx], 0

             it doesn't know whether you want a byte move or a word move. The
             8086 assembler has implicit sizing. It is the assembler's job to
             look at each instruction and decide whether you want to operate
             on a byte or a word. Other microprocessors do things differently.
             On the Motorola 68000, the assembler uses explicit sizing. Each
             instruction must explicitly state whether it is a byte or a
             word.{2} On the 68000 you have:

                      move.b    #213, (A1)
                      move.w    #213, (A1)

             The first instruction says to move a byte (the number 213) to the
             address in register A1 while the second instruction says to move



             ____________________

                2 Any of you who use the 68000 assembler know that this is
             fudging the facts a little bit.





             Chapter 11 - Addressing Modes                                 107
             _____________________________

             a word (the number 213) to the address in register A1.{3} 

             Back to the 8086. If the 8086 assembler looks at an instruction
             and it can't tell whether you want to move a byte or a word, it
             generates an error. When you use pointers with constants, you
             should explicitly state whether you want a byte or a word. The
             proper way to do this is to use the reserved words BYTE PTR or
             WORD PTR.

                      mov  [bx], BYTE PTR 213
                      mov  [bx], WORD PTR 213

             These stand for byte pointer and word pointer respectively. I
             find this terminology exceptionally clumsy, but that's life.
             Whenever you are moving a constant with a pointer, you should
             specify either BYTE PTR or WORD PTR.

             The Microsoft assembler makes some assumptions about the size of
             a constant. If the number is 256 or below (either positive or
             negative), you MUST explicitly state whether it is a byte or a
             word operation. If the number is 257 or above (either positive or
             negative), the assembler assumes that you want a word operation.

             Here's the previous code rewritten correctly:


                      mov  bx, offset variable6
                      mov  cx, 600
                 zero_loop:
                      mov  [bx], WORD PTR 0
                      add  bx, 2
                      loop zero_loop

             Let's add 435 to every element in the variable6 array:

                      mov  bx, offset variable6
                      mov  cx, 600
                 add_loop:
                      add  [bx], WORD PTR 435
                      add  bx, 2
                      loop add_loop

             How about multiplying every element in the array by 12?

                      mov  di, offset variable6
                      mov  cx, 600
                      mov  si, 12
                 mult_loop:
                      mov  ax, [di]
                      imul si
                      mov  [di], ax
                      add  di, 2
                      loop mult_loop

             ____________________

                3 A1 is a 68000 register.





             The PC Assembler Tutor                                        108
             ______________________

             None of these examples did any error checking, so if the result
             was too large, the overflow was ignored. This time we used DI for
             a change of pace. Remember, we may use BX, SI, DI or BP, but no
             others. You will notice that in all these examples, we started at
             the beginning of the array and went step by step through the
             array. That's fine, and that's what we normally would do, but
             what if we wanted to look at individual elements? Here's a sample
             program:

             ; + + + + + START DATA BELOW THIS LINE
             ; 
             poem_array  db "She walks in Beauty, like the night"
                         db "Of cloudless climes and starry skies;"
                         db "And all that's best of dark and bright"
                         db "Meet in the aspect ratio of 1 to 3.14159"
             character_count  db  149
             ; + + + + + END DATA ABOVE THIS LINE

             ; + + + + + START CODE BELOW THIS LINE

                 mov  bx, offset poem_array
                 mov  dl, character_count

             character_loop:
                 sub  ax, ax              ; clear ax
                 call get_unsigned_byte
                 dec  al                  ; character #1 = array[0]
                 cmp  al, dl              ; out of range?
                 ja   character_loop      ; then try again
                 mov  si, ax              ; move char # to pointer register
                 mov  al, [bx+si]         ; character to al
                 call print_ascii_byte
                 jmp  character_loop

             ; + + + + + END CODE ABOVE THIS LINE

             You enter a number and the program prints the corresponding
             character. Before starting, we put the array address in BX and
             the maximum character count in DL. After getting the number from
             get_unsigned_byte, we decrement AL since the first character is
             actually poem_array[0]. The character count has been reduced by 1
             to reflect this fact. It also makes 0 an illegal entry. Notice
             that the program checks to make sure you don't go past the end of
             the poem. This time we use BX to mark the beginning of the array
             and SI to count the number of the character.

             Once again, there are only specific combinations of pointers that
             can be used. They are:

                 BX with either SI or DI (but not both)
                 BP with either SI or DI (but not both)

             My version of the Microsoft assembler (v5.1) recognizes the forms
             [bx+si], [si+bx], [bx][si], [si][bx], [si]+[bx] and [bx]+[si] as
             the same thing and produces the same machine code for all six.







             Chapter 11 - Addressing Modes                                 109
             _____________________________

             We can get even more complicated, but to show that, we need
             structures. In databases they are called records. In C they are
             called structures; in any case they are the same thing - a group
             of different types of data in some standard order. After the
             group is defined, we usually make an array with the identical
             structure for each element of the array.{4} Let's make a
             structure for an address book.

                 last_name  db  15 dup (?)
                 first_name db  15 dup (?)
                 age        db  ?
                 tel_no     db  10 dup (?)

             In this case, all the data is bytes, but that is not necessary.
             It can be anything. Each separate piece of data is called a
             FIELD. We have the last_name field, the first_name field, the age
             field, and the tel_no field. Four fields in all. The structure is
             41 bytes long. What if we want to have a list of 100 names in our
             telephone book? We can allocate memory space with the following
             definition:

                 address_book   db  100 dup ( 41 dup (' ')) {5}

             Well, that allocates room in memory, but how do we get to
             anything? First, we need the array itself:

                 mov  bx, offset address_book

             Then we need one specific entry. Let's take entry 29 (which is
             address_book[28]). Each entry is 41 bytes long, so:

                 mov  ax, 28    ; entry (less 1)
                 mov  cx, 41    ; entry length
                 mul  cx
                 mov  di, ax    ; move to pointer

             That gives us the entry, but if we want to get the age, that's
             not the first byte of the structure, it's the 31st byte (actually
             address_book[28] + 30 since the first byte is at +0). We get it
             by writing:

                 mov  dl, [bx+di+30]

             This is the most complex thing we have - two pointers plus a
             constant. The total code is then:

                 mov  bx, offset address_book
                 mov  ax, 28    ; entry (less 1)
                 mov  cx, 41    ; entry length
             ____________________

                4 If you don't know about structures or records, now would be
             a good time to stop and go to a reference book about them. They
             are not actually covered here.

                5 Nesting of dup statements is allowed. Rather than having
             uninitialized data, this has blanks in all the spaces.





             The PC Assembler Tutor                                        110
             ______________________

                 mul  cx        ; entry offset from array[0]
                 mov  di, ax    ; move entry offset to pointer
                 mov  dl, [bx+di+30]  ; total address

             Though the machine code has only one constant in the code, the
             assembler will allow you to put a number of constants in the
             assembler instruction. It will add them together for you and
             resolve them into one number.{6}

             Once again, there are a limited number of registers - they are
             the same registers as before:

                 BX with either SI or DI (but not both) plus constant
                 BP with either SI or DI (but not both) plus constant

             We can work with structures on the machine level, but it looks
             like it's going to be hard to keep track of where each field is.
             Actually, it isn't so bad because of:

                               OUR FRIEND, THE EQU STATEMENT

             The assembler allows you to do substitution. If you write:

                 somestuff EQU  37 * 44

             then every place that the assembler finds the word "somestuff",
             it will substitute what is on the right side of the EQU. Is that
             a number or text? Sometimes it's a number, sometimes it's text.
             Here are four statements which are defined totally in terms of
             numbers. This is from the assembler listing. (The assembler lists
             how it has evaluated the EQU statement on the left after the
             equal sign.)



                                 
              = 0023               statement1 EQU  5 * 7 
              = 0025               statement2 EQU  statement1 + 6 - 4  
              = 000F               statement3 EQU  statement2 - 22 
              = 001F               statement4 EQU  statement3 + 16 

             and the assembler thinks of these as numbers (these numbers are
             in hex). Now in the next set, with only a minor change:


              = [bp + 3]                    statement1 EQU  [bp + 3] 
              = [bp + 3] + 6 - 4            statement2 EQU  statement1 + 6 - 4
              = [bp + 3] + 6 - 4 - 22       statement3 EQU  statement2 - 22 
             ____________________

                6 And it does it quite well. The assembler correctly evaluated
             the following:

                    add   ax, (-3*81)+44/8+[si+27]+6+[bx]-7+(43*96)-2 

             Not bad, huh?






             Chapter 11 - Addressing Modes                                 111
             _____________________________

              = [bp + 3] + 6 - 4 - 22 + 16  statement4 EQU  statement3 + 16 
              
             the assembler thinks of it as text. Obviously, the fact that it
             can be either may cause you some problems along the way. Consult
             the assembler manual for ways to avoid the problem.


             Now we have a tool to deal with structures. Let's look at that
             structure again.

                 last_name  db  15 dup (?)
                 first_name db  15 dup (?)
                 age        db  ?
                 tel_no     db  10 dup (?)

             We don't actually need a data definition to make the structure,
             we need equates:

                 LAST_NAME      EQU  0
                 FIRST_NAME     EQU  15
                 AGE            EQU  30
                 TEL_NO         EQU  31

             this gives us the offset from the beginning of each record. If we
             again define:

                 address_book   db  100 dup ( 41 dup (' '))

              then to get the age field of entry 87, we write:

                 mov  bx, offset address_book
                 mov  ax, 86    ; entry (less 1)
                 mov  cx, 41    ; entry length
                 mul  cx        ; entry offset from array[0]
                 mov  di, ax    ; move entry offset to pointer
                 mov  dl, [bx+di+AGE]  ; total address

             This is a lot of work for the 8086, but that is normal with
             complex structures. The only thing that takes a lot of time is
             the multiplication, but if you need it, you need it.{7}

             How about a two dimensional array of integers, 60 X 40

                 int_array  dw  40 dup  ( 60 dup ( 0 ))

             These are initialized to 0. For our purposes, we'll assume that
             the first number is the row number and the second number is the
             column number; i.e. array [6,13] is row 6, column 13. We will
             have 40 rows of 60 columns. For ease of calculation, the first
             array element is int_array [0,0]. (If it is your array, you can




             ____________________

                7 You will see more of the EQU statement.





             The PC Assembler Tutor                                        112
             ______________________

             set it up any way you want {8}). Each row is 60 words (120 bytes)
             long. To get to int_array [23, 45] we have:

                 mov  ax, 120   ; length of one row in bytes
                 mov  cx, 23    ; row number
                 mul  cx
                 mov  bx, ax    ; row offset to bx
                 mov  si, 45    ; column offset
                 sal  si, 1     ; multiply column offset by 2 (for word size)
                 mov  dx, [bx+si]    ; integer to dx

             Using SAL instead of MUL is about 50 times faster. Since most
             arrays you will be working with are either byte, word, or double
             word (4 bytes) arrays, you can save a lot of time. Let
             ELEMENT_NUMBER be the array number (starting at 0) of the desired
             element in a one-dimensional array. For byte arrays, no
             multiplication is needed. For a word:

                 mov  di, ELEMENT_NUMBER
                 sal  di,1      ; multiply by 2

             and for a double word (4 bytes):

                 mov  di, ELEMENT_NUMBER
                 sal  di, 1
                 sal  di, 1     ; multiply by 4

             This means that a one-dimensional array can be accessed very
             quickly as long as the element length is a power of 2 - either 2,
             4 or 8. Since the standard 8086 data types are all 1, 2, 4, or 8
             bytes long, one dimensional arrays are fast. Others are not so
             fast.

             As a quick review before going on, these are the legal ways to
             address a variable on the 8086:

                 (1) by name.

                           mov  dx, variable1

                 It is also possible to have name + constant.

                           mov  dx, variable1 + 27

                 The assembler will resolve this into a single offset number
                 and will give the appropriate information to the linker.

                 (2) with the single pointers BX, SI, DI and BP (which are
                 enclosed in square brackets).

                           mov  cx, [si]
             ____________________

                8 Bearing in mind that all compiled languages have fixed
             formats for arrays. If you want your array to interact with C,
             Fortran, Pascal or Basic, you'd better be sure you have the right
             format.





             Chapter 11 - Addressing Modes                                 113
             _____________________________

                           xor  al, [bx]
                           add  [di], cx
                           sub  [bp], dh

                 (3) with the single pointers BX, SI, DI and BP (which are
                 enclosed in square brackets) plus a constant.

                           mov  cx, [si+421]
                           xor  al, 18+[bx]
                           add  93+[di]-7, cx
                           sub  (54/7)+81-3+[bp]-19, dh

                 (4) with the double pointers [bx+si], [bx+di], [bp+si],
                 [bp+di]  (which are enclosed in square brackets).

                           mov  cx, [bx][si]
                           xor  al, [di][bx]
                           add  [bp]+[di], cx
                           sub  [di+bp], dh

                 (5) with the double pointers [bx+si], [bx+di], [bp+si],
                 [bp+di]  (which are enclosed in square brackets) plus a
                 constant.

                           mov  cx, [bx][si+57]
                           xor  al, 45+[di+23][bx+15]-94
                           add  [bp]+[di]-444, cx
                           sub  [6+di+bp]-5, dh

             These are ALL the addressing modes allowed on the 8086. As for
             the constants, it is the ASSEMBLER'S job to resolve all numbers
             in the expression into a single constant. If your expression
             won't resolve into a constant, it is between you and the
             assembler. It has nothing to do with the 8086 chip.