185

                                  CHAPTER 18 - PORTS


             In order to communicate with the outside world, the outside world
             being your printer, your disk drives, your modem etc., the 8086
             uses ports. A port is an address distinct from a memory address
             where the i/o device can be reached.{1}  When IBM set up the
             first PC, they decided what these port addresses would be and
             what the function of each bit at each address would be. Any VGA,
             EGA, CGA or monochrome card has to have it's ports at the same
             addresses as those set by IBM, and these ports have to do the
             same thing. 

             Normally, an i/o device has more than one port address. The
             device not only has to transfer the data, it has to tell the
             computer whether it is ready, find out if the computer wants to
             send information, confirm that the transfer was successful etc.
             COM1 is port addresses 3F8 - 3FF. COM2 is 2F8 - 2FF. The CGA
             adapter is ports 3D0 - 3DF. 

             In the CGA, port 3D9 sets the different colors. The 8086 writes
             to it, but can't read it. Port 3DA, it's neighbor, tells certain
             status information and is read only. 

             All control information for the video cards is passed back and
             forth through the ports. However, the video card comes into
             memory 50 times a second to see what it should write to the
             screen. The characters on the screen don't pass through the
             ports. The mountain comes to Mohammed. 

             The data does pass through a port on the way to your serial
             printer. The 8086 sends your printer control information through
             one port address and sends the data through a different port
             address. 

             The port instructions can be either with AL or AX. AL and AX are
             the only registers you can use, AL for a byte transfer and AX for
             a word transfer. There are two forms to the input instruction:

                 in   al, port_address
             or
                 in   al, dx

             port_address is a constant and is limited to 0 - 255. It is a one
             byte constant. DX is the only register than can be used with the
             second form. DX can contain any number from 0 - 65535. The
             ____________________

                1. There is memory address 0000 and there is port address
             0000; they are two entirely different things. You can reach
             memory address 0000 with the DS:SI pair 0000:0000, but DS:SI
             can't get to port address 0000. The instruction "out 0, al"
             writes the contents of al to port address 0000,  but the OUT
             instruction can't get anywhere near memory address 0000.

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             The PC Assembler Tutor                                        186
             ______________________

             following two pieces of code do the same thing:

                 in   al, 155

                 mov  dx, 155
                 in   al, dx

             This code moves one byte of data from port 155 to register AL. 

             The output instruction is similar. We have:

                 out  port_address, al
             or
                 out  dx, al

             where port_address is a constant 0-255 and DX can contain a
             number 0 - 65535. 

                 out  97, ax

             moves a word from AX to port addresses 97-98. Notice that both
             the IN and the OUT instructions follow the  DESTINATION, SOURCE
             ordering found in all the other 8086 instructions.

             The  "in  ax, port_address" form is not all that useful. If you
             look at the addresses for the video ports, for COM1 and COM2, you
             will see that they are all larger than 255. Also, most equipment
             can be at several different addresses. A modem can be at COM1,
             COM2, COM3, or COM4. If the port address is hard coded into the
             instructions, you need 4 subprograms to handle the 4 different
             addresses. It is easier to find out where the modem is, then use:

             modem_data_address dw   ?

                 mov  dx, modem_data_address 
                 in   al, dx

             and
                 mov  dx, modem_data_address
                 out  dx, al

             If you aren't planning on writing device drivers this is for
             background information only, since all standard i/o is done
             through DOS or BIOS interrupts. 

             One last thing is the parity flag. It has been sitting on the
             screen with all the other flags. What is it for?  When you send
             information over a modem, there is a large possibility of line
             interference. If it is text, and an occasional screw up is not
             too bad, using a parity check may be enough.{2}  Parity can be
             even or odd. Even means that an even number of bits are set to 1;
             odd means that an odd number of bits are set to 1. This is not
             whether the number is even or odd, it is whether the number of 1
             ____________________

                2. It is NEVER enough if you are transferring binary data or
             executable files.





             Chapter 18 - Ports                                            187
             __________________

             BITS is even or odd. Here's a short list.

                      NUMBER         BINARY         PARITY

                           6           0110         even
                           7           0111         odd
                           8           1000         odd
                           9           1001         even
                          10           1010         even

             8 is an even number but has odd parity, 9 is an odd number but
             has even parity. 6 has two 1 bits (even), 7 has three 1 bits
             (odd), 8 has one 1 bit (odd), 9 has two 1 bits (even) and 10 has
             two 1 bits (even).

             How does this help us? If there is a chance of 1/100 of screwing
             up a single bit in a byte, there is only a chance of 1/10,000 of
             screwing up two bits in a byte. What this means is that of every
             100 errors, 99 of them will will be detectable because of a
             change in parity (by changing a bit from 0 to 1 or from 1 to 0)
             and only 1 of them will go undetected because two changes will
             keep the same parity. This is a little obscure, so make sure you
             understand why before continuing.

             This doesn't help us much yet, because we don't know what the
             parity was originally. 9 has even parity, 7 has odd parity. What
             communications programs do is FORCE the parity. They can either
             force it even or force it odd.

             The standard ASCII characters end at 127 - that is, 0111 1111 
             (7F) is the highest legal number you can transmit. The left bit
             is unused, so we can use it to force the parity. We are going to
             force it even, but forcing it odd uses the same technique. 

             The steps are:

                 (1) Find the parity of the byte.

                 (2) If it is even, leave it alone, if it is odd, put a 1 in
                 the left hand bit. The parity is now even.

             If both the sending and receiving program have agreed on even
             parity, then on the receiving end, the program:

                 (1) Checks for even parity. If the parity is odd, it is an
                 error.

                 (2) Puts a 0 back in the left hand bit. The original number
                 is restored.

             We are going to make a loop with both parts and use show_regs to
             watch the parity flag. Here's the program:

             ; - - - - - - - - - - ENTER DATA BELOW THIS LINE

             error_banner  db  "Whoa! We have a screw up.", 13, 10, 0






             The PC Assembler Tutor                                        188
             ______________________

             ; - - - - - - - - - - ENTER DATA ABOVE THIS LINE

             ; - - - - - - - - - - ENTER CODE BELOW THIS LINE
                 mov  ax_byte, 0A3h            ; al binary
                 mov  bx_byte, 0A2h            ; unsigned half registers
                 mov  cx_byte, 0A2h            ; unsigned half registers
                 mov  dx_byte, 0A3h            ; dl binary
                 lea  ax, ax_byte
                 call set_reg_style

             comm_loop:
                 mov  ax, 0
                 call set_count                ; reset count to 0
                 mov  bx, 0                    ; clear registers
                 mov  cx, 0
                 mov  dx, 0
                 call show_regs                ; (1)

                 ; the sending program

                 call get_unsigned_byte
                 and  al, 7Fh             ; 0111 1111 - make sure al < 128
                 mov  bl, al                   ; copy to bl
                 call show_regs_and_wait       ; (2)

                 and  al, al                   ; check parity
                 call show_regs_and_wait       ; (3)

                 jpe  do_nothing
                 or   al, 80h                  ; if parity odd, set left bit

             do_nothing:
                 and  al, al                   ; check parity for show_regs
                 call show_regs_and_wait       ; (4)

                 ; the receiving program

                 mov  dl, al                   ; transmit from al to dl
                 mov  cl, dl                   ; copy to cl
                 call show_regs_and_wait       ; (5)

                 and  dl, dl
                 jpe  zero_left_bit            ; is parity even?
                 mov  ax, error_banner
                 call print_string

             zero_left_bit:
                 and  dl, 7Fh             ; 0111 1111  binary, left bit 0
                 mov  cl, dl                   ; copy to cl
                 call show_regs_and_wait       ; (6)
                 jmp  comm_loop

             ; - - - - - - - - - - ENTER CODE ABOVE THIS LINE

             First, we set the register style so AL and DL are binary, BL and
             CL are unsigned. We'll use AL and BL for sending, CL and DL for
             receiving. Next, we reset the counter to 0 so we can see where we





             Chapter 18 - Ports                                            189
             __________________

             are, and zero AX, BX, CX, and DX. We get a byte and make sure
             that it is 127 or less,{3} then send a copy to BL. BL stays
             unchanged for the rest of the loop. We test the parity. and if it
             is odd, change it. Finally, we send it off to DL.

             On the receiving end, we test the parity. If it is odd, we print
             an error message. Then we zero the left hand bit. It is faster to
             zero the left hand bit than to check to see if it needs to be
             zeroed, so we do it for all data. The result is put in CL for
             comparison. AL and DL are shown in binary form so you can count
             the number of 1 bits in the byte.

































             ____________________

                3. The following could happen if we didn't take this step. We
             get a number > 128 with odd parity. 131 (1000 0011  83h) is an
             example. The sending program sees that it is odd parity, so it
             puts a 1 in the left hand bit. But there is already a 1 in the
             left hand bit, so the parity doesn't change, it is odd. The
             receiving program gets the byte, tests it, notices that it is
             odd, and sends back a transmission error. Since the sending
             program didn't see anything wrong, it just sends the same byte
             again. It will never get through correctly. In real life, the
             sending program would probably test the byte to see if it was
             greater than 127 and print an error if it was.





             The PC Assembler Tutor                                        190
             ______________________

                                          SUMMARY


             POSSIBLE I/O INSTRUCTIONS

             in  ax, constant (= port address 0 - 255)
             in  ax, DX

             in  al, constant (= port address 0 - 255)
             in  al, DX

             out constant, ax  (constant = port address 0 - 255)
             out DX, ax

             out constant, al  (constant = port address 0 - 255)  
             out DX, al

             In these instructions DX holds a port address and 
             can be from  0 - 65535.


             PARITY

             Parity is whether the number of 1 bits in a byte (or word) is
             even or odd. The 8086 sets the parity flag after most arithmetic
             and all logical operations. If parity is even, the flag is 1, if
             parity is odd, the flag is 0.