16

                                 CHAPTER 3 - ASMHELP


             We are now going to introduce both the 8086 registers and a
             program for looking at them. You are going to get information
             flying at you at a rapid pace, so read both this and the next
             chapter carefully and slowly. 


             REGISTERS

             The 8086 has a number of registers. Remember, registers are
             places for storing data that are internal to the 8086 chip. They
             are much faster, but there are very few of them.

             There are 6 registers that you can use for addition and subtrac-
             tion of word (2 byte) sized numbers, as well as logical opera-
             tions on word (2 byte) numbers or data. These registers are AX,
             BX, CX, DX, SI, DI. In addition, there is a register which works
             the same way, but has a special function in all high-level
             languages (Basic, Pascal, C, etc.). This is BP, the base pointer.

             There is one more register that performs the same operations as
             the above seven, but it is RESERVED for special use and should
             never be used for anything. It is called SP (the stack pointer).

             There are 4 registers that tell the 8086 which memory segments
             you are in. They just sit there and help the 8086 find things in
             memory. You will learn how they work later. They are CS, DS, SS,
             ES. (That is Code Segment, Data Segment, Stack Segment and Extra
             Segment respectively). 

             There is the flags register which contains all the information
             the 8086 needs to evaluate its state. We will learn about this
             later. The flags register has no name, and there are machine
             instructions for manipulating individual flags in the register.

             Finally, there is IP, the instruction pointer, which points to
             the machine instructions. You have no direct access to this,
             which is good because you would screw it up for certain. The 8086
             handles the IP automatically and correctly.

             One word (two bytes or 16 bits) is the largest piece of data that
             the 8086 can handle naturally. It is possible to handle larger
             things, but we do it through software (which is slower), not
             hardware (which is faster). Sometimes we want to handle things
             one byte at a time as when we work with characters. The 8086
             gives us this possibility by letting us divide the AX, BX, CX,
             and DX registers into an upper half and a lower half. For any or
             all of these registers, we can replace one 2 byte register by two
             1 byte registers. The data in the full register stays the same,
             but we can look at each half. The two parts of AX are called AH
             (for A high) and AL (for A low). 

                 |------AX------|
                 0000000000000000
                 |--AH--||--AL--|






             Chapter 3 - ASMHELP.OBJ                                        17
             _______________________

             This is the 16 bit binary number 0 in the AX register. Using AX
             allows us to manipulate all 16 bits. Using AH allows us to
             manipulate the upper 8 bits (without affecting the lower 8 bits),
             and using AL allows us to manipulate the lower 8 bits without
             affecting the upper 8 bits. Similarly, for BX we have BH, BL, for
             CX we have CH, CL, and for DX we have DH, DL.


             SHOW_REGS

             We have named all the registers, now let's take a look at them.
             Included in the module asmhelp.obj is a program called show_regs.
             It shows all the above registers on the top 10 lines of your
             screen and allows you to enter data normally underneath. 

             When you call show_regs, it puts the current value of all the
             registers on the screen. Those values stay on the screen until
             the next call - i.e. the program does not change what is on the
             screen even though the registers may be changing value. You need
             to call show_regs every time that you want to see the current
             values of the registers.

             The first time you call show_regs, it clears the screen so you
             should call it right at the beginning of the program in order to
             initialize the screen.

             This time we want temp2.asm for a template; we will call this
             program prog3.asm, so make a copy of temp2.asm and give it the
             new name.  Let's take a look at it. The only differences are (1)
             there are a lot more programs in the EXTRN statements and (2) in
             the data segment DATASTUFF there are these definitons:

             ax_byte  db   2
             bx_byte  db   2
             cx_byte  db   2
             etc.

             These will be used for show_regs later, but you need to learn a
             few assembler instructions first.

             Here's our next program:

             TEMP2.ASM
             + + + + + + + + START CODE BELOW THIS LINE
                 call show_regs

             label_one:
                 call get_hex
                 call show_regs

                 call get_num
                 call show_regs

                 jmp  label_one

             + + + + + + + + END CODE ABOVE THIS LINE






             The PC Assembler Tutor                                         18
             ______________________

             That's all the program does. It asks for a number, then calls
             show_regs to show us what is in the registers. Note that one of
             the numbers is hex while the other number is decimal.

             Compile this, and link it with 

             >link prog3+\asmhelp ;

             and we're ready to go.

             The program reads information in the computer to find out what
             kind of monitor you have and where the screen output goes. It
             then puts the register information on the top lines. If it
             doesn't appear there, we have a screwup somewhere. The text
             should appear in black and white, but if you have a color monitor
             you can make it a blue background with white letters.{1} 


             *********************** SCREEN SHOT ***************************

                 AX  19825                             SI  00000 
                 BX  00000                             DI  00256 
                 CX  00255                             BP  17113 
                 DX  02596                             SP  00508 
              
                 CS  0AA4H   DS  0A54H   ES  0A24H   SS  0A34H   IP  0018H 
              
                 OF   DF  IEF   TF   SF   ZF   AF   PF   CF 
                       +    x         +    x         E            COUNT  00003

             -----------------------------------------------------------------
              
             The PC Assembler Helper   Version 1.0 
             Copyright (C) 1989  Chuck Nelson   All rights reserved. 
             Enter a two byte hex number  4df9 
             Enter any decimal number  +19825 
             Enter a two byte hex number 


             *****************************************************************

             This is how the screen looks after entering first a hex number,
             then a decimal number. The numbers in the registers will probably
             be different for you. Note that AX contains the last number that
             was entered. On the left side you will see the AX, BX, CX and DX
             ____________________

                1 To make a blue background and white letters, insert the code
             "call  set_blue" before the FIRST "call show_regs". i.e.:

                      call  set_blue
                      call  show_regs

                 label_one:
                      etc.

             This only works if it is allowed by the video board.





             Chapter 3 - ASMHELP.OBJ                                        19
             _______________________

             registers. For the time being, these registers will display
             unsigned numbers. On the right are the SI, DI, BP and SP
             registers. They are also unsigned numbers for the moment. Below
             that are the segment registers CS, DS, ES, and SS and the
             instruction pointer (IP). These are hex numbers and will always
             be hex numbers. The bottom line has OF, DF, IEF, etc.  These are
             the flags, and the marking underneath them (either a blank or
             some character) tells how they are set. Finally we have COUNT.
             This has nothing to do with the 8086. It is a counter that is
             incremented each time you call show_regs. 

             Keep entering numbers and watch the registers. You will notice
             that three things are changing - AX, IP and COUNT. AX has the
             last number you entered and IP keeps changing. Write down the
             value of IP each time it changes. It goes back and forth between
             two numbers. That is because you call show_regs in two different
             places in the loop, {2} and those are two different places in
             memory where the 8086 is reading the machine code. 

             Why is AX changing? You may have wondered in prog1.asm and
             prog2.asm how that information was going back and forth between
             your program and asmhelp.obj. The answer is that in all the
             programs in asmhelp.obj, if you need to pass information, it is
             passed via register AX. This is not the normal way to pass
             information. The normal way is more elegant but more complicated.
             We will cover that much later. The counter, of course, increases
             by 1 each time you call show_regs.

             Try entering a few more numbers and then it's time to go on to
             the next program. 


             MOVING DATA

             Obviously, we want to move data from memory to the 8086, from the
             8086 to memory, and between registers. We have the following
             possibilities: 

                 (1)  move from a register to memory
                 (2)  move from memory to a register
                 (3)  move a constant to memory
                 (4)  move a constant to a register
                 (5)  move from one register to another register

             That's it. There is no 8086 instruction that moves a single word
             or a byte from one place in memory to another.

             The move mnemonic for the 8086 is "mov".{3}  We need some sample
             data:
             ____________________

                2 IP actually has three different values, since you call
             show_regs once before you enter the loop.

                3 A mnemonic is a name for a machine instruction, which sounds
             like what the instruction is supposed to do - MOV for move, SUB
             for subtract, IMUL for integer multiplication, etc.





             The PC Assembler Tutor                                         20
             ______________________


             EXAMPLE DATA

             this_year     dw   1989
             total         dw   ?
             average       dw   ?
             time          dw   7

             age           db   ?         ; I hope you aren't older than 255
             poem          db   "In 1492 Columbus played a mean kazoo."
             secret_code   db   3Bh
             character     db   ?

             Here is some sample code. To move from register to memory, we
             have:

                      mov  total, ax
                      mov  time, si
                      mov  age, cl    
                      mov  character, bh

             The first thing that strikes the eye is that the destination is
             on the left and the source is on the right.{4}  This is standard
             for the 8086 instruction set, and it's going to take some getting
             used to. DESTINATION ON LEFT, SOURCE ON RIGHT. You are going to
             blow this one from time to time, so always double check to make
             sure that they are in the right order. 

             Also note that the 1 byte registers are matched up with 1 byte
             variables, and 2 byte registers are matched up with 2 byte data.
             If the sizes don't match, the assembler will complain.{5}  Thus:

                      mov  age, ax

             is an illegal instruction.

             For examples of memory to register moves, we have:

                      mov  ch, secret_code
                      mov  di, this_year
                      mov  dl, poem       ; moves 'I' to dl
                      mov  bx, time
             ____________________

                4 The computer community likes the words "destination" and
             "source". "Source" means FROM, and "destination" means TO. The
             8086 instruction set is designed:

                 MOV  TO, FROM

             which is exactly opposite to the way you would say it in an
             English sentence. For the 8086, it is always destination on the
             left, source on the right. 

                5 Half register and full register operations have different
             machine codes, and the assembler needs to know which code to use,
             so the two things must be the same number of bytes. 





             Chapter 3 - ASMHELP.OBJ                                        21
             _______________________


             Once again: (1) DESTINATION ON LEFT, SOURCE ON RIGHT, and (2) the
             sizes of the two objects must match.

             For constant to memory we have:

                      mov  total, 2986
                      mov  age, 36h
                      mov  secret_code, 0110100b
                      mov  average, (27/5) + 3

             The arithmetic is done by the assembler and anything that is made
             up totally of constants is legal. Thus:

                      mov  average, (((64+27)*51 )/(196-82))

             is legal but:

                      mov  average, this_year/time

             is illegal. The assembler makes either a one byte or a two byte
             constant to match the size of the destination. The constants for
             "total" and "average" are two byte constants while those for
             "age" and "secret_code" are one byte constants. The constants
             must be within range, that is -129 is too negative for a byte,
             256 is too positive for a byte, -32769 is too negative for a
             word, 65536 is too positive for a word. The assembler will give
             an error if the constant is out of range.

             You can also move a constant to a register:

                      mov  al, 'c'
                      mov  ax, 'c'
                      mov  di, 46280
                      mov  bl, 99

             The same rules apply. The constant must be within range and the
             assembler will make a constant the same size as the destination
             register (one or two bytes). These constants are actually
             imbedded in the machine code by the assembler, and are
             unchangable.

             Lastly, you can move data from one register to another:

                      mov  ax, cx         ; from cx to ax
                      mov  ah, bl         ; from bl to ah
                      mov  dl, dh         ; from dh to dl
                      mov  di, dx         ; from dx to di

             All this is summarized at the end of the chapter.


             It's time for program #4. All this program is going to do is get
             input and the move it to different registers. We are still using
             temp2.asm. Here's the program:

             TEMP2.ASM





             The PC Assembler Tutor                                         22
             ______________________

             ;+ + + + + + + + + + START DATA BELOW THIS LINE

             byte_data  db ?
             word_data  dw ?

             ;+ + + + + + + + + + END DATA ABOVE THIS LINE

             ;+ + + + + + + + + + START CODE BELOW THIS LINE

                 call show_regs

             This_is_a_very_long_label_name:
                 call get_hex                       ; (1)
                 call show_regs_and_wait

                 mov  dx, ax                        ; (2)
                 call show_regs_and_wait

                 mov  byte_data, al                 ; (3)
                 mov  ch, byte_data
                 call show_regs_and_wait

                 mov  word_data, ax                 ; (4)
                 mov  di, word_data
                 call show_regs

                 jmp  This_is_a_very_long_label_name

             ;+ + + + + + + + + + END CODE ABOVE THIS LINE

             There is a data section in this one, so copy those variables into
             your data section. Here is what the program does. (1) it gets a
             hex number from the keyboard, (2) it moves the number in ax to
             dx, (3) it moves one byte from al to ch via the variable
             byte_data, and (4) it moves two bytes from ax to di via
             word_data.

             There are two different subprograms - show_regs and
             show_regs_and_wait. They do the same thing except that
             show_regs_and_wait waits for you to hit the ENTER key before
             continuing. The computer works so fast that we wouldn't be able
             to see the changes in the screen if we didn't have a way of
             pausing. You can use COUNT on the screen to keep track of exactly
             where you are in the loop.

             Assemble program 4, link it to asmhelp.obj, and watch it work.
             There are two things to notice here. First, we are entering a hex
             number, but AX is displaying an unsigned number. It is not
             self-evident that the unsigned number in AX is the same as the
             hex number that you are entering. Secondly, though CH is
             changing, there doesn't seem to be any relationship between the
             number in AX and the number in CX. We will solve both problems in
             the next chapter.









             Chapter 3 - ASMHELP.OBJ                                        23
             _______________________

                                          SUMMARY


                           MOVING DATA

             You can:
                 (1)  move from a register to memory
                 (2)  move from memory to a register
                 (3)  move a constant to memory
                 (4)  move a constant to a register
                 (5)  move from one register to another register

                 The constants are actual constants which are imbedded in the
                 machine code.

                           REGISTERS

             The normal registers are AX, BX, CX, DX, SI, DI AND BP. AX, BX,
             CX, and DX can be divided into AH-AL, BH-BL, CH-CL AND DH-DL. The
             'H' is for high and the 'L' is for low.
             SP is committed and may not be used.
             The segment registers are CS, DS, ES, SS.
             The instruction pointer (IP) is not available to you.
             The register that holds the flags is manipulated by special
             machine instructions.



                           ASMHELP.OBJ

             Call show_regs to see what is in the 8086 registers. Count
             increments by one every time you call show_regs. 

             show_regs_and_wait is the same as show_regs except that it waits
             for you to hit the ENTER key to allow you time to look at the
             screen.

             Call set_blue at the outset if you have a color card and a color
             monitor and you want to have a blue background.

             get_num gets a signed or unsigned number from the keyboard. (1-5
             digits). It does no range checking to see whether the number is
             too big. All other input routines check to see if a number is too
             large for its data size.

             get_hex gets a hex number from the keyboard.  (1-4 digits)

             get_ascii gets characters from the keyboard.  (1 or 2 characters)

             get_binary gets a binary number from the keyboard (1 - 16 digits)

             print_num prints a number as hex, signed, unsigned, char, and
             binary.

             All data transfer to or from ASMHELP.OBJ is via the AX register.