56

                              CHAPTER 8 - SHIFT AND ROTATE


             There are seven instructions that move the individual bits of a
             byte or word either left or right. Each instruction works
             slightly differently. We'll make a standard program and then
             substitute each instruction into that program.


             SAL - SHL

             The instructions SHL (shift logical left) and SAL (shift
             arithmetic left) are exactly the same. They have the same machine
             code. They shift each bit to the left. How far? That depends.
             There are two (and only two) forms of this instruction. All other
             shift and rotate instructions have these two (and only these two)
             forms as well. The first form is:

                 shl  al, 1

             Which shifts each bit to the left one bit. The number MUST be 1.
             No other number is possible. The other form is:

                 shl  al, cl

             shifts the bits in AL to the left by the number in CL. If CL = 3,
             it shifts left by 3. If CL = 7, it shifts left by 7. The count
             register MUST be CL (not CX). The bits on the left are shifted
             out of the register into the bit bucket, and zeros are inserted
             on the right. The easy way to understand this is to fire up the
             standard program. Remember, from now on we always use
             template.asm.

             ;sal.asm
             ; + + + + + + + + + + + + + + + START CODE BELOW THIS LINE 
                    mov   ax_byte, 0A3h       ; half reg, low reg binary 
                    mov   bx_byte, 0A4h       ; half reg, low reg hex 
                    mov   cx_byte, 0A1h       ; half reg, low reg signed 
                    mov   dx_byte, 0A2h       ; half reg, low reg unsigned 
                    lea   ax, ax_byte 
                    call  set_reg_style 
              
                    mov   ax, 0               ; clear registers
                    mov   bx, 0 
                    mov   cx, 0 
                    mov   dx, 0 
                    mov   di, 0 
                    mov   bp, 0 
                    call  show_regs 
              
             outer_loop: 
                    call  get_hex_byte   ; get number and put in registers 
                    mov   bl, al 
                    mov   cl, al 

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             Chapter 8 - Shift and Rotate                                   57
             ____________________________

                    mov   dl, al 
                    mov   si, 8         ; 8 iterations of the loop
                    and   al, al        ; set the flags
                    call  show_regs_and_wait 
             shift_loop: 
                    sal   al, 1 
                    sal   bl, 1 
                    sal   cl, 1 
                    sal   dl, 1 
                    call  show_regs_and_wait 
                    dec   si 
                    jnz   shift_loop 
                    jmp   outer_loop 
              
             ; + + + + + + + + + + + + + + + END CODE ABOVE THIS LINE 

             This standard program is with bytes, not words. This is because
             if we had used words we would have performed 16 individual shifts
             and that would have been time consuming and boring. First we set
             the style to half registers. Notice that one is binary, one is
             hex, one is signed and one is unsigned. That covers all bases.
             All the registers are then cleared. It would be nice to use the
             loop instruction, but CX is committed, so we make our own loop
             instruction. We move 8 into SI. The loop instructions are:

                 dec  si
                 jnz  shift_loop

             DEC decrements a register or a variable by 1. Its counterpart INC
             increments a register or variable by 1. JNZ (jump if not zero)
             jumps to 'shift_loop' if SI is not zero.

             We get a hex byte in AL and put the same byte in BL, CL, and DL.
             This way we will be able to see what is happening in binary, hex,
             signed and unsigned. Before starting, we have:

                 and  al, al

             This is there to set the flags correctly before starting. All
             four are shifted left one bit each time, and then we look at the
             result.

             Assemble, link and run it. Enter the number 7. In binary, that is
             (0000 0111). Take a look at the flags before starting. It is a
             positive number so SF shows '+'. ZF is not set. PF shows 'O'. O
             stands for odd. Every time you perform an arithmetic or logical
             operation, the 8086 checks parity. Parity is whether the number
             contains an even or odd number of 1 bits. This contains 3 1 bits,
             so the parity is odd. The possible settings are 'E' for even and
             'O' for odd.{1} SAL checks for parity (though some of the other
             instructions don't).  Now press ENTER. It will shift left 1 and
             you will have (0000 1110). What does the unsigned number say now?
             14. Press ENTER again. (0001 1100) What does the unsigned number
             say? 28. Again (0011 1000) 56. Again (0111 0000) 112. Notice that
             ____________________

                1 This is for use by communications programs.





             The PC Assembler Tutor                                         58
             ______________________

             the signed number reads +112. Look at the CF and OF. They are
             both cleared. Things are going to change now. Press ENTER again.
             (1110 0000). SF is now '-'. OF, the overflow flag is set because
             you changed the number from positive to negative (from +112 to
             -32). What is the unsigned number now? 224. CF is cleared. PF is
             '0'. Shift again. (1100 0000) OF is cleared because you didn't
             change signs. (Remember, the leftmost bit is the sign bit for a
             signed number). PF is now 'E' because you have two 1 bits, and
             two is even. CF is set because you shifted a 1 bit off the left
             end. Keep pressing ENTER and watch SF, OF, CF, and PF.

             Let's look at the unsigned numbers we had until we started
             shifting 1 bits off the left end. We started with 7, then had 14,
             28, 56, 112, 224. This instruction is multiplying by 2. That's
             right, and it is MUCH faster than multiplication (about 50 times
             faster). Far and away the fastest way to multiply a register by
             2, 4 or 8 is to use sal.

                 ; by 2              ;by 4               ; by 8
                 sal  di,1           sal  di, 1          sal  di, 1
                                     sal  di, 1          sal  di, 1
                                                         sal  di, 1

             For a register, it is faster to use a series of 1 shifts than to
             load cl. For a variable in memory, anything over 1 shift is
             faster if you load cl.

             Do a few more numbers to see what is happening both with the
             number and the flags. CF always signals when a 1 bit has been
             shifted off the end.


             SAR and SHR

             Unlike the left shift instruction, there are two completely
             different right shift instructions. SHR (shift logical right)
             shifts the bits to the right, setting CF if a 1 bit is pushed off
             the right end. It puts 0s in the leftmost bit. Make a copy of
             SAL.ASM and replace the four instructions:

                    sal   al, 1 
                    sal   bl, 1 
                    sal   cl, 1 
                    sal   dl, 1 

             with SHR. We'll call the new program SHR.ASM. Run this one too.
             Instead of 7, use E0h (1110 0000) which is 224d. The first time
             you shift (0111 0000) the OF flag will be set because the sign
             changed. Keep shifting, noting the flags and the unsigned number.
             This time we have 224, 112, 56, 28, 14, 7, 3, 1. It is dividing
             by two and is once again MUCH faster than division. For a single
             shift, the remainder is in CF. For a shift of more than one bit,
             you lose the remainder, but there is a way around this which we
             will discuss in a moment. Do some more numbers till you are
             comfortable with the flags and the operation.

             If you want to divide by 16, you will shift right four times, so





             Chapter 8 - Shift and Rotate                                   59
             ____________________________

             you'll lose those 4 bits. But those bits are exactly the value of
             the remainder. All we need to do is:

                 mov  dx, ax    ; copy of number to dx
                 and  dx, 0000000000001111b ; remainder in dx
                 mov  cl, 4     ; shift right 4 bits
                 shr  ax, cl    ; quotient in ax

             Using a mask, we keep only the right four bits, which is the
             remainder.


             SAR

             SAR (shift arithmetic right) is different. It shifts right like
             SHR, but the leftmost bit always stays the same. This will make
             more sense when you run the program. Make another copy, call it
             SAR.ASM, and change the four instructions to SAR. The flags
             operate the same as for SHR and SHL. The overflow flag will never
             change since the left bit will always stay the same. 

             First enter 74h (+116). We will be looking at the signed numbers
             only. Copy down the signed numbers as you go along. They should
             be: 116, 58, 29, 14, 7, 3, 1, 0, 0. Now try 8Ch (-116). The
             numbers you should get are: -116, -58, -29, -15, -8, -4, -2, -1,
             -1. They started out the same, then they got off by one. The
             negative numbers are one too negative. Try  39h (+57). The
             numbers here are: 57, 28, 14, 7, 3, 1, 0, 0, 0. Just as it should
             be for division by 2. Now try C7 (-57). Here the numbers are:
             -57, -29, -15, -8, -4, -2, -1, -1, -1. This time it went screwy
             right off the bat. Once again, the negative numbers are one too
             negative. 

             SAR is an instruction for doing signed division by 2 (sort of).
             It is, however, an incomplete instruction. The rule for SAR is:
             SAR gives the correct answer if the number is positive. It gives
             the correct answer if the number is negative and the remainder is
             zero. If the number is negative but there is a remainder, then
             the answer is one too negative. The reason for this is a little
             complex, but we need to add some code if we want to do signed
             division.{2} For SHR, the remainder part was optional. Here it is
             not. We need to know whether the remainder is zero or not. For
             this example we will do a word shift left by 6. That's dividing
             by 64.

                 remainder_mask dw   002Fh     ; 63

                 call get_signed          ; number in ax
                 mov  bx, ax              ; copy in bx
                 and  bx, remainder_mask  ; the remainder
                 mov  cl,6                ; shift right 6 bits
                 sar  ax, cl
                 jns  continue            ; is it positive?
             ____________________

                2 Both the code and the reasons will be explained (but not
             proved) in the summary.





             The PC Assembler Tutor                                         60
             ______________________

                 and  bx, bx              ; is the remainder zero?
                 jz   continue
                 inc  ax
             continue:

             We get the remainder, then shift right 6 bits. Upon finishing
             SAR, the sign flag will be set correctly. Here is yet another
             jump. This one is JNS (jump on not sign) jumps if the sign flag
             is NOT set, that is if the number is positive. If it is positive,
             then everything is ok so we skip ahead. If the number is
             negative, then we check to see if there was a remainder. If there
             wasn't, everything is ok, so we go ahead. If there was a
             remainder, then we INC (add 1) ax. 

             Is the remainder correct? If the number was positive, the
             remainder is correct, but if the number was negative, then we
             need to do one more thing. After INC, but before 'continue' we
             have a SUB instruction:

                      inc  ax
                      sub  bx, 64    ; correct the remainder
                 continue:

             Why that is the correct number will be explained in the summary.
             What a lot of work when we could simply write:

                 mov  cx, 64
                 call get_signed
                 cwd                 ; sign extend
                 idiv cx             ; signed division

             Is there any advantage to this instruction? Not really. Remember
             that the more you shift, the longer it takes. If you shift 2,
             then it's about 1/3 faster than division. If you shift 14, then
             it is only 15% faster than division. Considering that even a slow
             PC can do 25000 divisions a second, you must be in serious need
             of speed to use this. In any case, you will never or almost never
             use SAR for signed division, while you will find lots of
             opportunity to use SHR and SHL for unsigned multiplication and
             division.


             ROR and ROL

             ROR (rotate right) and ROL (rotate left) rotate the bits around
             the register. We will just do one program since they operate the
             same way, only in opposite directions. Make another copy of
             SAL.ASM and put in ROR in the appropriate spots. 

             Enter a number. This time you will notice that the bits, rather
             than dissapearing off the end, reappear on the other side. They
             rotate around the register. The only flags that are defined are
             OF and CF. OF is set if the high bit changes, and CF is set if a
             1 bit moves off the end of the register to the other side. Do a
             few more, and we'll go on to the last two instructions.







             Chapter 8 - Shift and Rotate                                   61
             ____________________________

             RCR and RCL

             RCR (rotate through carry right) and RCL (rotate through carry
             left) rotate the same as the above instructions except that the
             carry flag is involved. Rotating right, the low bit moves to CF,
             the carry flag and CF moves to the high bit. Rotating left, the
             high bit moves to CF and CF moves to the low bit. There are 9
             bits (or 17 bits for a word) involved in the rotation. Make yet
             another copy of the program, and change those 4 instructions to
             RCR. Also, since we have 9 bits instead of 8, change the loop
             count to 9 from 8:

                 mov  si, 9

             Enter a number and watch it move. Before you start moving, look
             at CF and see if there is anything in it. There are only two
             flags defined, OF and CF. Obviously, CF is set if there is
             something in it. OF is wierd. In RCL (the opposite instruction to
             the one we are using), OF operates normally, signalling a change
             in the top (sign) bit. In RCR, OF signals a change in CF. Why? I
             don't have the slightest idea. You really have no need for the OF
             flag anyways, so this is unimportant.


             Well, those are the seven instructions, but what can you do with
             them besides multiply and divide?

             First, you can work with multiple bit data. The 8087 has a word
             length register called the status register.  Looking at the upper
             byte:

                 15 14 13 12 11 10  9  8
                        X  X  X

             bits 11, 12 and 13 contain a number from 0 to 7. The data in this
             register is not directly accessable. You need to move the
             register into memory, then into an 8086 register. If you want to
             find what this number is, what do you do?

                 mov  bx, status_register_data
                 mov  cl, 3
                 ror  bx, cl
                 and  bh, 00000111b

             we rotate right 3 and then mask off everything else. The number
             is now in BH. We could have used SHR if we wanted. Another 8087
             register is the control register. In the upper byte it has:

                 15 14 13 12 11 10  9  8
                              X  X

             a number from 0 to 3 in bits 10 and 11. If we want the
             information, we do the same thing:

                 mov  bx, control_register_data
                 mov  cl, 2
                 ror  bx, cl





             The PC Assembler Tutor                                         62
             ______________________

                 and  bh, 00000011b

             and the number is in BH. 

             You are now going to write a program that inputs an unsigned
             number and prints out its hex representation. Here it is:


             ; + + + + + + + + + + + + + + + START CODE BELOW THIS LINE 
                    mov   ax_byte, 0A5h        ; half regs, right ascii 
                    mov   bx_byte, 4           ; hex 
                    mov   dx_byte, 4           ; hex 
                    lea   ax, ax_byte 
                    call  set_reg_style 
                    call  show_regs 
              
             outer_loop: 
                    call  get_unsigned 
                    mov   bx, ax 
                    mov   dx, ax 
                    mov   cx, 4 
             inner_loop: 
                    push  cx                  ; save cx 
                    mov   cl, 4 
                    rol   bx, cl              ; rotate left 1/2 byte 
                    mov   al, bl              ; copy to al 
                    and   al, 0Fh             ; mask off upper 1/2 byte 
                    cmp   al, 10              ; < 10, 0 - 9 ;  > 9  A - F 
                    jae   use_letters 
                    add   al, '0'             ; change to ascii 
                    jmp   print_it 
             use_letters: 
                    add   al, 'A' - 10         ;  10 = 'A' 
             print_it: 
                    call  print_ascii_byte 
                    call  show_regs_and_wait 
                    pop   cx 
                    loop  inner_loop 
                    jmp   outer_loop 
             ; + + + + + + + + + + + + + + + END CODE ABOVE THIS LINE 

             AL will be shown in ascii while BX and DX will be in hex. We save
             the original number in DX. Since the first thing we want to print
             is the left hex character, we rotate left, not right. We move the
             low byte to AL, mask off everything but the low hex number and
             then convert to an ascii character. If it is 0 - 9, we add '0'
             (the character, not the number). If it is > 9, we add "'A' - 10"
             and get a letter (if the number is 10, we get 'A'). JAE means
             jump if above or equal, and is an unsigned comparison.{3}


             ____________________

                3 You are getting innundated with conditional jump
             instructions. Don't worry. As long as you understand each one
             when you run across it, you don't have to remember it. All jump
             instructions will be covered soon.





             Chapter 8 - Shift and Rotate                                   63
             ____________________________

             Finally, we print the ascii character that is in AL.{4}

             Another thing to notice is that just inside the loop we push CX.
             That is because we use CL for the ROL instruction. It is then
             POPped just before the loop instruction. This is typical. CX is
             the only register that can be used for counting in indexed
             instructions. It is common for indexing instructions to be
             nested, so you temporarily store the old value of CX while you
             are using CX for something different.

                 push cx        ; typical code for a shift
                 mov  cl, 7
                 shr  si, cl
                 pop  cx


             Finally, let's multiply large numbers by 2. Here's the code:

             ; + + + + + + + + + + + + + + + START DATA BELOW THIS LINE 
             byte1  db    ? 
             byte2  db    ? 
             byte3  db    ? 
             byte4  db    ? 
             error_message  db  "Result is too large.", 0
             ; + + + + + + + + + + + + + + + END DATA ABOVE THIS LINE 

             ; + + + + + + + + + + + + + + + START CODE BELOW THIS LINE 
             outer_loop: 
                    lea   ax, byte1           ; get 4 byte number 
                    call  get_unsigned_4byte 
              
                    shl   byte1, 1 
                    rcl   byte2, 1 
                    rcl   byte3, 1 
                    rcl   byte4, 1 
                    jnc   go_on
                    lea   ax, error_message
                    call  print_string
             go_on:
                    lea   ax, byte1 
                    call  print_unsigned_4byte 
                    jmp   outer_loop 
             ; + + + + + + + + + + + + + + + END CODE ABOVE THIS LINE 

             This will require some explaination. Get_unsigned_4byte gets a
             number from 1 to four billion. We put it in memory. Normally, the
             following instructions would be done word by word. We are doing
             them byte by byte so you can see the mechanics of the situation.
             The low byte is shifted left 1 bit. This doubles it, but may
             shift a 1 bit from the high bit into CF. If it does, then it will
             be present when we rotate byte2. That moves CF into the low bit
             and moves the high bit into CF. We do it again. And again. If
             there is an unsigned overflow, it will be signalled by CF being
             ____________________

                4 Any subroutine in ASMHELP.OBJ that involves a one byte input
             or output has the data in AL.





             The PC Assembler Tutor                                         64
             ______________________

             set after:

                 rcl  byte4, 1

             JNC (jump on not carry) will skip the error message if everything
             is ok. Print_string prints a zero terminated string, that is a C
             string which is terminated by the number (not the character) 0.
             Finally, we print the number.

             A word about large numbers in ASMHELP.OBJ. It is assumed that you
             would like to use commas if you could. Any data type over 1 word
             long allows commas. The following are considered the same by
             ASMHELP.OBJ in its input routines:

                 23546787
                 2,3,5,4,6,7,8,7
                 23,,5,46,,78,7
                 23,546787
                 23,546,787

             It always prints commas correctly in the print routines.









































             Chapter 8 - Shift and Rotate                                   65
             ____________________________

                                          SUMMARY

             All shift and rotate instructions operate on either a register or
             on memory. They can be either 1 bit shifts:

                 sal  cx, 1
                 ror  variable1, 1
                 shr  bl, 1

             or shifts indexed by CL (it must be CL):

                 rcl  variable2, cl
                 sar  si, cl
                 rol  ah, cl



             SHL and SAL

                 SHL (shift logical left) and SAL (shift arithmetic left) are
                 exactly the same instruction. They move bits left. 0s are
                 placed in the low bit. Bits are shoved off the register (or
                 memory data) on the left side, and CF indicates whether the
                 last bit shoved was a 1 or a 0. It is used for multiplying
                 an unsigned number by powers of 2.


             SHR

                 SHR (shift logical right) does the same thing as SHL but in
                 the opposite direction. Bits are shifted right. 0s are
                 placed in the high bit. Bits are shoved off the register (or
                 memory data) on the right side and CF indicates whether the
                 last bit shoved off was a 0 or a 1. It is used for dividing
                 an unsigned number by powers of 2.


             SAR

                 SAR (shift arithmetic right) shifts bits right. The high
                 (sign) bit stays the same throughout the operation. Bits are
                 shoved off the register (or memory data) on the right side.
                 CF indicates whether the last bit shoved off was a 1 or a 0.
                 It is used (with difficulty) for dividing a signed number by
                 powers of 2.


             ROR and ROL

                 ROR (rotate right) and ROL (rotate left) rotate the bits of
                 a register (or memory data) right and left respectively. The
                 bit which is shoved off one end is moved to the other end.
                 CF indicates whether the last bit moved from one end to the
                 other was a 1 or a 0.

             RCR and RCL






             The PC Assembler Tutor                                         66
             ______________________

                 RCR (rotate through carry right) and RCL (rotate through
                 carry left) rotate the bits of a register (or of memory
                 data) right and left respectively. The bit which is shoved
                 off the register (or data) is placed in CF and the old CF is
                 placed on the other side of the register (or data).


             INC
                 INC increments a register or a variable by 1.

                      inc  ax
                      inc variable1

             DEC
                 DEC decrements a register or a variable by 1.

                      dec  ax
                      dec  variable1



             The following is fairly technical. It is only for those willing
             to wade their way through a turgid explaination. If you don't
             understand it, forget it.

             CODE FOR SHL

             If you are shifting an UNSIGNED number right by 'X' bits, it is
             the same as dividing by (2 ** X)  1 bit = (2**1 = 2), 2 bits =
             (2**2 = 4), 7 bits = (2**7 = 128). This is the same as dividing
             by a number which is all 0s except the Xth bit which is 1 (for 0
             we have 0000 0001, for 1 we have 0000 0010, for 3 we have 0000
             1000, for 7 we have 1000 0000). The remainder mask will be this
             number minus 1 (for 0 we have 0000 0000, for 1 we have 0000 0001,
             for 3 we have 0000 0111, for 7 we have 0111 1111). 


             CODE FOR SAR

             The order of numbers is important for SAR. If you start with 0
             and add 1 each time, the actual sequence of signed numbers that
             you get (from the bottom up) is:


                 -1
                 -2
                  .
                  .
                 -32767
                 -32768
                 +32767
                 +32766
                  .
                  .
                  3
                  2
                  1
                  0




             Chapter 8 - Shift and Rotate                                   67
             ____________________________


             The positive numbers are increasing in absolute value while the
             negative numbers are decreasing in absolute value. If you divide
             by shifting and there is no remainder, then the quotient is
             exact. If there is a remainder, the quotient will truncate
             towards 0 IN THE ABOVE DIAGRAM. This means that positive numbers
             will truncate down, while the negative numbers will truncate
             towards -32768, and will be one too negative. 

             If the number was positive, the remainder will be positive and
             will be exactly the same as for SHR. If the number was negative,
             then things are more complicated. We'll take division by 32 as an
             example. If we divide by 32 (0010 0000) the remainder mask will
             be 31 (0001 1111). If the number is negative, then what we get
             when we AND the mask:

                 and  ax, 00011111b

             is not the remainder but (remainder + 32). In order to get the
             actual negative remainder, we need to subtract 32. This gives us
             (remainder + 32 - 32). 

                 remainder mask = divisor - 1
                 negative remainder correction = NEG divisor.