Fixed Disk System Trainning Course


1.	Introduction


	1.1	Basic Function of Disk Controller

	1.2	Disk Interface Standard

		A.	ST-506/412 Winchester
		B.	Enhanced Small Device Interface(ESDI)
		C.	Storage Module Device(SMD)
		D.	Enhanced SMD
		E.	Small Computer Systems Interface(SCSI)
		F.	Intelligent Peripheral Interface(IPI)
		G.	AT-Bus

	1.3	Coding

		A.	Frequency Modulation(FM)
		B.	Modified Frequency MOdulation(MFM)
		C.	Run Length Limited(RLL)
		D.	Group Code Recording(GCR)
		E.	Zone Bit Recording(ZBR)*

	1.4	Data Format

	1.5	Sector Interleaving

	1.6	Disk Formatting

		A.	Physical Format
		B.	Partitioning
		C.	Logical Format

	1.7	Translative Versus Non-Translative Mode


2.	Winchester Disk Controller


	2.1	System Configuration for Fixed Disk System

3.	Programming Sequence in Fixed Disk Service Program

4.	Q & A


		1.	Introduction


1.1	Basic Function of a Disk Controller


	1.	Write data to the disk
	
	2.	Read data from the disk

	3.	Serialize and de-serialize data

	4.	Control the disk drive(option)

	5.	Ensure data integrity

	6.	Provide reasonable system interface(option)

	7.	Buffer data to/from disk



1.2	Disk Interface Standard




	  ³
    High  ³
	  ³
	  ³
	  ³						     . IPI
	  ³
	  ³		      . SMD	      . ESMD
	  ³
	  ³					      . SCSI
 COST	  ³				   . ESDI
	  ³
	  ³
	  ³
	  ³			. ST-412HP
	  ³
	  ³	     . ST-506/412	 . AT Bus
	  ³
    Low	  ³   . 3.5 Floppy
	  ³
	  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ>
	    Low						   High
			   PERFORMANCE

	Fig 1 :    Fixed Disk Interface Versus Market


A.	ST-506 412 Winchester Interface


	1.	Industry standard since 1981

	2.	Low capacity Winchester(5 - 150 Mbytes)

	3.	small size

	4.	Serial data transfer rate of 5 Mbits/second

	5.	Cost(not performance) oriented

	6.	Simple disk interface(most effort is in the disk controller)


B.	Enhanced Small Device Interface(ESDI)

	
	1.	Substantial upgrade to ST-506/412 interface

	2.	Oriented towards high-capacity, high speed small winchesters

	3.	Also capable of handling magnetic tapes and optical disks

	4.	Serial transfer rate 10 Mbits/second

	5.	Controller complexity simpler


C.	Storage Module Device(SMD)

D.	Enhanced SMD

E.	Small Computer Systems Interface(SCSI)


	1.	ANSI defined intelligent, low-cost peripheral interface

	2.	Derived from SASI(Shgart Assoc. Systems Interface)

	3.	8-bit parallel data transfer, 1.5 to 4 Mbytes/second

	4.	Provides device independent software

	5. 	Function more as a computer interface than a disk interface

	6.	Requires lots of intelligence in the peripheral
	

F.	Intelligent Peripheral Interface(IPI)

G.	AT-Bus


	1.	Cost dowm

	2.	Data transfer rate

	3.	An I/O slot more for another add on card

	4.	The fixed disk controller is no longer required


1.3	Coding

	    There are 4 different ways of improving the storage capacity of
	disk drives:
	
	    1)	Added more platters
	    2)	Added more tracks per platter
	    3)	Increase BPI(Bit Per Inch)
	    4)	Use better encoding methods
	
	    For method 1, it will increase manufacture cost for extra platter
	and extra read/write head set.

	    For method 2, it will increase control logic complexity for write
	current precompensation and interfere.

	    For method 3, it will use better read/write set to shorten the
	length between read/write head and platter.

	    For method 4, it will increase the encoding/decoding complexity.


A.	Frequency Modulation(FM)


			       1 bit cell
				³<----->³
		ÚÄÄÄÄÄÄÄ¿       ÚÄÄÄÄÄÄÄ¿		        ÚÄÄÄÄÄÄÄ¿
		³   1   ³   0   ³   1   ³    0       0       0  ³   1   ³  0
  NRZ Data    ÄÄÙ       ÀÄÄÄÄÄÄÄÙ       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ       ÀÄÄÄÄ


		 c   d	 c	 c   d	 c	 c	 c	 c   d	 c
		ÚÄ¿ ÚÄ¿	ÚÄ¿     ÚÄ¿ ÚÄ¿ ÚÄ¿     ÚÄ¿     ÚÄ¿     ÚÄ¿ ÚÄ¿ ÚÄ¿ 
		³ ³ ³ ³	³ ³     ³ ³ ³ ³ ³ ³     ³ ³     ³ ³     ³ ³ ³ ³ ³ ³
  FM Data     ÄÄÙ ÀÄÙ ÀÄÙ ÀÄÄÄÄÄÙ ÀÄÙ ÀÄÙ ÀÄÄÄÄÄÙ ÀÄÄÄÄÄÙ ÀÄÄÄÄÄÙ ÀÄÙ ÀÄÙ ÀÄ



		ÚÄÄÄ¿   ÚÄÄÄÄÄÄÄ¿   ÚÄÄÄ¿       ÚÄÄÄÄÄÄÄ¿       ÚÄÄÄ¿   ÚÄÄÄ
  Disk Flux   	³   ³   ³       ³   ³   ³       ³       ³       ³   ³   ³
  Transitions ÄÄÙ   ÀÄÄÄÙ       ÀÄÄÄÙ   ÀÄÄÄÄÄÄÄÙ       ÀÄÄÄÄÄÄÄÙ   ÀÄÄÄÙ  
  


	FM Encoding Rules :

	1.	Insert clock pulse for each bit cell
	2.	Insert data pulse when NRZ data is "1"



B.	Modified Frequency Modulation(MFM)


			       1 bit cell
				³<----->³
		ÚÄÄÄÄÄÄÄ¿       ÚÄÄÄÄÄÄÄ¿		        ÚÄÄÄÄÄÄÄ¿
		³   1   ³   0   ³   1   ³    0       0       0  ³   1   ³  0
  NRZ Data    ÄÄÙ       ÀÄÄÄÄÄÄÄÙ       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ       ÀÄÄÄÄ

						ÚÄ¿	ÚÄ¿
						³ ³	³ ³
  Clock	      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

		    ÚÄ¿		    ÚÄ¿				    ÚÄ¿
		    ³ ³		    ³ ³				    ³ ³
  Data	      ÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄ

		     d	  	     d	  	 c	 c	     d	  
		    ÚÄ¿	            ÚÄ¿         ÚÄ¿     ÚÄ¿         ÚÄ¿     
		    ³ ³	            ³ ³         ³ ³     ³ ³         ³ ³    
  MFM Data    ÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄ


		    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿           ÚÄÄÄÄÄÄÄ¿           ÚÄÄÄÄÄ
  Disk Flux  	    ³               ³           ³       ³           ³           
  Transitions ÄÄÄÄÄÄÙ               ÀÄÄÄÄÄÄÄÄÄÄÄÙ       ÀÄÄÄÄÄÄÄÄÄÄÄÙ      
  


	MFM Encoding Rules :

	1.	Insert clock in pulse at the beginning of a bit cell only
		if NRZ data = 0 for two consecutive bits
	2.	If data bit = 1, insert data pulse in the middle of the bit
		cell.
	3.	If data bit = 0, no insertion of data pulses in the bit cell


C.	Run Length Limited(RLL)


	RLL 2,7 Encoding Rules :

	According to following table to encoding/decoding :

	ÚÄÄÄÄÄÄÄÄÄÂÄÄÄÄÂÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄ¿
	³ NRZ Data³10  ³11  ³000   ³010   ³011     ³0010    ³0011    ³
	ÃÄÄÄÄÄÄÄÄÄÅÄÄÄÄÅÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
	³ RLL 2,7 ³1000³0100³100100³001000³000100  ³00001000³00100100³
	ÀÄÄÄÄÄÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÙ


D.	Group Code Recording(GCR)

	4,5 GCR Encoding Rules :

	According to following table to encoding/decoding :

	ÚÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄ¿
	³ NRZ Data³0000 ³000 1³0010 ³0011 ³0100 ³0101 ³0110 ³0111 ³
	ÃÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
	³ 4,5 GCR ³11001³11011³10010³10011³11101³10101³10110³10111³
	ÀÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÙ

	ÚÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄ¿
	³ NRZ Data³1000 ³1001 ³1010 ³1011 ³1100 ³1101 ³1110 ³1111 ³
	ÃÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
	³ 4,5 GCR ³11010³01001³01010³01011³11110³01101³01110³01111³
	ÀÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÙ



E.	Zone Bit Recording(ZBR)

	
	    According to track no, the fixed disk drive is divided into serval
	zones. The tracks in the same zone have the same format, but the tracks
	in different zone may have different format.
		

1.4	Data Format


	 ÚÄ¿ 			        		              ÚÄ¿
	 ³ ³                                                          ³ ³
  Index	ÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄ


    	 ÚÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄ¿
	 ³Index delay³Sector³Sector³    . . . .     ³Sector³Sector³Final³
	 ³  Field    ³  0   ³  1   ³    . . . .     ³  N-1 ³  N   ³ Gap	³
	 ÀÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÙ

		     ³	    ³
	 ÚÄÄÄÄÄÄÄÄÄÄÄÙ	    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
    	 ÚÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÂÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ¿
	 ³Preamble 1 ³Address³ I.D.   ³EDC³Postamble 1³Sector³Inter sector³
	 ³(Synch 1)  ³ Mark  ³(Header)³ECC³           ³Data  ³     Gap    ³
	 ÀÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÁÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÙ

		             ³	      ³		      ³	     ³
	 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ	      ÀÄÄÄÄÄ¿	      ³	     ³
    	 ÚÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄ¿	      ³	     ³
	 ³ID AM³Track³Track³Head³Sector³ ID ³	      ³	     ³
	 ³     ³(MSD)³(LSD)³ #  ³  #   ³Flag³	      ³	     ³
	 ÀÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÙ	      ³	     ³
						      ³	     ³
		                                      ³	     ³
	                  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ	     ÀÄÄÄÄÄÄÄÄÄÄÄÄ¿
    	                  ÚÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄ¿
	                  ³Preamble 2 ³Address³Data³ Data ³EDC³Postamble 2³
	                  ³(Synch 2)  ³ Mark  ³Mark³Record³ECC³           ³
	                  ÀÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÙ


1.5	Sector Interleaving

	    The initial formatting of a disk determines where sectors are
	located within a track. It is not necessary to allocate sectors
	sequentially around the track. The Technique known as sector inter-
	leaving optimizes access times when, although sectors are accessed
	sequentially, a small amount of processing must be performed between
	sector read/write.


	interleave factor = 3
















	interleave factor = 2















1.6	Disk Formatting


	A.	Physical Format(initialization)

		Initializes the fixed disk with sectors and address so that
		data can be access

	B.	Partitioning

		Assign a partical amount of disk space to DOS

	C.	Logical Format

		Verify that the initialization of fixed disk drive was 
		successfully completed


1.7	Translative Versus Non-Translative Mode


	   Owing to using advanced technique, the new WDD contain more
	cylinders, more heads, and more sectors in a track. But due to
	DOS limitation, some DOS  software can't access the extra disk
	space. So some WDD manufacturer  support "Translative mode" to
	translate the extra disk space into DOS disk space.

	Example 1 :

	   Assume WDD have 1033 cylinders, 2 heads, 33  sectors/track in 
	non-translative mode, but it can have 1002 cylinders, 4 heads, and
	17 sectors/track in translative mode.

	  1033 * 2 * 33 = 68178 sectors/drive in non-translative mode
	  1002 * 4 * 17 = 68136 sectors/drive in translative mode

	   So it will loss 42 sectors in translative mode.


		2.	Winchester Disk Controller


2.1	System Configuration for Fixed Disk System


		  ÚÄÄÄÄÄÄÄÄ¿      		                    
     ÚÄÄÄÄÄÄÄÄÄÄÄÄ´        ³<ÄÄÄÄÄÄÄÄÄÄÄ¿      		                    
     ³	          ³ 8259A  ³		³
     ³	     ÚÄÄÄ>³        ³       	³	                     
     ³	     ³	  ÀÄÄÄÄÄÄÄÄÙ        	³                 ÚÄÄÄÄÄÄÄÄ¿
     ³ ÚÄÄÄÄÄÁÄÄ¿                   ÚÄÄÄÁÄÄÄÄ¿      Ú---->³ WDD 0  ³
     ³ ³  CPU   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ>³        ³<ÄÄÄÄÄ|ÄÄÂÄ>³        ³
     ³ ³ INT 13H³<----Â-------------³  WDC   ³      |  ³  ÀÄÄÄÄÄÄÄÄÙ
     ³ ³ -------³     |             ³        ³<-----|  ³  ÚÄÄÄÄÄÄÄÄ¿
     À>³ INT 0EH³     |             ÀÄÄÄÄÄÄÄÄÙ	    |  ÀÄ>³ WDD 1  ³
       ÀÄÄÄÄÄÄÄÄÙ     |   	        ^           À---->³        ³
	              |   	        |                 ÀÄÄÄÄÄÄÄÄÙ
		      |	                |  	                    
		  ÚÄÄÄÁÄÄÄÄ¿	        | 	                    
                  ³ DRAM   ³<-----------Ù    	                    
                  ÀÄÄÄÄÄÄÄÄÙ   			                      


	 Command/Control  ÄÄÄÄÄÄÄÄ

	 Data/Status      --------


  Fig :    System Configuration for Fixed Disk System


	3.	Programming Sequence in Fixed Disk Service Program

;+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
;Module_Name: read_sector_hd
;Calling Sequence:
;
;        Input :   AH = 02h
;                  AH(in stack) = no_error
;                  DL = drive no.(not value check)
;                  DH = head no.
;                  CH = cylinder low
;                  CL =  bit 7-6  -- cylinder high
;                        bit 5-0  -- sector no.(1 base)
;                  AL = no. of sectors to be read
;        output :  AH(in stack) = status of operation
;
;PDL:    IF WDC valid THEN
;           prepare task file
;           IF WDC ready THEN
;              write READ command to WDC
;           ENDIF
;           IF interrupt occurred THEN
;              read one sector from data register
;              get result back
;           ELSE
;        ELSE
;           return error code = 01H(invalid function call)
;        ENDIF
;+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
page

f02_00:  ; check valid_WDC

         call      valid_wdc            ; check valid_wdc
         jc        f02_60               ; goto f02_40 if error occurred

;        send read command block to WDC

         call      write_data           ; Send command
         mov       ah, 021h             ; BX = 021h for read command
         call      out_com              ; out command byte to WDC
         jc        f02_60               ; goto f02_60 if WDC not ready
         mov       di, [bp-4]           ; DI = offset of transfer address
         call      wait_drq             ;
         jc        f02_60               ;

f02_20:  ; wait DRQ and test 64K boundary

         cmp       di, 0fe00h           ; if in 64K boundary
         jb        f02_30               ; goto f02_30 if no boundary error
         mov       ax, es               ;
         add       ax, 20h              ;
         mov       es, ax               ; adjust ES
         sub       di, 200h             ; adjust DI
f02_30:
         call      wait_int             ; wait_interrupt
         jc        f02_60               ; goto f02_60 if time out
         mov       dx, hd_port0         ; data register
         mov       cx, 100h             ; count = 256 words
	 cld				;
	 cli				;
	 rep	   insw			;
	 sti				;

;        get result back

         call      get_result           ; get result byte into AL
         jc        f02_60               ;
         dec       byte ptr [bp-2]      ;
         jnz       f02_20		;
f02_60:
         jmp       disk_end


	4.	Q & A