INT 11H -  EQUIPMENT_I
        EQUIPMENT DETERMINATION
        This routine attempts to determine what optional devices are attached
        to the system.
INPUT -
        No registers
        The @EQUIPMENT variable is set during the power on diagnostics using
        the following hardware assumptions :
        Port 03FA = Interrupt ID Register of 8250 (Primary)
             02FA = Interrupt ID Register of 8250 (Secondary)
                Bits 7-3 are always 0
        Port 0378 = Output Port of Printer (Primary)
             0278 = Output Port of Printer (Secondary)
             03BC = Output Port of Printer (Monochrome-Printer)
OUTPUT -
        (AX) is set, Bit Significant, to indicate attached I/O
        Bit 15,14 = Number of Printer Attached
        Bit 13 = Internal Modem Installed
        Bit 12 = Not Used
        Bit 11,10,9 = Number of RS232 cards Attached
        Bit 8 = Not Used
        Bit 7,6 = Number of Diskette Drives
            00 = 1, 01 = 2 Only if Bit 0 = 1
        Bit 5,4 = Initial Video Mode
            0 0 - Unused
            0 1 - 40x25 BW using Color Card
            1 0 - 80x25 BW using Color Card
            1 1 - 80x25 BW using BW Card
        Bit 3 = Not used
        Bit 2 = Not used
        Bit 1 = Math Coprocessor
        Bit 0 = 1 (IPL Diskette Installed)
        No other register affected

PDL:
        Read btye of @EQUIP_FLAG (40:10) to AX register
        return