The Hitchhiker's Guide to X386/XFree86 Video Timing
  (or, Tweaking your Monitor for Fun and Profit)
  Eric S. Raymond esr@snark.thyrsus.com 1
  This is version 1.0, Jan 8th 1993.

  1.  Introduction


  Please direct comments, criticism, and suggestions for improvement to
  esr@snark.thyrsus.com.

  The XFree86 server allows users to configure their video subsystem and
  thus encourages best use of existing hardware.  This tutorial is
  intended to help you learn how to generate your own timing numbers to
  make optimum use of your video card and monitor.

  We'll present a method for getting something that works, and then show
  you how you can experiment starting from that base to develop settings
  that optimize for your taste.

  If you already have a mode that almost works (in particular, if one of
  predefined VESA modes gives you a stable display but one that's
  displaced right or left, or too small, or too large) you can go
  straight to the section on Fixing Problems.  This will enlighten you
  on ways to tweak the timing numbers to achieve particular effects.

  XFree86 allows you to hot-key between different modes defined in
  XF86Config (see XF86Config.man for details).  Use this capability to
  save yourself hassles!  When you want to test a new mode, give it a
  unique mode label and add it to the end your hot-key list.  Leave a
  known-good mode as the default to fall back on if the test mode
  doesn't work.  The Xconfig section at the end of the second Example
  Calculation provides a good example of how to record your experiments
  in a way that will help you quickly converge on a solution.

  First check out the Monitors file in lib/X11/doc If your monitor is in
  it, you can probably skip the rest of this document!  You may need to
  scale some of the timing numbers if the clock used to generate the
  mode in the database doesn't match what your card has available, but
  that's easy.


  2.  How Video Displays Work


  Knowing how the display works is essential to understanding what
  numbers to put in the various fields in the file Xconfig.  Those
  values are used in the lowest levels of controlling the display by the
  XFree86 server.

  The display generates a picture from a series of dots.  The dots are
  arranged from left to right to form lines.  The lines are arranged
  from top to bottom to form the picture.  The dots emit light when they
  are struck by the electron beam inside the display.  To make the beam
  strike each dot for an equal amount of time, the beam is swept across
  the display in a constant pattern.



    1. (from an original by Chin Fang


  fangchin@leland.stanford.edu; portions derive from a how-


  to by Bob Crosson crosson@cam.nist.gov,
  The pattern starts at the top left of the screen, goes across the
  screen to the right in a straight line, and stops temporarily on the
  right side of the screen.  Then the beam is swept back to the left
  side of the display, but down one line.  The new line is swept from
  left to right just as the first line was.  This pattern is repeated
  until the bottom line on the display has been swept.  Then the beam is
  moved from the bottom right corner of the display to the top left
  corner, and the pattern is started over again.

  Starting the beam at the top left of the display is called the
  beginning of a frame.  The frame ends when the beam reaches the the
  top left corner again as it comes from the bottom right corner of the
  display.  A frame is made up of all of the lines the beam traced from
  the top of the display to the bottom.

  If the electron beam were on all of the time it was sweeping through
  the frame, all of the dots on the display would be illuminated.  There
  would be no black border around the edges of the display.  At the
  edges of the display the picture would become distorted because the
  beam is hard to control there.  To reduce the distortion, the dots
  around the edges of the display are not illuminated by the beam even
  though the beam may be pointing at them.  The viewable area of the
  display is reduced this way.

  Another important thing to understand is what becomes of the beam when
  no spot is being painted on the visible area.  The time the beam would
  have been illuminating the side borders of the display is used for
  sweeping the beam back from the right edge to the left and moving the
  beam down to the next line.  The time the beam would have been
  illuminating the top and bottom borders of the display is used for
  moving the beam from the bottom-right corner of the display to the
  top-left corner.

  The adapter card generates the signals which cause the display to turn
  on the electron beam at each dot to generate a picture.  The card also
  controls when the display moves the beam from the right side to the
  left and down a line by generating a signal called the horizontal sync
  (for synchronization) pulse.  One horizontal sync pulse occurs at the
  end of every line.  The adapter also generates a vertical sync pulse
  which signals the display to move the beam to the top-left corner of
  the display.  A vertical sync pulse is generated near the end of every
  frame.

  The display requires that there be short time periods both before and
  after the horizontal and vertical sync pulses so that the position of
  the electron beam can stabilize.  If the beam can't stabilize, the
  picture will not be steady.

  In a later section, we'll come back to these basics with definitions,
  formulas and examples to help you use them.


  3.  Basic Things to Know about your Display and Adapter


  There are some fundamental things you need to know before hacking an
  Xconfig entry.  These are:

     1. your monitor's horizontal and vertical sync frequency options

     2. your video adapter's driving clock frequency, or "dot clock"

     3. your monitor's bandwidth

  The monitor sync frequencies:

  The horizontal sync frequency are just the number of times per second
  the monitor can write a horizontal scan line; it is the single most
  important statistic about your monitor.  The vertical sync frequency
  is the number of times per second the monitor can traverse its beam
  vertically.

  Sync frequencies are usually listed on the specifications page of your
  monitor manual.  The vertical sync frequency number is typically
  calibrated in Hz (cycles per second), the horizontal one in KHz
  (kilocycles per second).  The usual ranges are between 50 and 80Hz
  vertical, and between 31 and 135KHz horizontal.

  If you have a multisync monitor, these frequencies will be given as
  ranges.  Some monitors, especially lower-end ones, have multiple fixed
  frequencies.  These can be configured too, but your options will be
  severely limited by the built-in monitor characteristics.  Choose the
  highest frequency pair for best resolution.  And be careful --- trying
  to clock a fixed-frequency monitor at a higher speed than it's
  designed for can damage it.

  The card driving clock frequency:

  Your video adapter manual's spec page will usually give you the card's
  dot clock (that is, the total number of pixels per second it can write
  to the screen).  If you don't have this information, the X server will
  get it for you.  Even if your X locks up your monitor, it will emit a
  line of clock and other info to standard output.  If you redirect this
  to a file, it should be saved even if you have to reboot to get your
  console back.

  If you're using SGCS X, the line will look something like the
  following example, collected from a Swan local-bus S3 adapter.
  XFree86 uses a slightly different multi-line format.


       WGA: 86C911 (mem: 1024k clocks: 25 28 40 3 50 77 36 45 0 0 79 31 94 65 75 71)
       ---  ------       -----         --------------------------------------------
        |     |            |                 Possible driving frequencies in MHz
        |     |            +-- Size of on-board frame-buffer RAM
        |     +-- Chip type
        +-- Server type



  Note: do this with your machine unloaded (if at all possible).
  Because X is an application, its timing loops can collide with disk
  activity, rendering the numbers above inaccurate.  Do it several times
  and watch for the numbers to stabilize; if they don't, start killing
  processes until they do.  SVr4 users: the mousemgr process is
  particularly likely to mess you up.

  In order to avoid the clock-probe inaccuracy, you should clip out the
  clock timings and put them in your Xconfig as the value of the Clocks
  property --- this suppresses the timing loop and gives X an exact list
  of the clock values it can try.  Using the data from the example
  above:


       wga
               Clocks  25 28 40 3 50 77 36 45 0 0 79 31 94 65 75 71



  On systems with a highly variable load, this may help you avoid
  mysterious X startup failures.  It's possible for X to come up, get
  its timings wrong due to system load, and then not be able to find a
  matching dot clock in its config database --- or find the wrong one!

  The monitor's video bandwidth:

  Finally, it's useful to know your monitor's video bandwidth, so you
  know approximately what the highest dot clock you can use is.  There's
  a lot of give here, though --- some monitors can run as much as 30%
  over their nominal bandwidth.

  Knowing the bandwidth will enable you to make more intelligent choices
  between possible configurations.  It may affect your display's visual
  quality (esp.  sharpness for fine details).

  Your monitor's video bandwidth should be included on the manual's spec
  page.  If it's not, look at the monitor's highest rated resolution.
  As a rule of thumb, here's how to translate these into bandwidth
  estimates (and thus into rough upper bounds for the dot clock you can
  use):


               640x480                 25
               800x600                 36
               1024x768                65
               1024x768 interlaced     45
               1280x1024               110



  BTW, there's nothing magic about this table; these numbers are just
  the lowest dot clocks per resolution in the standard XFree86 Modes
  database.  The bandwidth of your monitor may be higher than the
  minimum needed for its top resolution, so don't be afraid to try a dot
  clock a few MHz higher.

  Also note that bandwidth is seldom an issue for dot clocks under 65MHz
  or so.  With an SVGA and most hi-res monitors, you can't get anywhere
  near the limit of your monitor's video bandwidth.  The following are
  examples:


               Brand                           Video Bandwidth
               ----------                      ---------------
               NEC 4D                          75Mhz
               Nano 907a                       50Mhz
               Nano 9080i                      60Mhz
               Mitsubishi HL6615               110Mhz
               Mitsubishi Diamond Scan         100Mhz
               IDEK MF-5117                    65Mhz
               IOCOMM Thinksync-17 CM-7126     136Mhz
               HP D1188A                       100Mhz
               Philips SC-17AS                 110Mhz
               Swan SW617                      85Mhz



  Even low-end monitors usually aren't terribly bandwidth-constrained
  for their rated resolutions.  The NEC Multisync II makes a good
  example --- it can't even display 800x600 per its spec.  It can only
  display 800x560.  For such low resolutions you don't need high dot
  clocks or a lot of bandwidth; probably the best you can do is 32Mhz or
  36Mhz, both of them are still not too far from the monitor's rated
  video bandwidth of 30Mhz.

  At these two driving frequencies, your screen image may not be as
  sharp as it should be, but definitely of tolerable quality. Of course
  it would be nicer if NEC Multisync II had a video bandwidth higher
  than, say, 36Mhz.  But this is not critical for common tasks like text
  editing, as long as the difference is not so significant as to cause
  severe image distortion (your eyes would tell you right away if this
  were so).

  What these control:

  The sync frequency ranges of your monitor, together with your video
  adapter's dot clock, determine the ultimate resolution that you can
  use.  But it's up to the driver to tap the potential of your hardware.
  A superior hardware combination without an equally competent device
  driver is a waste of money.  On the other hand, with a versatile
  device driver but less capable hardware, you can push the hardware's
  envelope a little.  This is the design philosophy of XFree86.


  4.  Interpreting the Basic Specifications


  This section explains what the specifications above mean, and some
  other things you'll need to know.  First, some definitions.  Next to
  each in parens is the variable name we'll use for it when doing
  calculations


     horizontal sync frequency (HSF)
        Horizontal scans per second (see above).


     vertical sync frequency (VSF)
        Vertical scans per second (see above).  Mainly important as the
        upper limit on your refresh rate.


     dot clock  (DCF)
        More formally, `driving clock frequency'; sometimes loosely
        called `bandwidth'.  The frequency of the crystal or VCO on your
        adaptor --- the maximum dots-per-second it can emit.


     video bandwidth (VB)
        The highest frequency at which your monitor's video signal can
        change.  This constrains the highest dot clock you can use and
        the overall sharpness of fine details in the video image.


     frame length (HFL, VFL)
        Horizontal frame length (HFL) is the number of dot-clock ticks
        needed for your monitor's electron gun to scan one horizontal
        line, *including the inactive left and right borders*.  Vertical
        frame length (VFL) is the number of scan lines in the *entire*
        image, including the inactive top and bottom borders.


     screen refresh rate (RR)
        The number of times per second your screen is repainted.  Higher
        frequencies are better, as they reduce flicker.  60Hz is good,
        VESA-standard 72Hz is better.  Compute it as

         RR = DCF / (HFL * VFL)

        Note that the product in the denominator is *not* the same as
        the monitor's visible resolution, but typically somewhat larger.
        We'll get to the details of this below.

  About Bandwidth:
  Monitor makers like to advertise high bandwidth because it constrains
  the sharpness of intensity and color changes on the screen.  A high
  bandwidth means smaller visible details.

  Your monitor uses electronic signals to present an image to your eyes.
  Such signals always come in in wave form once they are converted into
  analog form from digitized form.  They can be considered as
  combinations of many simpler wave forms each one of which has a fixed
  frequency, many of them are in the Mhz range, eg, 20Mhz, 40Mhz, or
  even 70Mhz.  Your monitor video bandwidth is, effectively, the
  highest-frequency analog signal it can handle without distortion.

  For our purposes, bandwidth is mainly important as an approximate
  cutoff point for the highest dot clock you can use.

  Sync Frequencies snd the Refresh Rate:

  Each horizontal scan line on the display is just the visible portion
  of a frame-length scan.  At any instant there is actually only one dot
  active on the screen, but with a fast enough refresh rate your eye's
  persistence of vision enables you to "see" the whole image.

  Here are some pictures to help:


        _______________________
        |                       |     The horizontal frame length
        |->->->->->->->->->->-> |     is the time in dot clocks
        |                      )|     required for the
        |<-----<-----<-----<--- |     electron beam to trace
        |                       |     a pattern like this
        |                       |
        |                       |
        |                       |
        |_______________________|

        _______________________
        |        ^              |     The vertical frame length
        |       ^ |             |     is the time in dot clocks
        |       | v             |     required for the
        |       ^ |             |     electron beam to trace
        |       | |             |     a pattern like this
        |       ^ |             |
        |       | v             |
        |       ^ |             |
        |_______|_v_____________|



  Remember that the actual raster scan is a very tight zigzag pattern;
  that is, the beam moves left <-> right and at the same time up <->
  down.

  Now we can see how the dot clock and frame size relates to refresh
  rate.  By definition, one hertz (hz) is one cycle per second.  So, if
  your horizontal frame length is HFL and your vertical frame length is
  VFL, then to cover the entire screen takes (HFL * VFL) ticks.  Since
  your card emits DCF ticks per second by definition, then obviously
  your monitor's electron gun(s) can sweep the screen from left to right
  and back and from bottom to top and back DCF / (HFL * VFL) times/sec.
  This is your screen's refresh rate, because it's how many times your
  screen can be updated thus REFRESHED per second!

  You need to understand this concept to design a configuration which
  trades off resolution against flicker in whatever way suits your
  needs.
  5.  Tradeoffs in Configuring your System


  Another way to look at the formula we derived above is

  DCF = RR * HFL * VFL

  That is, your dot clock is fixed.  You can use those dots per second
  to buy either refresh rate, horizontal resolution, or vertical
  resolution.  If one of those increases, one or both of the others must
  decrease.

  Note, though, that your refresh rate cannot be greater than the
  maximum vertical sync frequency of your monitor.  Thus, for any given
  monitor at a given dot clock, there is a minimum product of frame
  lengths below which you can't force it.

  In choosing your settings, remember: if you set RR too low, you will
  get mugged by screen flicker.

  You probably do not want to pull your refresh rate below 60Hz.  This
  is the flicker rate of fluorescent lights; if you're sensitive to
  those, you need to hang with 72MHz, the VESA ergonomic standard.

  Flicker is very eye-fatiguing, though human eyes are adaptable and
  peoples' tolerance for it varies widely.  If you face your monitor at
  a 90% viewing angle, are using a dark background and a good
  contrasting color for foreground, and stick with low to medium
  intensity, you *may* be comfortable at as little as 45Hz.

  The acid test is this: open a xterm with pure white back-ground and
  black foreground using xterm -bg white -fg black and make it so large
  as to cover the entire viewable area.  Now turn your monitor's
  intensity to 3/4 of its maximum setting, and turn your face away from
  the monitor.  Try peeking at your monitor sideways (bringing the more
  sensitive peripheral-vision cells into play).  If you don't sense any
  flicker or if you feel the flickering is tolerable, then that refresh
  rate is fine with you.  Otherwise you better configure a higher
  refresh rate, because that semi-invisible flicker is going to fatigue
  your eyes like crazy and give you headaches, even if the screen looks
  OK to normal vision.

  So let's say you've picked a minimum acceptable refresh rate.  In
  choosing your HFL and VFL, you'll have some room for maneuver.


  6.  Memory Requirements


  Available frame-buffer RAM may limit the resolution you can achieve on
  color or gray-scale displays.  It probably isn't a factor on displays
  that have only two colors, white and black with no shades of gray in
  between.

  For 256-color displays, a byte of video memory is required for each
  visible dot to be shown.  This byte contains the information that
  determines what mix of red, green, and blue is generated for its dot.
  To get the amount of memory required, multiply the number of visible
  dots per line by the number of visible lines.  For a display with a
  resolution of 800x600, this would be 800 x 600 = 480,000, which is the
  number of visible dots on the display.  This is also, at one byte per
  dot, the number of bytes of video memory that are necessary on your
  adapter card.

  Thus, your memory requirement will typically be (HR * VR)/1024 Kbytes
  of VRAM, rounded up.  In the example case, we'd need (936 * 702)/1024
  = 642K.  So if you have one meg, you'll have extra for virtual-screen
  panning.

  However, if you only have 512K on board, then you can't use this
  resolution.  Even if you have a good monitor, without enough video
  ram, you can't take advantage of your monitor's potential.  On the
  other hand, if your SVGA has one meg, but your monitor can display at
  most 800x600, then high resolution is beyond your reach anyway.

  Don't worry if you have more memory than required; XFree86 will make
  use of it by allowing you to scroll your viewable area (see the
  Xconfig file documentation on the virtual screen size parameter).
  Remember also that a card with 512K bytes of memory really doesn't
  have 512,000 bytes installed, it has 512 x 1024 = 524,288 bytes.

  If you're running SGCS X using an S3 card, and are willing to live
  with 16 colors (4 bits per pixel), you can set depth 4 in Xconfig and
  effectively double the resolution your card can handle.  S3 cards, for
  example, normally do 1024x768x256.  You can make them do 1280x1024x16
  with depth 4.


  7.  Computing Frame Sizes


  Warning: this method was developed for multisync monitors.  It will
  probably work with fixed-frequency monitors as well, but no
  guarantees!

  Start by dividing DCF by your highest available HSF to get the number
  of horizontal sweeps per second available.

  For example; suppose you have a Sigma Legend SVGA with a 65MHz dot
  clock, and your monitor has a 55KHz horizontal scan frequency.  The
  quantity (DCF / HSF) is then 1181.

  Now for our first bit of black magic.  You need to round this figure
  to the nearest multiple of 8.  This has to do with the VGA hardware
  controller used by SVGA and S3 cards; it uses an 8-bit register, left-
  shifted 3 bits, for what's really an 11-bit quantity.  Other card
  types such as ATI 8514/A may not have this requirement, but we don't
  know and the correction can't hurt.  So round the usable horizontal
  scans per second figure to 1176.

  This figure (DCF / HSF rounded to a multiple of 8) is the minimum HFL
  you can use.  You can get longer HFLs (and thus, possibly, more
  horizontal dots on the screen) by setting the sync pulse to produce a
  lower HSF.  But you'll pay with a slower and more visible flicker
  rate.

  As a rule of thumb, 80% of the horizontal frame length is available
  for horizontal resolution, the visible part of the horizontal scan
  line (this allows, roughly, for borders and sweepback time -- that is,
  the time required for the beam to move from the right screen edge to
  the left edge of the next raster line).  In this example, that's 944
  ticks.

  Now, to get the normal 4:3 screen aspect ratio, set your vertical
  resolution to 3/4ths of the horizontal resolution you just calculated.
  For this example, that's 708 ticks.  To get your actual VFL, multiply
  that by 1.05 to get 743 ticks.

  About that 4:3 --- a ratio of 4:3 for width to height of the displayed
  area approximates the Golden Section, (1 + sqrt(5))/2.  Human beings
  seem to be wired to find this kind of rectangle pleasant to look at;
  accordingly, video tubes and the standard resolutions such as 800x600,
  640x480 and 1024x768 all approximate it.  Though it's psychologically
  magic, it's not technically magic; nothing prevents you from using a
  non-Golden-Section ratio if that will get the best use out of your
  screen real estate.

  So, HFL=1176 and VFL=743.  Dividing 65MHz by the product of the two
  gives us a nice, healthy 74.4Hz refresh rate.  Excellent!  Better than
  VESA standard!  And you got 944x708 to boot, more than the 800 by 600
  you were probably expecting.  Not bad at all!

  You can even improve the refresh rate further, to almost 76 Hz, by
  using the fact that monitors can often sync horizontally at 2khz or so
  higher than rated, and by lowering VFL somewhat (that is, taking less
  than 75% of 944 in the example above).  But before you try this
  "overdriving" maneuver, if you do, make *sure* that your monitor
  electron guns can sync up to 76 Hz vertical.  (the popular NEC 4D, for
  instance, cannot.  It goes only up to 75 Hz VSF).

  So far, most of this is simple arithmetic and basic facts about raster
  displays.  Hardly any black magic at all!


  8.  Black Magic and Sync Pulses

  OK, now you've computed HFL/VFL numbers for your chosen dot clock,
  found the refresh rate acceptable, and checked that you have enough
  VRAM.  Now for the real black magic -- you need to know when and where
  to place synchronization pulses.

  The sync pulses actually control the horizontal and vertical scan
  frequencies of the monitor.  The HSF and VSF you've pulled off the
  spec sheet are nominal, approximate maximum sync frequencies.  The
  sync pulse in the signal from the adapter card tells the monitor how
  fast to actually run.

  Recall the two pictures above?  Only part of the time required for
  raster-scanning a frame is used for displaying viewable image (ie.
  your resolution).

  Horizontal Sync:

  By previous definition, it takes HFL ticks to trace the a horizontal
  scan line.  Let's call the visible tick count (your horizontal screen
  resolution) HR.  Then Obviously, HR < HFL by definition.  For
  concreteness, let's assume both start at the same instant as shown
  below:



        |___ __ __ __ __ __ __ __ __ __ __ __ __
        |_ _ _ _ _ _ _ _ _ _ _ _                |
        |_______________________|_______________|_____
        0                       ^               ^     unit: ticks
                                |   ^       ^   |
                                HR  |       |  HFL
                                |   |<----->|   |
                                |<->|  HSP  |<->|
                                HGT1         HGT2



  Now, we would like to place a sync pulse of length HSP as shown above,
  ie, between the end of clock ticks for display data and the end of
  clock ticks for the entire frame.  Why so?  because if we can achieve
  this, then your screen image won't shift to the right or to the left.
  It will be where it supposed to be on the screen, covering squarely
  the monitor's viewable area.

  Furthermore, we want about 30 ticks of "guard time" on either side of
  the sync pulse.  This is represented by HGT1 and HGT2.  In a typical
  configuration HGT1 != HGT2, but if you're building a configuration
  from scratch, you want to start your experimentation with them equal
  (that is, with the sync pulse centered).

  The symptom of a misplaced sync pulse is that the image is displaced
  on the screen, with one border excessively wide and the other side of
  the image wrapped around the screen edge, producing a white edge line
  and a band of "ghost image" on that side.  A way-out-of-place vertical
  sync pulse can actually cause the image to roll like a TV with a mis-
  adjusted vertical hold (in fact, it's the same phenomenon at work).

  If you're lucky, your monitor's sync pulse widths will be documented
  on its specification page.  If not, here's where the real black magic
  starts...

  You'll have to do a little trial and error for this part.  But most of
  the time, we can safely assume that a sync pulse is about 3.5 to 4.0
  microsecond in length.

  For concreteness again, let's take HSP to be 3.8 microseconds (which
  btw, is not a bad value to start with when experimenting).

  Now, using the 65Mhz clock timing above, we know HSP is equivalent to
  247 clock ticks (= 65x10**6 * 3.8 *10**(-6)) recall M=10**6,
  micro=10**(-6)

  Vertical Sync:

  Going back to the picture above, how do we place the 247 clock ticks
  as shown in the picture?

  Using our example, HR is 944 and HFL is 1176.  The difference between
  the two is 1176-944=232 < 247!  Obviously we have to do some
  adjustment here.  What can we do?

  The first thing is to raise 1176 to 1184, and lower 944 to 936.  Now
  the difference = 1184-936= 248. Hmm, closer.

  Next, instead using 3.8, we use 3.5 for calculating HSP; then, we have
  65*3.5=227.  Looks better.  But 248 is not much higher than 227.  It's
  normally necessary to have 30 or so clock ticks between HR and the
  start of SP, and the same for the end of SP and HFL.  AND they have to
  be multiple of eight!  Are we stuck?

  No!  let's do this, 936% 8==0, (936+32)% 8==0 too.  But 936+32=968,
  968+227=1195, 1195+32=1227.  Hmm.. this looks not too bad.  But it's
  not a multiple of 8, so lets round it up to 1232.

  But now we have potential trouble, the sync pulse is no longer placed
  right in the middle between h and H any more.  Happily, using our
  calculator we find 1232-32=1200 is also a multiple of 8 and
  (1232-32)-968=232 corresponding using a sync pulse of 3.57 micro
  second long, still reasonable.

  In addition, 936/1232 0.76 or 76%, still not far from 80%, so it
  should be all right.

  Furthermore, using the current horizontal frame length, we basically
  ask our monitor to sync at 52.7khz(=65Mhz/1232) which is within its
  capability.  No problems.

  Using rules of thumb we mentioned before, 936*75%=702, This is our new
  vertical resolution.  702*1.05=737, our new vertical frame length.

  Screen refresh rate = 65Mhz/(737*1232)=71.6 Hz.  This is still
  excellent.

  Figuring the vertical sync pulse layout is similar:


        |___ __ __ __ __ __ __ __ __ __ __ __ __
        |_ _ _ _ _ _ _ _ _ _ _ _                |
        |_______________________|_______________|_____
        0                      VR              VFL     unit: ticks
                                ^   ^       ^
                                |   |       |
                                |<->|<----->|
                                 VGT    VSP



  We start the sync pulse just past the end of the vertical display data
  ticks.  VGT is the vertical guard time required for the sync pulse.
  Most monitors are comfortable with a VGT of 0 (no guard time) and
  we'll use that in this example.  A few need two or three ticks of
  guard time, and it usually doesn't hurt to add that.

  Returning to the example: since by the definition of frame length, a
  vertical tick is the time for tracing a complete HORIZONTAL frame,
  therefore in our example, it is 1232/65Mhz=18.95us.

  Experience shows that a vertical sync pulse should be in the range of
  50us and 300us.  As an example let's use 150us, which translates into
  8 vertical clock ticks (150us/18.95us 8).


  9.  Putting it All Together


  The Xconfig file Table of Video Modes contains lines of numbers, with
  each line being a complete specification for one mode of X-server
  operation.  The fields are grouped into four sections, the name
  section, the clock frequency section, the horizontal section, and the
  vertical section.

  The name section contains one field, the name of the video mode
  specified by the rest of the line.  This name is referred to on the
  "Modes" line of the Graphics Driver Setup section of the Xconfig file.
  The name field may be omitted if the name of a previous line is the
  same as the current line.

  The dot clock section contains only the dot clock (what we've called
  DCF) field of the video mode line.  The number in this field specifies
  what dot clock was used to generate the numbers in the following
  sections.

  The horizontal section consists of four fields which specify how each
  horizontal line on the display is to be generated.  The first field of
  the section contains the number of dots per line which will be
  illuminated to form the picture (what we've called HR).  The second
  field of the section indicates at which dot the horizontal sync pulse
  will begin.  The third field indicates at which dot the horizontal
  sync pulse will end.  The fourth field specifies the total horizontal
  frame length (HFL).

  The vertical section also contains four fields.  The first field
  contains the number of visible lines which will appear on the display
  (VR).  The second field indicates the line number at which the
  vertical sync pulse will begin.  The third field specifies the line
  number at which the vertical sync pulse will end.  The fourth field
  contains the total vertical frame length (VFL).

  Example:

            #Modename    clock  horizontal timing  vertical timing

            "752x564"     40    752 784  944 1088  564 567 569 611
                          44.5  752 792  976 1240  564 567 570 600



  (Note: stock X11R5 doesn't support fractional dot clocks.)

  For Xconfig, all of the numbers just mentioned - the number of
  illuminated dots on the line, the number of dots separating the
  illuminated dots from the beginning of the sync pulse, the number of
  dots representing the duration of the pulse, and the number of dots
  after the end of the sync pulse - are added to produce the number of
  dots per line.  The number of horizontal dots must be evenly divisible
  by eight.

  Example:

  horizontal numbers: 800 864 1024 1088

  The sample line has the number of illuminated dots (800) followed by
  the number of the dot when the sync pulse starts (864), followed by
  the number of the dot when the sync pulse ends (1024), followed by the
  number of the last dot on the horizontal line (1088).

  Note again that all of the horizontal numbers (800, 864, 1024, and
  1088) are divisible by eight!  This is not required of the vertical
  numbers.

  The number of lines from the top of the display to the bottom form the
  frame.  The basic timing signal for a frame is the line.  A number of
  lines will contain the picture.  After the last illuminated line has
  been displayed, a delay of a number of lines will occur before the
  vertical sync pulse is generated.  Then the sync pulse will last for a
  few lines, and finally the last lines in the frame, the delay required
  after the pulse, will be generated.  The numbers that specify this
  mode of operation are entered in a manner similar to the following
  example.

  Example:

  vertical numbers: 600 603 609 630

  This example indicates that there are 600 visible lines on the
  display, that the vertical sync pulse starts with the 603rd line and
  ends with the 609th, and that there are 630 total lines being used.

  Note that the vertical numbers don't have to be divisible by eight!

  Let's return to the example we've been working.  According to the
  above, all we need to do from now on is to write our result into
  Xconfig as follows:


       < name >   DCF     HR  SH1 SH2   HFL   VR  SV1 SV2 VFL



  where SH1 is the start tick of the horizontal sync pulse and SH2 is
  its end tick; similarly, SV1 is the start tick of the vertical sync
  pulse and SV2 is its end tick.


       #name    clock   horizontal timing   vertical timing    flag
       936x702  65      936 968 1200 1232   702 702 710 737



  No special flag necessary; this is a non-interlaced mode.  Now we are
  really done.


  10.  Questions and Answers


  Q. The example you gave is not a standard screen size, can I use it?

  A. Why not?  There is NO reason whatsoever why you have to use
  640x480, 800x600, or even 1024x768.  XFree86 driver lets you config
  your hardware with a lot of freedom.  It usually takes two to three
  minutes to come up the right one.  The important thing to shoot for is
  high refresh rate with reasonable viewing area. not high resolution at
  the price of eye-tearing flicker!

  Q. It this the *only* resolution given the 65Mhz dot clock and 55Khz
  HSF?

  A. Absolutely not!  You are encouraged to follow the general procedure
  and do some trial-and-error to come up with a setting that's really to
  your liking.  Experimenting with this can be lots of fun.  Most
  settings may just give you nasty video hash, but nothing you do can
  actually damage a multi-sync monitor (unless you somehow force your
  card to clock it at way above its bandwidth --- if you stick
  reasonably close to the highest resolution the monitor is documented
  to support this can't happen).  Beware fixed-frequency monitors!  This
  kind of hacking around *can* damage them.

  Q. You just mentioned two standard resolutions. In Xconfig, there are
  many standard resolutions available, can you tell me whether there's
  any point in tinkering with timings?

  A. Absolutely!  Take, for example, the "standard" 640x480 listed in
  the current Xconfig.  It employs 25Mhz driving frequency, frame
  lengths are 800 and 525 => refresh rate   59.5Hz. Not too bad.  But
  28Mhz is a commonly available driving frequency from many SVGA boards.
  If we use it to drive 640x480, following the procedure we discussed
  above, you would get frame lengths like 812 and 505.  Now the refresh
  rate is raised to 68Hz, a quite significant improvement over the
  standard one.

  Q. But how about interlace/non-interlace?

  A. At a fixed dot clock, an interlaced display is going to flicker
  worse than a non-interlaced one, which is why the market has moved
  away from them.  What you buy with the increased flicker is higher
  resolution with a slower dot clock.  If the DCF were fast enough (say
  90MHz or up) even interlacing wouldn't produce flicker -- but at
  present speeds, interlaced monitors are a bad idea for X.

  Q. Can you summarize what we have discussed so far?

  A. In a nutshell:



     1. for any fixed driving frequency, raising max resolution incurs
        the penalty of lowering refresh rate and thus introducing more
        flicker.

     2. if high resolution is desirable and your monitor supports it,
        try to get a SVGA card that provides a matching dot clock or
        DCF. The higher, the better!


  11.  Two More Example Calculations

  Here's another hypothetical:

  An adapter card has a 40 MHz clock rate.  A display has a range of
  horizontal sync rates from 30 KHz to 37 KHz.  The minimum number of
  dots per line is 40,000,000/37,000 = 1,081.081, or approximately 1,081
  dots per line.

  We'll use this number of dots per line in the following calculations.
  So each line on our display must have at least 1081 dots.  We round
  this up to 1088 to make it divisible evenly by eight.  Now let's
  assume that the horizontal sync pulse should be 3.8 microseconds long.
  We need to find out how many dots it takes to make a 3.8 microsecond
  pulse.  We do this by first finding out how many microseconds are in
  one dot.  Since there are 40,000,000 dots per second, 1/40,000,000 is
  the number of seconds per dot.

  1/40,000,000 = .000000025 = .025 microseconds per dot


  Thus the number of dots for a 3.8 microsecond sync pulse is

  3.8 microseconds = D dots x .025 microseconds/dot

  or

  D dots = (3.8 microseconds) / (.025 microseconds/dot) = 152 dots

  So we have 1088 dots per line, 800 of which are the illuminated ones,
  with 152 for the sync pulse.  (Note that 152 is evenly divisible by
  eight.  If it weren't we would round it up until it was evenly
  divisible.)  This leaves us the task of calculating the time before
  and after the sync pulse that is necessary for the display.

  The rule of thumb for this is that we need about 30 ticks of guard
  time.  In this particular case, allocating 32 dots is convenient,
  because all the other quantities are divisible by 8.  This results in
  the timing being 800 dots for the viewable area, 152 dots for the
  pulse, and 1088 - (800 + 152) = 136 dots to divide between the two
  other times.  Half of 136 is 68 dots, so 68 dots are placed between
  the illuminated dots and the sync pulse, and 68 dots are placed after
  the sync pulse.  The horizontal numbers in the Xconfig line then
  become

  800 (800+68) (800+68+152) (800+68+152+68)

  or

  800 868 1020 1088

  Now we want to calculate the vertical numbers.  To begin, we must
  remember that the vertical numbers are not in terms of dots or
  microseconds per dot, but are expressed as numbers of lines!  So we
  have to calculate how much time it takes to display a single line.
  That's easy, because we know each line is 1088 dots and each dot is
  .025 microsecond.  Each line is, therefore,
  (1088 dots/line) x (.025 microseconds/dot) = 27.2 microseconds/line

  Since we chose 800 visible dots per line, let's choose the number of
  lines to be such that the ratio of horizontal to vertical is 4 to 3.
  Thus, 800 is 4 x 200, so the number of visible lines should be 3 x 200
  = 600.  Our target resolution is 800x600.

  We know that a vertical sync pulse should be in the range of 50 to 300
  microseconds.  If we chose 150 microseconds as a typical sync pulse,
  we find how many lines 150 microseconds is by dividing 150 by 27.2
  microseconds per line.

  (150 microseconds/pulse) / (27.2 microseconds/line) = 5.51 lines/pulse

  By rounding up (never down) to 6 lines/pulse we now have the vertical
  sync pulse width.

  To guess at the total number of lines per frame (illuminated lines
  plus nonilluminated lines in the border) we assume (from
  "Videotiming...") that the total number of lines will be 5% more than
  the number of viewable lines.  So the total number of lines is

  (600 lines) x (1.05) = 630 total lines per frame

  So now we must place the pulse in the time between the end of the
  illuminated lines and the end of the frame.  Since we have 630 total
  lines, 600 illuminated lines, and 6 lines for the pulse, we have

  630 - 600 - 6 = 24 lines left

  Some displays don't mind if the pulse begins immediately after the
  illuminated lines, but others might want a line or two between the
  last illuminated line and the beginning of the sync pulse.  Taking the
  latter course just to be safe, we add three lines between the last
  illuminated line and the beginning of the pulse.  The rest of the
  lines are added after the pulse ends.  So the vertical timing numbers
  become

  600 (600+3) (600+3+6) (600+3+6+21)

  or


  600 603 609 630

  Before we do anything else, we must check that the display can handle
  630 lines/frame at 27.2 microseconds/line.  We do this by calculating
  how many frames per second our configuration will generate, and
  comparing it to the display manual's entry for vertical sync rate.
  For 630 lines/frame at 27.2 micro- seconds/line, we have 630 x 27.2 =
  17,136 microseconds/frame.  17,136 microseconds/frame is 0.017136
  seconds/frame, or 1/0.017892 frames/second.

  1 / (0.017136 seconds/frame) = 58.4 frames/second

  If the manual says the vertical sync rate is 58.4 Hz, or 58.4 Hz is in
  the range of the display's vertical sync rate, we are fine.  If the
  display cannot handle this rate, we'll have to change the number of
  lines per frame by adjusting all of the timings proportionally.

  Now we combine the horizontal and vertical timing numbers together
  with the resolution and clock values to produce a test configuration
  for Xconfig.  Our line becomes

  "800x600"  40  800 868 1020 1088  600 603 609 630

  Now we have a configuration of XFree86 to try.  It may not work if any
  of our assumptions were grossly wrong, but in most cases it should at
  least give us a stable display.  Now it takes a little experimentation
  to produce something pleasing.

  An actual calculation

  My adapter card has a 40 MHz crystal on it so I started with a 40 MHz
  clock rate.  My display's maximum horizontal sync rate is 37 KHz, so
  the minimum dots per line are 40,000,000/37,000 = 1081.  My display's
  vertical sync rate is the range from 50 Hz to 90 Hz.

  My display's manual says that the largest horizontal sync pulse is
  3.92 microseconds.  With 0.025 microseconds per dot, the pulse is

  (3.92 microseconds) / (.025 microseconds/dot) = 156.8 dots

  Rounding this up to the nearest number evenly divisible by eight gives
  160 dots.

  The manual also says that the time between the last illuminated dot
  and the beginning of the sync pulse must be at least 0.67
  microseconds.  The number of dots in 0.67 microseconds at a 40 MHz
  clock rate - remember 40 MHz is .025 microseconds/dot - is

  D dots = (0.67 microseconds) / (.025 microseconds/dot) = 26.8 dots

  Since 26.8 is not evenly divisible by eight, round it up to 32 dots.

  My display's manual says the time after the sync pulse should be 3.56
  microseconds or more.  In dots, 3.56 microseconds is

  D dots = (3.56 microseconds) / (.025 microseconds/dot) = 142.4 dots

  Round 142.4 up to 144, so that it's evenly divisible by eight.

  So now for a horizontal line we have 800 illuminated dots, 32 dots
  between the illuminated dots and the sync pulse, 152 dots for the sync
  pulse, and 144 dots after the sync pulse.

  800 + 32 + 160 + 144 = 1136

  We now have a line that is 1136 dots long.  This is greater than the
  1088 we previously calculated, but remember that 1088 was the MINIMUM
  number of dots that could be on a line.  So 1136 dots per line is okay
  for starters.

  The numbers to enter on the Xconfig line so far are

  "800x?"  40  800 (800+32) (800+32+160) (800+32+160+144)...

  or

  "800x?"  40  800 832 992 1136...


  A line of 1136 dots at .025 microsecond/dot means that a line
  represents 1136 x .025 = 28.4 microseconds.

  Since we chose 800 dots/line horizontal resolution, we choose 600
  lines/frame as the vertical resolution.

  My display's manual says that the vertical sync pulse must be at least
  64 microseconds long.  In terms of lines, 64 microseconds is

  (64 microseconds/pulse) / (28.4 microseconds/line) = 2.25 lines/pulse
  We round 2.25 up to 3 lines for the vertical sync pulse.

  The manual says the time between the last displayed line and the start
  of the sync pulse must be at least 318 microseconds, and the delay
  after the end of the pulse must be at least 630 microseconds.  We
  calculate how many lines each of these time periods represents as
  follows.

  (318 microseconds) / (28.4 microseconds/line) = 11.20 lines

  (630 microseconds) / (28.4 microseconds/line) = 22.18 lines

  We round each of the times up to become 12 lines before the sync pulse
  and 23 lines after the pulse.  This makes our vertical timing numbers

  600 (600+12) (600+12+3) (600+12+3+23)

  or

  600 612 615 638

  Checking the frame rate to see if it falls within the rate of the
  display, we see that 638 lines/frame at 28.4 microseconds/line is
  18,119 microseconds/frame, which is 55.19 frames/second.  My display
  can handle anything from 50 Hz to 90 Hz, so the timing is all right.

  Putting the resolution, clock, horizontal, vertical timing numbers
  together on a video mode line in Xconfig results in

  "800x600"  40  800 832 992 1136  600 612 615 638

  This was the first video mode I tried.  It turned out not to be very
  satisfactory because there was too much flicker.  I tried other
  timings both above and below this setting as shown in the following
  example.  I finally settled on the "784x614" mode as a compromise
  between flicker and resolution.

  You'll notice that almost all of the clock frequencies are 40 MHz.
  Through experimentation I found that higher frequencies were beyond my
  adapter card's capabilities, and that lower frequencies didn't provide
  the resolution I wanted.

  Example: Timings I have tried:























       # the following line works but is right of center
       "752x564"  40  752  784  944 1088  564 567 569 611
       #        44.5  752 792  976 1240  564 567 570 600
       #
       # this line fixes the problem with the previous line
       #"752x564" 40  752  816  976 1088  564 567 569 611
       #
       # trying to increase the vertical display size, it works
       #"752x614" 40  752  816  976 1088  614 617 619 661
       #
       # trying to increase the horiz. display size, it works
       #"784x564" 40  784  816  976 1088  564 567 569 611
       #
       # the following works but is to the right of center
       #"784x614" 40  784  816  976 1088  614 617 619 661
       #
       # the following corrects the uncentered problem of the previous one
       "784x614"  40  784  848 1008 1088  614 617 619 661
       #
       # trying to increase the display size
       # the following works, the display is slightly off center to the left
       #"800x614" 40  800  864 1024 1088  614 617 619 661
       #
       # the following corrects the problem of the previous entry
       "800x614"  40  800  864 1024 1104  614 617 619 661
       #
       # increase the display size, it works
       "816x614"  40  816  880 1040 1120  614 617 619 661
       #
       # increase the display size, it works
       "800x620"  40  800  864 1024 1104  620 623 625 661
       #
       # increase the display size, it works
       "816x620"  40  816  880 1040 1120  620 623 625 661
       #
       # increase the display size, it works
       "832x630"  40  832  896 1056 1136  630 633 635 661
       #
       # change the display size, it works but flickers badly
       "848x618"  40  848  912 1072 1152  618 621 623 661




  12.  Fixing Problems with the Image.


  OK, so you've got your X configuration numbers.  You put them in
  Xconfig with a test mode label.  You fire up X, hot-key to the new
  mode, ... and the image doesn't look right.  What do you do?  Here's a
  list of common problems and how to fix them.

  You *move* the image by changing the sync pulse timing.  You *scale*
  it by changing the frame length (you need to move the sync pulse to
  keep it in the same relative position, otherwise scaling will move the
  image as well).  Here are some more specific recipes:

  The horizontal and vertical positions are independent.  That is,
  moving the image horizontally doesn't affect placement vertically, or
  vice-versa.  However, the same is not quite true of scaling.  While
  changing the horizontal size does nothing to the vertical size or vice
  versa, the total change in both may be limited.  In particular, if
  your image is too large in both dimensions you will probably have to
  go to a higher dot clock to fix it.  Since this raises the usable
  resolution, it is seldom a problem!

  The image is displaced to the left or right

  To fix this, move the horizontal sync pulse.  That is, increment or
  decrement (by a multiple of 8) the middle two numbers of the
  horizontal timing section that define the leading and trailing edge of
  the horizontal sync pulse.

  If the image is shifted left (right border too large, you want to move
  the image to the right) decrement the numbers.  If the image is
  shifted right (left border too large, you want it to move left)
  increment the sync pulse.

  The image is displaced up or down

  To fix this, move the vertical sync pulse.  That is, increment or
  decrement the middle two numbers of the vertical timing section that
  define the leading and trailing edge of the vertical sync pulse.

  If the image is shifted up (lower border too large, you want to move
  the image down) decrement the numbers.  If the image is shifted down
  (top border too large, you want it to move up) increment the numbers.

  The image is too wide (too narrow) horizontally

  To fix this, increase (decrease) the horizontal frame length.  That
  is, change the fourth number in the first timing section.  To avoid
  moving the image, also move the sync pulse (second and third numbers)
  half as far, to keep it in the same relative position.

  The image is too deep (too shallow) vertically

  To fix this, decrease (increase) the vertical frame length.  That is,
  change the fourth number in the second timing section.  To avoid
  moving the image, also move the sync pulse (second and third numbers)
  half as far, to keep it in the same relative position.

  Any distortion that can't be handled by combining these techniques is
  probably evidence of something more basically wrong, like a
  calculation mistake or a faster dot clock than the monitor can handle.

  Finally, remember that increasing either frame length will decrease
  your refresh rate, and vice-versa.

  $XConsortium: VidModes.sgml,v 1.3 95/01/27 16:14:33 kaleb Exp $
  Generated from XFree86: xc/programs/Xserver/hw/xfree86/doc/sgml/VidModes.sgml,v 3.5 1995/01/28 16:02:40 dawes Exp $