TDDD2MIF (1)    Imagine File to FrameMaker 1993/01/31     TDDD2MIF (1)


     [1mNAME[22m 

          TDDD2MIF  -  Convert  Imagine  Objects  to  FrameMaker (MIF)
          Format 


     [1mSYNOPSIS[22m 

          [1mTDDD2MIF[22m [[3moptions[0m][3m[0m[3m[0m [[3minput_file[0m][3m[0m[3m[0m [[3moutput_file[0m][3m[0m[3m[0m 


     [1mDESCRIPTION[22m 

          [1mTDDD2MIF[22m will read an Imagine object file in  binary  ([3mTDDD[0m[0m)
          or  ASCII  ([3mTTDDD[0m[0m)  format  (transparently to the user), and
          will output a  view  of  the  objects  in  FrameMaker's  MIF
          format.  

          By  default, all Turbo Silver "[1mEXTR[0m[0m" objects are read in and
          "internalized" so that Imagine can use them,  since  Imagine
          does not support "external" objects.  


     [1mOPTIONS[22m 


          -[1mall[22m 
                  Output  all  four  views  of the objects on a single
                  page.  (This is the default.) 

          [1m-top[0m[0m[3m[0m[0m[1m[0m[0m[3m[0m[0m[1m[0m[0m[3m[0m[0m 
                  Output only a top view of the objects.  

          [1m-front[0m[0m[3m[0m[0m[1m[0m[0m[3m[0m[0m[1m[0m[0m[3m[0m[0m 
                  Output only a front view of the objects.  

          [1m-right[0m[0m[3m[0m[0m[1m[0m[0m[3m[0m[0m[1m[0m[0m[3m[0m[0m 
                  Output only a right view of the objects.  

          [1m-iso[0m[0m[3m[0m[0m[1m[0m[0m[3m[0m[0m[1m[0m[0m[3m[0m[0m 
                  Output only an isometric view of the objects.  



     [1mIDENTIFICATION[22m 

          Author: Glenn M. Lewis 

          Revision Number: 38; Release Date: 1993/01/31.  



                                      -1-


     TDDD2MIF (1)    Imagine File to FrameMaker 1993/01/31     TDDD2MIF (1)


          The entire [3mT3DLIB[0m[0m collection of source and  executables  are
          Copyright   ©  1988-1993  by  Glenn  M.  Lewis.  All  Rights
          Reserved.  Source code of [3mT3DLIB[0m[0m may not be used in whole or 
          in part in any commercial endeavor without the prior written 
          permission of the author.  

          Imagine is Copyright © by Impulse Inc.  


     [1mSEE ALSO[22m 

          bumpit(1),    mbb(1),    readwrite(1),    set_brush_path(1),
          set_texture_path(1),  spherize(1), tddd2dxf(1), tddd2nff(1),
          tddd2off(1),    tddd2pov(1),    tddd2ps(1),     tddd2ray(1),
          tddd2vort(1) 


     [1mBUGS[22m 

          No bugs known.  
































                                      -2-